## Slide 1: About OMICS Group
OMICS Group International is an amalgamation of Open Access publications and worldwide international science conferences and events. Established in the year 2007 with the sole aim of making the information on Sciences and technology ‘Open Access’, OMICS Group publishes 400 online open access scholarly journals in all aspects of Science, Engineering, Management and Technology journals. OMICS Group has been instrumental in taking the knowledge on Science & technology to the doorsteps of ordinary men and women. Research Scholars, Students, Libraries, Educational Institutions, Research centers and the industry are main stakeholders that benefitted greatly from this knowledge dissemination. OMICS Group also organizes 300 International conferences annually across the globe, where knowledge transfer takes place through debates, round table discussions, poster presentations, workshops, symposia and exhibitions.

## Slide 2: About OMICS Group Conferences
OMICS Group International is a pioneer and leading science event organizer, which publishes around 400 open access journals and conducts over 300 Medical, Clinical, Engineering, Life Sciences, Phrama scientific conferences all over the globe annually with the support of more than 1000 scientific associations and 30,000 editorial board members and 3.5 million followers to its credit.
OMICS Group has organized 500 conferences, workshops and national symposiums across the major cities including San Francisco, Las Vegas, San Antonio, Omaha, Orlando, Raleigh, Santa Clara, Chicago, Philadelphia, Baltimore, United Kingdom, Valencia, Dubai, Beijing, Hyderabad, Bengaluru and Mumbai.

## Slide 3: Biodegradation of poly(ε-caprolactone)/poly(lactic acid) composites: The effect of fiber load and compatibilization
Presented By Akos Noel Ibrahim (PhD)
At
Material Science and Engineering Conference
San Antonio, USA October 06-08, 2014

## Slide 4: Introduction
The development of green composite materials has become necessary due to
environmental concern
over utilization and exploitation of resources that cannot be replaced or reintroduced into the environment.
This has prompted research interest in industries and the academic community.

## Slide 5: Introduction contd.
To solve the above mentioned problems materials scientist and engineers adopts the following.
Developing biodegradable materials with properties that can be manipulated.
Preparing polymeric materials without using toxic or noxious components
Developing materials that can naturally be broken down by the environment.

## Slide 6: Introduction contd.
To obtain eco-friendly composites, the following materials were used.
Natural fibers as reinforcement in composites production.
Biodegradable polymers (PCL and PLA) were used as matrix. This in addition to environmental protection is to reduce cost and also create a new class of composite materials.

## Slide 7: Figure1. Classification of Reinforcing Natural/Biofibers
Reinforcing natural/Biofibers
Non-wood natural/biofibers
Wood fibers
Straw fibers
Bast
Leaf
Seed/Fruit
Grass fibers
E.g. soft and hard woods
Recycled wood fibers E.g. Newspaper/magazines fibers
E.g. rice/wheat/corn straws
E.g. kenaf, flax, jute, hemp
E.g. henequen, sisal, pineapple leaf fiber
Bamboo fiber, switch grass

## Slide 8: Composition of natural fibers
All natural fibers whether wood or non wood are
Cellulosic in nature.
Cellulose and lignin are the major components found in natural biofibers.
Lignin is the material that gives support to the structure of plants.

## Slide 9: Table1. Chemical composition of some natural fibers
Fiber | Cellulose (%) | Lignin (%) | Hemicellulose (or pentosan) (%) | Pectin (%) | Ash (%)
Abaca | 56-63 | 7-9 | 15-17 | - | 3
Kenaf (bast) | 31-57 | 15-19 | 21.5-23 | - | 2-5
Hemp | 57-77 | 3.7-13 | 14-22.4 | 0.9 | 0.8
Ramie | 68.6-91 | 0.6-0.7 | 5-16.7 | 1.9 | -
Jute (bast) | 45-71.5 | 12-26 | 13.6-21 | 0.2 | 0.5-2
Henequen | 77.6 | 13.1 | 4-8 | - | -
Flax fiber | 71 | 22 | 18.6-20.6 | 2.3 | -

## Slide 10: Poly (lactic acid), PLA
PLA is a biodegradable thermoplastic that can be produced from sources that are considered renewable such as tapioca products, corn starch, and sugarcane.
PLA can be synthesized through condensation polymerization of lactic acid and ring opening polymerization of lactide to produce polylactide.
Properties
It is highly crystalline
Has Melting point of 150oC
Glass transition temperature between 60-65oC

## Slide 11: Figure 3: Synthesis of PLA

## Slide 12: Advantages of PLA
It is eco-friendly
Has good biocompatibility especially in biomedical applications
Has better thermal processibility than most biopolymers
Its production save’s energy as such reduces cost
Limitations of PLA
Its toughness is poor
It is hydrophobic
It is chemically inactive as such difficult to modify

## Slide 13: Poly (ε-caprolactone), PCL
PCL is petroleum derived synthetic biodegradable polymer.
It is tough at ambient temperature and fairly rigid with an average modulus like that of polyethylene.
PCL mixes a lot with other polymers and has some good mechanical properties.
Properties
It exhibits good solvent, oil, water, and chlorine resistance.
Has low melting point (Mpt) between 58-62oC.
Low glass transition temperature, Tg; -60oC.
PCL is a highly degradable polymer and semi crystalline.

## Slide 14: Figure 4: Preparation of Poly (ε-caprolactone)

## Slide 15: Advantages of PCL
It can be processed easily due to its low melting point
PCL is highly degradable and also eco-friendly
Has good biocompatibility especially in medical applications
Limitations of PCL
Its low Tg (-60°C) and melting point (58-62°C) reduces its chances of being used in some applications e. g. outdoor applications

## Slide 16: Research interest
In view of the above limitations, PCL and PLA were blended and reinforced with treated palm press fibers to achieve enhancement of the blends mechanical properties.
This is to expand the composites outdoor application areas.
To achieve the properties enhancement the following was employed to prepare the blends and composites.

## Slide 17: Methodology
  The palm fibers were washed and treated with sodium hydroxide after which they were dried, pulverized and a maximum of 400μm particle size used as reinforcement.
  The blends and composite specimens used for determinations were prepared using twin screw extruder and injection molding machine.

## Slide 18: Characterization
The Morphology and biodegradation of the fibers, blends and composites was studied using:
Field Emission Scanning Electron Microscopy (FESEM)
Fourier Transform Infrared Spectroscopy (FTIR)

## Slide 19: Results And Discussion
Fig. 1 FESEM micrographs of (a) untreated and (b) treated fibers

## Slide 20: Fig. 2 FTIR of treated, untreated fibers, uncompatibilized and compatibilized blend

## Slide 21: Fig. 3 FESEM micrographs of (a) PCL/PLA (90/10), (b) PCL/PLA/DCP (90/10/0.01phr) (c) PCL/PLA/TF (90/10/25), (d) PCL/PLA/TF/DCP (90/10/10/0.01phr)

## Slide 22: Biodegradation
Fig. 4 Residual weights of neat polymers, compatibilized blend and composites

## Slide 23: Fig. 5 FESEM micrographs after 90 days soil burial (a90) PCL (b90) PLA (c90) PCL/PLA/DCP (d90) PCL/PLA Mag. x500

## Slide 24: Fig. 6 FESEM micrographs after 90 days soil burial (e90) PCL/PLA/DCP/10 (f90) PCL/PLA/DCP/15 (g90) PCL/PLA/DCP/20 (h90) PCL/PLA/DCP/25 (i90) PCL/PLA/10 (j90) PCL/PLA/15 (k90) PCL/PLA/20 (l90) PCL/PLA/25 Mag. x500

## Slide 25: Conclusions
The following conclusions were drawn:
Optimized PCL/PLA composites were successfully prepared with treated palm press fibers.
The incorporation of DCP improved the blend compatibility and biodegradation.
The alkali treatment increased the interaction between the fibers and the matrix.
The rate of biodegradation of the composites increased with fiber load (10 wt. % to 25 wt. %)

## Slide 26
Thank You For Your Attention

## Slide 27: Let Us Meet Again
We welcome you all to our future conferences of OMICS Group International
Please Visit: http://materialsscience.conferenceseries.com/
Contact us at
materialsscience.conference@omicsgroup.us
materialsscience@omicsgroup.com