## Slide 1
PROCESS OPTIMIZATION OF BIOETHANOL PRODUCTION FROM PEELS OF CASSAVA CULTIVARS USING DIFFERENT MICROBIAL INNOCULANTS.
by
Uyoh Edak Aniedi1, Obianwa Chibuzor Uchenna1 and Igile Godwin2
Department of Genetics & Biotechnology1 and Department of Biochemistry2
UNIVERSITY OF CALABAR,
NIGERIA
AUGUST 2015

## Slide 2
CASSAVA IS CULTIVATED EXTENSIVELY AS A FOOD CROP IN NIGERIA AND OTHER TROPICAL REGIONS
PROCESSED INTO TAPIOCA, GARRI, FUFU AND CASSAVA FLOUR
3RD LARGEST SOURCE OF CARBOHYDRATE IN THE WORLD
THERE’S A GROWING INTEREST IN THE CONVERSION OF ORGANIC WASTES LIKE CASSAVA PEELS INTO USEFUL END-PRODUCTS LIKE BIOETHANOL.

## Slide 3
ATTRACTIVE FEATURES OF CASSAVA:
high yielding
able to grow on marginal soils
requires minimal labour and mangt costs
Thus, good candidate for bioethanol prod

## Slide 4
AIM OF STUDY - TO OPTIMIZE THE PRODUCTION OF BIOETHANOL USING DIFFERENT MICROBIAL INOCULANTS FOR THE SIMULTANEOUS SACCHARIFICATION AND FERMENTATION OF CASSAVA PEELS IN 3 CASSAVA VARIETIES .

## Slide 5: INNOCULANTS USED
    Aspergillus niger + Saccharomyces cerevisiae
    Aspergillus niger + Saccharomyces cerevisiae + Rhizopus nigricans
    Spirogyra africana + Saccharomyces cerevisiae + Rhizopus nigricans
    Aspergillus niger + Saccharomyces cerevisiae + Spirogyra africana
    Rhizopus nigricans + Saccharomyces cerevisiae

## Slide 6
METHODOLOGY :
Peels from 3 cassava cultivars TME 0505, TME 419, and TME 4779, were washed, dried in an oven at 120oC for 3hours, ground into a fine texture using a locally made milling machine & sieved with 1.5µ nylon sieve.
Cultured under anaerobic condition at different pH in small bioreactors using the five inoculants separately.

## Slide 7
Optical Density (microbial growth) was measured using a spectrophotometer every 3 days.
Trial fermentation was done to find out the optimal parameters required for high ethanol yields
Amount of Ethanol produced was recorded at 7, 14 & 21 days using optimal parameters

## Slide 8
Inoculum | Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21
Rhizopus/yeast | 1.131 (5) | 1.22 (4) | 1.339 (4) | 1.485 (5) | 1.33 (5) | 1.22 (5) | 1.064 (5) | 0.94 (5)
Aspergillus/yeast | 0.915 (6) | 1.272 (6) | 1.535 (5) | 1.383 (5) | 1.262 (5) | 1.255 (5) | 1.011 (5) | 0.901 (6)
Aspergillus/ Rhizopus/yeast | 1.12 (5) | 1.34 (5) | 1.401 (5) | 1.471 (5) | 1.125 (5) | 0.95 (6) | 1.001 (6) | 0.997 (6)
Rhizopus/Spirogyra/yeast | 0.804 (5) | 0.914 (5) | 1.42 (5) | 1.608 (5) | 1.632 (5) | 1.35 (6) | 1.226 (6) | 0.928 (6)
Aspergillus/ Spirogyra/ yeast | 0.929 (5) | 1.056 (5) | 1.614 (5) | 1.61 (5) | 1.456 (5) | 1.232 (6) | 1.325 (6) | 1.05 (6)
TABLE 1
Optical densities (indicating microbial growth) for different inoculum at 540nm and the observed pH (in brackets) in cassava cultivar TME 0505

## Slide 9
Chart: 
| Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21
Rhizopus/yeast | 1.131 | 1.22 | 1.339 | 1.485 | 1.33 | 1.22 | 1.064 | 0.94
Aspergillus/yeast | 0.915 | 1.272 | 1.535 | 1.383 | 1.262 | 1.255 | 1.011 | 0.901
Aspergillus/ Rhizopus/yeast | 1.12 | 1.34 | 1.401 | 1.471 | 1.125 | 0.95 | 1.001 | 0.997

Rhizopus/Spirogyra/yeast | 0.804 | 0.914 | 1.42 | 1.608 | 1.632 | 1.35 | 1.226 | 0.928

Aspergillus/ Spirogyra/ yeast | 0.929 | 1.056 | 1.614 | 1.61 | 1.456 | 1.232 | 1.325 | 1.05



## Slide 10
 | TME 419 |  |  |  |  |  |  |  | 
Inoculum | Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21 | 
Rhizopus/yeast | 1.03 (5) | 1.362 (4) | 1.345 (5) | 1.551 (5) | 1.194 (5) | 1.23 (6) | 0.992 (6) | 1.011 (6) | 
Aspergillus/yeast | 0.94 (5) | 0.997 (4) | 1.349 (5) | 1.245 (5) | 1.139 (5) | 1.147 (5) | 1.202 (6) | 1.101 (6) | 
Aspergillus/ Rhizopus/yeast | 0.983 (5) | 1.008 (5) | 1.42 (5) | 1.22 (5) | 1.036 (5) | 0.995 (6) | 1.002 (6) | 0.922 (6) | 
Rhizopus/Spirogyra/yeast | 0.801 (6) | 1.294 (5) | 1.643 (5) | 1.62 (5) | 1.52 (6) | 1.41 (6) | 1.229 (6) | 1.16 (8) | 
Aspergillus/ Spirogyra/ yeast | 0.903 (5) | 1.087 (5) | 1.639 (5) | 1.598 (5) | 1.401 (6) | 1.4 (6) | 1.34 (6) | 1.2 (8) | 
TABLE 2
Microbial growth from different inoculants at optical density of 540nm and the observed pH, in cultivar TME 419

## Slide 11
Chart: 
| Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21
Rhizopus/yeast | 1.03 | 1.362 | 1.345 | 1.551 | 1.194 | 1.23 | 0.992 | 1.011
Aspergillus/yeast | 0.94 | 0.997 | 1.349 | 1.245 | 1.139 | 1.147 | 1.202 | 1.101
Aspergillus/ Rhizopus/yeast | 0.983 | 1.008 | 1.42 | 1.22 | 1.036 | 0.995 | 1.002 | 0.922

Rhizopus/Spirogyra/yeast | 0.801 | 1.294 | 1.643 | 1.62 | 1.52 | 1.41 | 1.229 | 1.16

Aspergillus/ Spirogyra/ yeast | 0.903 | 1.087 | 1.639 | 1.598 | 1.401 | 1.4 | 1.34 | 1.2



## Slide 12
 | TME 4779 |  |  |  |  |  |  | 
Inoculum | Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21
Rhizopus/yeast | 0.929 (4) | 1.376 (5) | 1.629 (5) | 1.648 (5) | 1.243 (5) | 1.012 (5) | 1.002 (5) | 0.957 (5)
Aspergillus/yeast | 1.036 (5) | 1.245 (5) | 1.432 (5) | 1.307 (4) | 1.14 (5) | 1.125 (5) | 1.011 (6) | 0.942 (5)
Aspergillus/ Rhizopus/yeast | 1.075 (5) | 1.471 (5) | 1.587 (5) | 1.553 (5) | 1.229 (5) | 1.156 (6) | 1.114 (6) | 1.116 (6)
Rhizopus/Spirogyra/yeast | 1.049 (5) | 1.061 (5) | 1.634 (5) | 1.413 (5) | 1.476 (6) | 1.321 (6) | 1.225 (6) | 1.164 (8)
Aspergillus/ Spirogyra/ yeast | 1.096 (5) | 1.115 (5) | 1.628 (5) | 1.48 (6) | 1.296 (6) | 1.305 (6) | 1.312 (6) | 1.126 (8)
TABLE 3
Microbial growth for different inoculum at optical density of 540nm and the observed pH, on cassava cultivar TME 4779

## Slide 13
Chart: 
| Day 0 | Day 3 | Day 6 | Day 9 | Day 12 | Day 15 | Day 18 | Day 21
Rhizopus/yeast | 0.929 | 1.376 | 1.629 | 1.648 | 1.243 | 1.012 | 1.002 | 0.957
Aspergillus/yeast | 1.036 | 1.245 | 1.432 | 1.307 | 1.14 | 1.125 | 1.011 | 0.942
Aspergillus/ Rhizopus/yeast | 1.075 | 1.471 | 1.587 | 1.553 | 1.229 | 1.156 | 1.114 | 1.116

Rhizopus/Spirogyra/yeast | 1.049 | 1.061 | 1.634 | 1.413 | 1.476 | 1.321 | 1.225 | 1.164

Aspergillus/ Spirogyra/ yeast | 1.096 | 1.115 | 1.628 | 1.48 | 1.296 | 1.305 | 1.312 | 1.126



## Slide 14
RESULTS OF FERMENTATION AT OPTIMIZED PARAMETERS
pH 5.0, temperature 28oC, increased surface area of substrate, substrate concentration and inoculant culture concentration on Days 7, 14 and 21 are shown in tables 5, 6 and 7.

## Slide 15
TABLE 5
Ethanol yield obtained on the 7th day from three cassava cultivars treated with the different inoculants
 | TME 0505 |  | TME 419 |  | TME 4779 | 
inoculum | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm)
A | 13.33b ± 1.33 | 10.71b ± 1.07 | 13.33b ± 0.88 | 10.71b ± 0.71 | 17.33b ± 2.94 | 13.92b ± 1.88
B | 13b ± 0.58 | 10.44b ± 0.47 | 15.33 b ± 0.34 | 12.32 b ± 0.27 | 16.00 b ± 1.00 | 12.86 b ± 0.80
C | 13.33 b ± 0.34 | 10.71 b ± 0.27 | 14.66 b ± 0.88 | 11.78 b ± 0.71 | 16.00 b ± 0.00 | 12.85 b ± 0
D | 18a ± 1.00 | 14.46 a ± 0.80 | 18.33 a ± 2.03 | 14.73 a ± 1.63 | 23.67 a ± 0.67 | 19.01 a ± 0.53
E | 17.33 a ± 0.88 | 13.92 a ± 0.71 | 18 a ± 0.58 | 14.46 a ± 0.47 | 21.33 a ± 0.33 | 17.14 a ± 0.26
Control | 8.67c ± 1.20 | 6.96 c ± 0.97 | 8.67 c ± 1.46 | 6.96 c ± 1.17 | 11 c ± 1.00 | 8.84 c ± 0.80

## Slide 16
TABLE 6
Ethanol yield obtained on the 14th day from three cassava cultivars treated with different inoculants
 | TME 0505 |  | TME 419 |  | TME 4779 | 
inoculum | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm)
A | 12.33b ± 0.88 | 9.91 b ± 0.70 | 13.67 b± 0.88 | 10.98b ± 0.71 | 17 b ± 3.22 | 13.66 b ± 2.58
B | 17.67b ± 1.20 | 14.19b ± 0.97 | 17b ± 1.53 | 13.67 b ± 1.23 | 16 b ± 1.00 | 12.86b ± 0.80
C | 13.67b ± 1.20 | 10.97b ± 0.97 | 12.67b ± 0.34 | 10.17b ± 0.27 | 14b ± 2.33 | 11.24b ± 1.61
D | 15.67b ± 1.86 | 12.49b ± 1.46 | 14.46b ± 1.77 | 11.78b ± 1.42 | 21.33 b ± 0.88 | 17.14 b ± 1.87
E | 19.57a ± 1.33 | 15.8a ± 1.07 | 19a ± 1.16 | 15.26a ± 0.93 | 22.33a ± 0.88 | 17.94a ± 0.70
Control | 6.67c ± 0.88 | 5.89c ± 0.97 | 7c ± 0.58 | 5.62c ± 0.81 | 9.33c ± 2.60 | 9.34c ± 1.17

## Slide 17
TABLE 7
Ethanol yield obtained on the 21st day from three cassava cultivars treated with different inoculants
 | TME 0505 |  | TME 419 |  | TME 4779 | 
inoculum | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm) | vol (ml) | mass (g/cm)
A | 10.66b ± 0.34 | 8.57b ± 0.27 | 11.67b ± 1.20 | 9.37b ± 0.96 | 15.33b ± 2.33 | 12.32b ± 1.88
B | 14b ± 0.58 | 11.25b ± 0.47 | 15.33b ± 1.86 | 12.31b ± 1.49 | 13b ± 1.00 | 10.45b ± 0.80
C | 11b ± 0.58 | 8.84b ± 0.47 | 11.33b ± 0.33 | 9.11b ± 0.27 | 11b ± 0.58 | 9.37b ± 0.96
D | 17a ± 1.53 | 13.66a ± 1.22 | 15.67a ± 1.67 | 12.59a ± 1.34 | 22a ± 1.73 | 17.67a ± 1.39
E | 21a ± 1.53 | 16.87a ± 1.22 | 21.33a ± 0.66 | 17.14a ± 0.53 | 21.33a ± 0.34 | 17.14a ± 0.27
Control | 9.67c ± 0.67 | 7.77c ± 0.54 | 7.67c ± 0.88 | 6.16c ± 0.71 | 10c ± 1.00 | 8.03c ± 0.80

## Slide 18
Parameter Tested | TME 4779 | TME 419 | TME 0505
Moisture Content (%) | 62.19 | 63.59 | 64.15
Dry Matter (%) | 34.92 | 30.72 | 25.77
Starch (%) | 72.19 | 70.44 | 69.85
Fibre (%) | 3.42 | 3.22 | 3.12
Ash (%) | 0.45 | 0.47 | 0.28
Protein (%) | 2.25 | 1.15 | 1.26
Fat (%) | 0.61 | 0.72 | 0.78
Carbon Nitrogen Phosphorus(ppm) | 12.27 | 6.29 | 8.56
TABLE 8
Proximate Analysis of Cassava Cultivars

## Slide 19
DISCUSSION
The yield reported in this study competes favorably with (and sometimes better than) those reported from cassava peels using other inoculants, potato peels and spoilt mangoes by other workers.
Growth curves obtained using the five treatments differed slightly, reflecting differences in the enzymatic composition of these microorganisms and in the composition of peels of the three cassava varieties.

## Slide 20
An optimum pH of 5.0 obtained in this study is the pH at which each curve showed maximum activity.
Cassava cultivar 4779 when treated with Rhizopus nigricans, Spirogyra africana and Saccharomyces cereviceae gave the highest yield of 19.01g/cm3 and percentage concentration yield of 22% on the 7th day.
This may be attributed to the presence of Spirogyra as an additional carbon source for the microorganisms.

## Slide 21
Spirogyra generally is known to be autotrophic and its carbohydrate composition can also lead to increase in the release of sugars for fermentation. This result is in line with the work of Sulfahri et al., (2011) but gave a higher yield in the presence of cassava peel substrate and good pH conditions.

## Slide 22
Ethanol yield obtained in the present study is much lower than the 67.7% and 63.8% reported by Oyeleke and Jubril 2009 when Aspergillus niger and Zymomonas mobilis were used simultaneously on guinea corn husk and millet husk respectively.
In line with reports that Saccharomyces cerevisiae is a non- amylolytic microorganism unable to hydrolyse strarch ( Jumai et al., 2006), low concentrations of ethanol were obtained in this study.

## Slide 23
TME 4779 has the highest % starch composition of 72.19, Carbon-Nitrogen- Phosphorus (ppm) of 12.27 and dry matter of 34.92%; this may have contributed to the higher ethanol yield from it. Also the low fibre and ash content of cassava cultivar TME 0505 made it susceptible to quick microbial breakdown.

## Slide 24
CONCLUSION
The process of bioethanol production can be optimized for increased ethanol yield at a reduced period of fermentation by improving the various parameters affecting the medium (pH, substrate surface area and concentration).
Bioethanol production from Spirogyra holds a significant potential due to their low percentage of lignin and hemicellulose content compared to other ligno-cellulosic plants.

## Slide 25
Spirogyra can be cultivated and proliferated more, as a major feedstock for biofuel production.
Cassava cultivars can be developed with higher starch content and lower fibre values so that the wastes generated can have higher bioethanol potential.

## Slide 26
. There is need to invest in large-scale biotechnology plants for conversion of biomass (agricultural wastes) to useful products as this will provide wealth and employment.
. The use of agricultural wastes instead of staple foods for biofuel production will not infringe on available food supply. It will in addition reduce pollution arising from improper management of these wastes.

## Slide 27
THANKS FOR YOUR ATTENTION