## Slide 1: About OMICS Group
OMICS Group International is an amalgamation of Open Access publications and worldwide international science conferences and events. Established in the year 2007 with the sole aim of making the information on Sciences and technology ‘Open Access’, OMICS Group publishes 400 online open access scholarly journals in all aspects of Science, Engineering, Management and Technology journals. OMICS Group has been instrumental in taking the knowledge on Science & technology to the doorsteps of ordinary men and women. Research Scholars, Students, Libraries, Educational Institutions, Research centers and the industry are main stakeholders that benefitted greatly from this knowledge dissemination. OMICS Group also organizes 300 International conferences annually across the globe, where knowledge transfer takes place through debates, round table discussions, poster presentations, workshops, symposia and exhibitions.

## Slide 2: About OMICS Group Conferences
OMICS Group International is a pioneer and leading science event organizer, which publishes around 400 open access journals and conducts over 300 Medical, Clinical, Engineering, Life Sciences, Phrama scientific conferences all over the globe annually with the support of more than 1000 scientific associations and 30,000 editorial board members and 3.5 million followers to its credit.
OMICS Group has organized 500 conferences, workshops and national symposiums across the major cities including San Francisco, Las Vegas, San Antonio, Omaha, Orlando, Raleigh, Santa Clara, Chicago, Philadelphia, Baltimore, United Kingdom, Valencia, Dubai, Beijing, Hyderabad, Bengaluru and Mumbai.

## Slide 3: Green Chemistry at Merck – A Development Chemist’s Perspective
Ingrid Mergelsberg
Merck Process Chemistry, Merck & Co., Inc., Whitehouse Station, NJ
International Summit on Past and Present Research Systems of Green Chemistry
August 25-27, 2014 Philadelphia, USA

## Slide 4: About Merck
Named Merck in US and Canada; MSD elsewhere
More than 120 years old
Medicines, vaccines, animal health (and consumer products)
Our mission is to discover, develop and provide meaningful, innovative products that save and improve lives
Do so in a sustainable fashion so we can continue serving patients for another 120 years

## Slide 5: Green and Sustainable Chemistry at Merck
Greening Merck
Presidential Green Chemistry Award Winners
2005: Merck – A Redesigned, Efficient Synthesis of Aprepitant, the Active Ingredient in Emend®
2006: Merck – Novel Green Synthesis for β-Amino Acids Produces the Active Ingredient in Januvia™
2010: Merck – Greener Manufacturing of Sitagliptin Enabled by an Evolved Transaminase
Notes: 5

## Slide 6: What Do Process Chemists Do?
Provide active pharmaceutical ingredient (API) for development
  Preclinical: 1-10 kg
  Ph I: 10-20 kg
  Ph II: 50-200 kg
  Ph III: 200-2000 kg
    Requires a good synthetic route: safe, robust, productive, impurity control, API phase, reasonable cost, freedom to operate (intellectual property) and environmentally benign
Identify the manufacturing route for commercial supply
  Requires a great synthetic route to support the product for years to come. Need the lowest-cost route (consider emerging market and expanded access) and must be sustainable

## Slide 7: Key Message
Good science is the key to Green Chemistry and low- cost synthesis
  If we focus on developing the best chemistry, then, almost always, this leads to the lowest cost and greenest process
  “Best chemistry at launch” provides environmental and economical benefit over the lifetime of the product
  Innovation is the key for unbeatable chemistry
“In every case I know, the green option is the low-cost option” David Constable, 2008

## Slide 8: Diabetes: A Growing Worldwide Epidemic
18
23
14
33
132
1.3
14
16
9
27
85
1
23%
44%
50%
24%
57%
30%
Estimated incidence in 2010 (millions)
World
2000: 151 million
2010: 221 million (+46%)
Adapted from Amos AF et al. Diabet Med 1997;14:S7-S85.
Estimated incidence in 2000 (millions)
% increase from 2000 to 2010

## Slide 9: Sitagliptin: DPPIV Inhibitor for Diabetes Mellitus Type 2
First-in-class dipeptidyl peptidase-4 (DPPIV) inhibitor
Once-daily oral treatment
Approved by FDA in 2006
Active Ingredient in Januvia® and Janumet®
Notes: For Asymmetric Autocatalysis Enables an Improved Synthesis of Efavirenz, see E. M. Carreira, Angew. Chem. Int. Ed. 2011, 50, 2957 –2961. http://onlinelibrary.wiley.com/doi/10.1002/anie.201006689/pdf

## Slide 10: Efficient Synthesis: Sitagliptin, 1st GMP Delivery
>100 kg manufactured, 52% overall yield - 8 steps from acid 1
3 productive bond-forming steps (38% desired)
5 functional group manipulations (62% undesired)
Can we do it in only 3 steps?

## Slide 11: Is This Reaction Possible?

## Slide 12: Efficient Synthesis: Sitagliptin 1st-Generation Manufacturing Route: One-Pot Reaction
1 step (one-pot reaction, direction isolation) to ketoamide or enamine amide!
  Single solvent: compatible reagents to enable one-pot reaction
Need unprecedented asymmetric hydrogenation of unprotected enamine
  82% yield
  PMI = 14

## Slide 13: Efficient Synthesis: Sitagliptin 2nd-Generation Manufacturing Route: Chemocatalysis
New asymmetric hydrogenation
2-step synthesis, 63% overall yield
No protecting groups
Implemented at factory scale (>100 MT produced)
~80% reduction in PMI, no aqueous waste
0
50
100
150
200
250
300
Total Waste
Aqueous Waste
Waste Generated (kg)
1st Generation
New Route

## Slide 14: Supply of Critical Elements Is Not Sustainable
American Chemical Society
ACS Green Chemistry Institute®

## Slide 15: Sitagliptin 3rd-Generation Route: Ideal Process
Avoid formation of intermediate enamine?
Improve ee and avoid isolation of crude sitagliptin for ee upgrade?
Eliminate the high-pressure hydrogenation and specialized equipment?
Eliminate heavy metal and carbon treatment to remove it?
  Rh: $1,000 - $10,000 per ounce
Can we use an enzyme for the direct conversion?

## Slide 16: Efficient Synthesis: Biocatalysis With Enzymes
Environmentally benign technology
  Catalysts are grown in E. coli, renewable
  Operate in aqueous systems
Economically attractive
  Stable manufacturing costs
Enabling technology
  Opens access to unique synthetic sequences
More sustainable. It’s Green!

## Slide 17: Can We Use a Transaminase Enzyme?
Model with accumulated pocket mutations
Starting protein homology model
No activity with natural enzyme
Activity and selectivity established
Problem….Our substrate looks nothing like the natural a-ketoacid substrate
Enzyme
Evolution
cf
Notes: Modification and expansion of active site enabled pro-sitagliptin ketone to fit, establishing baseline activity. Only a single orientation of the substrate ketone (into the small and large binding pockets) prior to imine formation establishes the basis for selectivity.

## Slide 18: Codexis Collaboration – Enzyme Evolution
Unique technology for making enzyme improvements through amino acid changes
Define backbone: stable to solvents and temperature; easy to express, etc
Develop library of specificities on this backbone

## Slide 19: Sitagliptin: The Ultimate Manufacturing Process?
7th-round enzyme evolution (collaboration with Codexis), >95% conversion, >99.9%ee
PMI reduction from 30 to 23
Saves multi-million $/year versus the asymmetric hydrogenation approach
Lower costs enable the medicine to be available to emerging markets such as India
2010 EPA Presidential Green Chemistry award
Notes: The ultimate manufacturing route, which we are now using to makie sitagliptin employs a direct enzyme mediated amination of the same keto amide.
This occurs in high high yield and ee. We believe the reaction mechaniism proceeds via the well known biological enzymatic transamination mediated by an amino transferase and pyridoxal 5 phospahatre as co-factor. In this process isopropyl amine acts as N donor instead of alanaine in the natural process….acetone is removed to drive the process to completion….the key enzymatic step is the formal 1,3 shift that occurs in the catalytic site of the aminotransferase…
The amino transferase for this process was discovered in collaboratiin with a company called codexis….the initial yield in this reaction was about 1% with high

## Slide 20: Conclusion
Green Chemistry is a Merck corporate commitment
Low costs, Green Chemistry and good science go hand-in-hand
When it comes to developing a manufacturing route, it’s easy being green
GREEN
CHEMISTRY
CATALYTIC
ENERGY EFFICIENT
ATOM EFFICIENT
SAFE
AVOID WASTE
NON-TOXIC
ENVIRONMENTALLY
FRIENDLY
SUSTAINABLE
GOOD SCIENCE

## Slide 21: Let Us Meet Again
We welcome you all to our future conferences of OMICS Group International
Please Visit: www.omicsgroup.com
www.conferenceseries.com
www.pharmaceuticalconferences.com