## Slide 1: INTEGRATED RIVER BASIN MANAGEMENT IN WESTERN GHAT REGION THROUGH A CASE STUDY
Dr A B Anitha
Scientist F & Head
Surface Water Division
Centre for Water Resources Development and Management
Kozhikode ,Kerala
September 2014

## Slide 2: Need for an Integrated River Basin Management
No interdepartmental cooperation among the user Departments
  Downstream users are not aware of the upstream interventions
Integrated River Basin Management should consider multiple water uses in a river basin
Coordination with other sectors and levels of government –(nation planning , regional planning)
  Will help the planners and decision makers in solving water management issues

## Slide 3: Database
Survey of India Toposheets
Rainfall and Runoff data from IMD, CWC WRD, KSEB
IRS data for landuse classification
Present utilization and future demand of water from KWA, WRD, KSEB, KSPCB and Dept. of Industries
Block wise groundwater data from CGWB
Modern tools like GIS, GPS and Remote Sensing Techniques were used

## Slide 4: Hydrological Analysis Done
Spatial and temporal water availability and demand
Water quality status
Present water resources utilization
Future water resources demand
Spatial water balance
Surplus/deficit
Management strategies

## Slide 6
location details of raingauge stations.docx
Mean monthly rainfall.docx
Spatial and Temporal Distribution of Rainfall

## Slide 8
Isohyetal map of Chaliyar
Annual rainfall varies from 2130-4625 mm

## Slide 9
Location details of river gauging stations.docx
Spatial and Temporal Analysis of Runoff

## Slide 11: Mean monthly Surface Water Availability (MCM) in Chaliyar River Basin
Station | Area, Sq.km | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Total
Kuniyil | 1876 | 626 | 1262.9 | 952.6 | 503.1 | 420.6 | 240.8 | 73.9 | 38.4 | 12.7 | 9.3 | 7 | 43.6 | 4190.9
Koodathai | 117 | 76.1 | 154.9 | 119 | 52.3 | 49.5 | 35.3 | 15.4 | 6.6 | 3.7 | 2.9 | 2.8 | 8.3 | 526.8
Mukkom | 206.3 | 189.8 | 354.2 | 250.2 | 98.4 | 80 | 47.2 | 15.8 | 7.7 | 3.7 | 3.4 | 4.4 | 14.5 | 1069.3
Total | 2199.3 | 891.9 | 1772 | 1321.8 | 653.8 | 550.1 | 323.3 | 105.1 | 52.7 | 20.1 | 15.6 | 14.2 | 66.4 | 5787
Ungauged area | 723.7 | 241.5 | 162.6 | 82.5 | 22.1 | 5.0 | 0.6 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 514.4
Total Catchment area | 2923 | 1133.4 | 1934.6 | 1404.3 | 675.9 | 555.1 | 323.9 | 105.1 | 52.7 | 20.1 | 15.6 | 14.2 | 66.4 | 6301.4
T N Area | 388 | 9.4 | 13.2 | 22.7 | 35.1 | 98.8 | 124.9 | 43.3 | 6.5 | 2.4 | 14.9 | 8.1 | 22.7 | 402
Kerala | 2535 | 1124.0 | 1921.4 | 1381.6 | 640.8 | 456.3 | 199.0 | 61.8 | 46.2 | 17.7 | 0.7 | 6.1 | 43.7 | 5899.4
Total Surface Water Availability in Kerala |  |  |  |  |  |  |  |  |  |  | 5899 MCM |  |  | 

## Slide 12: Utilizable Yield (MCM) of Chaliyar river Basin
Station | Area, Sq.km | Jun | Jul | Aug | Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May | Total
Kuniyil | 1876.0 | 626.0 | 1262.9 | 952.6 | 503.1 | 420.6 | 240.8 | 73.9 | 38.4 | 12.7 | 9.3 | 7.0 | 43.6 | 4190.9
Highland | 1313.2 | 372.5 | 751.4 | 566.8 | 299.3 | 250.3 | 143.3 | 44.0 | 22.8 | 7.6 | 5.5 | 4.2 | 25.9 | 2493.6
Midland | 562.8 | 126.8 | 255.7 | 192.9 | 101.9 | 85.2 | 48.8 | 15.0 | 7.8 | 2.6 | 1.9 | 1.4 | 8.8 | 848.7
 | Total | 499.2 | 1007.2 | 759.7 | 401.2 | 335.4 | 192.0 | 58.9 | 30.6 | 10.1 | 7.4 | 5.6 | 34.8 | 3342.2
Koodathai | 117.0 | 76.1 | 154.9 | 119.0 | 52.3 | 49.5 | 35.3 | 15.4 | 6.6 | 3.7 | 2.9 | 2.8 | 8.3 | 526.8
Highland | 46.8 | 25.9 | 52.7 | 40.5 | 17.8 | 16.8 | 12.0 | 5.2 | 2.2 | 1.3 | 1.0 | 1.0 | 2.8 | 179.1
Midland | 70.2 | 25.1 | 51.1 | 39.3 | 17.3 | 16.3 | 11.6 | 5.1 | 2.2 | 1.2 | 1.0 | 0.9 | 2.7 | 173.8
 | Total | 51.0 | 103.8 | 79.7 | 35.0 | 33.2 | 23.7 | 10.3 | 4.4 | 2.5 | 1.9 | 1.9 | 5.6 | 353.0
Mukkom | 206.3 | 189.8 | 354.2 | 250.2 | 98.4 | 80.0 | 47.2 | 15.8 | 7.7 | 3.7 | 3.4 | 4.4 | 14.5 | 1069.3
Highland | 140.4 | 109.8 | 204.9 | 144.8 | 56.9 | 46.3 | 27.3 | 9.1 | 4.5 | 2.1 | 2.0 | 2.5 | 8.4 | 618.7
Midland | 66.1 | 40.0 | 74.6 | 52.7 | 20.7 | 16.9 | 9.9 | 3.3 | 1.6 | 0.8 | 0.7 | 0.9 | 3.1 | 225.3
 | Total | 149.8 | 279.6 | 197.5 | 77.7 | 63.1 | 37.3 | 12.5 | 6.1 | 2.9 | 2.7 | 3.5 | 11.4 | 844.0
Total Catchment | 2199.3 | 700.0 | 1390.5 | 1036.9 | 513.9 | 431.7 | 252.9 | 81.7 | 41.1 | 15.5 | 12.0 | 10.9 | 51.8 | 4539.2
Runoff in T N Area | 388.0 | 9.4 | 13.2 | 22.7 | 35.1 | 98.8 | 124.9 | 43.3 | 6.5 | 2.4 | 14.9 | 8.1 | 22.7 | 402.0
Utilizable yield in Kerala |  | 690.6 | 1377.3 | 1014.2 | 478.8 | 332.9 | 128.0 | 38.4 | 34.6 | 13.1 | -2.9 | 2.8 | 29.1 | 4137.2
Monsoon yield | 4021.9 |  |  |  |  |  |  |  |  |  |  |  |  | 
Non monsoon yield | 115.2 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 13
Month | Dependability | Maruthapuzha | Punnapuzha | Karimpuzha | Chaliyar | Kanchirapuzha |  | Kuthirapuzha | Areacode | Mukkom | Koodathai | Kuniyil
Dec | 50% | 7.1 | 18.7 | 26.2 | 17.1 | 3.7 | 8.4 |  | 64 | 15.8 | 14 | 65.5
 | 75% | 5 | 14.3 | 16.6 | 8.7 | 2.5 | 6.3 |  | 31 | 8.8 | 7 | 45.6
 | 90% | 4 | 9.2 | 9 | 4.7 | 0.7 | 3.9 |  | 8.7 | 3.9 | 4.3 | 0
Jan | 50% | 4 | 10 | 11 | 9.1 | 2 | 5.1 |  | 33 | 7 | 4 | 29.3
 | 75% | 2.5 | 4.9 | 1 | 4.7 | 0.6 | 3 |  | 19.1 | 3.7 | 0 | 3.6
 | 90% | 1 | 2.8 | 0 | 1.1 | 0 | 0.9 |  | 5.5 | 0.2 | 0 | 0
Feb | 50% | 2.2 | 4.2 | 4.2 | 5.5 | 1 | 2.1 |  | 18 | 2 | 2 | 11.1
 | 75% | 1.7 | 1.4 | 0 | 3.1 | 0.2 | 1 |  | 7.3 | 0.9 | 0 | 0
 | 90% | 0 | 0 | 0 | 0 | 0 | 0 |  | 1.9 | 0 | 0 | 0
Mar | 50% | 2.2 | 3.2 | 1.5 | 5.1 | 0.2 | 1.2 |  | 14 | 2 | 1.6 | 4.7
 | 75% | 0.9 | 0 | 0 | 0 | 0 | 0 |  | 5.2 | 0 | 0 | 0
 | 90% | 0 | 0 | 0 |  | 0 | 0 |  | 1.1 | 0 | 0 | 0
Apr | 50% | 2.2 | 3.9 | 1.1 | 4.3 | 0.2 | 1.8 |  | 12 | 2.1 | 2.1 | 2.6
 | 75% | 1 | 0.5 | 0 | 0.7 | 0 | 0 |  | 2.5 | 0 | 0 | 0
 | 90% | 0 | 0 | 0 | 0 | 0 | 0 |  | 0.5 |  | 0 | 0
May | 50% | 3 | 5.9 | 8.1 | 6.7 | 1 | 6.3 |  | 20 | 9 | 4 | 12.3
 | 75% | 2 | 2.4 | 2 | 2 | 0 | 3.2 |  | 7.4 | 2 | 0 | 0
 | 90% | 0 | 0.6 | 0 | 0.6 | 0 | 0 |  | 2.7 | 0.6 | 0 | 0
50%, 75% and 90% dependable flows of sub basins of Chaliyar

## Slide 14: Flow Duration Curves
Chart: Fig 3.11 Flow duration curves -Kuniyil Station for summsr months
| 3.3333333333333335 | 6.666666666666667 | 10 | 13.333333333333334 | 16.666666666666664 | 20 | 23.333333333332913 | 26.666666666666668 | 30 | 33.333333333333329 | 36.666666666665975 | 40 | 43.333333333333336 | 46.666666666665975 | 50 | 53.333333333333336 | 56.666666666665975 | 60 | 63.333333333333329 | 66.666666666666657 | 70 | 73.333333333333258 | 76.666666666666671 | 80 | 83.333333333333258 | 86.666666666666671 | 90 | 93.333333333333258 | 96.666666666666671
Dec | 215.8 | 154.6 | 145.8259 | 142.4057 | 138.2352 | 127.7859 | 118 | 102.9 | 91.6 | 91.1 | 77.7 | 70.5 | 69.1 | 66.2709 | 65.5 | 62.5 | 55.3 | 53.6 | 51.4 | 46.9 | 46.7 | 46 | 45.6 | 44.1252 | 9.2664 | 4.7032 | 0 | 0 | 0
Jan | 294.1911 | 82.1 | 65.0865 | 53 | 51.5835 | 51.1 | 49.7405 | 46.6 | 44.4 | 37.5 | 36.7 | 35 | 33 | 32.6 | 29.3 | 28.6 | 28.3 | 24.8 | 22.9 | 21.9 | 21.5 | 20.8 | 3.6366 | 0 | 0 | 0 | 0 | 0 | 0
Feb | 54.5472 | 32.5296 | 28.7 | 26.4 | 22.2 | 18.1 | 16.1654 | 15.6 | 15.2 | 14.8 | 14.7 | 14.6 | 14.4 | 13.6 | 11.1 | 10.2 | 9.8 | 9.5 | 8.6 | 8.6 | 8.4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Mar | 63.0063 | 55.1802 | 26.6 | 22.8 | 14.9 | 12.8 | 10.6 | 8.7 | 8.7 | 7.2 | 6.8 | 6.5 | 5.2 | 4.7 | 4.7 | 4.2 | 4.1 | 3.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Apr | 63.0409 | 20.1 | 20 | 19.1 | 16.7 | 9.2 | 8.5 | 7.9 | 7.1 | 7 | 5.5 | 4.6 | 4.1 | 3.8 | 2.6 | 1.9 | 1.5682 | 1.4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
May | 333.1235 | 295.3 | 171.9257 | 97.3 | 92.1969 | 48.6 | 33.5 | 26.7 | 25.1 | 21.7 | 19.4 | 19.1 | 16.2 | 12.8 | 12.3 | 11.3 | 9.8 | 7.7 | 6.7 | 4.7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 15
  GROUNDWATER RESOURCES OF CHALIYAR
Groundwater resources of Chaliyar.docx

## Slide 18: Water Availability
Surface Water
Monsoon flow: 5723 MCM
Non monsoon: 176 MCM
Utilizable flow
Monsoon flow: 4022 M MCM
Non monsoon: 115 MCM
Groundwater Potential:283.25 MCM
GW Draft : 140 MCM 4 blocks semi critical ;
8 Blocks safe

## Slide 19: Water Quality Status
Higher level of dissolved solids in coastal region
75% of wells show significant level of nitrate
bore wells having high iron
Except for pH, all the quality variables comply with the desirable limit
The spatial trends of chloride, sulphate, sodium and calcium
Low concentrations of these constituents confirming the good quality of water except few wells in the coastal area.

## Slide 21
STATUS OF WATER RESOURCES UTILIZATION AND FUTURE DEMAND FOR VARIOUS PURPOSES

## Slide 22: Water for Domestic Purpose
Present Utilization
  No. of Schemes: 42 Schemes in Kozhikode &
  Malappuram Districts
  - Water utilization - 218 MLD
  80 MCM
  Future Demand
    No. of new Schemes – 45
  Water utilization - 409 MLD
  150 MCM

## Slide 24: Water for Irrigation
No major schemes
One medium scheme for salinity arresting
  4 Diversion Schemes
  24 Lift Irrigation Schemes
  30 Vented Cross Bars
  4 Ongoing medium schemes
  Net irrigated area - 15,423 ha
  Proposed schemes
  - 6 major,5 medium and many check dams
  Net area to be irrigated – 20,368 ha

## Slide 25
Topographical View of Regulator cum Bridge
at Kavanakkallu
Upstream view of Kavanakkallu Regulator-cum Bridge
EXISTING WATER RESOURCES STRUCTURES

## Slide 27: Hydel Power Generation
Present Utilisation
4 small hydro electric schemes in Chaliyar river basin which produces 16.6 MW power making use of 308 MCM of water.
Four schemes are under construction which can produce 17.7 MW power making use of 183 MCM of water
Future Schemes
- 3 major schemes
-12 small hydel schemes
- 15 small shcemes under feasibility stage
Power generation – 342 MW, 932.13 MU, 1437 MCM

## Slide 29: Water for other purposes
INDUSTRIAL WATER REQUIREMENT-12.35 MCM
WATER FOR SALINITY EXCLUSION-184MCM
INLAND NAVIGATION 39 Km length
  ECOLOGICAL BALANCE 10-15 % of Annual flow
  17 MCM during non monsoon months

## Slide 30
Season | Utilizable potential, MCM |  |  | Present utilization, MCM | Surplus/Deficit MCM | Future DemandMCM | Surplus/Deficit MCM
 | Surface | Ground | Total |  |  |  | 
Monsoon | 4022 | 56 | 4078 | 46.5 | Surplus | 87 | Surplus
Non monsoon | 115 | 84 | 199 | 332.5 | Deficit (-133.5) | 413 | Deficit (-214)
Water Balance

## Slide 31: CONCLUSIONS
Chaliyar basin is at present deficit by 133.5 MCM of water during non monsoon period and will have a deficit of fresh water of 214 MCM by 2040 AD
For successful planning, implementation and management of a river basin ,there should be an organization at the basin level for all developmental activities related to water resources irrespective of administrative boundaries
Few more projects are needed for the sustainable development of the river basin.

## Slide 32
Thank you