## Slide 1: Algorithms for Optimal Scheduling of Multiple Spacecraft Maneuvers
Motivation Maneuvers SSV P2P Conclusions
. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .
Atri Dutta
Aerospace Engineering Wichita State University
International Conference and Exhibition on Satellite Houston, TX
August 19, 2015

## Slide 2: WSU Astronautics Research Laboratory (2014 –)
Motivation Maneuvers SSV P2P Conclusions
Multi-rendezvous mission planning
All-electric satellites Spacecraft attitude control
CubeSat for science experiments and technology demonstration

## Slide 3: Presentation Overview
Motivation Maneuvers SSV P2P Conclusions
Motivation
Optimal Transfer for a Spacecraft
3
Maneuvers by a Single Servicing Spacecraft
4 Peer-to-Peer Maneuvers
5
Concluding Remarks

## Slide 4: Active Debris Removal
Motivation Maneuvers SSV P2P Conclusions
Recent studies have indicated that at least 5 objects need to be removed every year for stable on-orbit debris management
Many debris removal techniques likely require multi-rendezvous mission planning

## Slide 5: Servicing of Satellite Constellations
Motivation Maneuvers SSV P2P Conclusions

## Slide 6: Mixed Servicing Strategy
Motivation Maneuvers SSV P2P Conclusions
Mixed strategy outperforms the single service vehicle strategy with increasing number of satellites in the constellation
Mixed strategy does even better with asynchronous maneuvers and optimal P2P trip times
*Dutta and Tsiotras, “Asynchronous Optimal Mixed Peer-to-Peer Satellite Refueling Strategies,” Journal of the Astronautical Sciences, Vol. 54 (3-4), Dec 2006, pp. 543-565.

## Slide 7: Challenges
Motivation Maneuvers SSV P2P Conclusions
Continuous optimization: optimization over transfers
Combinatorial aspects: target selection, optimization over sequences
NP-hard: polynomial time algorithm
Researchers have used genetic algorithms, branch-and-bound methods, Greedy random adaptive search procedures

## Slide 8: Greedy Random Adaptive Search Procedure
Motivation Maneuvers SSV P2P Conclusions
Widely used in operations research community to solve k-assignment problem
Multiple phases: construction of a basic feasible solution, local search, path relinking
Known to yield good quality solutions
X
X
X

## Slide 9: Presentation Overview
Motivation Maneuvers SSV P2P Conclusions
Motivation
Optimal Transfer for a Spacecraft
3
Maneuvers by a Single Servicing Spacecraft
4 Peer-to-Peer Maneuvers
5
Concluding Remarks

## Slide 10: Two-Impulse Transfer
Motivation Maneuvers SSV P2P Conclusions
Multi-revolution solutions to Lambert’s Problem

## Slide 11: Circular Orbit Rendezvous Cost (1 of 2)
Motivation Maneuvers SSV P2P Conclusions
Transfer time t f (TU)
Lead angle  0 (deg)
1
2
3 4
5
6
−300
−200
−100
0
100
200
300
0.3
2 0.5
4 1
1 2 4
0.3
0.5
0.3
0.5
1
10 7 4 2
2 4

## Slide 12: Circular Orbit Rendezvous Cost (2 of 2)
Motivation Maneuvers SSV P2P Conclusions
0
1
2
4
5
6
0
10
8
6
4
2
14
12
3
Time (TU)
 V (TU)
No coasting Coasting

## Slide 13: Low-Thrust Rendezvous
Motivation Maneuvers SSV P2P Conclusions
Lower the propulsive cost of missions
Enhance the flexibility of missions

## Slide 14: Presentation Overview
Motivation Maneuvers SSV P2P Conclusions
Motivation
Optimal Transfer for a Spacecraft
3
Maneuvers by a Single Servicing Spacecraft
4 Peer-to-Peer Maneuvers
5
Concluding Remarks

## Slide 15: Problem Statement
Motivation Maneuvers SSV P2P Conclusions
Service vehicle needs to visit m out of n candidate targets
s1, s2, . . . , sn
Sequence σ : J ›→ I, where J = {1, 2, . . . , m} and
I = {1, 2, . . . , n}
Time at which transfers take place: τi , where i ∈ J , Time duration of the maneuvers: t (σ(i ), σ(j )), where i , j ∈ J , Maximum mission time T
Objective is to minimize cost of a sequence
min C(σ(I))
σ(I)

## Slide 16: Basic Feasible Solution
Motivation Maneuvers SSV P2P Conclusions
Set time duration for the transfers to be equal at the beginning
t (σ(i ), σ(i + 1)) =
T
m + 1
, for all i ∈ I
Cost is uniquely defined for each transfer (i , j ), only a subset of these transfers are considered based on some user-defined value η
E0 = E\{(i , j ) : c (i , j ) > c + η(c¯ − c )}
The elements of σ(J ) are picked in m iterations, with the element k being picked in the k th iteration
(k − 1, k ) ∈ Ek−1
Selection of a target will make irrelevant several transfers that are dropped from the set being considered

## Slide 17: Local Search (1 of 2)
Motivation Maneuvers SSV P2P Conclusions
Difference between two sequences:
δ (σ1, σ2) = {k : σ1(k ) ƒ= σ2(k )}
Distance between two sequences is simply the cardinality of the difference between them:
d (σ1, σ2) = |δ (σ1, σ2) |
Neighborhood of the sequence is given by all sequences that have distance less than or equal to k

## Slide 18: Local Search (2 of 2)
Motivation Maneuvers SSV P2P Conclusions
S0
S1
S2
We consider k ≤ 2
(a) {0, 3, 4, 1, 0} and {0, 3, 2, 1, 0}
(b) {0, 3, 4, 1, 0} and {0, 3, 1, 4, 0}
S3
S4
S0
S1
S2
S3
S4
(a)
(b)

## Slide 19: Numerical Example
Motivation Maneuvers SSV P2P Conclusions
Visiting 5 satellites out of 8 in a circular orbit.
 | Basic Feasible Solution | Cost (DU/TU) | Targets Not Visited
- | s0 → s5 → s2 → s7 → s3 → s8 → s0 | 0.6730 | s1, s4, s6
1 | s0 → s5 → s2 → s7 → s3 → s1 → s0 | 0.6166 | s4, s6, s8
2 | s0 → s5 → s1 → s7 → s3 → s2 → s0 | 0.5820 | s4, s6, s8
3 | s0 → s5 → s1 → s7 → s4 → s2 → s0 | 0.0036 | s3, s6, s8
4 | s0 → s5 → s1 → s6 → s4 → s2 → s0 | 0.0025 | s3, s7, s8
5 | s0 → s5 → s1 → s6 → s4 → s2 → s0 | 0.0025 | s3, s7, s8

## Slide 20: Optimal Transfer Time Allotments
Motivation Maneuvers SSV P2P Conclusions
0 1
0
1
5
4
3
2
2 3 4
Time (TU)
 V (TU)
i3
6 A
i0
B A
i1 i1
i
B 2 A
i2B
A B
i3 i4
A B A B
i4 i5 i5 i6
5 6
Binary Integer Programming Problem (Shen and Tsiotras, 2003)
Iterative algorithm: avoid the solution of the binary integer programming problem (ASC, 2015)

## Slide 21: Presentation Overview
Motivation Maneuvers SSV P2P Conclusions
Motivation
Optimal Transfer for a Spacecraft
3
Maneuvers by a Single Servicing Spacecraft
4 Peer-to-Peer Maneuvers
5
Concluding Remarks

## Slide 22: Problem Statement
Motivation Maneuvers SSV P2P Conclusions
Given
Fuel-deficient satellites Service spacecraft Satellite characteristics
Maximum time for mission Allow
Orbital transfers for delivery of fuel to fuel-deficient satellites
Goal
Minimum fuel expenditure during the overall refueling mission
All satellites must be fuel-sufficient at the end of refueling mission

## Slide 23: P2P Maneuver and Constellation Graph
Motivation Maneuvers SSV P2P Conclusions
Satellite roles (active/ passive) not known apriori!
Feasible P2P Maneuvers
Active satellites have enough fuel to complete their forward trips
Both satellites must be fuel-sufficient at the end of a P2P maneuver

## Slide 24: NP-hard P2P Problem
Motivation Maneuvers SSV P2P Conclusions
Figure: E-P2P Maneuver.
Assumption: All satellites are similar, perform similar functions and can interchange their orbital positions.
3-index assignment problem
Good-quality solutions
*Dutta and Tsiotras, “An Egalitarian Peer-to-Peer Satellite Refueling Strategy,” Journal of Spacecraft and Rockets, Vol. 45 (3), 2008, pp. 608-618.
*Coene, Spieksma, Dutta and Tsiotras, “On the Computational Complexity of P2P Refueling Strategies,” INFOR: Information Systems and Operational Research, Vol. 50, No. 2, 2012, pp. 88-94.

## Slide 25: P2P Local Search
Motivation Maneuvers SSV P2P Conclusions

## Slide 26: General P2P Strategy
Motivation Maneuvers SSV P2P Conclusions
C-P2P + E-P2P
Theorem
CLB ≤ CCE ≤ min{CC, CE}
Lower Bound Computation
Bipartite matching Solvable in polynomial time
Figure: C-P2P Maneuver. Figure: Global Minima (Cost = Lower Bound).
*Dutta and Tsiotras, “A Network Flow Formulation for Cooperative Peer-to-Peer Refueling Strategies,” Journal of Guidance, Control and Dynamics, Vol. 33(5), 2010, pp. 1539-1549.

## Slide 27: Comparison of (Impulsive) P2P Strategies
Motivation Maneuvers SSV P2P Conclusions
*Dutta, “Optimal Cooperative and Non-Cooperative Peer-to-Peer Maneuvers for Refueling Satellites in Circular Constellations,” Ph.D. Dissertation, Georgia Institute of Technology, Atlanta GA USA, 2009.

## Slide 28: Presentation Overview
Motivation Maneuvers SSV P2P Conclusions
Motivation
Optimal Transfer for a Spacecraft
3
Maneuvers by a Single Servicing Spacecraft
4 Peer-to-Peer Maneuvers
5
Concluding Remarks

## Slide 29: Concluding Remarks
Motivation Maneuvers SSV P2P Conclusions
GRASP Methodology is useful for both types of multi-rendezvous maneuver planning problem
Good-quality solutions for P2P servicing problem
Preliminary framework developed for SSV case
Straightforward to incorporate operational constraints like mandatory target visits and imposed roles on satellites
GRASP methodology can incorporate low-thrust transfers and cooperative rendezvous maneuvers
Future research focussed on extending the studies in a number of ways