## Slide 1: Acetic Acid Removal from Pretreated Wood Extract
Dr. Aymn Abdulrahman
Monday, September 12th, 2016
University of Jeddah, Department of Chemical Engineering, Jeddah, Saudi Arabia
University of Maine, Department of Chemical and Biological Engineering, Orono, Maine 04469 USA

## Slide 2: Outline
Introduction
Motivation
Objectives
Material and Method
Procedure
Results and Conclusion
Future Work
Acknowledgment

## Slide 3
Maine is a Forest state ( covers 90 % of the state)
STRATEGIC GOAL : Evolve existing pulp mills into forest biorefineries.
  Pulp, paper, and wood products
  Renewable energy
  Chemical products
INTEGRATED FOREST BIOREFINERY

## Slide 4: Deriving optimal value from wood components
Cellulose: strong fibers
Lignin: highest energy density
Hemicellulose:
low strength
low energy density
Most soluble
Fermentation feedstock?

## Slide 5
Van Heiningen Process: From Lab to Mill Floor – Success of DOE FC36-04GO14306 (2004-08)
Forest Products Industry of the Future ,Drew Ronneberg, DOE Headquarters
Notes: 5

## Slide 6: Overall Pulp and Biorefinery
Wood Chips
Hot Water
Extractor
Kraft pulping process
Green Liquor
Wood chips
Pulp and paper
Lignin Removal
HAc Removal
Ethanol
Fermentation
water
Acid Hydrolysis
Sulfuric Acid
Sugar Concentration
Solvent
Solvent+ HAc
Distillation
HAc

## Slide 7: Motivation
Acetic acid is a valuable product
Acetic acid can inhibit ethanol fermentation
Acetic acid presents in extract:
GL extract : 8-9 g/L
HW extract :1-3 g/L
Acetic acid structure

## Slide 8: Lignocellulose Extraction
USDA Agricultural Research Service
http://www.biomassmagazine.com/article-print.jsp?article_id=1533
7 acetyl groups per every 10 xyloses

## Slide 9: Alkaline Hydrolysis
-
Saponification
Apply under alkaline condition
Ref. (Sjostrom, 1993)

## Slide 10: Hemicellulose Extract
Extraction :
  Using a 60 L rotating digester
  7 kg ( dry weight) of fresh chips (16mm 22.6mm 3mm)
  Mixing with green liquor (1.4 % of Na2O)
  Ratio of Liquid : Wood chip=4:1
  Rotating speed (2 rpm) at 160 ◦C for 110 minutes
  Collecting the free-draining extract
Secondary Hydrolysis of Extract:
  with 4 % (w/v) H2SO4 for 60 min at 121C

## Slide 11
Composition of Extract | GL Extract2 [g/L] | GL Extract3 [g/L]
Glucose | 0.09 | 0.36
XMG1 | 0.11 | 1.62
Arabinose | 0.02 | 0.24
Acetic Acid | 8.32 | 9.40
Total Sugars | 0.22 | 2.22
Composition of 3 % Na2O Green Liquor (GL) Extracted Northern Hardwood
a 1 xylose, mannose, and galactose, 3 secondary hydrolyzed with 72 % sulfuric acid, 2 analyzed without secondary hydrolysis. ( By Dr. Um)

## Slide 12: Objectives
Recovery of acetic acid from hemicellulose extract
Optimization of Liquid-Liquid Extraction (pH, ratio of org: aq. )
Recycling of solvent by distillation
Select between two solvents
Determine the most efficient configuration of the extraction system

## Slide 13: Methods
Liquid-Liquid Extraction
  Clean System (Acetic acid in DI-water) (10 g/L)
  Hemicellulose Extract (GL extract)
Separations
  Centrifuge
  Distillation

## Slide 14: Extraction Flow Diagram
Hemicellulose Extract
Liquid-Liquid Extraction
Fermentation
Solvent
Solvent + HAc
Distillation
HAc
Centrifuge
Centrifuge
Pure Acetic Acid Recovery
Solvent
Aqueous Phase
Solvent Recycle
Volatile solvent

## Slide 15: Materials
Solvent
  Trioctylphosphine oxide (TOPO)
  ( [CH3(CH2)7]3PO mol wt. 386.64 )
  Undecane ( C11H24, mol. wt. 156.3 )
  Trioctylamine (TOA) ( [CH3(CH2)7]3N mol wt. 353.67 )
  Octanol ( CH3(CH2)7OH mol wt. 130.23 )
Acetic Acid ( CH3COOH )
Sulfuric acid ( H2SO4 )
Sodium Hydroxide ( 0.05 M NaOH )
( using phenolphthalein as indicator )

## Slide 16: TOPO
Strong solvating extractant
Strong hydrogen bonding acceptors, induces the carboxylic acid to transfer to the extract phase
CH3COOH + TOPO(org) CH3COOH(TOPO)org
High boiling point
Excellent chemical stability
Low solubility in water
Expensive component (dilute with undecane + recycle)
Molecular Formula: [CH3(CH2)7]3PO
Molecular Wight : 386.64
Melting Point: 50-55 ºC
Boiling Point: 201-202 ºC
Trioctylphosphine oxide

## Slide 17: TOA
Strong solvating extractant
CH3COOH + TOA(org) CH3COOH(TOA)org
High boiling point
Low solubility in water
Less expensive component
Molecular Formula: [CH3(CH2)7]3N
Molecular Wight : 353.67
Melting Point: -40 ºC
Boiling Point: 365 – 367 ºC
Trioctyl amine

## Slide 18: Analysis
Aqueous phase
  High Performance Liquid Chromatography (HPLC) (Bio-Rad Aminex HPX-87H Column)
Organic phase
  Gas Chromatography (GC) with He as carrier gas and FID
  Titration with standardized 0.05 M NaOH solution
pH meter

## Slide 19: L-L Extraction Procedure
Load
Sample:
C11 +TOPO (10mL:10mL)
vigorous shaking for 30 seconds
Analysis
Water Bath
70  C
Centrifuge
(9000 rpm, 20 minutes)
Residence time is 60 minutes
For Small Scale

## Slide 20
For 2 L Working Volume (1L org: 1L aqu)
Load
Sample:
C11 +TOPO (1 L:1 L)
Centrifuge
Analysis
Mixing and heating at 70 C for 60 min
For 60 min

## Slide 21: Two Phases Separation
* Phase separation after TOPO-undecane extraction at 70  C and pH=1
* (Byung-Hwan Um, 2008)

## Slide 22: Distillation
Separate acetic acid from TOPO/C11
C11 returned to boiling flask
HAC determined by GC and Titration

## Slide 23: Results
Comparing two solvents:
Extraction conditions + efficiency
Compatibility with green liquor Extract
Recyclability
Washing Solvent

## Slide 24
Note: For Clean System
Initial concentration of pure acetic acid solution= 10 g/L, at 70 C, Ratio [1:1]
TOA
Chart: Effect of varied concentrations of Extractant in organic solution
| 50.0 | 90.0 | 180.0 | 280.0 | 370.0 | 460.0 | 550.0
TOPO | 41.8 | 53.7 | 64.9 | 70.2 | 74.7 | 75.4 | 75.9
TOA | 82 | 91 | 90 | 88 | 88

## Slide 25
Note: - This is for clean system
- Initial concentration of pure acetic acid solution= 10 g/L , at 70 C
Chart: Effect of varied ratios of organic to aqueous phase
| 0.25 | 0.5 | 0.670000000000002 | 1.0 | 1.5 | 2.0
TOPO | 37 | 52.9 | 61.2 | 74.6 | 81.5 | 86.5
TOA | 41 | 66 | 75 | 84 | 91 | 92

## Slide 26
Chart: Effect of varied pH
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0
TOPO | 74.7 | 74.1 | 72.9 | 54.1 | 18.2
TOA | 46 | 71 | 75 | 77 | 44
Note: - This is for clean system
- Initial concentration of pure acetic acid solution= 10 g/L , at 70 C , Ratio [1:1]

## Slide 27
Note: Extraction for Clean system, initial concentration of pure acetic acid solution= 10 g/L, 370 g/L for TOPO, 200 g/L for TOA, volume ratio of organic:aqueous phases[1:1]
Chart: Extraction % VS Extraction Temperature
| 30.0 | 50.0 | 70.0 | 90.0 | 110.0
TOPO pH 1 | 73.9 | 74.1 | 74.2 | 74 | 72
TOPO pH 5 | 18 | 18.7 | 19.6 | 17.3 | 16.9
TOA pH 1 | 42 | 43 | 45 | 46
TOA pH 5 | 39 | 44 | 44 | 44

## Slide 28
Chart: Extraction % VS Recycle #
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0
Clean System Extraction | 64 | 64 | 64 | 63 | 63
Green Liqour Extraction | 61 | 59 | 39 | 11 | 6
Note: Initial aqueous acetic acid concentration is 10 g/L for clean system and 8.7 g/L for green liquor, 370 g/L TOPO/undecane, 70 C , 1:1 ratio and pH is 1

## Slide 29
Chart: Organic Washing by Water VS NaOH
| Org before washing | Org after washing | Lignin Extracted
Washing by DI-water (0.04 % Lignin removal) | 4.5 | 4.3 | 0.2
Washing by 1 M NaOH Solution (73 % Lignin removal) | 1.2 | 3.3

## Slide 30
Org. before extraction
Org. after extraction
Org. after washing by 1 M NaOH
Organic Washing by NaOH

## Slide 31
Chart: Extraction % VS Recycle #
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0
Extraction Before Hyrdolysis | 61 | 59 | 39 | 11 | 6
Extraction After Hydrolysis & Washing | 62 | 62 | 61
Note: This is for green liquor extract system with 8.7 g/L initial acetic acid concentration, using 370 g/L of TOPO/Undecane, 1 pH, volume ratio organic:aqueous: 1

## Slide 32
Chart: Solvent Recycling
| 1.0 | 2.0 | 3.0
TOPO GL | 61.5688 | 61.76 | 60.7792
TOPO CS | 64 | 64 | 64 | 63 | 63
TOA GL | 41 | 37 | 33
TOA CS | 50 | 25 | 0
Note: CS; clean system
GL; green liquor extract system
Initial aqueous acetic acid concentration is 10 g/L for clean system and 8.7 g/L for green liquor
The extraction conditions were 1 pH, 1 ratio and at 70 C
Using 370 g/L TOPO/undecane, 200 g/L TOA/Octanol

## Slide 33: Comparison between TOPO & TOA
 | TOPO | TOA
Solvent concentration in organic | 370 g/L | 200 g/L
pH | 3 or lower | 2-4
Ratio | 1:1 | 1.5:1
Clean system | 64% | 91%
Green liquor | 62% | 41%
Handling | Hard at room temp. | Easy at room temp.
Cost | Expensive | Less expensive
Recyclability | Stable | Deteriorates

## Slide 34: Conclusions
Liquid-liquid extraction recovered acetic acid from two systems:
  Clean system ( acetic acid in D-water )
  Hemicellulose extract ( green liquor extract )
Compared two solvents:
  TOPO in Undecane
  TOA in Octanol
Best extraction conditions have been determined for TOPO and TOA extraction system (extractant concentration, Ratio. pH)
TOPO shows better recyclability than TOA
Acetic acid may be a viable co-product for a kraft pulp mill

## Slide 35: Future Work
TOA separation by distillation
Analysis of organics in aqueous phase
Scale up to pilot scale

## Slide 36: Acknowledgment
University of Jeddah
Dr. G. Peter van Walsum
Thesis Committee members (Dr. van Heiningen and Dr. Wheeler)
Dr. Byung-Hwan Um & Audrey Polifka
Dr. Martin Lawoko & Dr. Sara Walton