## Slide 1: Precursors Influencing Tropospheric Ozone formation and Apportionment in three districts of Ilupeju Industrial Estate, Lagos
AZEEZ, LUQMON ADEYEMI
OSUN STATE UNIVERSITY

## Slide 2
OUTLINE
INTRODUCTION
SAMPLING METHODS
RESULTS AND DISCUSSION
CONCLUSION

## Slide 3
Air pollution in developing countries and cities
Tropospheric ozone – formation: photo-oxidation of the precursor gases such as CO, CH4 and non-methane hydrocarbons in the presence of sufficient amount of nitrogen oxide (NOx) (Volkamer et al., 2010; Kgabi and Sehloho, 2012)
NO2 + UV photons (hv) O + NO
O + O2 O3
Effects of tropospheric ozone – highly corrosive, irritant to lung, respiratory inflammation, impairment of photosynthesis (Nair et al., 2002, Olajire and Azeez, 2014)

## Slide 4
Sampling location
Ilupeju Industrial Estate is one of the industrial estates established in Lagos in Oshodi-Isolo, Local Government Area. Industries situated in the districts are shown on the map
Figure 1: Map of Ilupeju Industrial estate showing sampling locations
Measurement and analyses of hazardous pollutants, meteorological parameters, ozone and volatile organic compounds were done according to the methods of Olajire et al., (2011); Olajire and Azeez (2014)

## Slide 5
RESULTS AND DISCUSSION
Table 1: Average concentrations of toxic pollutants and meteorological parameters
Pollutants | SL1 | SL2 | SL2
 | Mean | Mean | Mean
NO2 (ppm) | 1.1 ± 0.23 | 0.56 ± 0.03 | 0.98 ± 0.29
NO (ppm) | 0.2 ± 0.01 | 0.08 ± 0.02 | 0.23 ± 0.05
SO2 (ppm) | 0.52 ± 0.13 | 0.32 ± 0.19 | 0.81 ± 0.21
CO (ppm) | 14.6 ± 1.73 | 13.90 ± 3.30 | 15.59 ± 1.07
O3 (ppb) | 17.2 ± 1.40 | 17.0 ± 1.10 | 18.8 ± 2.50
TVOC (ppm) | 8.22 ± 0.13 | 6.86 ± 0.05 | 7.08 ± 0.12
Wind speed (ms-1) | 0.74 ± 0.04 | 1.00 ± 0.16 | 1.26 ± 0.22
Temperature (oC) | 32.84 ± 0.99 | 32.22 ± 0.49 | 32.68 ± 1.04
Pressure (hPa) | 14.15 ± 0.07 | 14.52 ± 0.14 | 14.59 ± 0.61
Heat Index (oC) | 35.40 ± 3.95 | 36.70 ± 1.74 | 36.22 ± 2.49
Humidity (%) | 66.26 ± 1.48 | 66.14 ± 1.87 | 64.88 ± 2.13
TVOC/NOx | 6.32 | 10.72 | 5.85
NOx – Nitrogen oxide, SO2 – Sulphur dioxide, CO – Carbon monoxide, TVOC – Total volatile organic compounds

## Slide 6
Chart: Time (hour)
| 0 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
NO2 | 0.55 | 0.55 | 1.1 | 1.32 | 1.2 | 0.8 | 0.8 | 0.7 | 0.6 | 1 | 1.3 | 1.3 | 1.1
Figure 2a: Diurnal variations of nitrogen (IV) oxide (NO2)
Chart: Time (hour)
| 0 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Ozone | 11 | 14 | 13 | 13.5 | 16 | 22 | 23.5 | 22.4 | 21 | 22 | 14 | 13.6 | 13.4
Figure 2b: Diurnal variations of ozone (O3)
Chart: Time (hour)
| 0 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
TVOC | 4.2 | 4.2 | 8.22 | 7.8 | 7.08 | 4.6 | 4.8 | 5.2 | 4.58 | 4.19 | 8.08 | 6.9 | 6.17
Figure 2c: Diurnal variations of total volatile organic compounds (TVOC)
Two peaks shown could be as a result of vehicular activities coinciding with rush hours (Wang et al., 2002; Duan et al., 2008
Diurnal pattern shows two peaks; 11.00 – 13.00 and 15.00. High peaks of O3 observed in the noon could be due to the formation of ozone from photo-oxidation of the precursor gases such as CO, CH4 and non-methane hydrocarbons in the presence of sufficient amount of nitrogen oxide (NOx) (Nair et al., 2002
Peaks of TVOC coincided with rush hours

## Slide 7
Pollutants | Component |  |  | Communalities
 | F1 | F2 | F3 | Extraction
Nitrogen oxide | 0.882 |  |  | .850
Sulphur (IV) oxide | 0.512 |  |  | .945
Carbon (II) oxide | 0.618 |  | 0.617 | .839
Pressure |  | 0.850 |  | .795
Wind speed | 0.899 |  |  | .842
Temperature |  | 0.610 | 0.568 | .903
Ozone |  | 0.919 |  | .930
TVOCs | 0.710 |  | 0.799 | .653
Extraction Method: Principal Component Analysis. Rotation Method: Varimax with Kaiser Normalization. Only factor loadings ≥ 0.5 listed
Table 3: Factor analysis of toxic pollutants and meteorological parameters

## Slide 8
VOC | Concentration (µgm-3) |  |  | MDL (µgm-3) | MIRa | O3 formation (µgm-3) |  | 
 | SL1 | SL2 | SL3 |  |  | SL1 | SL2 | SL3
Alkane H/C |  |  |  |  |  |  |  | 
Ethane | 10.39±0.50 | 7.89±0.13 | 11.70±2.14 | 0.64 | 0.25 | 2.60 | 1.97 | 2.93
Propane | 9.22±0.76 | 7.61±0.28 | 7.47±0.69 | 0.1 | 1.15 | 10.60 | 8.75 | 8.59
Butane | 12.09±0.27 | 13.27±1.12 | 10.03±0.23 | 0.1 | 2.54 | 30.71 | 33.71 | 25.48
Pentane | 8.46±0.49 | 10.55±1.45 | 5.66±0.27 | 0.1 | 3.94 | 33.33 | 41.57 | 22.30
Hexane | 2.19±0.31 | 7.12±0.61 | 4.41± 0.04 | 0.1 | 5.61 | 12.29 | 39.94 | 24.74
Heptanes | 5.58±0.52 | 2.64±0.05 | 5.51±0.08 | 0.2 | 7.15 | 39.90 | 18.88 | 41.38
Octane | 4.81±0.15 | 9.33±0.99 | 2.53±0.19 | 0.3 | 8.68 | 41.75 | 80.98 | 21.96
Decane | 2.65±0.45 | 6.03±0.13 | 3.88±0.22 | 0.3 | 11.60 | 30.74 | 69.95 | 45.01
Alkene H/C |  |  |  |  |  |  |  | 
Ethene | 6.88±1.01 | 5.27±0.47 | 8.05±0.16 | 0.13 | 8.52 | 58.62 | 44.90 | 68.59
Propene | 13.97±2.70 | 17.15±0.40 | 12.75±1.72 | 0.6 | 26.30 | 367.41 | 451.05 | 335.33
Aromatic H/C |  |  |  |  |  |  |  | 
Benzene | 8.45±0.27 | 8.82±0.84 | 9.18±0.50 | 0.19 | 1.23 | 10.39 | 10.85 | 11.29
Toluene | 13.39±0.03 | 15.58±0.19 | 15.06±3.20 | 0.47 | 5.96 | 79.80 | 92.86 | 89.76
Ethylbenzene | 6.32±0.10 | 4.88±0.12 | 6.78±0.66 | 0.82 | 7.10 | 44.87 | 34.65 | 48.14
m,p-Xylene | 28.53±5.29 | 20.76±0.17 | 22.36±0.81 | 0.51 | 19.00 | 542.07 | 394.44 | 424.84
o-xylene | 10.97±2.52 | 11.51±3.15 | 8.01±0.28 | 0.29 | 13.70 | 150.29 | 157.69 | 109.74
Chlorinated H/C |  |  |  |  |  |  |  | 
TCE | 9.94±0.32 | 13.06±0.30 | 7.35±0.55 | 0.14 | 0.64 | 6.36 | 83.58 | 4.70
TeCE | 21.39±0.75 | 16.61±1.14 | 18.26±0.72 | 0.66 |  |  |  | 
B/T | 0.63 | 0.57 | 0.61 |  |  |  |  | 
Toluene/ m,p-xylene | 0.45 | 0.75 | 0.67 |  |  |  |  | 
Σ Xylene/CO | 2.71 | 2.32 | 1.95 |  |  |  |  | 
TCE/CO | 0.68 | 0.94 | 0.47 |  |  |  |  | 
TeCE/CO | 1.47 | 1.19 | 1.17 |  |  |  |  | 
Alkane H/C – Alkane hydrocarbons, Alkene H/C – Alkene hydrocarbons, Aromatic H/C – Aromatic hydrocarbons, Chlorinated H/C – Chlorinated hydrocarbons, O3 formation (µgm-3) = a[VOC]×MIR, MDL – Method detection limit
Table 4: Average concentrations and ozone formation abilities of VOC species

## Slide 9
Benzene to toluene ratio has been used to identify VOCs sources. A B/T ratio of 0.5 has been reported to be characteristic of combustion from vehicular activities while higher values have been reported for bio-fuel burning, charcoal and coal burning (Barletta et al., 2002; Zhao et al., 2004)
B/T ratios (table 4) of 0.63, 0.57 and 0.61 for SL1, SL2 and SL3 respectively suggest that vehicular activities were the major VOC contributors to aromatic hydrocarbons emission in this study. The ratios in this study are in agreement with results obtained by (Barletta et al., 2005).
Other ratios that can be used as markers to identify VOC emission sources are toluene/m,p-xylene, xylene/CO, TCE/CO and TeCE/CO (Wang et al., 2002; Zhang et al., 2012; Olajire and Azeez, 2014). These ratios are therefore indicators of solvent use relative to combustion sources. Low ratios (table 4) calculated for all locations suggest solvent evaporation. This agrees with results obtained by Zhao et al., 2002; Zhang et al., 2012)

## Slide 10
Table 5: Factor analysis of VOC species |  |  |  | 
Compounds | Component |  |  | Communalities
 | F1 | F2 | F3 | Extraction
ethane |  |  |  | 0.922
propane |  | 0.948 |  | 0.956
butane | 0.969 |  |  | 0.945
pentane | 0.969 |  |  | 0.942
hexane |  |  |  | 0.949
heptane |  | 0.674 |  | 0.997
octane | 0.950 |  |  | 0.991
decane | 0.574 |  |  | 0.953
ethene |  |  |  | 0.915
propene | 0.835 |  |  | 0.892
benzene |  |  | 0.900 | 0.819
toluene |  |  | 0.775 | 0.709
ethylbenzene |  |  |  | 0.890
m/p-xylene |  | 0.947 |  | 0.900
o-xylene | 0.765 |  |  | 0.821
TCE | 0.977 |  |  | 0.987
TeCE |  | 0.962 |  | 0.961
Extraction Method: Principal Component Analysis. Rotation Method: Varimax with Kaiser Normalization. Only factor loadings ≥ 0.5 listed

## Slide 11
Ozone Formation and Apportionment
The ratio of VOCs/NOx can be used to evaluate whether the production of O3 is VOC-sensitive or NOx-sensitive (Carter, 1994). Morning VOCs/NOx ratios lower than 10 were equated with VOC-sensitive peak ozone and Morning VOCs/NOx ratios greater than 20 correspond to NOx-sensitive peak ozone (Sillman, 1999; Pudasainee et al., 2006). In this study, TVOC to NOx ratios (table 1) are lower than 10 in SL1 and SL3 while it is higher than 10 at SL2. This indicates that at all locations, O3 formation is VOCs sensitive.
Photochemical reactivity of measured VOCs were estimated using maximum incremental reactivity (MIR). The results are presented in table 4. m/p – xylene was the highest contributor to O3 formation at SL1 and SL3 while propene had highest contribution at SL2. Ethane contributed the least to O3 formation

## Slide 12
Conclusion
In this study, we have reported the concentrations of toxic pollutants, volatile organic compounds and meteorological parameters measured in three locations of Ilupeju indusrial Estate. Concentrations of toxic pollutants such as CO, NO2 and SO2 were higher than acceptable limits and were dependent on meteorological parameters such as temperature, pressure, humidity and wind speed. Majority of VOCs ratios revealed solvent related and unburned fuel emissions from these locations except B/T ratio which indicated a traffic related emission. m,p - xylene and propene were the major contributors to O3 formation at SL1, SL2 and SL3 respectively. Ozone determined was VOC sensitive at all locations. PCA of the results showed traffic related emission sources for toxic pollutants and solvent use as sources for VOCs.

## Slide 13
References
Olajire AA, Azeez L (2014). Source apportionment and ozone formation potential of volatile organic compounds in Lagos, Nigeria. Chemistry and Ecology. 30(2):156-168
Pudasainee D, Sapkota B, Shrestha ML, Kaga A, Kondo A, Inoue Y (2006). Ground level ozone concentrations and its association with NOx and meteorological parameters in Kathmandu valley, Nepal. Atmospheric Environment. 40: 8081–8087.
Volkamer R, Sheehy P, Molina LT, Molina MJ (2010). Oxidative capacity of the Mexico City atmosphere – Part 1: A radical source perspective. Atmospheric Chemistry and Physics. 10:6969-6991.
Kgabi NA, Sehloho RM (2012). Tropospheric Ozone Concentrations and Meteorological Parameters, Global Journal of Scientific Frontier in Research and Chemistry. 12: (2012) 10–21.
Nair PR, Chand D, La S, Modh KS, Naja M, Parameswaran M, Ravindran S, Venkataramani S (2002). Temporal variations in surface ozone at Thumba (8.6N, 77 E) –a tropical coastal site in India. Atmospheric Environment. 36: 603–610.
Barletta B, Meinardi S, Simpson IJ, Khwaja HA, Blake DR, Rowland FS (2002). Mixing ratios of volatile organic compounds (VOCs) in the atmosphere of Karachi, Pakistan.Atmospheric Environment. 36: 3429–3443.