## Slide 1
Assessing Healthcare Liquid Waste Management of Hospitals in Kathmandu Valley, Nepal
Bandana K Pradhan, PhD
Department of Community Medicine & Public Health
Institute of Medicine
and
Pushkar K Pradhan, PhD
Central Department of Geography
Tribhuvan University, Kathmandu, Nepal
Earth Science International Conference
San Francisco, USA July 28-30 2014

## Slide 2
Introduction
Nepal got EPA in 1996 and since then all industries and hospitals must have approvals of EIA/IEE
Hospitals being built before EPA 1996 required to comply with EIA/IEE within the stipulated time – 10 years
  About 95% water used in the hospitals being released as healthcare untreated liquid waste into the rivers, of which 20% hazardous

## Slide 3
Ward/OT
Toilet/bathroom
OPD
Kitchen
Laboratory
Collection
Drainage
Treatment plant
Discharge
Low priority to HCLW- as only one hospital TUTH but not functioning
River –Samakhusi

## Slide 4
Chart: Wastewater status of surface water, KTM
| Domestic | Industry
Wastewater(million m3 ) | 30 | 2.1
BOD (x000 tonnes) | 16.4 | 1.15
TSS (x000 tonnes) | 25.5 | 1.41
Solid waste (000tonnes) | 25 | 0.14
  People residing nearby the rivers have to use the river water for different domestic activities
  Total waste water – HCLW contribution 1%; Industrial wastewater = (6+1)%

## Slide 5
Chart: Trend of diarrhoeal disease incidence
| 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
DI | 125 | 160 | 180 | 185 | 182 | 190 | 200 | 220 | 210 | 200 | 185 | 390 | 490 | 500
  MDR bacteria – 100% effluent samples from hospitals
  Resistance of antibiotics including penicillin, various generations of Cephalosporin, Cotrimoxazole, Gentamycin and Quinolones
  about one third of deaths of under-five children due to water borne diseases such as cholera, typhoid fever, dysentery and gastro-enteritis

## Slide 6
Objectives
Analyze hospital liquid waste management practices and their possible impacts on the people, based in Kathmandu valley – the capital city

## Slide 7
Research Design
Study area:
Kathmandu Valley area: 570 km2 comprises rural parts of three districts and five municipalities
About 2 million population
Population density: >3500/ km2

## Slide 8
  Data Acquired
Identified and located the hospitals (public and private) >50 beds within KTM and chosen 18 hospitals
Observed HCLWM practice through observation protocol
Laboratory analysis
    Collected effluent samples
    All chemical parameters including BOD and COD & bacteriological analysis, based on Standard Method (APHA 2000)

## Slide 9
Findings
General characteristics of hospitals
H-type | H-bed (mean) | Total Staff (m) | Staff | 
 |  |  | WM (%) | LW
Private | 96 | 200 | 15 | No
Public | 364 | 692 | 21 | No
Note: H =hospital, WM – waste management, LW =liquid waste

## Slide 10
Hospital type | WM policy/ guideline |  | EIA /I EE approval |  | Total
 | Yes | No | Yes | No | Number
Private | 3 (33) | 6 (66) | 3 | 3*+3 | 9
Public | 4 (44) | 5 (55) | 1 | 8 | 9
Waste Management Status
Note: *ToR approved for IEE study of the hospital
Findings (contd.)

## Slide 11
Water used and wastewater generated and treatment plants status by hospitals types
H type | Water used ( l/day m3) | HCLW /day (m3) | LWTP |  | Total
 |  |  | Yes | No | 
Private | 38.5 | 34.6 | 0 | 5*+4 | 9
Public | 112.1 | 100.9 | 1 | 2*+ 6 | 9
Total | 151.6 | 136.5 | 1 (6) | 17 (94) | 18
* Primary treatment

## Slide 12
Chart: Heterotrophic counts from the Hospital Effluent
HC-a | 4 | 12 | 6 | 10 | 13 | 123 | 231 | 6 | 10
HC-b | 20 | 34 | 167 | 231 | 123 | 167 | 20 | 34 | 167
Parameter | p value
H count (cfu/ml) | 0.04

## Slide 13
Chart: Pollutant load in the Effluent of Public and Private Hospitals
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
COD-a | 310 | 400 | 350 | 410 | 412 | 350 | 310 | 401 | 390
COD-b | 414 | 390 | 401 | 390 | 302 | 414 | 414 | 390 | 401
COD/BOD-a | 2.1 | 2 | 1.9 | 2.4 | 2.5 | 1.9 | 2.1 | 1.9 | 2.1
COD/BOD-b | 1.7 | 2.1 | 1.9 | 2.1 | 2.7 | 1.7 | 1.7 | 2.1 | 1.9
Parameter | p value
COD (mg/l) | 0.2
COD/BOD | 0.5
Direct discharge of HCLWW
Water withdrawal for DW

## Slide 14
Chart: Concentration of DO (mg/l)
DO -a (mg/l) | 1.2 | 1 | 0.5 | 1.1 | 1.3 | 1.1 | 1.2 | 0.5 | 1.1
DO -b (mg/l) | 1.1 | 0.8 | 1.5 | 1.2 | 1.1 | 1.5 | 1.1 | 0.8 | 1.5
Residual Chlorinea-a | 3 | 4 | 6 | 5 | 7 | 0.4 | 0 | 6 | 5
Residual-b Chlorinea | 0.1 | 0.2 | 0 | 0 | 0.4 | 0 | 0.4 | 0 | 0.3
Parameter | p value
DO (mg/l) | 0.2
R-Cl (mg/l) | 0.02

## Slide 15
Potential health hazard

## Slide 16
Potential health hazard spatial analysis

## Slide 19
Conclusions
Direct discharge into nearby river
Bacteriological load in the HCLW higher in public hospitals than in private hospital
Weak monitoring of EIA /IEE of hospitals
Use of river water for different purposes – lack of awareness
Potential health impacts of hospital effluents to population living nearby hospitals/rivers
Yet to ascertain HCLW direct impacts between private and public hospitals on population

## Slide 20
Recommendations
Healthcare without harm principle should be strictly followed by constructing reliable HCLW treatment plants
Monitoring – hospitals have followed EIA/IEE treatment of effluents
Awareness to both population and healthcare stakeholders about the health impacts of HCLW
Research/bench mark data generation on health impacts of HCLW