## Slide 1: Solvent Interaction Analysis (SIA): A New Approach to Structure-Focused Clinical Proteomics Boris Zaslavsky Analiza / Cleveland Diagnostics Cleveland, Ohio USA

## Slide 2: Protein Biomarker Features
Expression level
Structure
Protein-protein and protein-ligand interactions

## Slide 3: Aqueous Two-Phase Partitioning - Fundamentals (1): Solvent is water, with added polymers and salts
4.9% PEG
1.8% Dextran 93.3% Water
2.6% PEG 7.3% Dextran 90.1% Water
Example 2
17.7% Ficoll
5.7% Dextran 76.6% Water
6.7% Ficoll 15.6% Dextran 77.7% Water
Example 1

## Slide 4
Aqueous Two-Phase Partitioning - Fundamentals (2):
K, the partition coefficient, is defined as the ratio of solute concentrations in the two phases
All procedures are performed with a liquid handling workstation and the concentration assay instrument: using UV- or fluorescence reader or ELISA immunoassay
PEG-rich phase
Dex-rich phase
Aqueous
Phases
Add solute
Mix
Settle
Sample and analyze
Ctop
Cbot

## Slide 5: Solvent Interaction Analysis
Measured Property – protein-solvent interactions (inaccessible by other means in HTS mode)
Defined by nature and arrangement of solvent-exposed groups (i.e. by 3-D structure)
Sensitive to changes in:
  Chemical structure;
  Conformation;
  Protein-protein and protein-partner interactions

## Slide 6: Sensitivity of SIA (1): Effect of Amino Acid Sequence

## Slide 7: Sensitivity of SIA (2): Effect of Amino Acid Replacement on Protein Partitioning

## Slide 8: Sensitivity of SIA (3): Protein Aggregation
Product A - Pure Protein Product B - Same Protein in the Presence of an Excipient Aggregation is easily detected!

## Slide 9: Sensitivity of SIA (4): Effect of Altered Glycosylation on Hemoglobin Partitioning
ATPS | Control-N 7.6% GHb | Control-E 15.0% GHb
#1 | 0.573 ± 0.027 | 0.634 ± 0.019
#2 | 0.337 ± 0.021 | 0.269 ± 0.009
#3 | 0.205 ± 0.020 | 0.290 ± 0.015
#4 | 0.836 ± 0.015 | 1.113 ± 0.029
#5 | 1.025 ± 0.018 | 1.277 ± 0.011
Glycohemoglobin Control-N contains 7.6% GHb; Glycohemoglobin Control-E contains 15.0% GHb

## Slide 10: Sensitivity of SIA (5): Carbohydrate-Deficient Transferrin
Transferrin K ~1.78
CDT K ~0.845
CDT – desialylated Tf

## Slide 11: Biologically Relevant Observations (1)
Partition coefficient of a protein in vitro and in serum may differ under the same SIA conditions
Protein (human) | K-value (pure protein) | K-value (in serum/plasma)
Transferrin | 1.78 ± 0.04 | 0.53 ± 0.12
Prostate specific antigen | 1.90 ± 0.06 | 1.11 ± 0.01
Albumin | 0.69 ± 0.01 | 1.28 ± 0.02
Immunoglobulin G | 4.42 ± 0.02 | 4.19 ± 0.04

## Slide 12: Biologically Relevant Observations (2)
Partition coefficient of a protein in different biological fluids (e.g., serum and urine) may differ
Protein | K-value (in serum) | K-value (in urine)
Prostate specific antigen | 1.11 ± 0.01 | 1.60 ± 0.10

## Slide 13: Discovery of Structural Changes in Cancer
Structural Classification + Biological Identification
Solvent Interaction
Analysis Assay:
1000s of simultaneous experiments
MS:
Label-free Discovery
Multiplexed
ELISA:
Discovery (known
Proteins
Clinical screening
ELISA:
Discovery (known proteins)
Clinical screening

## Slide 14: How to Choose SIA Chemistries: Example
Dashed lines denote experimental error limits
White symbols are systems that can be used for a biomarker test
Notes: Each protein that undergoes structural changes (or protein-protein interactions) was examined with 24 proprietary test chemistries. In this shotgun approach, many tests failed due to variety of technical reasons (e.g., the instrument signal was out of range), and many did not show statistically significant differences between the pooled samples and were thus disqualified. Test chemistries that are potential useful as structural tests are denoted outside the error bars (typically related to the ELISA error bars and not to the SIA inherently tight CV). For example, system #15 produced a change in the measured signal of over 120% between the normal and positive cases. The choice of a specific test chemistry depends on additional criteria, including insensitivity to changes that are not related to cancer, ease of handling, cost, and ability to multiplex with additional proteins to result in a highly specific test. These considerations are typically evaluated downstream during test development.

## Slide 15: Stage I Ovarian Cancer vs. Control Pools (Benign) Multiplexed Immunoassay (7/06)
RED: 1st choice
No structural changes
Notes: A second tier study demonstrated several proteins whose structural index K values for cancer and control were sufficiently outside the equi-value line.

## Slide 16: Building an SIA-Based Assay
Structural Classification + Biological Identification
Solvent Interaction
Analysis Assay:
1000s of simultaneous experiments
MS:
Label-free Discovery
Multiplexed
ELISA:
Discovery (known
Proteins
Clinical screening
ELISA:
Discovery (known proteins)
Clinical screening

## Slide 17: Example of ATPS screen Prostate Specific Antigen (malignant vs benign)

## Slide 18: Total Serum PSA Level Is Not Predictive of Cancer

## Slide 19: PSA Structure Is Cancer Predictive

## Slide 20: PSA/SIA outperforms existing tPSA Test
Parameter | Value
AUC | 0.90
Standard Error | 0.02
95% CI | 0.85 – 0.94
P value | <0.0001
AnalizaDx
tPSA
Notes: 20

## Slide 21: Benign & Cancer IsoPSA vs. PSA > 4 ng/ml

## Slide 22: Feasibility Data: Structural Biomarkers for Breast Cancer
Notes: The final example directly compares our structural test against the gold-standard tests for breast cancer today – two different types of mammography. The comparison is performed using a conventional statistical test called Receiver-Operating Characteristics (ROC), a test that essentially compares the trade-off between sensitivity and specificity (defined in the next slide) of any diagnostic test.
No diagnostic test is 100% sensitive and 100% specific. Depending on the significance of making one type of mistake vs. another, alternative tests can be quantitatively compared. For example, mammography can typically detect 70% of breast cancer cases (sensitivity) but at a cost of making a mistake rate of 30% in flagging normal cases as potentially positive (100 – specificity). The comparison between ANALIZA’s-Newco’s performance and that of mammography is remarkable.
We already have plans to further refine and improve the test, and follow-up studies that focus on early breast cancer studies, cross-sensitivity to other conditions and cancers, etc., will be performed. However, the number of patients involved in this early study, and the significant performance improvement of this low-cost serum based test over expensive mammography can not be under-appreciated.

## Slide 23: Solvent Interaction Analysis – The Assay
Focus:
Use change in protein structure to identify healthy vs. disease
K =
CDx technology:
Biofluid placed in aqueous two-phase system
Proteins partition between top & bottom based on structure
Specific ratio (K) for protein + structure + SIA chemistry
16
4
10
30
48
12
Amount= 20 40 60
K= 4 .3 4
Notes: 23

## Slide 24: Thank You

## Slide 25: De Novo Discovery of Structurally Changed Biomarkers in Cancer
Structural Classification + Biological Identification
Solvent Interaction
Analysis Assay:
1000s of simultaneous experiments
MS:
Label-free Discovery
Multiplexed
ELISA:
Discovery (known
Proteins
Clinical screening
ELISA:
Discovery (known proteins)
Clinical screening

## Slide 26: Label-Free, MS-Based Discovery
Peptides: Exoproteases? Albumin? Amplification?
Isoforms
Protein-Protein Interactions

## Slide 27: What Does DK at Same M/Z Mean?
Stage I OC
SELDI/TOF
Q10 chip
NCI 3/07
18 cancer
20 normal

## Slide 28: M/Z Data is Easily Converted to Standard Stem Plots

## Slide 29: Multivariate Marker Performance: Stage I Ovarian Cancer
34 potential biomarkers selected visually from composite MS plots
Biomarker selection1 using:
  Wilcox test
  Forward selection with mahalanobis distance
  SVM recursive feature elimination
Final set leave-one-out cross validation performance:
  10 biomarkers: 100% correct classification
  3 biomarkers: ~90% correct classification
1 Lixin Gong, Insightful Corp., using S+ ProteomeLab 2.0