## Slide 1: Optimization of textural properties of predried and deep-fat-fried carrot slices as a function of process conditions
by Dr. Cem BALTACIOĞLU1
Dr. Erkan KARACABEY2 and Dr. Erdoğan KÜÇÜKÖNER2
1 Food Engineering Deparment, Engineering Faculty, Niğde University, Niğde, Turkey
2 Food Engineering Deparment, Engineering Faculty, Suleyman Demirel University, Isparta, Turkey

## Slide 2: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 3: Deep-Fat-Frying
Popular cooking method
  Especially for vegetables
    Carrot
Frying
  Using vegetable oil
  At high temperature levels
  For certain time

## Slide 4: Deep-Fat-Frying
What is going on during deep-fat-frying?
  Type of dehydration process including simultaneous heat and mass transfer
    Rapid temperature raise
    Water molecules evaporate
    Increasing internal pressure of frying material
    Decreasing moisture content
    Case hardening
    Crust formation depending on frying material

## Slide 5: Deep-Fat-Frying
Important points for evaluation of deep-fat-fried products
  Oil uptake
  Moisture content
  Textural properties
  Taste, flavor, aroma
  Surface color
  Shape, size etc.

## Slide 6: Deep-Fat-Frying
Textural properties should meet the consumer expectations
  Texture is significant and determinative characteristic for fried products for consumer’s perception
  Vary depending on type of product

## Slide 7: Deep-Fat-Frying
Factors affecting textural properties of final fried product
  Raw material
    Type
    Composition
  Preprocess
    Boiling
    Drying
    Other possible applications

## Slide 8: Deep-Fat-Frying
Main project was about the control of oil absorption of fried carrot slices.
As a pretreatment, drying was performed to decrease the moisture content of carrot slices
There is a relation between initial moisture content of frying material and its final oil content.
Less moisture content resulted in limited oil absorption.

## Slide 9: Deep-Fat-Frying
As a pretreatment,
  Conventional oven drying
  Microwave oven drying
  To decrease the moisture content of carrot slices

## Slide 10: Deep-Fat-Frying
Factors affecting textural properties of final fried product
  Frying process
    Oil temperature
    Process time
    Frying material/Oil volume (w/v)

## Slide 11: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 12: Aim of the study
Main purpose of the current study as a part of main project was
  To evaluate the change of textural properties of deep-fat-fried product , initial moisture content was lowered by two different drying methods (conventional oven and microwave oven).
  To optimize the predrying and deep-fat-frying process conditions in terms of textural properties

## Slide 13: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 14: Material & Methods
Carrots were purchased from local producer’s orchard to avoid changes due to carrot type and environmental-climatic variations.
Stored @ +4oC
Before process
  washed
  peeled
  sliced (slice thickness selected according to preliminary studies to determine consumer demands towards conventionally fried carrot slices)
  boiled for 90 sec in boiling water (~ 100oC) (enough for enzyme inactivation)

## Slide 15: How was carrot slice predried and fried?
Predrying
  Conventional oven
    Constant air flow (around 0.8 m/sec)
    temperature is adjustable (from 50oC to 300oC)
  Microwave oven
    Temperature is adjustable (from 30oC to 100oC)
Deep-fat-frying
  Industrial fryer
    Temperature is adjustable (from 50oC to 200oC)

## Slide 16: Experimental Design
For optimization experimental design should be created using different tools including statistical based ones
For conventional predrying & frying
  Central Composite Design
    4 independent variables at 5 levels with 4 central points
For microwave predrying & frying
  Full Factorial Design
    3 independent variables at 3 levels

## Slide 17: Coded & Real Values of Independent Variables of Conventionally Predrying & Deep-Fat-Frying
Independent Variable | Real/Coded Values of Variables |  |  |  | 
Drying Temperature (oC) | 41 / -2 | 48 / -1 | 55 / 0 | 62 / 1 | 69 / 2
Weight Loss (%) | 10 / -2 | 12.5 / -1 | 15 / 0 | 17.5 / 1 | 20 / 2
Frying Temperature (oC) | 120 / -2 | 135 / -1 | 160 / 0 | 165 / 1 | 180 / 2
Frying Time (sec) | 120 / -2 | 240 / -1 | 360 / 0 | 480 / 1 | 600 / 2

## Slide 18: Experimental Design of Conventional Predrying & Deep-Fat-Frying
Run Order | Drying Temperature | Weight Loss | Frying Temperature | Frying Time
1 | -1 | -1 | 1 | 1
2 | 1 | -1 | -1 | 1
3 | 1 | -1 | 1 | 1
4 | 0 | 0 | 2 | 0
5 | 0 | 0 | 0 | -2
6 | 0 | 0 | 0 | 0
7 | 1 | 1 | -1 | 1
8 | -1 | 1 | 1 | -1
9 | 0 | 0 | 0 | 0
10 | -1 | 1 | -1 | -1
11 | -2 | 0 | 0 | 0
12 | 2 | 0 | 0 | 0
13 | -1 | -1 | 1 | -1
14 | -1 | 1 | -1 | 1
15 | 0 | 0 | -2 | 0
16 | 0 | -2 | 0 | 0
17 | -1 | 1 | 1 | 1
18 | 0 | 2 | 0 | 0
19 | 1 | -1 | -1 | -1
20 | 1 | 1 | 1 | 1
21 | -1 | -1 | -1 | 1
22 | -1 | -1 | -1 | -1
23 | 1 | 1 | 1 | -1
24 | 0 | 0 | 0 | 2
25 | 1 | 1 | -1 | -1
26 | 0 | 0 | 0 | 0
27 | 1 | -1 | 1 | -1
28 | 0 | 0 | 0 | 0

## Slide 19: Coded & Real Values of Independent Variables of Predrying Using Microwave oven & Deep-Fat-Frying
Independent Variable | Real/Coded Values of Variables |  | 
Weight Loss (%) in Microwave Oven | 10/ -1 | 15/ 0 | 20/ 1
Frying Temperature (oC) | 140 / -1 | 160 / 0 | 180 / 1
Frying Time (sec) | 200 / -1 | 350 / 0 | 500 / 1

## Slide 20: Experimental Design of Microwave Predrying & Deep-Fat-Frying
Run Order | Weight Loss | Frying Temperature | Frying Time
1 | 0 | 0 | 0
2 | 1 | 1 | 1
3 | 1 | 0 | 0
4 | 1 | 0 | 1
5 | 0 | -1 | 1
6 | -1 | 1 | 0
7 | -1 | 1 | 1
8 | 0 | -1 | -1
9 | 0 | 1 | 0
10 | 1 | 1 | 0
11 | 0 | 0 | 1
12 | 1 | -1 | 1
13 | 1 | 0 | -1
14 | -1 | 0 | 0
15 | 1 | -1 | -1
16 | -1 | 0 | 1
17 | 1 | -1 | 0
18 | 0 | 1 | -1
19 | 0 | 1 | 1
20 | -1 | -1 | 1
21 | -1 | 1 | -1
22 | 1 | 1 | -1
23 | 0 | 0 | -1
24 | -1 | -1 | 0
25 | 0 | -1 | 0
26 | -1 | 0 | -1
27 | -1 | -1 | -1

## Slide 21: Textural Properties
Predried and Fried Carrot Slices were subjected to texture analysis.
  TPA Analysis (cylindirical prob-30 mm diameter)
    hardness
    elasticity
    cohesiveness
    chewiness
  Cutting Hardness (LKB prob)
    cutting hardness

## Slide 22: Optimization
Statistical method
  Response Surface Methodology
    Minitab Statistical Package Program
  Full Quadratic Model
    For conventional drying and frying
    For microwave drying and frying

## Slide 23: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 24: Textural properties measured for conventionally predried and fried carrot slices
Run Order | Hardness, g force | Elasticity | Cohesiveness | Chewiness | Cutting force, g force
1 | 494.10 | 7.25 | 0.77 | 2746.34 | 418.42
2 | 491.29 | 8.98 | 0.35 | 5223.12 | 762.95
3 | 747.02 | 7.35 | 0.35 | 7401.48 | 871.39
4 | 420.07 | 3.72 | 0.16 | 2519.88 | 401.29
5 | 2055.64 | 16.47 | 0.85 | 29136.72 | 1137.52
6 | 492.18 | 4.49 | 0.33 | 2001.03 | 662.77
7 | 836.92 | 6.53 | 0.69 | 11768.32 | 638.08
8 | 637.78 | 8.46 | 0.50 | 4370.96 | 785.44
9 | 374.93 | 4.13 | 0.17 | 3159.75 | 1065.72
10 | 1254.31 | 10.80 | 0.53 | 16388.11 | 925.73
11 | 1029.35 | 3.60 | 0.17 | 4554.69 | 1041.91
12 | 697.35 | 9.11 | 0.34 | 6673.15 | 941.92
13 | 1003.17 | 10.94 | 0.70 | 9427.18 | 736.27
14 | 1142.03 | 8.58 | 0.50 | 3288.18 | 667.85
15 | 2605.95 | 4.34 | 0.85 | 15615.83 | 855.06
16 | 699.12 | 7.43 | 0.51 | 4980.77 | 1236.99
17 | 605.08 | 2.98 | 0.13 | 3662.58 | 907.23
18 | 301.12 | 3.00 | 0.10 | 2300.00 | 888.83
19 | 2105.69 | 18.18 | 0.87 | 33048.78 | 1513.50
20 | 648.90 | 5.00 | 0.16 | 2950.00 | 413.10
21 | 1883.51 | 4.20 | 0.84 | 3196.26 | 950.37
22 | 2871.82 | 12.67 | 0.85 | 30828.77 | 1056.23
23 | 1204.07 | 8.37 | 0.51 | 9090.02 | 1017.36
24 | 597.44 | 6.68 | 0.61 | 5957.69 | 585.70
25 | 1248.08 | 16.20 | 0.70 | 21379.64 | 1228.83
26 | 132.02 | 0.00 | 0.30 | 1990.00 | 689.77
27 | 770.65 | 14.45 | 0.85 | 8535.15 | 992.32
28 | 1050.38 | 4.18 | 0.39 | 2376.30 | 846.08

## Slide 25: Developed models and corresponding performance parameters of conventionally predried and fried carrot slice’s textural properties
Model coefficients | Hardness, g force |  | Elasticity |  | Cohesiveness |  | Chewiness |  | Cutting force, g force | 
Model Sabiti Etiketi | coefficient | p-value | coefficient | p-value | coefficient | p-value | coefficient | p-value | coefficient | p-value
intercept | 512.38 | * | 3.20 | * | 0.30 | ** | 2381.77 | ns | 816.09 | ***
DTemp | -208.60 | ns | 2.52 | * | 0.00 | ns | 2477.09 | ns | 65.83 | ns
WL | -298.84 | ns | -2.17 | * | -0.22 | ** | -2739.23 | ns | -117.84 | ns
FTemp | -841.22 | *** | -1.88 | ns | -0.23 | ** | -8594.12 | *** | -209.13 | *
FTim | -596.93 | ** | -5.73 | *** | -0.18 | * | -11599.20 | *** | -310.83 | ***
DTemp*Dtemp | 398.15 | ns | 4.91 | * | 0.05 | ns | 4474.96 | ns | 163.60 | ns
WL*WL | 34.92 | ns | 3.78 | ns | 0.10 | ns | 2501.42 | ns | 234.60 | ns
FTemp*Ftemp | 1047.81 | ** | 2.59 | ns | 0.30 | * | 7928.90 | * | -200.13 | ns
FTim*Ftim | 861.34 | * | 10.14 | *** | 0.52 | *** | 16408.25 | *** | 33.30 | ns
Dtemp*WL | 609.18 | ns | -2.15 | ns | 0.29 | ns | 2367.04 | ns | -241.94 | ns
FTemp*FTim | 501.39 | ns | 2.48 | ns | -0.15 | ns | 15876.63 | *** | 195.95 | ns
Regression | *** |  | *** |  | *** |  | *** |  | ** | 
R2 | 78.6 |  | 82.1 |  | 75.5 |  | 90.4 |  | 70.1 | 
R2adj | 66.0 |  | 71.6 |  | 61.1 |  | 84.7 |  | 52.5 | 
Lack-of-fit | ns |  | ns |  | ns |  | ** |  | ns | 
*, p≤0.05; **, p≤0.01; ***,p≤0.001, ns: statistically non-significant DTemp: Drying temperature (oC), WL: Weight loss (%), FTemp: Frying temperature (oC), FTim: Frying time (sec) |  |  |  |  |  |  |  |  |  | 

## Slide 26: Optimal process conditions for desired values of corresponding responses of conventionally dried and fried carrot slices
Cutting force
Chewiness
Cohesiveness
Elasticity
Hardness
Drying Temp Weight Loss Frying Temp Frying Time

## Slide 27: Textural properties measured for predried in microwave oven and fried carrot slices
Run Order | Hardness, g force | Elasticity | Cohesiveness | Chewiness | Cutting force, g force
1 | 1101.22 | 18.63 | 0.67 | 17980.71 | 896.39
2 | 169.63 | 0.86 | 0.28 | 57.62 | 1035.09
3 | 461.42 | 12.87 | 0.54 | 7185.23 | 776.04
4 | 138.97 | 1.79 | 0.43 | 37.61 | 466.35
5 | 559.64 | 3.29 | 0.38 | 2125.79 | 783.24
6 | 444.34 | 5.01 | 0.28 | 6841.00 | 713.91
7 | 163.89 | 2.07 | 0.17 | 134.72 | 928.47
8 | 2294.74 | 8.45 | 0.83 | 17203.22 | 1566.36
9 | 611.27 | 8.12 | 0.26 | 5055.00 | 723.34
10 | 771.65 | 4.30 | 0.26 | 2229.00 | 1123.72
11 | 176.15 | 6.96 | 0.39 | 4106.00 | 369.84
12 | 70.92 | 3.12 | 0.47 | 100.09 | 819.33
13 | 1382.92 | 9.01 | 0.83 | 7893.84 | 1571.29
14 | 1314.98 | 16.32 | 0.65 | 16307.72 | 935.99
15 | 2322.30 | 12.34 | 0.88 | 12394.11 | 1949.03
16 | 548.87 | 6.12 | 0.44 | 5892.00 | 493.61
17 | 1074.70 | 11.87 | 0.68 | 11387.37 | 1058.99
18 | 1088.61 | 16.10 | 0.66 | 12929.68 | 2050.40
19 | 171.18 | 2.98 | 0.37 | 225.24 | 1365.27
20 | 748.40 | 5.57 | 0.65 | 9155.67 | 958.91
21 | 1414.92 | 9.75 | 0.53 | 17158.30 | 1716.83
22 | 1040.12 | 4.12 | 0.34 | 5559.23 | 1182.99
23 | 1637.41 | 18.55 | 0.86 | 26248.23 | 1411.81
24 | 2257.98 | 10.10 | 0.86 | 17042.78 | 1118.68
25 | 896.79 | 16.07 | 0.67 | 13331.84 | 1073.59
26 | 2558.09 | 10.61 | 0.69 | 23273.52 | 2126.19
27 | 3537.92 | 5.60 | 0.89 | 13044.46 | 1926.10

## Slide 28: Developed models and corresponding performance parameters of predried in microwave oven and fried carrot slice’s textural properties
Model coefficients | Hardness, g force |  | Elasticity |  | Cohesiveness |  | Chewiness |  | Cutting force, g force | 
Model Sabiti Etiketi | coefficient | p-value | coefficient | p-value | coefficient | p-value | coefficient | p-value | coefficient | p-value
intercept | 831.71 | * | 16.6182 | *** | 0.611766 | *** | 15062.0 | *** | 771.916 | ***
WL | -308.71 | *** | -0.6032 | ns | -0.024588 | ns | -3444.8 | *** | -51.993 | ns
FTemp | -438.211 | *** | -1.2822 | ns | -0.176086 | *** | -2533.1 | ** | -23.013 | ns
FTim | -807.187 | *** | -3.4305 | *** | -0.161492 | *** | -6326.1 | *** | -460.049 | ***
WL*WL | 186.000 | ns | -3.7132 | ** | -0.018118 | ns | -2373.2 | ns | 23.389 | ns
FTemp*Ftemp | 55.496 | ns | -3.9997 | ** | -0.087511 | * | -3993.0 | * | 222.179 | *
FTim*Ftim | 119.777 | ns | -4.4039 | ** | 0.020801 | ns | -2065.7 | ns | 326.656 | **
FTemp*FTim | 311.419 | ** | -0.8048 | ns | 0.031397 | ns | -330.8 | ns | 104.885 | ns
Regression | *** |  | *** |  | *** |  | *** |  | *** | 
R2 | 90.96 |  | 74.5 |  | 85.4 |  | 82.9 |  | 78.7 | 
R2adj | 87.55 |  | 65.2 |  | 80.1 |  | 76.6 |  | 70.8 | 
Lack-of-fit | ns |  | ns |  | ns |  | ns |  | ns | 
*, p≤0.05; **, p≤0.01; ***,p≤0.001, ns: statistically non-significant WL: Weight loss (%), FTemp: Frying temperature (oC), FTim: Frying time (sec) |  |  |  |  |  |  |  |  |  | 

## Slide 29: Optimal process conditions for desired values of corresponding responses of dried in microwave oven and fried carrot slices
Cutting force
Chewiness
Cohesiveness
Elasticity
Hardness
Weight Loss Frying Temp Frying Time

## Slide 30: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 31
Figure 1. Change of hardness of carrot slices conventionally predried and fried under effects of frying temperature and time
Drying temperature, 55oC
Weight loss, 15%
hardness, g force
frying temperature, oC
frying time, sec
Drying temperature, 55oC
Weight loss, 15%
frying temperature, oC
frying time, sec
elasticity
Figure 2. Change of elasticity of carrot slices conventionally predried and fried under effects of frying temperature and time

## Slide 32
Figure 3. Change of cohesiveness of carrot slices conventionally predried and fried under effects of frying temperature and time
Drying temperature, 55oC
Weight loss, 15%
cohesiveness
frying temperature, oC
frying time, sec
Drying temperature, 55oC
Weight loss, 15%
frying temperature, oC
frying time, sec
chewiness
Figure 4. Change of chewiness of carrot slices conventionally predried and fried under effects of frying temperature and time

## Slide 33
Drying temperature, 55oC
Weight loss, 15%
cutting force,
g force
frying temperature, oC
frying time, sec
Figure 5. Change of cutting force of carrot slices conventionally predried and fried under effects of frying temperature and time

## Slide 34
Figure 6. Change of hardness of carrot slices predried in a microwave and fried under effects of frying temperature and time
Figure 7. Change of elasticity of carrot slices predried in a microwave and fried under effects of frying temperature and time
Weight loss, 15%
hardness, g force
frying temperature, oC
frying time, sec
Weight loss, 15%
frying temperature, oC
frying time, sec
elasticity

## Slide 35
Figure 8. Change of cohesiveness of carrot slices predried in a microwave and fried under effects of frying temperature and time
Figure 9. Change of chewiness of carrot slices predried in a microwave and fried under effects of frying temperature and time
Weight loss, 15%
cohesiveness
frying temperature, oC
frying time, sec
Weight loss, 15%
frying temperature, oC
frying time, sec
chewiness

## Slide 36
Figure 10. Change of cutting force of carrot slices predried in a microwave and fried under effects of frying temperature and time
Weight loss, 15%
cutting force,
g force
frying temperature, oC
frying time, sec

## Slide 37: Outline
Introduction to Deep-Fat-Frying
Aim
What we did
What we obtained
Let’s Discuss it
Conclusion

## Slide 38
It could be suggested that
  Partial drying before frying is important pretreatment in terms of food characteristics.
  Texture is one of them and mainly affected by frying conditions and partially predrying ones.
  Weight loss is the main factor affecting textural properties of carrot slices during predrying carried according to both drying method in case of the range of parameters studied.
  Studied parameters ranges were not severe to modify textural properties of carrot slices, but its partial effects on moisture content directly affects further frying process, so indirectly textural properties.

## Slide 39: Acknowledgements
Current study was financially supported by TUBITAK (Project No: 113R015).

## Slide 40
Thank you for your attentions…