## Slide 1: Improved testing for the pathogenic fungi Aspergillus fumigatus
Ceri Gwyther
Ben Stephens
Toni Gladding
STEM Faculty, Open University, Milton Keynes, UK.
ceri.gwyther@open.ac.uk

## Slide 2: Aims:
What is Aspergillus fumigatus?
Why is it a problem for the waste industry?
Current environmental monitoring methods
New and improved testing: RNA extraction
New and improved testing: RT-qPCR assay
What next?

## Slide 3: Aspergillus fumigatus: Leading cause of invasive aspergillosis

## Slide 4
Case 1
Coughing with expectoration of rubbery brown casts and blood from the lower respiratory tract
Night sweats
Weight loss
Underlying sarcoidosis
Case 2
Coughing with green plugs
Breathlessness
Wheezing
Existing allergic rhinitis and asthma
ADVISED NOT TO WORK WITH COMPOST
Implications for the waste industry

## Slide 5: Implications for the waste industry
Sensitive receptor: nearest place to the permitted activities where people are likely to be for prolonged periods (250 m).

## Slide 6: Current bioaerosol monitoring methods
Impaction
Impingement
Filtration

## Slide 7: Current bioaerosol monitoring methods
Only 10% of microorganisms are culturable
Stressed microorganisms may not grow on SELECTIVE media
VBNC microorganisms won’t grow at all
Current sampling techniques come with their own stressors
A. fumigatus
A. flavus
Something else?
Underestimation
Overestimation

## Slide 8: Why select for A. fumigatus?
Waste industry
Hospital
A. fumigatus causes 90% of all Aspergillosis cases
Environment agency stipulate AF in permits
Correct antimicrobial treatment depends on correct diagnosis
Single assay for both purposes

## Slide 9: New and improved testing
Coriolis µ

## Slide 10: Quantitative PCR
Ref: Qiagen, 2010.
Does not distinguish between live and dead cells

## Slide 11: Reverse transcriptase-qPCR
RNA
Reverse transcribed
cDNA
qPCR

## Slide 12: New and improved testing
Two objectives:
Extract RNA from bioaerosols
Design a reverse transcriptase – quantitative PCR assay specific for A. fumigatus

## Slide 13: RNA extraction from pure culture
Freeze-thaw
Lyticase digestion
Phenol chloroform extraction
FastRNA Pro Red Kit
Aqueous phase containing RNA
Phase lock gel
Organic phase
Phase lock tubes
Unable to break the conidial cell wall

## Slide 14: RNA extraction from pure culture
Precipitation
Lithium chloride
Ammonium
acetate
Isopropanol
Co-precipitation
Conidia collection
Centrifugation
Filtration
Extraction buffer
Bead beating
Bead size
Bead type
Duration
TRIzol
Phase
separation

## Slide 15: Optimising the assay: Bead size
Bead ID | Material | Size (mm)
LMC | Silica | 1.0
TSC | Glass | 1.0
TSD | Zirconia/silica | 1.0
LMY | Zirconium oxide | 0.5
TSE | Glass | 0.5
TSF | Zirconia/silica | 0.1
TSG | Glass | 0.1
LME | Ceramic Silica Glass | 1.4 0.1 4
Bead ID | Material | Size (mm)
LMC | Silica | 1.0
TSC | Glass | 1.0
TSD | Zirconia/silica | 1.0
LMY | Zirconium oxide | 0.5
TSE | Glass | 0.5
TSF | Zirconia/silica | 0.1
TSG | Glass | 0.1
LME | Ceramic Silica Glass | 1.4 0.1 4
n = 6

## Slide 16: Optimising the assay: Beating times
n = 6
n = 6
Beating time
1. 40 sec @ setting 6.5
2. 25 sec, 5 sec break, 25 sec @ 6.5
3. 1 min, 2 min on ice, 1 min @ 6.0
4. As 3, but frozen for 30 min prior to beating
Beating time
1. 40 sec @ setting 6.5
2. 25 sec, 5 sec break, 25 sec @ 6.5
3. 1 min, 2 min on ice, 1 min @ 6.0
4. As 3, but frozen for 30 min prior to beating

## Slide 17: Optimising the assay: filters
n = 6
P > 0.05
25 mm, 0.8 µm polycarbonate filter
Beating time
1. 1 min, 2 min on ice, 1 min @ 6.0
2. As above for a total of 5 min
3. 5 min continuous @ 6.0
4. 5 min continuous @ 4.0
1
2
3
4

## Slide 18: Optimising the assay: precipitation
 | Precipitation method
A | Isopropanol (12,000g, 10 min)
B | Isopropanol (12,000g, 60 min)
C | NaCl and isopropanol
D | Ammonium acetate and isopropanol
E | Sodium acetate and ethanol
F | PEG and NaCl
G | LiCl (10 M)
H | LiCl (4 M)
 | Precipitation method
A | Isopropanol (12,000g, 10 min)
B | Isopropanol (12,000g, 60 min)
C | NaCl and isopropanol
D | Ammonium acetate and isopropanol
E | Sodium acetate and ethanol
F | PEG and NaCl
G | LiCl (10 M)
H | LiCl (4 M)

## Slide 19: RNA extraction
Precipitation
Lithium chloride
Ammonium
acetate
Isopropanol
Co-precipitation
Conidia collection
Centrifugation
Filtration
Extraction buffer
Bead beating
Bead size
Bead type
Duration
TRIzol
Phase
separation

## Slide 20: RNA extraction
Co-precipitation
Filter
Extract with
sorbitol buffer
Beat with 0.1 mm
zirconium beads
1 min 2 min on ice
1 min @ 6.0
Precipitation
Conidia collection
Bead beating
TRIzol
Isopropanol

## Slide 21: RNA Extraction: What next?
105
104
103
102
106

## Slide 22: RT-qPCR assay
MIQE Guidelines
(Minimum Information for Publication of Quantitative
Real-Time PCR Experiments)

## Slide 23: Gene of interest
ACACGCTTCTTCTTGGATTGGATTTTGTCGCCTCTCTCGTACTCGGATCACTGGTTACAAGCGCAAGCTTCTTGGTGTGCCATCCGAGAAGGGCTCCGGCGATGTTCCTAGGGCTCGTCTCACCAATATTTTCTTCAGCGAGATTATTGCACCCCTAGTACTTGTTGCTGTGACGCTGGTTCCTTATCTCTACATCAACTCCAGGACTGGAGTACGTGATAACCCGGAACCTACGGATGCCATCCTGCGACTCGCCATTGTTGCCGCTGGACCAATCGCCATCAACGCAGGTGTTGCTGGTGTTTTCTTCGGCATGGCCTGCTGTATGGGACCCATCTTCAGCATGTGCTGCAAGAAATTCGGTGCTGTTCTCGCTGCCATTGCGCACGCTATAGCTGTCATTGTACTGCTCGCCATCTTCGAAGTCATGTTCTTCCTTGAATCCTGGTCCTGGCCGAGAATGCTCATTGGCATGATTGCAGCAGCGGCCATTCAGCGTTTCATCTACAAGCTCATCATTGCCCTTGCATTGACCCGCGAGTTCAAGCATGACCAGTCTAATATCGCATGGTGGACTGGCAAGTGGTACAACATGGGTTGGCACTCGATGTCACAACCCGGTCGTGAGTTCCTGTGCAAGATTACGGAGTTGGGATACTTCTCTGCAGACTTCGTTTTGGGTCACGTACTCTTGTTCGCCATGCTGCCTGCCCTCTGCGTCCCATTCATTGATAAATTCCACTCGGTCATGCTCTTCTGGCTGCGCCCAAGGTAAGGAACAATTTTCACCACGATATTTGATCTTATCTTGTCTAACACTCGTCTAGTCGCCAAATCCGCCCTCCAATTTACTCACTGAAGCAATCGAAGCTCAGGAAGAGAAGAGTCATCCGCTTTGCTATTCTCTACTTTGGGATGCTCATTCTGTTCCTTGTCCTTCTCATTGCCCCACTTGTTGTTCGCTCTATGGGATTGGTTAAAACTCCCAATCTTCCATTCAACTTGCTCCAGCCTCTTGACAAGGACAACAACGATACTATGGTGACATACACCGGCAACAACATTCCCGCTGGATTTGAGCCAGTTGAGAGCGCCTCGAGCGTGGCTACTGCAACGAGCTAG
FKS1 gene
Codes for the fksP protein
Involved in the production of glucan in the cell wall
Single copy gene

## Slide 24: Primer specificity
NCBI Blastn database

## Slide 25: Primer specificity
Species | Strain | Accession no.
Aspergillus fumigatus | Af293 | XM_746025.1
Aspergillus clavatus | NRRL 1 | XM_001268294.1
Aspergillus flavus | NRRL 3357 | XM_002383365.1
Aspergillus nidulans | FGSC A4 | XM_656241.1
Aspergillus niger | CBS 513.88 | XM_001390940.2
Aspergillus nominus | NRRL 13137 | XM_015556015.1
Aspergillus oryzae | RIB40 | XM_001816621.2
Aspergillus terreus | NIH 2624 | XM_001212456.1
Baudoinia panamericana | UAMH 10762 | XM_007675218.1
Candida dubliniensis* | CD36 | XM_002417149.1
Capronia coronate | CBS 617.96 | XM_007727032.1
Cladophialophora bantiana | CBS 173.52 | XM_016768205.1
Cladophialophora carrionii | CBS 160.54 | XM_008725355.1
Cladophialophora immunda | Unknown | XM_016395370.1
Cladophialophora yegresii | CBS 114405 | XM_007757823.1
Cyphellophora europea | CBS 101466 | XM_008721799.1
Exophiala oligosperma | Unknown | XM_016405660.1
Exophiala spinifera | Unknown | XM_016384822.1
Fonsecaea erecta | Unknown | XM_018837737.1
Fonsecaea pedrosoi | CBS 160.54 | XM_013423062.1
Neosartorya fischeri | NRRL 181 | XM_001258382.1
Neurospora tetrasperma | FGSC 2508 | XM_009854667.1
Penicillium chrysogenum Wisconsin | 54-1255 | XM_002564403.1
Penicillium digitatum | Pd1 | XM_014679162.1
Saccharomyces cerevisiae | S288C | NM_001182231.1
Talaromyces atroroseus | Unknown | XM_020260475.1
Talaromyces marneffei | ATCC 18224 | XM_002147459.1
Talaormyces stipitatus | ATCC 10500 | XM_002481595.1
Trichoderma gamsii | Unknown | XM_018810875.1
Ustilago maydis | 521 | XM_011389324.1
Verticillium albo-atrum* | VaMs.102 | XM_003001921.1
In silico specificity:
Sequence is specific for A. fumigatus

## Slide 26: Primer specificity
Species | Strain
Aspergillus fumigatus | Af293
Aspergillus alliaceus (Petromyces) | DSMZ 813
Aspergillus clavatus | DSMZ 816 (NRRL 1)
Aspergillus flavus | DSMZ 1959
Aspergillus nidulans (Emericella) | DSMZ 820
Aspergillus niger | DSMZ 2143
Aspergillus terreus | DSMZ 826
Neosartorya fischeri | DSMZ 3700 (NRRL 181)
Penicillium glabrum | DSMZ 2017
In vivo specificity:
Awaiting results

## Slide 27: RT-qPCR assay: What next?
Test the primers against microorganisms similar to A. fumigatus
Test assay against A. fumigatus isolates that have been collected from field samples

## Slide 28: And finally…
Air sampling + RNA extraction+ RT-qPCR assay = Improved method of A. fumigatus detection
Expand the methods to include other pathogens of interest as part of our commercial Pathogen Suite

## Slide 29: References
Bustin et al., 2010. MIQE précis: Practical implementation of minimum standard guidelines for fluorescence based quantitative real-time PCR experiments. BMC Molecular Biology, 11:74.
Denning, 1998. Invasive Aspergillosis. Clinical Infectious Diseases, 26:781-805
Environment Agency, 2010. Composting and potential health effects from bioaerosols: our interim guidance for permit applicants. Position Statement 031. Bristol, UK.
Environment Agency, 2017. Environmental Monitoring of Bioaerosols at Regulated Facilities. Technical Guidance Note (Monitoring). Bristol, UK.
Hererra et al., 2009. Strain-Dependent Variation in 18S Ribosomal DNA Copy Numbers in Aspergillus fumigatus. Journal of Clinical Microbiology, 47:1325-1332.
Kousha et al., 2011. Pulmonary aspergillosis: a clinical review. European Respiratory Review, 20:156-174.
Latge, 1999. Aspergillus fumigatus and Aspergillosis. Clinical Microbiology Reviews, 12:310-350.
Morgan et al., 2005. Incidence of invasive aspergillosis following hematopoietic stem cell and solid organ transplantation: Interim results of a prospective multicentre surveillance program. Medical Mycology, 43: S49-S58.
Smith, 2005. Quantitative real-time PCR in Osborn & Smith, 2005. Molecular Microbial Ecology. Taylor & Francis, Abingdon, UK.
Poole & Wong, 2013. Allergic bronchopulmonary aspergillosis in garden waste (compost) collectors—occupational implications. Occupational Medicine, 63:517-519.
Qiagen, 2010. Critical Factors for Successful Real-Time PCR.
Thorne, et al., 1992. Comparison of bioaerosol sampling methods in barns housing swine. Applied and Environmental Microbiology, 58:2543–2551.
Williams et al., 2013. WR1121 Defra Project Bioaerosols and odour emissions from composting facilities. London, UK.

## Slide 30: Acknowledgements
Thanks to HEIF for their funding
Any Questions?
ceri.gwyther@open.ac.uk