## Slide 1: Fatty acid methyl esters (FAME) from oil seeds grown in arid lands
Taoufik Houachri, David Bolonio, Alberto Llamas, Ana-María Al-Lal, José Rodríguez-Fernández, Mohamed El Gazzah, Martin Mittelbach, Magín Lapuerta and Laureano Canoira

## Slide 2
Sustainable Biofuels: a real alternative
The transport sector consumes about 30 % of the total energy use and 93 % of that consumption uses oil products, the least diversified sector
Price volatility
Energy independence

## Slide 3
CO2 levels and climate change
Sustainable Biofuels: a real alternative

## Slide 4
The IEA “Biofuels for Transport” roadmap describes the steps necessary to reach approximately 760 Mtoe (32 EJ) in 2050, a share of 27 % of total transport fuel
Sustainable Biofuels: a real alternative

## Slide 5
Partners
-Universidad Politécnica de Madrid
-Universidad de Castilla-La Mancha
-University of Graz
-Faculté des Sciences de Tunis
Rare species of potential oleaginous plants
Extraction of oil and analysis
Prediction of properties
Development of equations
Selection of the most promising species
Direct measurement of properties
Collection of bigger amounts
Previous studies
Framework of the project

## Slide 6
Hot-summer Mediterranean climate:
-Winters: mild temperatures with moderate rainfall
-Summers: hot and dry
-Temperatures in July and August can exceed 40 °C
Tunisia’s climate similar to Spain
Plants
Ibicella lutea
Onopordum nervosum
Silybum marianum
Peganum harmala
Smyrnium olusatrum
Tunisia
Solanum elaeagnifolium

## Slide 7
Ibicella lutea
Family: Martinyaceae
Devil’s claw
Native to South America
Onopordum nervosum
Family: Asteraceae
Cotton thistle
Native to the Iberian Peninsula
Peganum harmala
Family: Nitraceae
Sirian rue
Native to the Mediterranean area and South East Asia
Plants

## Slide 8
Silybum marianum
Family: Asteraceae
Cardus marianus
Native of Southern Europe through to Asia
Smyrnium olusatrum
Family: Apiaceae
Alexanders
Native from the Mediterranean area
Solanum elaeagnifolium
Family: Solanaceae
Silverleaf nightshade
Native from South and Central America
Plants

## Slide 9
Seeds
Soxhlet extraction
Hexane, 24 h
Oil
Degumming
95 °C, 30 min
85 wt % orthophosphoric acid, 0.2 vol %
Esterification
60 °C, 4 h
p-Toluensulfonic acid 0.5 wt % Methanol (molar ratio 6:1)
Transesterification
60 °C, 3 h
Sodium methoxide 1 wt %
Methanol (molar ratio 6:1)
Purification
Analysis
Gas Chromatography (GC-FID)
Differential Scanning Calorimetry (DSC)
Experimental procedure

## Slide 10
GC-FID
DSC
FAME Solanum elaeagnifolium
COT: Crystallization Onset Temperature
Analytical methods

## Slide 11
Cetane Number
Density
Lapuerta, M., Rodríguez-Fernández, J., & Armas, O. (2010). Correlation for the estimation of the density of fatty acid esters fuels and its implications. A proposed biodiesel cetane index. Chemistry and physics of lipids, 163(7), 720-727.
Ramírez-Verduzco, L. F., Rodríguez-Rodríguez, J. E., & del Rayo Jaramillo-Jacob, A. (2012). Predicting cetane number, kinematic viscosity, density and higher heating value of biodiesel from its fatty acid methyl ester composition. Fuel, 91(1), 102-111.
Kinematic viscosity
Prediction of properties

## Slide 12
Lower heating value
Higher heating value
Smoke Point (OESI)
Prediction of properties
Lapuerta, M., Rodríguez-Fernández, J., & Armas, O. (2010). Correlation for the estimation of the density of fatty acid esters fuels and its implications. A proposed biodiesel cetane index. Chemistry and physics of lipids, 163(7), 720-727.
Llamas, A., Lapuerta, M., Al-Lal, A. M., & Canoira, L. (2013). Oxygen Extended Sooting Index of FAME blends with aviation kerosene. Energy & Fuels, 27(11), 6815-6822.
Barrientos, E. J., Lapuerta, M., & Boehman, A. L. (2013). Group additivity in soot formation for the example of C-5 oxygenated hydrocarbon fuels. Combustion and Flame, 160(8), 1484-1498.

## Slide 13
Oxidation stability (Induction Time)
Cold flow performance
-Cloud Point
-Pour Point
-Cold Filter Plugging Point
Sarin, A., Arora, R., Singh, N. P., Sarin, R., & Malhotra, R. K. (2010). Blends of biodiesels synthesized from non-edible and edible oils: influence on the OS (oxidation stability). Energy, 35(8), 3449-3453.
Dunn, R. O. (1999). Thermal analysis of alternative diesel fuels from vegetable oils. Journal of the American Oil Chemists' Society, 76(1), 109-115.
Prediction of properties

## Slide 14
Composition and crystallization onset temperature
Results
 | C10:0 | C14:0 | C15:0 | C16:0 | C16:1 | C18:0 | C18:1 | C18:2 | C18:3 | C20:0 | Fatty acid ester content (%wt.) |  | COT (°C)
Ibicella lutea |  |  |  | 9.10 | 0.33 | 2.33 | 52.36 | 35.88 |  |  | 97.90 |  | -0.52
Onopordum nervosum |  |  |  | 9.08 |  | 3.56 | 27.02 | 60.34 |  |  | 99.6 |  | 8.39
Peganum harmala |  |  |  | 4.02 |  | 2.57 | 26.93 | 53.62 | 2.44 | 1.27 | 63.13 |  | 3.15
Silybum marianum |  | 0.08 | 0.02 | 9.44 | 0.07 | 7.11 | 25.48 | 49.26 | 0.19 | 3.95 | 97.63 |  | 10.80
Smyrnium olusatrum | 2.36 | 0.16 | 0.07 | 5.26 | 0.26 | 1.07 | 74.14 | 14.1 | 0.48 | 0.25 | 60.63 |  | -26.85
Solanum elaeagnifolium |  |  |  | 9.86 | 0.59 | 4.24 | 20.92 | 63.32 | 1.07 |  | 97.9 |  | -5.50

## Slide 15
FAME | Cetane number | Density at 15 °C (kg/m3) | Kinematic viscosity at 40 °C (mm2/s) | LHV (MJ/kg) | OESI | Induction time (h) | CFPP (°C)
Ibicella lutea | 57.4 | 882.4 | 4.19 | 37.35 | 8.01 | 2.6 | -3.2
Onopordum nervosum | 53.3 | 885.4 | 4.00 | 37.31 | 8.26 | 2.6 | -3.2
Peganum harmala | 49.1 | 890.1 | 3.85 | 37.38 | 8.98 | 1.5 | -5.8
Silybum marianum | 58.8 | 882.6 | 4.27 | 37.39 | 8.14 | 2.7 | -3.0
Smyrnium olusatrum | 60.0 | 880.3 | 4.29 | 37.33 | 7.72 | 1.8 | -5.1
Solanum elaeagnifolium | 52.7 | 885.9 | 3.95 | 37.3 | 8.29 | 2.8 | -2.8
Standard EN14214 |  |  |  |  |  |  | 
Lower limit | 51 | 860 | 3.50 |  |  | 8 | country specific
Upper limit | - | 900 | 5.00 |  |  | - | 
Results
Estimated properties

## Slide 16
Conclusions
Seeds from six oleaginous plants native (Tunisia)
Oil extraction
FAME production
GC-FID: Ester profiles
DSC: COT values
Cetane number, density and viscosity values
EN14214
Cold flow performance
Poor but aceptable in warm climate countries
Oxidation stability
Need of additives
Future studies
Intensive farming
Life cycle analysis
1
2
3
4
5
Tons of oil per hectare?
Sustainable biofuel source?

## Slide 17
Thank you for your attention
Questions?
David Bolonio
david.bolonio@upm.es
Universidad Politénica de Madrid (Spain)