## Slide 1
CO2-Prophet model based evaluation of
CO2-EOR and storage potential
in mature oil reservoirs
( Based on Journal of Petroleum Science and Engineering, Vol. 134 (2015), pp. 79–86)
By
Dayanand Saini, Ph.D.
Assistant Professor of Petroleum Engineering
3rd World Congress on
Petrochemistry and Chemical Engineering
November 30, 2015, Atlanta,

## Slide 2
Outline
  Motivation
  CO2-Prophet Model Based EOR and Storage Potential Estimation Methodology
  Model Calibration for Candidate Reservoirs
  Calibration Results (Reservoir X, Reservoir Y)
  Prediction Results (Reservoir X, Reservoir Y)
  Summary
Slide 2

## Slide 3
Motivation
Slide 3
33% of the total GHG emissions from stationary sources
Reference: California Air Resources Board

## Slide 4
Motivation
Slide 4
California’s greenhouse gas (GHG) emission reduction goals:
        By 2020- at 1990 levels
        (~ 427 MMTCO2e)
        By 2050- 80% below 1990 levels
        By 2030- 40% below 1990 levels
Executive Order B-30-15 (2015)
Carbon Capture and Storage (CCS) is an important option
References: California Air Resources Board Report, 2007
California Carbon Capture and Storage Review Panel Report, 2010

## Slide 5
113 CO2-EOR projects in the USA
Use of 60 million metric tons (MMT) of natural and industrial CO2 per year for EOR
Stored nearly 10 MMT of CO2 from natural gas processing and industrial sources in underground formations in 2013
US CO2 EOR and Geologic CO2 Storage
Slide 5
Reference: Wallace and Kuuskraa, 2014

## Slide 6
CO2-EOR in California
Slide 6
California CO2 Injection Projects
(Winslow, 2012; Jeschke et. al, 2000)
Basin | Field/Area | CO2 EOR Type | Period | Net mcf CO2 Injected
Los Angeles | East Coyote/Hualde Dome | WAG | 1982-84 | 143,080
Los Angeles | Huntington Beach/A-37 | Cyclic | 1981-82 | 183,892
Los Angeles | Wilmington (Fault Block I, III, V) | WAG | 1981-87 | 14,283,496
Ventura | Ventura/D-6(C) | Pilot | 1988 | 216,159
San Joaquin | North Coles Levee/Stevens | Flood | 1981-84 | 1,706,355
San Joaquin | Lost Hills/Belridge Diatomite | Pilot | 2000-01 | 216,514
San Joaquin | Elk Hills/Stevens | WAG | Active | -

## Slide 7
Incident CO2Storage in CO2-EOR Operations
Slide 7
North Coles Levee CO2 Pilot, Injection/production material balance (MacAllister,1989)

## Slide 8
CO2-EOR Potential in California
Slide 8
Basin | No. of Reservoirs | OOIP (Billion Bbls) | Cumulative Recover/Reserves (Billion Bbls) | ROIP (Billion Bbls)
San Joaquin | 29 | 11.9 | 3.8 | 8.1
Los Angeles | 36 | 14.1 | 4.2 | 9.9
Coastal | 23 | 5.9 | 1.8 | 4.1
Total | 88 | 31.9 | 9.8 | 22.1
California’s “Stranded Oil” amenable to CO2-EOR
(Advanced Resources International (ARI) Inc. 2005)

## Slide 9
CO2-EOR and Storage Candidate Reservoirs in the San Joaquin Valley
Slide 9
Field | Formation(s)
Asphalto | Stevens, 64 Zone
Buena Vista | Stevens, B27, Antelope
Coalinga | Nose Area
Coals Levee North | Richfield
Coals Levee South | Stevens
Cuyama South | Homan
Cymric | Oceanic, Phacoides
Edision | Vedder-Freeman, West Area Chanac
Elk Hills | Stevens, Upper
Fruitvale | Etchegoin-Chanac
Greeley | Stevens, Vedder
Stevens Sand
Asphalto, Buena Vista, Coles Levee South, Elk Hills, Greeley, Ten Section, Yowlumne
(Source: Advanced Resources International (ARI) Inc. 2005, Gillespie, 2010)
Field | Formation(s)
Guikarral Hills | Main Area
Kettleman Dome North | Temblor
McKittrick | Phacoides, Point of Rocks
Paloma | Paloma Sands
Raisin City | Zilch Sand
Russell Ranch | Dibblee Sands
Tejon Grapevine | Central Area
Ten Section | Stevens
Wheeler Ridge | L-36 Reserve
Yowlumne | Yowlumne (Stevens)
Kettleman Hills (N. Dome) | Vaqueros

## Slide 10
CO2-EOR and Storage Candidate Reservoirs in the San Joaquin Valley
Slide 10
Stevens Sand
Asphalto,
Buena Vista,
Coles Levee South,
Elk Hills,
Greeley,
Ten Section,
Yowlumne
Image modified from Scheirer and Magoon, 2007 USGS Professional Paper 1713

## Slide 11
CO2-Prophet Model Based EOR and Storage Potential Estimation Methodology
Slide 11
CO2-Prophet model is a screening tool that falls between crude empirical correlations and sophisticated numerical simulators
Can assist in estimating incidental CO2 storage potential associated with future CO2-EOR operations
(amount of CO2 injected-amount of CO2 produced)

## Slide 12
Slide 12
CO2-Prophet and CMG GEM® Comparison
(Source: Advanced Resources International (ARI) Inc. 2005)

## Slide 13
CO2-Prophet Model Calibration
Slide 13
Involves a match between simulated and actual field water cut versus cumulative oil recovery history since waterflooding

## Slide 14
Model Calibration for the Reservoirs Evaluated (Reservoir X and Reservoir Y)
Slide 14
Reservoirs evaluated in this study were already been found amenable for CO2-EOR and CO2 storage (ARI, 2005 and Gillespie, 2010)
Both the Reservoirs produce from the Stevens Sand
Relied on the data available in public domain
      Original oil in place (OOIP)
      Water saturation at the beginning of waterflooding
      Dykstra-Parsons coefficient
      Minimum miscibility pressure (MMP)
      Average reservoir pressure (waterflooding)

## Slide 15
Calibration Results (Reservoir X)
Slide 15
Field water cut versus cumulative oil recovery history
(80-acre-line drive)

## Slide 16
Calibration Results (Reservoir Y)
Slide 16
Field water cut versus field cumulative oil recovery since inception curves
(Reservoirs X (line drive), A (line drive), B (5-spot), and Y (5-spot??))
line drive
5-spot

## Slide 17
Calibration Results (Reservoir Y)
Slide 17
Field water cut versus cumulative oil recovery history (40-acre-5-spot)

## Slide 18
Prediction Results (Reservoir X and Reservoir Y)
Slide 18
Continuous miscible CO2 and 1:1 WAG injection scenarios
1 Hydrocarbon pore volume (HCPV) fluid injection
Single pattern (line drive or 5-spot) results were converted to field level results using representative no. of flooding patterns
Incidental CO2 storage:
amount of CO2 injected-amount of CO2 produced
A simple MS Excel® macro was written to read and refresh (as and when required) modal output file stored in text format

## Slide 19
Prediction Results (Reservoir X and Reservoir Y)
Slide 19
Screen shot of MS Excel® spreadsheet used for reading modal output file stored in text format

## Slide 20
Slide 20
Amount of injected and produced CO2 in different injection modes @1 HCPV fluid Injection (equivalent to a project life of 34 years)
80 acre-line drive pattern
Prediction Results (Reservoir X, ~1 MMT CO2 injection/year)

## Slide 21
Slide 21
Field wide CO2-EOR and storage potential predication results @1 HCPV fluid Injection
(equivalent to a project life of 34 years)
Chart: Ratio of average (operating) reservoir pressure to reservoir fracture pressure
| 0.51 | 0.63 | 0.72
1:1 water alternating gas (WAG) injection mode | 19.8 | 19.8 | 19.8
Continuous CO2 injection mode | 7.4 | 7.8 | 8
Chart: Ratio of average (operating) reservoir pressure to reservoir fracture pressure
| 0.51 | 0.63 | 0.72
1:1 water alternating gas (WAG) injection mode | 8.9 | 10.55 | 11.35
Continuous CO2 injection mode | 6.35 | 7.8 | 8.6
Prediction Results (Reservoir X, ~1 MMT CO2 injection/year)

## Slide 22
Slide 22
Amount of injected and produced CO2 in different injection modes
@1 HCPV fluid Injection (equivalent to a project life of 25 years)
40-acre-5-spot pattern
Prediction Results (Reservoir Y, ~1 MMT CO2 injection/year)

## Slide 23
Slide 23
Field wide CO2-EOR and storage potential predication results
@1 HCPV fluid Injection
(equivalent to a project life of 25 years)
Chart: Ratio of average (operating) reservoir pressure to reservoir fracture pressure
| 0.47 | 0.59 | 0.68
1:1 water alternating gas (WAG) injection mode | 38 | 37.8 | 37.9
Continuous CO2 injection mode | 18.7 | 19.7 | 20.3
Chart: Ratio of average (operating) reservoir pressure to reservoir fracture pressure
| 0.47 | 0.59 | 0.68
1:1 water alternating gas (WAG) injection mode | 8.55 | 10.32 | 11.25
Continuous CO2 injection mode | 7.2 | 9.1 | 10.1
Prediction Results (Reservoir Y, ~1 MMT CO2 injection/year)

## Slide 24
Summary
  Both of the reservoirs investigated in the study have potential for a large scale (injection of more than 1 MMT CO2 per year) CO2-EOR and storage project.
  Compared to continuous miscible CO2 injection, 1:1 WAG injection looks to be more promising recovery process in terms of both the incremental recovery and the amount of CO2 stored incidentally in the reservoir.
  The analysis presented in the study can be potentially used to identify candidate reservoirs beyond initial screening and simple estimations.
Slide 24

## Slide 25
Thank You
Dayanand Saini
dsaini@csub.edu
661-654-2845
Slide 25