## Slide 1: About OMICS Group
OMICS Group International is an amalgamation of Open Access publications and worldwide international science conferences and events. Established in the year 2007 with the sole aim of making the information on Sciences and technology ‘Open Access’, OMICS Group publishes 400 online open access scholarly journals in all aspects of Science, Engineering, Management and Technology journals. OMICS Group has been instrumental in taking the knowledge on Science & technology to the doorsteps of ordinary men and women. Research Scholars, Students, Libraries, Educational Institutions, Research centers and the industry are main stakeholders that benefitted greatly from this knowledge dissemination. OMICS Group also organizes 300 International conferences annually across the globe, where knowledge transfer takes place through debates, round table discussions, poster presentations, workshops, symposia and exhibitions.

## Slide 2: About OMICS Group Conferences
OMICS Group International is a pioneer and leading science event organizer, which publishes around 400 open access journals and conducts over 300 Medical, Clinical, Engineering, Life Sciences, Pharma scientific conferences all over the globe annually with the support of more than 1000 scientific associations and 30,000 editorial board members and 3.5 million followers to its credit.
OMICS Group has organized 500 conferences, workshops and national symposiums across the major cities including San Francisco, Las Vegas, San Antonio, Omaha, Orlando, Raleigh, Santa Clara, Chicago, Philadelphia, Baltimore, United Kingdom, Valencia, Dubai, Beijing, Hyderabad, Bengaluru and Mumbai.

## Slide 3: VIBRATION ANALYSIS OF A DIESEL ENGINE FUELLED WITH SUNFLOWER AND CANOLA BIODIESELS
Erinç Uludamara, Gökhan Tüccarb, Kadir Aydına, Mustafa Özcanlıc
a Department of Mechanical Engineering, Çukurova University, Adana, Turkey
b Department of Mechanical Engineering, Adana Science and Technology University, Adana, Turkey
c Department of Automotive Engineering, Çukurova University, Adana, Turkey
International Conference and Exhibition on
Automobile Engineering
September 01-02, 2015 Valencia, Spain

## Slide 4: Contents
Introduction
Biodiesel
Purpose of the Study
Material and Method
Preparation of Test Fuels
Determination of Test Fuel Properties
Experimental Set-up
Calculation of RMS value
Axes of the Test Engine
Result and Discussion
Comparison of Different Fuels
Comparison at Different Engine Speeds
Comparison of different fuels at x- y- z axes
Total arms Values of Canola Biodiesel
Total arms Values of Sunflower Biodiesel
Conclusion
Conclusion
Acknowledgements

## Slide 5: Introduction
Advantages of Biodiesel
Renewable, Non-toxic, Biodegradable
Lower exhaust emissions
Can be used with little or no engine modifications

## Slide 6: Purpose of the Study
Biodiesel is one of the most popular alternative fuel. The usage of biodiesel is increasing day by day. Therefore, all effects of biodiesel on internal combustion engines must be known.
In this study, vibration effect of canola and sunflower biodiesels at different engine speed was investigated in longitudinal, vertical and lateral axes.

## Slide 7: Material and Method
Experiments were conduced at 6 different engine speeds with 11 different fuels.
Low Sulphur Diesel
1300 rpm
1600 rpm
1900 rpm
2200 rpm
2500 rpm
2800 rpm
Sunflower Biodiesel and its blends
1300 rpm
1600 rpm
1900 rpm
2200 rpm
2500 rpm
2800 rpm
Canola Biodiesel and its blends
1300 rpm
1600 rpm
1900 rpm
2200 rpm
2500 rpm
2800 rpm

## Slide 8: Preparation of Test Fuels
Sunflower/ Canola
Oil
Methanol
(Reactant )
Sodium Hydroxide (Catalyst)
Transesterification
Washing
Drying
Biodiesel
Glycerin
Preparation of Biodiesels

## Slide 9: Preparation of Test Fuels
TEST FUELS |  |  | 
Fuel Name | Ratio of Low Sulphur Diesel (% by volume) | Ratio of Biodiesel (% by volume) | Abbreviation
Low Sulphur Diesel | 100 | - | D
Sunflower Biodiesel | 80 | 20 | S20
 | 60 | 40 | S40
 | 40 | 60 | S60
 | 20 | 80 | S80
 | - | 100 | S100
Canola Biodiesel | 80 | 20 | C20
 | 60 | 40 | C40
 | 40 | 60 | C60
 | 20 | 80 | C80
 | - | 100 | C100

## Slide 10: Determination of Test Fuel Properties
Fuel Properties of Test Fuels |  |  |  | 
Test Fuels | Density (kg/l) | Cetane Number | Kinematic Viscosity at 40oC (mm2/s) | Gross Heating Value (kcal/kg)
D | 0,837 | 59,3 | 2,7 | 45857
S20 | 0,844 | 53,8 | 4,2 | 44246
S40 | 0,854 | 53,0 | 4,5 | 43430
S60 | 0,865 | 50,9 | 4,6 | 42472
S80 | 0,876 | 47,6 | 5,1 | 41388
S100 | 0,886 | 44,5 | 5,5 | 39149
C20 | 0,846 | 54,3 | 4,5 | 43413
C40 | 0,857 | 53,4 | 4,8 | 42986
C60 | 0,867 | 51,7 | 5 | 41756
C80 | 0,877 | 49 | 5,2 | 40129
C100 | 0,883 | 46 | 5,4 | 38363
Zeltex ZX 440 NIR petroleum analyzer: Cetane Number
Tanaka AKV 202 auto kinematic viscosity test: Viscosity
Kyoto electronics DA-130: Density Measurement
IKA-Werke C2000 Bomb Calorimeter: Gross Heating Value

## Slide 11: Experimental Set-up
Brand | Mitsubishi Canter
Model | 4D31
Configuration | In line 4
Type | Direct injection diesel with glow plug
Displacement | 3298cc
Bore | 100 mm
Stroke | 105 mm
Power | 91 HP @ 3500rpm
Torque | 223 Nm @ 2200rpm
Oil Cooler | Water cooled

## Slide 12
Technical Data of Measuring System | 
Brand | SINUS Messtechnik GmbH Soundbook_MK2
Resolution | 24 Bit
Number of Channels | 4 Measuring Channels (LEMO)
Accuracy | EN 60651 and EN 60804 class 1, IEC 61672-1 class 1, group Z, percentages according to DIN 45657
Sampling rates | 51.2 kHz
Transducer Supply | Polarization voltage 20 V, 63 V or 200 V and ICP (2mA, 4mA)
Time Weighting | Fast =0.125 s
 | Slow =1 s
 | Impulse =0.035 s
 | Peak = 20µs
Technical Specifications of Accelerometer (PCB-356A33) | 
Brand | PCB-356A33
Performance | 
Sensitivity (±10 %) | 1.02 mV/(m/s²)
Measurement Range | ±4905 m/s² pk
Frequency Range (±5 %) | 2 to 10000 Hz
Frequency Range (±5 %) | 2 to 7000 Hz
Resonant Frequency | ≥55 kHz
Broadband Resolution (1 to 10000 Hz) | 0.04 m/s² rms
Non-Linearity | ≤1 %
Transverse Sensitivity | ≤5 %
Environmental | 
Overload Limit (Shock) | ±98100 m/s² pk
Temperature Range | -54 to +121 °C
Physical | 
Sensing Element | Ceramic
Sensing Geometry | Shear
Housing Material | Titanium

## Slide 13: Calculation of RMS value
aw : weighted acceleration (m/s2)
T: measurement time
atotal: combined acceleration of three axes

## Slide 14: Axes of the Test Engine

## Slide 15
D@2200 rpm
C60@2200 rpm
Comparison of Different Fuels

## Slide 16
C60@1300 rpm
C60@2200 rpm
Comparison at Different Engine Speeds

## Slide 17
D : Low Sulphur Diesel
B20 : 20% biodiesel ratio into D (by volume)
B40 : 40% biodiesel ratio into D (by volume)
B60 : 60% biodiesel ratio into D (by volume)
B80 : 80% biodiesel ratio into D (by volume)
B100: Biodiesel
Comparison of different fuels at x- y- z axes

## Slide 18
D : Low Sulphur Diesel
B20 : 20% biodiesel ratio into D (by volume)
B40 : 40% biodiesel ratio into D (by volume)
B60 : 60% biodiesel ratio into D (by volume)
B80 : 80% biodiesel ratio into D (by volume)
B100: Biodiesel
Comparison of different fuels at x- y- z axes

## Slide 19: Total arms Values of Canola Biodiesel

## Slide 20: Total arms Values of Sunflower Biodiesel

## Slide 21: CONCLUSIONS
Vibration amplitude increased with engine speed.
Canola and sunflower biodiesel addition into the low sulphur diesel fuel decreased the vibration acceleration of the diesel engine. Sunflower biodiesel was improved the vibration amplitude more than canola biodiesel.
Up to 40% biodiesel blend of canola and sunflower biodiesels with low sulphur diesel fuel, vibration values significantly improved, and the least value observed with 60% biodiesel blend for most of the test fuel.
The results also showed that, even though total arms of all frequencies were highest at longitude axis, at all engine speeds; the maximum vibration amplitude occurred in vertical axis due to upward and downward piston movement.

## Slide 22: Acknowledgements
The authors would like to thank to SINUS Messtechnik GmbH for their technical support.

## Slide 23
Thank you for
your attention!
Erinç ULUDAMAR
Research Assistant
Çukurova University
Department of Mechanical
Engineering
Automotive Division