## Slide 1: Response Time of GaN-based Deep Submicron Plasmonic Terahertz Detectors G. Rupper1, S. Rudin1, and M. Shur2 1U.S. Army Research Laboratory, Adelphi, Maryland, USA ‎2Rensselaer Polytechnic Institute, Troy, New York, USA

## Slide 2
Plasmonic FET Devices
Plasma waves propagate with a higher velocity than the electron drift velocity. This allows devices based on the plasma wave propagation to operate at higher frequencies the devices based on electron drift.
~
~
Uac
Ugs
S
D
Gate
x = 0
x = L
High Mobility
Low Mobility
Tunable Detector
Broadband Detector
~~
~
Uac
ΔU
Ugs
Gate
Source
Drain
j
Detector Configuration:
  Uac from RF radiation, j < en/2W
Source Configuration:
Uac = 0, j > en/2W

## Slide 3
Plasmonic FET Detectors
Advantages of Plasmonic FET THz Detectors:
  High Responsivity1 (kV/W)
  Low Noise Effective Power2 (pW/Hz½)
  Tunable by gate voltage
  (for high mobility, short channel devices)
  Fast Response?
1) Fatimy et. al. J. App. Phys. (2010),
Watanabe et. al. IEEE Sensors (2013)
Kurita et. al. Appl. Phys. Lett. (2012)
2) Sun et. al. Appl. Phys. Lett (2012)

## Slide 4
The 2-D electron gas plasma is modeled with a hydrodynamic model
Density balance equation
Navier-Stokes equation
Heat equation
Solved numerically for arbitrary signals
Plasma Modeling

## Slide 5
Electric Potential Model
Above threshold
Below threshold
=
=
Above threshold
Below threshold

## Slide 6
Frequency Response
Device Parameters:
GaN
L=100nm
d=15nm
µ=800 cm2/Vs
U0=Ugs-Uth=0.1V

## Slide 7
Large Signal Response
Small signal output proportional to Ua2 (Intensity)
Large signal output proportional to Ua (Electric Field)

## Slide 8
Small Signal Propagation
Ua=0.02V
Small signals have a smooth density transition across the device

## Slide 9
Transition Point Signal Propagation
Ua=0.1V
At the transition intensity, we start to see a wave front propagating across the device and reflecting off of the drain

## Slide 10
Large Signal Propagation
Ua=0.5V
Large signals have a clear shock wave propagation across the device

## Slide 11
Step Response

## Slide 12
Step Response
High Mobility,
No Viscosity
Response is an exponentially decaying square wave

## Slide 13
Step Response
Viscosity quickly attenuates high order modes leaving single harmonic frequency

## Slide 14
Step Response
Thermal effects also attenuates high order modes leaving single harmonic frequency

## Slide 15
Step Response
Low mobility eliminates periodic ringing
All mobilies have short delay before exponential decay begins

## Slide 16
Analytical Step Response
Based on perturbation small signal analysis
Decay time:
Oscillation period:

## Slide 17
Step Response Approximations
Low Mobility
High Mobility
With Gradual Channel Approx.
From Drift Model

## Slide 18
Numerical and Analytical Solution
Good agreement between numerical solution (lines) and analytical solution (dots)
GCA/Drift model reasonable above threashold
Does not include pressure effects

## Slide 19
Thermal Effects
Thermal effects reduces the decay time for high mobilities
Small changes for low mobilities

## Slide 20
For low mobilities, increasing mobility increases the modulation frequency response.
For high mobilities, increasing mobility decreases the detector bandwidth, and decreases modulation frequency response.
There is an optimal mobility for the largest possible modulation frequency response.
Above threshold response to AM signal

## Slide 21
U0=0.1V f0=0.81THz
Modulation Cutoff Frequency
Optimal mobility for maximum cutoff frequency
Large range of mobilities for high bandwidth (>50GHz)
Experimental mobility (~800 cm2/Vs) close to maximum

## Slide 22
Modulation Cutoff Frequency
Drift model
Good for low mobility, above threashold
Scaling constant fit to data
Kachorovskii and Shur, Solid State Elec. (2007)

## Slide 23
Modulation Cutoff Frequency
Good model for all mobilities
Overestimates peak

## Slide 24
Modulation Cutoff Frequency
High mobility limited by bandwidth of detector
Allows gate voltage tunable detector

## Slide 25
Summary
We have simulated the response of a plasmonic FET detector to step and modulated input signals
Plasmonic FET THz detectors have a fast response time (~ps). Can be used for very high bandwidth (>100GHz) signals
There is a mobility that provides the maximum detector bandwidth for modulated signals
High mobility detectors provide tunable passband detectors

## Slide 26
Aknowledgement
The work at RPI (M. Shur) was supported in part by the U.S. Army Research Laboratory through the Collaborative Research Alliance (CRA) for Multi-Scale Modeling of Electronic materials (MSME).