## Slide 1: What Landauer Limit? Ultra-low power electronics, and the minimum energy for computation
Gregory Snider, Alexei Orlov, and Craig Lent
Department of Electrical Engineering
University of Notre Dame

## Slide 2: Outline
The power dilemma and resulting limits
The Landauer Principle
A word about state variables
Experiments
Possible ways forward

## Slide 3: Moore’s Law
The number of transistors per chip doubles every 18 months

## Slide 4
Power Density
Multi-core processors necessary to keep chips from melting
4004
8008
8080
8085
8086
286
386
486
Pentium
Pentium Pro
Pentium II
III
4
Itanium
Itanium 2
Core 2 Duo
Hot Plate
Rocket Nozzle
Sun’s Surface
Nuclear Reactor

## Slide 5: Is Heat Really a Problem?
Every Problem is an opportunity:
Home heating, Global warming, etc.
Applications for waste heat:

## Slide 6: Power in Conventional Logic
Conventional CMOS
V
Vin
Vout
C
How to reduce power?
Reduce V
Reduce C
Reduce f (multi-core)
Turn off parts of the circuit (α)
Reduce passive power
P = N(αCV2 f + Passive Dissipation)
{
2EBit
Notes: 6

## Slide 7
Focus on Active or Passive Power?
Passive Power seems the most threatening!
Solution: Improve the switch!
The Perfect Switch
V
Vin
Vout
C
You’ve fixed Static Power issue, but not the active power!
If EBit =100 kBT, f=100 GHz, N=1011 cm-2
P = 4 kW/cm2
From Haensch
IBM J. Res. Dev. 2006

## Slide 8: Fundamental limits for computation?
Is there a fundamental lower limit on energy dissipation per bit?
i.e. is there a minimum amount of heat that must be generated to compute a bit?
Notes: 8

## Slide 9: Minimum energy for computation
Maxwell’s demon (1875) – by first measuring states, could perform reversible processes to lower entropy
Szilard (1929), Brillouin (1962): measurement causes kBT ln(2) dissipation per bit.
Landauer (1961,1970): only destruction of information must cause dissipation of kBT ln(2) per bit (Landauer’s Principle)
Bennett (1982): full computation can be done without erasure.
logical reversibility  physical reversibility
Still somewhat controversial.
Maxwell’s Demon
Notes: 9

## Slide 10: The Debate
Exorcist XIV: The wrath of Maxwell’s demon. Part I: From Maxwell to Szilard, Earman, J., & Norton, J. D., Studies in History and Philosophy of Modern Physics, 29, 435 (1998).
Exorcist XIV: The wrath of Maxwell’s demon. Part II: From Szilard to Landauer and beyond, Earman, J., & Norton, J. D., Studies in History and Philosophy of Modern Physics, 30, 1 (1999).
Eaters of the lotus: Landauer’s principle and the return of Maxwell’s demon, Norton, J. D., Studies in History and Philosophy of Modern Physics, 36, 375 (2005).
The (absence of a) relationship between thermodynamic and logical reversibility, Maroney, O. J. E. Studies in History and Philosophy of Modern Physics, 36, 355 (2005)
The connection between logical and thermodynamic irreversibility, James Ladyman, Stuart Presnell, Anthony J. Short, Berry Groisman, Studies in History and Philosophy of Modern Physics, 38, 58 (2007).
Notes: 10

## Slide 11: Analysis of erasure process
Helpful to examine and contrast two cases:
Erasure with a copy
  Reversible logical operation (No Data Destroyed)
  Key feature:
    The copy biases the system toward the state it’s in
Erasure without a copy
  Irreversible logical operation (Data Destroyed)
  Key feature:
    The system cannot be biased toward the state it’s in, so there’s an uncontrolled step

## Slide 12
What About State Variables?
Does the choice of a state variable affect this analysis?
If we use a different state variable like spin, the problem goes away, right?
Isn’t using charge as the state variable the real problem?

## Slide 13
A Little History
Beginning in 2003 Zhirnov, Cavin, and Hutchby from SRC have published a series of highly influential papers indicting charge as a state variable.
V.V. Zhirnov, et al., Proceedings of the IEEE, 91, p. 1934-39, 2003.
Fig. 1. Energy model for limiting device: w = width of left-hand well (LHW) and right-hand well (RHW); a = barrier width; E = barrier energy
Their conclusions:
At least kBT ln2 must be dissipated at each transition
This result was generalized to all charge-based devices
This is true for CMOS, but what about other charge based devices?

## Slide 14
What About “Reversible” Computing?
Following Landauer, the idea is to avoid erasure of information.
A key technology in reversible computing is adiabatic charging and discharging of capacitors: recycle charge rather than throwing it to ground.
The SRC critique: Cavin’s Demon

## Slide 15: Cavin’s Demon
Proc. SPIE Vol. 5844, pp. 1, 2005
Fluct. and Noise Letters, Vol. 5, pp. C29, 2005.
Assertion 1. Energy must be dissipated to make logic transitions.
Problem: Since there is no input this is really just creating a bit of information.
Energy spent by the demon must be > kBT ln2

## Slide 16: Cavin’s Demon
Assertion 2: Charging a capacitor requires at least kBT ln2 of energy

## Slide 17: Cavin’s Demon
Assertion 3:
SRC’s Conclusion: Charge is dead!
This is a systems level assertion that depends on the signal generator. However, signal generators can scale differently than integrated circuits!
Signal generator concerns apply equally to the control signals for every state variable
IC
Less than 200 W/cm2
Sig.
Gen.
Worst case: Signal generator more easily cooled than and IC!

## Slide 18: Is this Conclusion Correct?
Let’s find out!
The challenge: kBT ln2 at RT = 3 zJ!

## Slide 19: Sanity Check

## Slide 20: The Landauer Principle
Nature 483, p189, 2012

## Slide 21: The Landauer Principle
The SRC group rejects the Landauer Principle, but can it be tested?
Room temperature operations on a 30 kBT bit of information
Dissipation was measured as low as 0.01 kBT, confirming the Landauer Principle.
JJAP, 51, pp. 06FE10, 2012.

## Slide 22: The Landauer Principle
Measured dissipation was 0.005 kBT (15 yJ).
Room temperature operations on a 73 kBT bit of information
Copy 1
Copy 0
Erase 1
Erase 0

## Slide 23: Experimental Summary
Notes: 23

## Slide 24: Is There Any Hope?
Yes, but transistors may not be the best way!
It is time to do something different.
Represent binary information by charge configuration!
Quantum-dot Cellular Automata
A cell with 4 dots
Tunneling between dots
2 extra electrons
Polarization P = -1
Bit value “0”
Developed in the early 90s by
Craig Lent
Wolfgang Porod
Gary Bernstein

## Slide 25: Charge configuration represents bit
isopotential surfaces
“1”
“null”
+
“0”

## Slide 26: Neutral mixed-valence zwitterion (self-doped)
Awitterionic mixed-valent nido-1,2-diferrocenyl-undecacarborane.
Synthesis:
John Christie, Kenneth Henderson
Imaging:
Alex Kandel, Natalie Wasio,
Rebecca Quardokas

## Slide 27: Conclusions
Energy recycling can enable power reduction
Charge is a viable state variable
Alternative state variables face the same limits as charge
There is no fundamental lower limit on the energy needed for computation – only practical ones
The key is to trade speed for power, a trade-off that is already being made.
Low energy dissipation key to implantable applications.