## Slide 1
Cost reduction for biodiesel production from distillery/domestic mixed wastewater by Rhodosporidium toruloides
Jiayin Ling, Renata Alves de Toledo, Yuan Tian, Hojae Shim
Department of Civil and Environmental Engineering
Faculty of Science and Technology
University of Macau
Recycling 2015
World Congress and Expo on Recycling
Spain, Barcelona, July 20th-22nd

## Slide 2: Introduction
Shortage of fossil fuel
  Energy crisis & High energy prices
  Environmental security
Biodiesel: renewable & environmentally friendly

## Slide 3: Introduction
Large amount of food industry wastewater generated
Annual wastewater generated from brewery in China:
210,000,000 tons by 2012
Food industry wastewater is difficult to treat
High COD
High TN and TP
Could lead to eutrophication and algal blooms
Cost-effective treatment process is required
Notes: 3

## Slide 4: Some Challenges in Biodiesel Industry
1st Generation Biodiesel—derived from vegetable oils
crops (e.g., rapeseed, soybean)
2nd Generation Biodiesel—produced using oils from
non-edible plants (e.g., Jatropha, Ricinus)
Crops for biodiesel production vs. Crops for food supply
More cropland, less forest, more green house gas
3rd Generation Biodiesel—processing oils from
oleaginous microorganisms (e.g., Microalgae, Yeast)
Usage of fertilizer or external carbon source required
Cost of production too high

## Slide 5: Introduction
YPD medium is rich in glucose and nutrient
(Yeast extract 10 g/L, Peptone 20 g/L,
Glucose 20 g/L)
High density culture
Preparation of high cell density seed
culture
High lipid production
in real wastewater
Large amount of spent YPD medium generated (80-90% of seed culture medium)

## Slide 6: Objectives
To explore potential of reusing spent seed culture
medium
To assess lipid productivity and removal efficiencies
for organics and nutrients for cells produced from spent medium, compared to cells
grown in fresh medium

## Slide 7: Materials and Methods
YPD
biomass
lipid
biodiesel
2nd
YPD
WW
biomass
lipid
biodiesel
3rd
YPD
WW
biomass
lipid
biodiesel
Yeast
Yeast
Yeast
Yeast
Yeast
Yeast
Nutrient supplement
Nutrient supplement
Nutrient removal
Nutrient removal
Nutrient removal
Reuse
Reuse
36 h
36 h
36 h
2-5 days
2-5 days
2~5 days
Reused YPD medium
WW

## Slide 8: Materials and Methods
Wastewater
Rice wine distillery wastewater (Foshan)
Domestic wastewater (Macau)
Seed Culture Medium (YPD medium)
Yeast extract 10 g/L
Peptone 20 g/L
Glucose 20 g/L
Characteristics of Wastewater
Wastewater | SCOD (mg/L) | TN (mg/L) | TP (mg/L) | NH3-N (mg/L) | pH
Distillery Wastewater | 59,900 | 2,680 | 380 | 204 | 3.7
Domestic Wastewater | 49 | 11 | 2 | 8 | 7.6
Mixed Wastewater (1:1) | 29,100 | 1,255 | 179 | 107 | 3.7

## Slide 9: Materials and Methods
Oleaginous Microorganisms
  Oleaginous yeast Rhodosporidium toruloides
Experimental Setup
  Inoculated to 50 mL sterilized YPD fresh, 2nd, and 3r
  time used medium with or without nutrient supplement
  Cultured at 30℃, 200 rpm, 36 h
  Harvested by centrifuging at 4,000 rpm for 10 min
  Dry weights of cells produced by each type of medium were measured

## Slide 10: Materials and Methods
Experimental Setup
  Different kinds of seed culture were centrifuged at
  4,000 rpm for 10 min to cell density of 1.5 X 109 cells/mL
  Inoculated in 30 mL real non-sterile distillery/
  domestic mixed wastewater with initial cell density of 2 x 107 cells/mL and cultured at 30℃, 200 rpm, 5 day
  Yeast biomass was harvested by centrifuging
  COD, TN, TP, pH of supernatant measured

## Slide 11: Materials and Methods
Analytical Methods
Dry weight of yeast biomass: dried at 80℃ to
constant weight
Lipid yield: acid-heat method
COD, TN, TP: Hach method

## Slide 12: Results
Medium type | Fresh | Reused (2nd time) |  | Reused (3rd time) | 
Nutrient addition (%) | 100 | 0 | 10 | 0 | 50
Cell yield (g/L) | 6.04±0.84 | 3.17±1.08 | 3.67±0.31 | 2.65±0.71 | 3.81±0.43
Yeast cell yields from fresh and reused media

## Slide 13: Results
Time (day) | 0 | 2 | 3 | 4 | 5
Fresh YPD | 29,100 | 6,229 | 3,417 | 2,545 | 1,971
2nd time used YPD | 29,100 | 3,938 | 2,903 | 3,250 | 2,100
2nd time used YPD with 10% nutrient supplementation | 29,100 | 3,963 | 3,283 | 2,455 | 2,286
3rd time used YPD | 29,100 | 11,046 | 4,404 | 2,760 | 2,231
3rd time used YPD with 50% nutrient supplementation | 29,100 | 11,250 | 3,158 | 2,556 | 2,471
COD in Wastewater (mg/L)

## Slide 14: Results
Time (day) | 0 | 2 | 3 | 4 | 5
Fresh YPD | 1,255 | 659 | 541 | 659 | 726
2nd time used YPD | 1,255 | 618 | 554 | 709 | 794
2nd time used YPD with 10% nutrient supplementation | 1,255 | 634 | 609 | 694 | 823
3rd time used YPD | 1,255 | 798 | 624 | 681 | 675
3rd time used YPD with 50% nutrient supplementation | 1,255 | 808 | 577 | 674 | 641
Time (day) | 0 | 2 | 3 | 4 | 5
Fresh YPD | 179 | 49 | 33 | 35 | 41
2nd time used YPD | 179 | 46 | 51 | 44 | 45
2nd time used YPD with 10% nutrient supplementation | 179 | 50 | 33 | 46 | 47
3rd time used YPD | 179 | 64 | 39 | 31 | 36
3rd time used YPD with 50% nutrient supplementation | 179 | 76 | 43 | 34 | 38
Total Nitrogen in Wastewater (mg/L)
Total Phosphorus in Wastewater (mg/L)

## Slide 15: Results
Chart: Biomass
| 2 | 3 | 4 | 5
Fresh YPD | 6.0078 | 6.5678 | 6.4867 | 5.96
2nd time used YPD | 7.4189 | 6.4533 | 6.0717 | 6.265
2nd time used YPD with 10% nutrient supplement | 7.3889 | 7.1589 | 6.57 | 5.4417
3rd time used YPD | 5.7067 | 6.8967 | 6.6317 | 6.1583
3rd time used YPD with 50% nutrient supplement | 5.4744 | 6.4733 | 6.2683 | 6.2017

## Slide 16: Results
Chart: Lipid Yield
| 2 | 3 | 4 | 5
Fresh YPD | 2.5778 | 2.4922 | 1.895 | 2.0867
2nd time used YPD | 2.7444 | 2.4 | 1.8667 | 1.96
2nd time used YPD with 10% nutrient supplement | 2.1833 | 2.2056 | 2.0233 | 1.8117
3rd time used YPD | 2.1611 | 1.8256 | 2.1333 | 1.9733
3rd time used YPD with 50% nutrient supplement | 2.2878 | 2.2789 | 1.9767 | 1.9283

## Slide 17: Results
Chart: Lipid Content (%)
| 2 | 3 | 4 | 5
Fresh YPD | 42.9184 | 38.2015 | 29.2634 | 35.0031
2nd time used YPD | 36.8994 | 37.3513 | 30.9503 | 31.379
2nd time used YPD with 10% nutrient supplement | 29.6101 | 30.8464 | 30.7948 | 33.2769
3rd time used YPD | 37.8753 | 26.431 | 32.215 | 32.0724
3rd time used YPD with 50% nutrient supplement | 41.8161 | 35.5562 | 31.6241 | 31.0892

## Slide 18: Results
 | Amount of spent medium generated by 1 L fresh medium (mL) | Amount of cells produced by spent medium from 1 L fresh medium (g/L) | Amount of cells produced by 1 L medium (g/L) | Medium amount required to produce the amount of cells produced by 50 L fresh medium (L) | Total cost of materials for medium (USD) | Price for glucose (USD/kg) | Price for peptone (USD/kg) | Price for yeast extract (USD/kg)
Use of fresh medium only | 800 | 0 | 6 | 50 | 389 | 9.8 | 270 | 218.5
Use of fresh and 2nd time used medium | 800 | 2.4 | 8.4 | 35.7 | 278 | 9.8 | 270 | 218.5
Cost for producing amount of cells produced from
50 L fresh medium

## Slide 19: Conclusion
The spent YPD medium generated while in preparation of seed culture with high cell density was successfully reused for the 2nd time without further addition of nutrient.
The cells produced by reused medium showed remarkable biomass production with similar lipid productivity and higher removal efficiencies for organics and nutrients in real non-sterile mixed wastewater in shorter cultivation time compared to the fresh medium.
Cells produced from the 3rd time used medium did not show a good performance regardless of nutrient supplementation.
Reutilization of spent medium showed high potential in the reduction of material cost for microbial lipid production process.

## Slide 20: Acknowledgements
University of Macau Multi-Year Research Grants:
MYRG204(Y3-L4)-FST11-SHJ, MYRG2014-00112-FST
Macau Science and Technology Development
Fund: FDCT/061/2013/A2
Ms. Ling, PhD student; Dr. Toledo, post-doc;
Ms. Tian, MS student