## Slide 1
Onion Waste Recycling to Produce the Value Added by-Products
Hyeun-Jong Bae

## Slide 2
South Korea

## Slide 3
Chonnam National University

## Slide 5: CHONNAM NATIONAL UNIVERSITY
Serving the community With Global Vision
Bioenergy Research Center
2010-2019 Priority Research Center
Chonnam National University

## Slide 6
High Value Creation in Biomass Bioconversion
Developing Advanced Biotechnology System
Development of Efficient Pretreatment Methods
1
Biomass Bioconversion
by Enzymatic Process
2
3
Biotechnolgy is key Competences of BRC

## Slide 7
Onion waste is produced from various processed onions.
They are one of major industrial waste.

## Slide 8
Design Agricultural Wastes Recycling
Cost reduction of Waste treatment
Value Added Material Production
Environmental-Friendly Safe to handle Wastes
BRC Pioneering Following Issues

## Slide 9
From FAO (Food and Agriculture Organization of the United Nations)
World Onion Production
83 million tons of onions are produced annually (2013)
Country | Thousand Tons
World | 82,852
China | 22,600
India | 16,309
United States | 3,277
Iran | 2,260
Russia | 2,081
Egypt | 2,025
Turkey | 1,819
Korea, South | 1,196
Spain | 1,187
Algeria | 1,183
Others | 28,915

## Slide 10
Source: The Times of India
High yields are found in Korea, Japan, Europe and the USA.

## Slide 11
yr | ton
2009 | 1,372,291
2010 | 1,411,646
2011 | 1,520,016
2012 | 1,195,737
2013 | 1,294,009
Onion Production (Dry) in South Korea
Production Area | (ha)
Chonnam | 12,080
Kyungnam | 5,294
Kyungpook | 2,602
Chobuk | 1,654

## Slide 12
Crystalline
Amorphous
Crystalline
Endo cellulase
CBH I
CBH II
β-glucosidase
NR
R
Cellobiose
Enzymatic bio-process- biodegradation of lignocellulose

## Slide 13
Strategy for Enzyme Cost Reduction
Increase
Enzyme Activity
Low Cost
Mass Production

## Slide 14
Produce of Onion Waste Hydrolysates by Enzymatic Bioprocess

## Slide 15
Onion Skin Waste
Enzymatic hydrolysis
Onion sugars
Bioethanol
Fermentation

## Slide 16
We evaluated the use of OSW for biosugar and Quercetin production
Onion production
82.9 million T/yr
Onion Skin Waste
Value-added byproduct
Quercetin
Bio-ethanol
Notes: Onions are low in calories, very low in sodium, and contain no fat or cholesterol. Furthermore, onions contain fiber and flavonoid

## Slide 17
% (w/w) | Onion skin
Rhamnose | 2.5
Arabinose | 1.4
Xylose | 4.2
Mannose | 3.7
Galactose | 2.8
Glucose | 40.6
Total (sugar) | 53.7
Quercetin | 0.1- 0.2
Chemical composition (% dry weight) of onion skin waste.

## Slide 18
Cellulase (FPU/g OS) | Pectinase (mg/ g OS) | Xylanase (mg/g OS) | Glucose (mg/mL) | Conversion rate (%)
4.8 | 0.06 | 0.1 | 0.4 | 9.9
4.8 | 0.06 | 0.5 | 1.65 | 40.6
4.8 | 0.06 | 0.75 | 2.53 | 62.3
4.8 | 0.06 | 1.0 | 3.3 | 81.3
4.8 | 0.16 | 0.1 | 0.55 | 13.5
4.8 | 0.16 | 0.5 | 1.76 | 43.3
4.8 | 0.16 | 0.75 | 2.66 | 65.5
4.8 | 0.16 | 1.0 | 3.5 | 86.2
12 | 0.06 | 0.1 | 0.67 | 16.5
12 | 0.06 | 0.5 | 2.19 | 53.9
12 | 0.06 | 0.75 | 2.88 | 70.9
12 | 0.06 | 1.0 | 3.72 | 91.6
12 | 0.16 | 0.1 | 0.86 | 21.2
12 | 0.16 | 0.5 | 2.37 | 58.4
12 | 0.16 | 0.75 | 3.16 | 77.8
12 | 0.16 | 1.0 | 3.83 | 94.3
24 | 0.06 | 0.1 | 1.46 | 36.0
24 | 0.06 | 0.5 | 2.87 | 70.7
24 | 0.06 | 0.75 | 3.63 | 89.4
24 | 0.06 | 1.0 | 3.92 | 96.6
24 | 0.16 | 0.1 | 1.60 | 39.4
24 | 0.16 | 0.5 | 2.94 | 72.4
24 | 0.16 | 0.75 | 3.85 | 94.8
24 | 0.16 | 1.0 | 4.01 | 98.5
Glucose Concentration of OSW Hydrolysate under
Different Enzyme Loading Conditions.

## Slide 19
Optimized enzyme loading volume – 90% bioconversion rate
Pec: 0.16 mg
Xyl: 1mg

## Slide 20
Sugar Analysis after Enzymatic Hydrolysis

## Slide 21
Thin-layer chromatography (TLC) plates showing the presence of quercetin in isolated onion skin wastes (OSWs) samples before and after enzymatic hydrolysis.
약 1.6 배 증가

## Slide 22
SMNP
Receptor 1
ZnCl2
Extracts of onion skin
EDTA
+
Receptor 1
TSMNP-Zn
TSMNP
Silica coated magnetic nanoparticle
Terpyridine receptor
Biomagnetic Separation Techniques
Notes: 먼저 silica coated magnetic nanoparticle (SMNP)을 준비 후 Zn와 잘 결합하는 성질을 가진 terpyridine 유도체 (receptor 1)를 SMNP의 표면에 도입시킵니다.
이후 ZnCl2를 이용하여 terpyridine 유도체가 도입된 magnetic nanoparticle에 Zn 이온을 도입시킵니다.
준비된 TSMNP-Zn에 양파 껍질 추출물을 첨가하면 TSMNP-Zn은 quercetin과 잘 결합을 이룰 수 있습니다.
TSMNP-Zn에 결합된 quercetin을 분리시키기 위하여 quercetin 보다 Zn이온과 결합력이 뛰어난 EDTA를 첨가하면 원하는 quercetin을 분리시킬 수 있습니다.
참고로 SMNP 만드는 과정입니다.
먼저 FeCl3와 FeCl2를 이용하여 magnetic nano particle (MNP)을 합성하였고 여기에 TEOS를 이용하여 MNP 표면을 silica로 코팅하였습니다. Silica 코팅 이유는 receptor 1을 도입시키기 위해서 입니다. Receptor 1 말단에 도입된 -Si-(OEt)3가 공유결합(covalent bonding)에 의해 silica 표면에 잘 붙습니다.

## Slide 23
10 ton
(M.C: 80%)
Glucose: ≒ 800kg
Enzymatic hydrolysis
Fermentation
(≒90%)
Quercetin: 20kg → 32kg
2. Extraction
(≒75%)
EtOH: ≒ 370kg
Mass balance –Bioethanol and quercetin production
Quercetin: 21.6kg
1. Separation
(≒90%)
1.6배

## Slide 24
Thank you for your attention.

## Slide 26
QUESTIONS?
Question
??????
Question
??????
baehj@chonnam.ac.kr
Hyeun-Jong Bae