## Slide 1: How to make “green” plastics “greener”
·
SP Technical Research Institute of Sweden
Department of Chemistry, Materials and Surfaces
Ignacy Jakubowicz
SP Group owners 100 % RISE
Subsidiaries 10
Employees 1400
Postgraduates 400
Turnover 180 MUSD
Customers More than 10,000
Papers and Reports 520

## Slide 2: Sweden's most extensive resource for research, innovation and development
www.sp.se

## Slide 3
Latex
Chitin
Various definitions are used:
Bio-degradable
Bio-compatible
Made from renewable resources
What are bio-plastics or ”green” plastics?
Sugar
Starch
Cellulose

## Slide 4: Renewable feedstock for polymers
Thermal gasification with stem and oxygen
Fermentation
Ethanol (C2H5OH)
Synthesis gas (CO + H2)
ethylene
Methanol (CH3OH)
Ethylene, propylene, butylene
Hydrogen gas (H2)
Solar
cell
Biomass
Polymers
Diverting agricultural land from producing food crops to producing feedstock for the bio-economy leads to food insecurity and food prices
Bio-based plastics can be seen as a part of a broader bio-based economy

## Slide 5
Why should we make plastics from renewable feedstock?
Production cost of ethylene in the future?
Price & supply of crude oil
Reduce emissions of CO2
Improved public opinion about plastics
Political decisions
Customer demands
LEGO Group to invest 1 Billion DKK boosting search for sustainable materials

## Slide 6: Why biodegradable plastics?
EN 13432 composting
Special products for better economy & environment
Littering
“The antisocial littering issue falls not within the scope of this standard.
Plastics’ biodegradability is not an encouragement to antisocial behaviours.”
Workshop 15 June 2015
Notes: Materialen bearbetads i form av en produkt (kniv) två gånger på industri (Hammarplast) för att simulera återvinning av produktionspill.

## Slide 7
Is biological recycling the ideal solution?
Value as materials – can be recycled
Value as feedstock – can be converted to useful chemicals
Energy value – can be incinerated with energy recovery
Biodegradation to CO2 and water is equivalent to incineration but without recovery of any useful value and should be the very last option
Workshop 15 June 2015
Notes: Bearbetning (extruderad och pressad)
Granulat och sex cyklar bearbetad material har granskat i syfte med nedbrytning av materialet under processbetingelse för både PLA/HDPE och PLA/PC.

## Slide 8: Do we need to recycle bio-plastics?
Process Energy
Transportation Energy
Energy of Material Resource
New raw material to each product
New raw material to the first generation then 100% recycled
Chart: 
| HDPE | PLA
 | 29 | 56
 | 52 | 0
 | 5 | 5
 | 29 | 56
 | 0 | 0
 | 5 | 5
 | 29 | 56
 | 0 | 0
 | 5 | 5
1
1
2
2
3
Renewable resources are finite because they can only be replenished at a certain rate
Sustainability is superior to renewability

## Slide 9: Why should we recycle bio-based plastics?
EU Waste Framework Directive 2008/98/EC, the Landfill Directive 1999//31/EC and the Packaging and Packaging Waste Directive 94/62/EC targets by weight :
50 % for household and 70 % for construction and demolition waste by 2020
packaging waste 80 % by 2030
plastics 60 % by 2025
End of Life Vehicles Directive (2000/53/EC):
min. 95 % recovery, 85 % recycling by 2015
Waste Electrical and Electronic Equipment Directive, 2012/19/EU,
min. 85 % recycling by 2016
Waste Policy and Legislation in European Union

## Slide 10: Drivers for the future development in bio-plastics production
Durable bio-plastics that can be recycled constitute a much more resource efficient and environmentally beneficial solution
The market demand: bio-plastics must meet the same processing and performance specifications that exist for conventional fossil based polymers
The most dynamic development is in “drop-in” bio-based polymers

## Slide 11: Bio-based engineering plastics
PA11 (100 % bio-C, Arkema), PA1010 (99 % bio-C, EMS-Grivory)
PA610 (62 % bio-C, EMS-Grivory),
bio-PET (30 % bio-C)
Polytrimethylene terephthalate PTT (28 % bio-C, DuPont)
Polyethylene furanoate PEF (100 % bio-C)
PA
PET
Bio-based polymers as replacement
for fossil-based are not identical

## Slide 12: Challenges for plastics industry
Only bio-plastics
Only fossil-plastics
Both fossil and bio plastics exist at the same time
Bio-based plastics
Fossil-based plastics
Develop recovery systems and end markets for post-consumer waste
Prevent contamination of the existing recycling systems
Prepare suitable labelling system and increase public awareness
Develop collection, separation and sorting technologies for bioplastics
Develop processing technology
Evaluate their indoor and outdoor ageing and durability properties
Develop additives to enhance durability, compatibility and other properties
Evaluate safety and health factors
Develop business models and policy instruments

## Slide 13: Sustainable management of bio-plastic waste
A part of the Mistra programme ”Closing the loop”

## Slide 14
Acknowledgments
Organizing committee for the kind invitation
MISTRA for the financial support
My co-workers for the fruitful collaboration
Thank you for your kind attention !