## Slide 1: BIODIESEL APPLICATION AND BIODIESEL STANDARDIZATION IN CHINA
Research Institute of Petroleum Processing SINOPEC
Dec.6, 2016
1

## Slide 2: CONTENT
1 Status and Development Trend of Biodiesel in China
2 Application Technology Study
3 Biodiesel Standardization in China
4 Predictions and Suggestions
2

## Slide 3
1
Status and Development Trend of Biodiesel in China
3

## Slide 4: Particulate matter (PM) emission from diesel fuel vehicles makes great contribution to smog
At the mercy of the winds?

## Slide 5: Biodiesel can decrease PM emission enormously , EPA’s report
source:http://www.epa.gov/otaq/models/analysis/biodsl/p02001.pdf.

## Slide 6: BIODIESEL：Fatty Acid Methyl Esters (FAME)
Material of biodiesel：
CH2OCOR' CHOCOR"
催化剂
CH2OH CHOH
CH2OH
3 CH3OH
R'COOCH3
R"COOCH
3
R"'COOCH3
CH2OCOR'"'
Vegetable oil or Animal fat
（triglycerides ）
Methanol
KOH glycerin
FAME
EU
RRaappeesseeeeddooiill
US
SSooyybbeeaannooiill
cat

## Slide 7: Other Advantages of Biodiesel
Biodiesel
Renewable
Environmentally
-friendly
Safe to use
Increasing diesel
production
Food security
Alternative for fossil fuels
Lowering the greenhouse gas emissions
High flash point
Reducing the import of petroleum
Safely reuse waste oil

## Slide 8
3 million tons of gutter oil is eaten yearly in China
Source: Prof. He Dongping from Wuhan Polytechnic University

## Slide 9: China Biodiesel Feedstock: Waste oil
4 kinds of waste oil in China
Acidified oil
Byproducts of vegetable oil company. COFCO, China’s leading vegetable oil producer, has 400,000~500,000 t/y
Sewage oil
Oil recovered from restaurants kitchen sewage system
(3) Leftover oil
Oil recovered from the leftovers of restaurants
(4) Used cooking oil
Frying oil from some food processing plants and certain kinds of restaurants such as KFC and McDonalds
9
50 million tons/year

## Slide 10: China Biodiesel Feedstock: wood-plant oil
10
Jatrophaa (麻风树）
Yunnan, Guizhou, Sichuan

## Slide 11: China Biodiesel Feedstock: wood-plant oil
Pistacia Chinesis Bunge（黄连木）
Hebei, Shanxi, Henan, Shannxi
11

## Slide 12: China Biodiesel Feedstock: wood-plant oil
Sapindus mukorossi Gaerth (Chinese Soapberry Seed，无患子 )
12
South Part of China

## Slide 13: China Biodiesel Feedstock: algae
13

## Slide 14: Government Support
producers
Renewable Energy Law
2006
Subsidies
Law
Tax Exemptions
Investment
subsidy
Consumption tax
Value-added tax
>70%
waste oil as
feedstock
20%
investment
Ministry of Finance
14

## Slide 15: 2015 Biodiesel Production
Production 800,000 tons
y
Production Capacit 2,584,000 tons
Source: http://www.chinabd.org.cn/
507,000, 64%
87,000, 11%
182,000, 23%
19,600, 2%
Sewage oil Leftover oil Acidified oil others
15

## Slide 16: Production and Development Trend
Production |  | Capacity
93,000 tons
150,000 tons
150,000 tons
140,000 tons
80,000 tons
80,000 tons
60,000 tons
40,000 tons
100,000 tons
60,000 tons
Source: http://www.chinabd.org.cn/
16

## Slide 17: Main Obstacles
Lack of raw materials
Lack of mandatory standards
Both of BD100 and B5 are voluntary standards at present
Technical obstacles
oxidation stability material compatibility
17

## Slide 18: Application Technology Study
2
18

## Slide 19: Main Projects
National 863 scheme
Projects from Sinopec
Projects from SAC
Projecs from NEA

## Slide 20: Study Examples
Oxidation and antioxidants Why?
Methyl oleate
How to do?
We developed a series of antioxidants
We applied 33 patents including PCT, USP,and EP
Methyl linoleate
Methyl linolenate
Unsaturated FAME

## Slide 21: Antioxidant S-1403
CNOOC, Hainan plant
21
10tons used in CNOOC’s Hainan biodiesel plant
industrial test in Zhuoyue Biodiesel Co. in Fujian and Jiesen Biodiesel Co. in Zhejiang

## Slide 22: Material Compatibility Study
Metal corrosion of biodiesel and biodiesel blends
Swelling property of rubber and plastics
Results and suggestions
Change some kinds of metals and rubbers
Blend less than 10% biodiesel into diesel fuels

## Slide 23: Field Test of Biodiesel
Chery Automobile Co
Nanjing IVECO Co.
Conclusion
No negative effect when biodiesel content is no more than 10%
B5
B10
B20
B5
B10
B20

## Slide 24
3
Biodiesel Standardization in China

## Slide 25: Biodiesel National Specification
Introduction of the project
Sponsored by SAC
(Standardization Administration of the People's Republic of China ) and SINOPEC
Organized by SAC/TC280/SC1
(TC280:Technical Committee 280 on Petroleum Products and Lubricants; SC1:Subcommittee 1 on Petroleum Fuels and Lubricants)
Two standards for the two products of biodiesel BD100
B5
25

## Slide 26
26
Reversion of BD100 is still going on
BD100 Specification of China
Standard No. GB/T 20828

## Slide 27
27
Reversion of B5 is still going on
B5 Specification of China
Standard No. GB/T 25199

## Slide 28: •Test Methods Standardization of Biodiesel in China
Oxidation Stability of Biodiesel Test Method Standard
Based on EN 14112:2003(Rancimat)
As a petrochemical standard (NB/SH/T 0825-2010)
FAME Content in Middle Distillates Test Method Standard
Based on EN 14078:2003(Infrared spectrometry) As a national standard (GB/T 23801-2009)

## Slide 29: •Test Methods Standardization of Biodiesel in China
Oxidation Stability of Biodiesel Blend Test Method Standard
Based on EN 15751:2009
As a petrochemical standard (NB/SH/T 0873-2013)
Oxidation Stability of Biodiesel Blend Test Method Standard
Based on ASTM D7462-11
As a petrochemical standard (NB/SH/T XXXX)

## Slide 30
4
Predictions and Suggestions

## Slide 31
Chinese government will continue supporting biodiesel industries because of the severe air pollution
Biodiesel productivities are decreasing due to the price of crude oil
Public transportations in big cities should use biodiesel as demos
Developing new profitable products with biodiesel

## Slide 32: Thank You for Your Attention!
Questions and Suggestions?
32