## Slide 1: Consolidated Bioprocessing of Lignocellulosic Materials for Cost-Competitive Bioenergy Production
L.P. Christopher
Biorefining Research Institute
Lakehead University
Thunder Bay, ON, Canada

## Slide 2: Biomass and Bioenergy
Demand for production of renewable energy currently driven by four major factors:
  increasing energy demands
  fluctuating oil prices & concerns about oil reserves
  growing food needs
  increasing GHG emissions
Biomass share of US energy supply: from 3% in 2004 to 5.5% in 2014.
US DOE: 1.3 billion dry tons of biomass available for bioprocessing to displace 30% of the nation's consumption of liquid transportation fuels
Billion Ton:: Forest residues (~30%); Dedicated Crops (~25%); Crops & Agri Residues (~40%);

## Slide 3
Economic benefits
  Reduced dependence on imported petroleum
Environmental benefits
  Reduced GHG emissions
  Reduced pollution by utilizing industrial & agricultural waste
  Biodegradable, reusable & recyclable products
Social benefits
  Social development of rural communities
  Improvements in human health and quality of life
DOE’s Billion Ton Biomass : 30% of US gasoline demand
Billion Ton Vision

## Slide 4: Biorefinery Concept : C-neutral, Waste-free Bioprocessing

## Slide 5
Consolidated Bioprocessing (CBP)
Four processing steps for biomass conversion carried out in one bioreactor by a single organism or microbial consortium:
Enzyme production
Enzymatic hydrolysis of biomass to fermentable sugars
Fermentation of hexose sugars
Fermentation of pentose sugars

## Slide 6
Advantages of CBP
Advantages of Thermophilic CBP
Hydrolysis and fermentation carried out at the same temperature – a drawback of SSF: reduced cooling costs; increased enzymatic hydrolysis efficiency
Continuous evaporation of ethanol from broth under vacuum: reduced ethanol intolerance; simplified distillation
Overall processing cost reduction over SSF – 4-fold

## Slide 7: Impact of Processing Steps on Biofuel Production Cost
Consolidated bioprocessing to cellulosic ethanol
has the greatest potential for cost reductions (40-60%)

## Slide 8
Engineering Ethanologens for CBP
Engineering enzyme production capabilities
Engineering pentose-fermenting capabilities

## Slide 9
One of the world's largest petrified forests, located in WY, USA
2.2 million acres in area, larger than the states of Rhode Island or Delaware
About half (10,000) of the geothermal features and two-thirds (300) of the world's geysers are located in YNP
One of the greatest locations of thermophilic microbial diversity
Yellowstone National Park
Bioprospecting for Extremophiles with CBP Capabilities

## Slide 10: Extremophiles from Yellowstone National Park - YNP, WY
Discovery of new thermophilic bacteria
Sampling
Sampling
Enrichment
Isolation
Identification
Characterization
Optimization

## Slide 11: Bioethanol

## Slide 12: Bioethanol Feedstocks

## Slide 13: Switchgrass (SWG)
Availability of switchgrass biomass in the United States
(http://bioweb.sungrant.org/Technical/Biomass+Resources/Agricultural+Resources
/Crop+Residues/Corn+Stover/Default.htm)
Energy crop (low nutrient/water requirements; high adaptability to any weather/soil/land conditions)
High yields (25 t/ha or 10 t/acre on average)
High carbohydrate (>65%) and low lignin (<20%) content (favors bioprocessing)
Low energy cost: $2.5/GJ ($3.5/GJ for natural gas; $17/GJ for crude oil)
Production predicted to increase up to 10-fold by 2020
(from current 30 million t/year in 2010 to 300 million t in 2020)

## Slide 14: Feedstock Pretreatment
Single screw extruder
Screw speed : 100 rpm
Barrel temperature: 100°C
Mechanical extrusion mixes, grinds, sterilizes & disrupts plant cell walls
Can be combined with chemical & enzymatic pretreatments
Does not change biomass composition or create inhibitors
Switchgrass
Parameters | Untreated SWG (%) | Pretreated SWG (%)
Glucose | 25.5±5.8 | 25.2±3.5
Xylose | 17.4±2.1 | 17.6±2.0
Arabinose | 4.9±1.2 | 4.8±1.3

## Slide 15: Cellulase Characterization
Broad pH optima: 4-6
Broad temperature optima: 70-85oC
Remarkable thermostability: 50% residual activity after incubation at 70oC for 7 days

## Slide 16: Hydrolysis and Fermentation Process Configurations
At 20% solids loadings - partial liquefaction of biomass observed after 36 h
Process continued as SSF
Liquefaction (70oC)
SSF
(30oC)
Pretreatment (100oC)
Distillation
(78oC)
PRETREATMENT
Total
hydrolysis
Bacterial SSF
Liquefaction
Saccharification
DOWN STREAM PROCESSING, ETHANOL DISTILLATIO
Fermentation
SSF
Liquefaction
Total
hydrolysis
Fermentation
SSF
Fermentation
60
PRETREATMENT
Total
hydrolysis
Bacterial SSF
Liquefaction
Saccharification
DOWN STREAM PROCESSING, ETHANOL DISTILLATION
Fermentation
SSF
Liquefaction
Total
hydrolysis
Fermentation
SSF
Fermentation
PRETREATMENT
Total
hydrolysis
Bacterial SSF
Liquefaction
Saccharification
DOWN STREAM PROCESSING, ETHANOL DISTILLATION
Fermentation
SSF
Liquefaction
Total
hydrolysis
Fermentation
Fungal
SSF
Fermentation
70
50
40
30
Temperature (oC)

## Slide 17: Enzymatic Hydrolysis: 50oC vs 70oC
Temperature vs Enzyme Loadings
Temperature vs Solids Loadings
Temperature vs Time
RSM Modeling of Enzymatic Hydrolysis: All 4 parameters had significant impact on cellulose conversion yields
Parameter | Advantages at 70oC vs 50oC
Enzyme loadings | At the same glucose yield, 4-times lower enzyme loadings required (5 FPU g-1 DM vs 20 FPU g-1 DM)
Solids loadings | At the same solids loadings, 30-60% higher glucose yields obtained
Hydrolysis time | At the same glucose yield, 2.7-times shorter hydrolysis times required (36 h vs 96 h)

## Slide 18: CBP for Ethanol Production
Microorganism : Geobacillus sp. R7
Substrate(0.5 g/L) : corn stover, prairie grass
Temperature : 600C
pH : 7
Agitation : 150 rpm
Time : 216 h (9 d)
Chart: Time (h)
| 0 | 24 | 72 | 120 | 168 | 192 | 216
PCS- Cellulase | 0 | 1.074 | 1.467 | 1.729 | 1.95 | 2.987 | 1.048
PPCG-Cellulase | 0 | 2.62 | 2.594 | 3.013 | 2.96 | 2.687 | 2.358
PCS-Ethanol | 0 | 0.014 | 0.023 | 0.02 | 0.021 | 0.02 | 0.018
PPCG-Ethanol | 0 | 0.025 | 0.031 | 0.035 | 0.035 | 0.031 | 0.028
Under limited oxygen (microaerophilic) conditions:
Enzyme production/hydrolysis/fermentation in 1 step
Clostridium sp. CBP biomass to ethanol capabilities
First report on Geobacillus sp.
Parameters | Geobacillus sp.
End products from cellulose (aerobic) | glucose, cellobiose
End products from cellulose (microaerophilic) | glucose, cellobiose, acetic acid, ethanol

## Slide 19: Advantages of Thermostable Cellulases
Increased reaction/conversion rates due to improved mass transfer rates allowing the use of lower enzyme dosages resulting in higher yields of fermentable sugars;
Improved substrate solubility and reduced viscosity of feedstock allowing the use of higher solids loadings;
Reduced hydrolysis times resulting in significant cost savings

## Slide 20: Biohydrogen

## Slide 21
Economy
H2 Importance
H2 is considered the fuel of the future due to:
  high energy density of 143 MJ/Kg (H2) - compared to 26.9 MJ/Kg for EtOH (> 5-fold) and 43.5 MJ/Kg for gasoline (> 3-fold)
  eco-friendly: non-polluting - water is the only product, no GHG
  renewable: can be produced from plant biomass and organic waste
Improves energy efficiency (when integrated with fuel cells)
Strengthens energy security
Global demand of 45 million t/year (9 million t/year in the U.S. = 20% of total)

## Slide 22: H2 Production Technologies
H2
Chemical
Methane reforming
Biological
Biophotolysis
Electrolysis
Photo-
fermentation
Dark
fermentation
2H2O → 2H2 + O2
C6H12O6 + 12 H2O → 12 H2 + 6CO2
C6H12O6 + 2H2O → 2CH3COOH+ 4H2 + 2CO2
Non-renewable
GHG
96% of total prod.
High capital cost
4% of total prod.
(Renewable)
O2 inhibits H2ase/
N2ase
Low yields/rates
Low photochem.
efficiency
No GHG
Higher rates/ yields
No light required
No GHG
Broad substrate
utilization

## Slide 23: CBP for H2 Production
H2 energy production cost (biomass): $15-25/GJ
H2 energy production cost (steam reforming): $11/GJ
Crude oil energy production cost: $17/GJ
SWG/MSW
Pretreatment
Saccharification
Dark fermentation
H2
Direct conversion
Acid hydrolysis - fermentation inhibitors
Enzymatic hydrolysis – expensive
Direct conversion of biomass (CBP) omitting pretreatment and saccharification would decrease H2 energy costs (target: <$11/GJ) and increase cost competitiveness of production process.
Novel H2 overproducing strain
COST

## Slide 24: Municipal Solid Waste (MSW)
Source: Center for Sustainable System, University of Michigan (2009)
Microbial fermentation
MSW – 250 million t in U.S. (2010)
Close to 5 lb/person/day waste generation
> 60% biodegradable material
Pollution burden with no significant cost value
Huge potential for environmental/ economic benefits

## Slide 25: H2 Production Parameters & C-Balance of Isolate A
Parameter | Polymeric Substrates |  | 
 | Cellulose | SWG | 
Max H2 concentration (mmol/L) | 23.18 | 14.29 | 
Vol H2 production rate (mmol/L/h) | 0.16 | 0.10 | 
H2 yield (ml/g substrate) | 260.49 | 310.33 | 
Cellulose vs SWG
Higher H2 concentration (23 g/l) and volumetric productivity (0.16 mmol/L/h)– on cellulose
20% higher H2 yield (310 ml/g) on SWG over cellulose
Carbon material balance
48-54% of carbon - directed towards cell biomass formation
25–35% of carbon - released as CO2
11-27% of carbon - converted to metabolites (acetate and lactate)

## Slide 26: H2 Production by Thermophilic Isolate A
Control
Glucose
Switchgrass
40 mmol H2/L on 1% glucose after 96 h (or 4 mol/mol glucose)
18 mmol H2/L on 3% SWG after 96 h
No chemical or biological pretreatment of SWG required
The highest reported level of H2 production rate – 0.16 mmol/L/h from untreated SWG
Isolate A under non-optimized conditions produced 0.32 mmol/L /h (2-fold increase)

## Slide 27: Impact of Processing Steps on Production Costs
Consolidated bioprocessing (CBP) has potential for 40-60% cost reductions
Pretreatment can reduce processing costs by 20-30%
Thermophilic CBP (TCBP) has the greatest potential for cost savings: 75% on average
H2 from biomass:
$15-25/GJ
H2 by steam reforming: $11/GJ
Crude oil: $17/GJ

## Slide 28: Advantages of Thermophilic Bioprocessing
Broad range of complex polymeric substrates to produce H2
Thermodynamically-favorable reaction of H2 formation at higher T
Theoretical H2 yield of 4 mol/mol glucose reached
No physico-chemical pretreatment of SWG required
Decreased risk of contamination by microorganisms that compete for the same substrates
Potential cost savings from thermophilic consolidated bioprocessing (TCBP) estimated at 75% on average

## Slide 29
Thank you