## Slide 2: Denitrifying Bioreactor Midwestern Cornbelt Nutrient Sequestration: Fine Tuning Treatment Technology Lu Zhang, Joe Magner May 29th, 2014

## Slide 3: Nutrient Reduction Strategy

## Slide 4: Denitrification Overview
NO3−
NO2−
NO
N2O
N2

## Slide 5: Why Bioreactor
Subsurface flow
Relatively consistent nitrate concentration over a drainage season at a given site
Biostimulation
High reduction rate
Space

## Slide 6: Lab Study
Design Schematic
The two bioreactors simulate horizontal flow in the field with a length to width ratio of 14:7.
The size of each bioreactor is 0.98m (L) * 0.2m (W) * 0.67m (H).
One has transparent sides to provide view of the inside. Both sides are covered with tarp to prevent light effect on microbial growth.
Each chamber has two baffles inside to guide the flow. Water enters from the bottom on one side and comes out from the top on the other side.
Soil from the field site (mostly Clarion-Storden loams) is used to seal the top. When water is running, the soil on top is always saturated providing anaerobic condition inside.
Nutrient water is prepared in the storage tank and pumped into the overhead tank. Six flow meters are used to control the flow rate in each chamber.
PVC containers are used to catch outflow for nitrate probe uses.

## Slide 7: Lab Study
Design Components
Variables
Alternative C sources: food source for denitrifying bacteria
  Woodchips- mix of hardwood
  Biochar- “caramelized woodchips”
  Corn cob
Residence time
  24 and 8-hour
Controlled factors
Nitrate concentration: 21±1 ppm
Temperature: T is around room temperature
Processes competing for available C: oxygen availability

## Slide 8: Lab Study
Research Method
Nutrient removal is evaluated by nitrate reduction and phosphorus reduction. Nitrate is measured on a daily-base. Phosphorus is measured every three days.
Nitrous oxide production will be measured to determine the effect on greenhouse gases emission.
The in-situ residence time will be determined by bromide tracer.
Residence time is designed to be 24 hours (50ml/min flow rate) for the first 3 months and 8 hours (150 ml/min) for the next 2 months.

## Slide 9: Lab Study- 24 hr result

## Slide 10: Lab Study- 24 hr result

## Slide 11: Lab Study- 24 hr result

## Slide 12: Lab Study- 24 hr result

## Slide 13: Lab Study- 24 hr result

## Slide 14: Lab Study- 8 hr result

## Slide 15: Lab Study- 8 hr result

## Slide 16: Lab Study- 8 hr result

## Slide 17: Lab Study- 8 hr result

## Slide 18: Lab Study- 8 hr result

## Slide 19: Summary
Woodchip: nitrate removal
Biochar: orthophosphate removal, N2O, longevity
Corn Cob: environmental resilience

## Slide 20: Questions?