## Slide 1
.
6th World Congress on Biotechnology
New Delhi, India-2015
BIOPURIFICATION SYSTEM FOR A PESTICIDES MIXTURE DEGRADATION
MC.Diez,1N. Millahueque, 2F. Gallardo
1Chemical Engineering Department, 2Chemical Sciences and Natural Resource Department.
3Environmental Biotechnology Center-BIOREN
Universidad de La Frontera, PO Box 54D, Temuco Chile. cristina.diez@ufrontera.cl

## Slide 2
Source: www.trademap.org
PESTICIDES CONSUMPTION IN SOUTH AMERICA
Chile import approximately 50,000 Tons of pesticides per year
(SAG 2012)

## Slide 3
Place | Detected pesticides | Levels | Sample | Ref.
Aconcagua River | Lindane, diazinon, oxifluorphen, dicofol, azinfos-methyl, metabenzotiazuron, lenacil , diflubenzuron, atrazine | 0.1-1.12 μg/L | Water | Baéz et al. (1996)
Traiguen River | Simazine, 2,4-D, pichloram, hexazinone, carbendazim | 0.2-9.7 μg/L | Water | Palma et al. (2004)
San Pedro lake Lleu-Lleu, Icalma | Heptachlor, aldrin, endrin, pp´-DDT, pp'-DDE, pp'-DDD | 1.68-0.89 ng/g | Sediments | Barra et al. (2001)
Chillan River | Heptaclor, endrin, endosulfan, metoxichlor | 35-58 ng/L | Water | Cooman et al. (2005)
Limari River basin | 2,4 D, Aldicarb, atrazine + N-dealkyl metabolites, captan, carbofuran, chlorothalonil, cyanazine, dimethoate, diclofop-methyl, parathion, pentachlorophenol, simazine, trifularine | 1-0.05 μg/L | Water | DGA (2004)
Nuble Region | Aldrin, DDT, Dieldrin |  | Soil | Henriquez et al. (2006)
PESTICIDES DETECTED IN SOME PLACES IN CHILE
(Diez , MC. 2010)
EU: 0.1 μg/L for 1 pesticide and 0.5 μg/L for overall pesticides, in water.

## Slide 4
Point-Source Contamination
Intensive Agriculture
Fruits culture
Environment
Impacts
Pesticides Consumption
Inadequate Handling
Contamination of Soil and Water
PROBLEM: CONTAMINATION
CONTAMINATION BY PESTICIDES
Overflow
Spills
Handling

## Slide 5
Pesticide
0.1 µg/L
1 dm2
1 g/dm2 = 1 ton/ha
1g of
active ingredient
POINT-SOURCE CONTAMINATION
Castillo et al., 2008
50-90% of the pesticides found in water fonts come from point-source contamination
10,000 m3 water
Handling
Spillage
Washes
Others

## Slide 6
6
SOLUTION TO AVOID POINT-SOURCE CONTAMINATION
Biobed technology is based on the adsorption and degradation potential of organic biomix composed of top soil (25%), peat (25%) and straw (50%), and the grass layer.
Biobed
Ramp
Biomix
Gravel or clay
Collection well
Diez et al., 2013
BIOBED
www.lechosbiologicos.cl

## Slide 7
Clay Low permeability and high sorption capacity.
Increase the pesticide retention time in the biobed.
Soil Provides sorption capacity and acts as an inoculum of microorganisms.
Soils with low organic matter content and sandy texture are associated with leaching of pesticides.
Straw Provides nutrients for the microorganisms (white-rot fungi), which produce ligninolytic enzymes catalysing the degradation of a broad spectrum of chemicals.
Peat Contributes to sorption capacity, moisture control, and also abiotic degradation of pesticides.
Helps to maintain aerobic conditions and humidity.
Grass: Maintains optimal level of temperature for microbial activity, regulates the moisture in the bed and is an indicator of pesticide spillage.
Rhizospheric degradation of pesticides.
IMPORTANCE OF THE COMPONENTS OF BIOBEDS
Enzymes
LiP
MnP
Laccase

## Slide 8
Type of soil
Peat availability
Lignocellulosic material availability
Organic matter and nutrients (N, P, K)
C/N ratio (> 30) , pH < 6
Components of biomix
Pesticides characteristics
Water solubility
Adsorption Coefficient (Koc)
Chemical structure
FACTORS AFFECTING PESTICIDES DEGRADATION IN BIOBED
Suitable conditions for lignin degrading fungi as WRF

## Slide 9
NPK concentration of 0.5 and 1.0%, modified the bacterial community and affected TCP (3,5,6-trichloro-2-pyridinol) degradation (Tortella et al., 2010)
b
a
DGGE banding pattern (a) and clustering representation (b) of the bacterial 16S rRNA genes amplified with the primers sets EUBf933- GC/ EUBr1387
NPK ADDITION. MICROBIAL DIVERSITY EVALUATION
TCP accumulation in a biobed biostimulated with NPK fertilizer after 40 days of incubation. (Initial chlorpyrifos conc. 160 mg kg-1)

## Slide 10
CHLORPYRIFOS AND METABOLITE CHARACTERISTICS
Chlorpyrifos
(O,O-Diethyl-O-(3,5,6-trichloro-2-pyridyl) phosphorothioate)
Principal metabolite
TCP
(3,5,6-trichloro-2-pyridinol )
Chlorpyrifos TCP
Water Solubility (mg/L) 1.4 80.9
Adsorption Coefficient (Koc) 6000 149
Aerobic Soil Half-Life (days) 7-15 52 GUS Index 0.15 (low) 2.9 (high)
GUS <1.8 Low probability of lixiviation

## Slide 11
ATRAZINE CHARACTERISTICS
Atrazine
Water Solubility (mg/L) 33
Adsorption Coefficient (Koc) 40-155
Aerobic Soil Half-Life (days) 35-50 GUS Index 3.3 (high)
Deisopropylatrazine (DIA)
Deethylatrazine (DEA)
Hydroxiatrazine (HA)
Degradation products
Atrazine
GUS >1.8 High probability of lixiviation

## Slide 12
3,5 DCA
3,5-dichloroaniline
Iprodione
3-(3,5-dichlorofenil)-N-isopropil-2,4-dioxoimidazolidine-1-carboxamide
IPRODIONE CHARACTERISTICS
Principal metabolite
Iprodione 3,5 DCA
Water Solubilidad (mg/L) 13,9 600
Adsorption Coefficient (Koc) 370-700
Aerobic Soil Half-Life (days) 42-80 215-319
GUS Index 2,7 (high)
GUS >1.8 High probability of lixiviation

## Slide 13
CASE OF STUDY - RHIZOSPHERIC EFFECT

## Slide 14
BIOPURIFICACION SYSTEM INSTALLATION
Units of 1m3 with and without vegetal cover + control without pesticides

## Slide 15
ASSAY CONDITIONS
Pesticides and Metabolites
Peroxidase and Dehydrogenase
Organic Acids
Temperature and Humidity
EVALUATIONS
0 to 60 days
BIOMIXTURE
Trumao Soil, Wheat Straw, Peat
(1:2:1 %v), 60% WHC
PESTICIDES (35 mg a.i./kg each)
Atrazine
Chlorpyrifos (484 mg L-1 each)
Iprodione
COMERCIAL VEGETAL COVER
(Festuca sp and Lolium perenne)
HYDRAULIC LOAD
1.2 L/day

## Slide 16
Chart: Depth (cm)
| ATZ | HA | CHL | TCP | IPR | 3,5 DCA | ATZ | HA | CHL | TCP | IPR | 3,5 DCA | L1 | L2
15 | 0.9 | 1.744 | 12.528 | 0.604 | 2.16 | 0.828
35 | 1.272 | 1.912 | 0.512 | 7.402 | 0.636
55 | 0.672 | 0.54
Pesticides and metabolites concentrations in the biomix after 60 days at three depth of biobed. L1, with pesticides and vegetal cover; L2, with pesticides without vegetal cover.
L1
RESIDUAL PESTICIDES AND METABOLITES

## Slide 17
DEHYDROGENASE ACTIVITY
Dehydrogenase activity in biomix . L1, with pesticides and vegetal cover; L2, with pesticides without vegetal cover; L3, without pesticides with vegetal cover; L4, without both pesticides and vegetal cover. A (15 cm), B (35 cm) and C (55 cm).
Chart: Time (d)
| A | B | C | A | B | C | A | B | C | A | B | C | L1 | L2 | L3 | L4
0 | 34.96 | 37.375 | 42.46 | 22.04 | 39.0425 | 32.0425 | 19.7925 | 18.0425 | 31.29 | 17.9575 | 13.875 | 11.7918
15 | 67.125 | 71.95 | 70.025 | 74.2 | 81.625 | 48.045 | 69.2 | 76.125 | 69.025 | 43.0425 | 24.79 | 22.2075
30 | 36.6075 | 59.3 | 54.005 | 64.55 | 74.925 | 47.6 | 65.1 | 54.25 | 50.725 | 31.335 | 15.455 | 11.11
60 | 29.875 | 29.125 | 28.2925 | 27.5425 | 28.4575 | 33.54 | 30.5425 | 31.04 | 27.7925 | 8.0425 | 5.62 | 3.9475

## Slide 18
PHENOLOXIDASE ACTIVITY
Phenoloxidase activity in biomix. L1, with pesticides and vegetal cover; L2, with pesticides without vegetal cover; L3, without pesticides with vegetal cover; L4, without both pesticides and vegetal cover. A (15 cm), B (35 cm) and C (55 cm).
Chart: Time (d)
| A | B | C | A | B | C | A | B | C | A | B | C | L1 | L2 | L3 | L4
0 | 0.27213 | 0.27213 | 0.27213 | 0.27213 | 0.54427 | 0.060474 | 0.48379 | 0.18142 | 0.39308 | 0.39308 | 0.27213 | 0.45356
15 | 0.21166 | 0.2419 | 0.39308 | 0.27213 | 0.15119 | 0.21166 | 0.5745 | 0.2419 | 0.27213 | 0.63498 | 0.33261 | 0.5745
30 | 0.18142 | 0.21166 | 0.60474 | 0.30237 | 0.66522 | 0.33261 | 0.15119 | 0.2419 | 0.2419 | 0.63498 | 0.33261 | 0.48379
60 | 0.18142 | 0.21166 | 0.15119 | 0.27213 | 0.2419 | 0.15119 | 0.21166 | 0.21166 | 0.18142 | 0.27213 | 0.30237 | 0.21166

## Slide 19
Chart: Time (d)
| 0 | 15 | 30 | 60
L1 | 0.13616 | 0.026167 | 0.043712
L3 | 0.071721 | 0.066206
Chart: Time (d)
| 0 | 15 | 30 | 60
L1 | 1.2483 | 1.1995 | 0.56764 | 0.90533
L3 | 0.91531 | 1.0767 | 1.0257 | 1.1875
Chart: Time (d)
| 0 | 15 | 30 | 60
L1 | 1.4841 | 4.8816 | 0.77139 | 0.09942
L3 | 1.368 | 1.8797 | 0.75575 | 0.15782
Chart: Time (d)
| 0 | 15 | 30 | 60
L1 | 0.19741 | 0.096115 | 0.033524
L3 | 0.80381 | 0.54152 | 0.066074
Organic acids extracted from the rhizosphere after 60 days at 15 cm biobed depth. L1, with pesticides and vegetal cover and L3, with vegetal cover without pesticides.
ORGANIC ACIDS EXUDATION

## Slide 20
TEMPERATURE AND HUMIDITY RECORD

## Slide 21
Confocal laser scanning micrographs (CLSM) of wheat straw. A, wheat straw at initial time (0 day); B, wheat straw for L1 biomix; C, wheat straw for L2 biomix; D, wheat straw for L3 biomix; E, wheat straw for L4 biomix. Micrographs B, C, D and E were taken after 60 days of operation.
A
C
D
E
B
CLSM OF WHEAT STRAW OF BIOMIX
Confocal laser scanning microscopy (CLSM) images of colonization and lignocellulosic component degradation by WRF. Lignin (green channel), cellulose (red channel) and fungal mycelium (blue channel).

## Slide 22
MAIN CONCLUSIONS
The degradation of the pesticides was high (>95%) and was highest in biobeds with vegetal cover (L1).
At the hydraulic load used (1.2 L d-1), no pesticide residues were obtained in lixiviates of the biobeds system (L1 and L2)
Dehydrogenase activity was similar in all treatments except in biobed without both pesticides and vegetal cover, where low values were obtained (L4).
Contrarily, phenoloxide activity was highest in biobed without both pesticides and vegetal cover (L4).
Oxalic, malic and succinic acids exudation were highest at the first 15 days in contaminated biobed with vegetal cover (L1), instead of, citric acid was highest in uncontaminated biobed (L3).

## Slide 23
La Araucania, South of Chile
www.lechosbiologicos.cl
www.bioren.cl
THANKS YOU
Acknowledgements: Financed by FONDECYT 1120963 and CONICYT/FONDAP/15130015 projects

## Slide 24
DIFUSSION MATERIALS

## Slide 25
BIOBED CONSTRUCTION