## Slide 1
Development of Improved Compact Cornmill for White Corn
Michael A. Gragasin, Ph.D.
Philippine Center for Postharvest Development and Mechanization (PHilMech)
Department of Agriculture, Philippines

## Slide 2
Rice is the food staple for about half of the world’s 7 billion people. Around 90% of the rice produced is consumed in Asia, home to more than two-thirds of the world’s poor and hungry.
Rice is thinly traded in the world market, accounting for only around 6% of the total world production in 2010.

## Slide 3
The Philippines is the 8th largest rice producer in the world, accounting for 2.8% of global rice production. However, the Philippines was also the world's largest rice importer in 2010.
2004-2013

## Slide 4
The population of the Philippines is estimated at 97 million. Its annual growth rate of around 2% – among the world’s highest.
Philippine population: 97million (2010)

## Slide 5
The government aggressively implemented the Food Staple Sufficiency Program in 2010 to increase rice production, maintain per capita consumption of rice and increase consumption of other staple foods such as CORN.

## Slide 6: IMPORTANCE OF WHITE CORN
White corn serves as main food staple of about 15% of the total population (mostly in major islands of Visayas and Mindanao) in the form of corn grits.

## Slide 7
The poor quality of corn grits is one of the major causes of the diminishing consumption of white corn in the country from 20% in 1980s to 15% of the total population nowadays.
The poor quality of corn grits can be attributed to the poor performance of available corn mill in the country.

## Slide 8
Why there is a need to develop
a village-type corn mill?

## Slide 9
General:
To develop an improved village type cornmill for white corn.
Specific:
Establish parameters in coming up with an improved design;
2. Design and fabricate an improved village type corn mill;
Examine the technical performance of the proto-type village cornmill; and,
4. Determine the economic viability of the cornmill.
PROJECT OBJECTIVES

## Slide 10
METHODOLOGY
Evaluated the Performance of Existing Cornmills

## Slide 11
METHODOLOGY
Came up with a New Design of Village-Type Cornmill

## Slide 12
METHODOLOGY
Fabricated the Prototype Unit

## Slide 13
METHODOLOGY
Subjected the Prototype Unit to Laboratory Tests

## Slide 14
METHODOLOGY
Conducted Physical Analysis on the Output of the Prototype Unt

## Slide 15
METHODOLOGY
Modified/
Improved the Design to Achieve the Desired Output

## Slide 16
METHODOLOGY
Subjected the Prototype Unit to Field Testing

## Slide 17
METHODOLOGY
Modified/
Improved the Design to Achieve the Desired Output

## Slide 18
RESULTS

## Slide 19
Establishment of parameters to come up with an improved design
For Objective No. 1
What TO BE IMPROVE on the design of existing
corn mills?

## Slide 20: Results of performance evaluation of commercial village cornmill
Type of Cornmill | Input Cap. (kg/h) | Output Cap. (kg/h) | Main Product Rec. (%) | Degermi-nation Eff. (%) | Labor Reqt. | Power/fuel consumption
A | 109.70 | 29.71 | 54.80 | 87.79 | 1-2 | 1 L/h diesel
B | 121.75 | 13.06 | 24.80 | 85.70 | 1-2 | 3.06 kW/hr
C | 65.06 | 14.55 | 64.70 | 50.65 | 1-2 | 1 L/h diesel
D | 69.88 | 14.51 | 67.80 | 56.22 | 1-2 | 1 L/h diesel
Lower than 64%
Low milling
recovery
High postharvest
losses
Lower supply of
corn grits
in the market
1st Design Consideration

## Slide 21: Results of performance evaluation of commercial village cornmill
Type of Cornmill | Input Cap. (kg/h) | Output Cap. (kg/h) | Main Product Rec. (%) | Degermi-nation Eff. (%) | Labor Reqt. | Power/fuel consumption
A | 109.70 | 29.71 | 54.80 | 87.79 | 1-2 | 1 L/h diesel
B | 121.75 | 13.06 | 24.80 | 85.70 | 1-2 | 3.06 kW/hr
C | 65.06 | 14.55 | 64.70 | 50.65 | 1-2 | 1 L/h diesel
D | 69.88 | 14.51 | 67.80 | 56.22 | 1-2 | 1 L/h diesel
Lower than 80%
High presence of
Impurities
(tip cap, hull & germ)
in the corn grits
Displeasure
on the part of consumers to eat corn
2nd Design Consideration
Shift to rice

## Slide 22: Results of performance evaluation of commercial village cornmill
Type of Cornmill | Input Cap. (kg/h) | Output Cap. (kg/h) | Main Product Rec. (%) | Degermi-nation Eff. (%) | Labor Reqt. | Power/fuel consumption
A | 109.70 | 29.71 | 54.80 | 87.79 | 1-2 | 1 L/h diesel
B | 121.75 | 13.06 | 24.80 | 85.70 | 1-2 | 3.06 kW/hr
C | 65.06 | 14.55 | 64.70 | 50.65 | 1-2 | 1 L/h diesel
D | 69.88 | 14.51 | 67.80 | 56.22 | 1-2 | 1 L/h diesel
Low output capacity of existing cornmills
3rd Design Consideration

## Slide 23: Results of performance evaluation of commercial village cornmill
Type of Cornmill | Input Cap. (kg/h) | Output Cap. (kg/h) | Main Product Rec. (%) | Degermi-nation Eff. (%) | Labor Reqt. | Power/fuel consumption
A | 109.70 | 29.71 | 54.80 | 87.79 | 1-2 | 1 L/h diesel
B | 121.75 | 13.06 | 24.80 | 85.70 | 1-2 | 3.06 kW/hr
C | 65.06 | 14.55 | 64.70 | 50.65 | 1-2 | 1 L/h diesel
D | 69.88 | 14.51 | 67.80 | 56.22 | 1-2 | 1 L/h diesel
4th Design Consideration
High production cost per kg output of corn grits due to low output capacity of village-type corn mill

## Slide 24: Results of performance evaluation of commercial village cornmill
Type of Cornmill | Input Cap. (kg/h) | Output Cap. (kg/h) | Main Product Rec. (%) | Degermi-nation Eff. (%) | Labor Reqt. | Power/fuel consumption
A | 109.70 | 29.71 | 54.80 | 87.79 | 1-2 | 1 L/h diesel
B | 121.75 | 13.06 | 24.80 | 85.70 | 1-2 | 3.06 kW/hr
C | 65.06 | 14.55 | 64.70 | 50.65 | 1-2 | 1 L/h diesel
D | 69.88 | 14.51 | 67.80 | 56.22 | 1-2 | 1 L/h diesel
5th Design Considerations
How small is a village-type cornmill to become viable?

## Slide 25
Sagbayan Public Market, Bohol
August 28, 2013
Cebu City Public Market
June 15, 2012
How to satisfy the demand of the market ?
6th Design Consideration
Size No. 14
Size No. 16

## Slide 26
What we will do for those harvest that are highly contaminated with aflatoxin?
7th Concern

## Slide 27
For Objective No. 2
Design and fabrication of an improved village type cornmill

## Slide 28
Degermer and milling
Components
Grader Assembly

## Slide 29
DEGERMER
HAMMER MILL
GRADER
PROCESS FLOW

## Slide 30
Fabrication of the cornmill machine incorporating the different design of each cornmill component

## Slide 31
Degermination
Assembly
After Field Testing

## Slide 32
DEGERMER ASSEMBLY

## Slide 33
Performance of Emery Stone with Dented Screen Huller

## Slide 34
2
Size Reduction
Assembly
Size Reduction
Assembly

## Slide 35
Performance of the hammer mill with different number of spokes

## Slide 36
Specifications:
Screens
#10 : Slotted Sheet (2mm)
#14 : Slotted Sheet (1.4mm)
#18 : Wire Mesh (0.74mm)
Speed : 50 RPM
Dimensions
(L x W x H) mm : 1,105 x 695 x 879
CORN MILL GRADER

## Slide 37
Specifications:
Screens
#10 : Slotted Sheet (2mm)
#14 : Slotted Sheet (1.4mm)
#18 : Wire Mesh (0.74mm)
Speed : 50 RPM
Dimensions
(L x W x H) mm : 1,105 x 695 x 879
CORN MILL GRADER

## Slide 38
Examine the technical performance of the proto-type village cornmill
For Objective No. 3

## Slide 39
Performance Test Result of the
PHilMech Developed Compact Cornmill
• Output Capacity: 160.8 kg/h
• Output Recovery: 64.7%
• Degerming Efficiency: 94.7%
• Prime Mover: 5 hp, Single-phase
• Labor Requirement: 1 person
• Power Consumption: 4.17KW/hr
• Overall Dimensions:
Length: 157 cm
Width: 116 cm
Height: 192 cm
• Overall Weight : 476 kg

## Slide 40: Aflatoxin content of corn grits and corn by products after milling, ppb
Corn on cobs
Corn grains
Cracked corn
Corn grits # 12

## Slide 41
Determine the economic viability of the cornmill
For Objective No. 4

## Slide 42
Economic Analysis

## Slide 43
PHilMech Compact Cornmill

## Slide 44
SUMMARY & CONCLUSION
Notes: For the conclusion

## Slide 45: SUMMARY AND CONCLUSION
This research has successfully designed and developed an innovative compact cornmill.
The technical performance of the cornmill have fully satisfied the minimum product recovery of 64% and minimum degermer efficiency of 80% as set by PAES.
The developed cornmill is economically viable given a financial internal rate of return of 54.5% and payback period of 2.4 years. The computed cost of milling per kilogram output is only Php1.18/kg (US$26/t).

## Slide 46
Higher grits
recovery
Higher degerming
efficiency
Salvage reject
corn grain due to
aflatoxin
contamination
Low operating
cost per kg output
Adequacy
of corn grits supply
Accessibility
of good quality
corn grits
Availability
of sufficient and safe supply of corn grits
Affordability
of corn grits in
the market
Potential Impact of the
Developed Technology
Induced consumption of corn as food
Reduced pressure to the government in producing the food requirements of the country
Output
Impact (4A’s)
Effect
Food Sufficiency in the country

## Slide 47
Michael Gragasin, Ph.D.
Supervising Science Research Specialist
Philippine Center for Postharvest Development
and Mechanization (PHilMech)
Department of Agriculture, Philippines
Tel No : +63-44-4560-290 loc 400
Fax No : +63-44-4560-110
E-mail: kitgragasin@yahoo.com

## Slide 48
Brand name : TECO Elec. & Mach.
Co., Ltd.
Type : Single-phase
Induction Motor
Rated power : 5 HP (3.7kW)
@ 1750 RPM
Current : 26 A
Voltage : 220 V
Frequency : 60 Hz
HITACHI
Single-phase
Condenser Motor
2 HP (1.49 kW)
@ 1730 RPM
10 A
220 V
60 Hz
FOR DEGERMER
FOR HAMMER MILL &
GRADER
FOR PNEUMATIC
ELEVATOR
TECO Elec. &
Mach. Co, Ltd.
Single-phase
Induction Motor
0.5 HP (0.37 kW)
@ 3470 RPM
3.2 A
220 V
60 Hz
Notes: The final design of cornmill will utilizes three single-phase electric motors of different horsepower. A 5hp, 2hp and 0.5hp will use to run the degermer assembly, hammer mill and grader assembly, and elevator assembly respectively.