## Slide 1
Bioprocess Development
Upstream and Downstream
Technologies
Monica Chuong, PhD School of Pharmacy-Boston

## Slide 2: References

## Slide 3: Solid State Fermentation
Microorganisms grow on a moistened solid
surface without free flowing water, but have
free access to air.
Low capital investment, water utilization, waste water, and energy requirement (no agitation)
No foam formation
Simple fermentation media
Less space
Less control techniques
Ease in controlling bacterial contamination
Ease in induction and suppression of spores
Low downstream processing

## Slide 7: Submerged Fermentation
The microorganisms and the substrate are
present in the submerged state in the liquid medium.
Large solvent
The heat and mass transfer are more efficient
Amenable for modeling the process
Process scale-up is easy.
More popular

## Slide 16
Pall’s XRS 20 Bioreactor is a bi-axial agitation bioreactor containing a pre-sterilized single-use biocontainer and a control tower.
http://vertassets.blob.core.windows.net/image/ cb1ce0d0/cb1ce0d0-5ccc-4096-8b57- 80ef507bc2e8/wavebioreactorimage.jpg

## Slide 17: Stirred Bioreactors
15 L
150 L Bioreactor
1500 L Bioreactor
From CRAB Web Master
17

## Slide 18: Boehringer Ingelheim Biotechnology Process Plant
http://www.pharmaceutical- technology.com/projects/biberach/images/bild_2.jpg

## Slide 19: Stirred Tank Reactors
The least expensive shape is 1:1 ratio (liquid height to tank diameter)
Aeration (causing air to circulate through) allows longer contact times between the rising bubbles and liquid
Only 70-80% volume should be filled with liquid.
Foam breaker is preferred to be installed, because antifoam agents reduce the rate of oxygen transfer.

## Slide 21: Sterilization
Sterilization of the fermenter and medium may be done separately or together.
The transport lines should be maintained aseptic.
Inside the fermenter should have minimum number of joints. The joints are made with welding and the joint points should be made as smooth as possible to avoid potential sources of contamination.
Threaded Joints
Flanged Joints
21

## Slide 22: Batch Sterilization of Liquid Medium
(a) temperature time plot
(b) reduction in the viable
cell number with time

## Slide 25: Oxygen Transfer from Gas Bubble to Cell

## Slide 26
Mass transfer coefficient kLa: characterize the oxygen transfer capability of fermenters (oxygen transfer coefficient) a = liquid gas interfacial area;
kL= liquid phase mass transfer coefficient

## Slide 27
CAL: oxygen dissolved in the fermentation broth.
CAL, 1 and CAL, 2: two [O2] measured during re-oxygenation at t1 and t2 (re-oxgenation is not steady state).

## Slide 28: Stirred Patterns
Mixing and bubble dispersion are achieved by mechanical agitation.
Requires high input of energy
Baffles are used to reduce vortexing.
Radial-flow impeller
in a baffled tank
Axial-flow impeller
in a baffled tank

## Slide 29: Impellers
Stirred Tank With Baffles

## Slide 30: Sparger
Oxygen is measured in its dissolved form as dissolved oxygen (DO)

## Slide 31
The capacity of the stirrer in handling gas
The amount of gas
introduced.

## Slide 32
Impeller flooding: at high gassing rates or low stirrer speeds, liquid flow up the middle of the vessel.
Impeller loading: at higher stirrer speeds or lower gas flow rates, the impeller is loaded as gas is dispersed towards the vessel walls.
Complete gas dispersion.

## Slide 34: Process Control

## Slide 35: Scale-Ups vs. Scale-Down
Geometric similarity
Kinematic similarity
Dynamic similarity

## Slide 36
Geometric
Similarity

## Slide 37
Kinematic Similarity
Requires geometric similarity and characteristic velocities scale by the same ratio.
Dynamic Similarity
Requires both geometric and kinematic similarity and adds the characteristic forces scale by the same ratio.

## Slide 38: Dynamic Similarity
Maintain the rate of turbulent energy dissipation (), or power intensity (power/volume, P/V) constant.

## Slide 39: Bubble Column Bioreactors (BCRs)

## Slide 40
Homogeneous vs. heterogeneous bubble columns
No mechanical
agitation.
Aeration and mixing are achieved by gas sparging.

## Slide 41
Bubble Columns (Cont’d)
Gas-liquid mass transfer coefficients in reactors depend largely on
gas flow rate
bubble diameter
gas hold-up
Accurate estimation of the mass-transfer coefficient is difficult (exact bubble sizes and liquid circulation patterns are impossible to predict).

## Slide 42: Air Lift Bioreactors (ARLs)

## Slide 43: Airlift Reactors
http://www.babonline.org/bab/045/0001/bab0450001.htm
http://s9.postimg.org/ya85far7j/bab0450001f03.gif

## Slide 44: Airlift Reactors
For plant and animal cell culture, because the shear levels are significantly lower than the stirred vessels.
The very high hydrostatic pressure at the bottom of these vessels considerably improves gas-liquid mass-transfer.

## Slide 45: Airlift Reactors (Cont’d)
Gas hold-up and decreased fluid density
cause liquid in the riser to move upwards.
Gas disengages at the top of the vessel leaving heavier bubble-free liquid to recirculate through the downcomer.
Liquid circulates in airlift reactor as the result of the density different between riser and downcomer.

## Slide 46
Because riser and downcomer are further
apart, gas disengagement is more effective.
The liquid densities differ in riser and downcomer are greater.
The circulation is faster and mixing is better.

## Slide 47: Airlift Reactors
Large airlift reactors can have the
capacities of thousands of cubic meters.
The height of airlift reactors is about 10 times the diameter. For deep shaft systems the height-to-diameter ratio may be increased up to 100 (built underground).
The very high hydrostatic pressure at the bottom of these vessels considerably improves gas-liquid mass-transfer.

## Slide 48: Glass Bead Reactor
For long term culture of attached dependent cell lines.

## Slide 49: Microreactors
Parallel Flow
Cross Flow

## Slide 50: Packed Bed Bioreactors (PBRs)

## Slide 51: Packed-Bed Reactor with Medium
For perfusion culture of mammalian cells.
immobilized microorganism cells and
51

## Slide 52: Fluidized Bed Reactors (FBRs)
52

## Slide 53: Fluidized Bed Reactor
Fine inert carriers provide large surface area for adherence and growth of microorganism to adhere and grow.
The carriers are fluidized to enhance mass transfer and degradation rate of organic pollutants.
53

## Slide 54: Four Modes of Operation
Batch reactor
Stirred semi-batch
Continuous stirred
(Above three: Completely stirred and uniform in composition)
Continuous plug flow reactors

## Slide 55: Modes of Reactor Operations
Plug-flow: The long tube and lack of stirring device in the direction of flow.

## Slide 56: Downstream Processing

## Slide 57: Spray Dryer Lyophilizer
57
Nanofiltration (NF)
Reverse Osmosis (RO)

## Slide 58
Supercritical Extraction Plant
Distillation Plant
Centrifugation Plant

## Slide 59
Homogenization Unit
Freezer Rooms
Demineralized Water Plant
Steam Generation Plant

## Slide 60
Chilled Water Plant
Warm Water Plant
Compressed Air Station

## Slide 61: Effluent Treatments
Incineration

## Slide 62: Trickling Filter (Packed Bed Bioreactors)

## Slide 63
Biochemical oxygen demand (BOD)
The amount of
organisms in
oxygen consumed breaking down the
by these organic
materials in waste water.
Chemical oxygen demand (COD): The amount of oxygen required to chemically oxidize organic compounds in water.
However, COD is less specific, since it measures everything that can be chemically oxidized, rather than just levels of biologically active organic matter.
S-2 + 2 O2 → SO4-2 or 4Fe + 3O2 → 2Fe2O3

## Slide 64: Rotating Biological Contactors
www.edie.net/products
www.madep-sa.com/english/wwtp.html
info.industry.siemens.com
wpcontent.answers.com

## Slide 65: Activated Sludge
Mechanism: Develop biological floc to reduces the organic content of the sewage.

## Slide 66: Anaerobic Digesters
Acid fermenting bacteria degrade the waste to free volatile fatty acids, mainly acetic and propionic acid.
They are then converted to Methane and CO2.
The gas product (biogas) is a useful by-product.

## Slide 67: Landfilling (Solid and Liquid Wastes)
Landfill gas (50-60% methane) can be collected for energy source.
techalive.mtu.edu/.../LandfillCrossSection.jpg67
www.eia.doe.gov/.../images/landfill.gif

## Slide 68: Bioprocess Economics

## Slide 69
Bioprocess Economics (Cont’d)

## Slide 70: Acknowledgements
70
monica.chuong@mcphs.edu
Chemical Engineering, Civil and Environmental Engineering, University of Houston
Chemical Engineering, Oregon State University
School of Pharmacy, Massachusetts College of
Pharmacy and Health Sciences (MCPHS) University
Thank You! Questions?