## Slide 1
2016. 10. 25
Susceptibility assessment of climate change-induced geo-disasters in Korea
World Conference on climate Change
October 24-26, 2016 Valencia, Spain
Moonhyeon Hong
Yonsei University
Sangseom Jeong
Junghwan Kim
Kwangwoo Lee
Notes: Hello, I’m Moonhyun Hong from Yonsei University, Korea
Today I will present the “susceptibility assessment of climate change-induced geo-disasters in South Korea”
This study covers a framework for assessing the expected damage costs of infrastructure for geo-disasters such as landslide and debris flow.

## Slide 2
Introduction
A case study on landslides
Susceptibility assessment of landslide
Conclusions
I
II
III
IV
Notes: The presentation will be progressed following these contents

## Slide 3
Ⅰ
Introduction
2 .
Climate change-induced geo-disaster
1 .
Climate change
3.
Schematic diagram of study procedure

## Slide 4
Warming
Rainfall increase
                Climate change
                More severe fluctuation in rainfall patterns (Rainfall intensity, frequency and quantity)
                Triggering the geo-disaster (landslide)
1
Climate change
Notes: In the Asia-Pacific region, there is an evidence of prominent increases in the intensity and frequency of extreme events
under intense rainfall and severe storms, which trigger more geo-disasters.

## Slide 5
Global climate change is affecting regional weather patterns, rainfall trends, and their variability
Extreme events like landslides related to geotechnical engineering are caused by climate change, particularly in Asia-Pacific Regions
Backgrounds
2
Climate change-induced geo-disaster
One of the most critical disaster related geotechnical engineering
Extreme rainfall is main factor of landslides
Subject of analysis: landslides

## Slide 6
3
Schematic diagram of study procedure
Climate change scenario
Regional climate model
Frequency analysis
Changes of probabilistic rainfall
Estimation of future design rainfall
Landslide analysis
(GIS based landslide prediction model)
Estimation of the initial volume of debris flow (from landslide analysis)
Debris flow simulation
(apply the initial volume)
Impact assessment of urban infrastructure
(from the result of debris flow simulation)
Expected damage cost of infrastructure due to landslide and debris flow under climate change
(Lee et al., 2015)

## Slide 7
Ⅱ
2 .
Prediction model for landslide analysis
3.
Analytical model for the debris flow
1 .
Study area: Umyeonsan (MT.)
A case study on landslides

## Slide 8
1
Study area
Umyeonsan(Mt.) is located in south-east of Seoul
151 landslides and 33 debris flows occurred in 20 watersheds
The accumulated rainfall of 24-h was 424.5 mm.
Seoul metropolitan
(Jeong et al., 2015)
Umyeonsan (Mt.) landslide in July 2011

## Slide 9
1
Study area
Raemian
watershed
Study area: Raemian watershed, Umyeonsan (Mt.)
Umyeonsan (Mt.)
(Jeong et al., 2015)

## Slide 10
Background
2
Prediction model for landslide analysis
Considering rainfall intensity, duration and real-time rainfall
Predicting the rainfall infiltration-groundwater flow from
landslide mechanism
Reflecting topography, hydrology, spatial characteristics
Initial volume of debris flow based on regional scale hazard map
(by applying future design rainfall)
“Prediction model for rainfall-induced landslide
based on 3D spatial data”

## Slide 11
Topography: Slope, slope direction
Hydrology : Precipitation data
Spatial data : Soil and forestry
Geotechnology: Unsaturated soil
Infiltration : Modified G-A Model
Failure model : Infinite slope model
3D GIS data
Physical Model
2
Prediction model for landslide analysis
(Kim et al., 2014)
Notes: 등

## Slide 12
3
Analytical model for the debris flow
Debris flow model with erosion and entrainment of soil
(Lee et al., 2016)
Simulation of debris flow based on Coupled Eulerian-Lagrangian (CEL) method
Considering the erosion and entrainment of soil layer by debris flow
Debris flow
Structures
Initial volume of debris flow

## Slide 13
Ⅲ
2 .
Applied future design rainfall
3.
Result of landslide analysis
1 .
Site investigation and input parameters
Susceptibility assessment of landslide
4.
Debris flow simulation

## Slide 14
Seismic Prospecting
In-Situ Permeability
SWCC
Borehole Shear Test
Direct Shear Test
SPT
Site investigation
1
Site investigation and input parameters

## Slide 15
Input parameters: soil properties and depth
1
Site investigation and input parameters
Soil Property
Soil Depth
Raemian watershed : 4.0~10.0 m
(Kim et al., 2014)

## Slide 16
Future design rainfall based on climate change scenario
2
Applied future design rainfall
Future period: S0 (1971-2000), S1 (2011-2040), S2 (2041-2070), S3 (2071-2100)
Applied rainfall: 100-year return periods, 24-hour duration
S0 (1971-2000): 18.16 mm/hr
S1 (2011-2040): 24.71 mm/hr
S2 (2041-2070): 26.65 mm/hr
S3 (2071-2100): 32.53 mm/hr
Applied rainfall intensity
(Lee et al., 2015)

## Slide 17
3
Result of landslide analysis
S0 (1971-2000)
S1 (2011-2040)
S2 (2041-2070)
S3 (2071-2100)
S0 : 546
S2 : 5,301
Initial volume of debris flow
S1 : 4,330
S3 : 7,463
Safety factor
0 – 0.8
0.8 – 1.0
1.0 – 1.2
1.2 – 1.5
1.5 – 2.0
2.0 – 3.0
3.0 – 5.0
0
0.2
0.4
0.6
0.8
km
0.1

## Slide 18
Impact assessment of urban infrastructure
(from the result of debris flow simulation)
4
Debris flow simulation
S0 (1971-2000)
S3 (2071-2100)
S0 : 7,802 , 0.5 - 1
S1 : 61,874 , 1 – 1.5
S2 : 75,749 , 1 – 1.8
S3 : 106,643 , 1.5 - 2
Damaged area and height
S0 : € 395,672.5
S1 : € 4,465,180.91
S2 : € 6,549,371.71
S3 : € 10,227,664.08
Expected damage cost

## Slide 19
Summary
Period for analysis (yr) | Applied rainfall intensity (mm/hr) | Initial volume of debris flow () | Damaged areas () | Damaged heights () | Expected damage costs (€)
S0 (1971-2000) | 18.16 | 546 | 7,802 | 0.5-1.0 | 395,673
S1 (2011-2040) | 24.71 | 4,330 | 61,874 | 1.0-1.5 | 4,465,181
S2 (2041-2070) | 26.65 | 5,301 | 75,749 | 1.0-1.8 | 6,549,372
S3 (2071-2100) | 32.53 | 7,463 | 106,643 | 1.5-2.0 | 10,227,664
Period for analysis (yr) | Applied rainfall intensity (mm/hr) |  |  |  | Expected damage costs (€)
S0 (1971-2000) | 18.16 | 546 | 7,802 | 0.5-1.0 | 395,673
S1 (2011-2040) | 24.71 | 4,330 | 61,874 | 1.0-1.5 | 4,465,181
S2 (2041-2070) | 26.65 | 5,301 | 75,749 | 1.0-1.8 | 6,549,372
S3 (2071-2100) | 32.53 | 7,463 | 106,643 | 1.5-2.0 | 10,227,664

## Slide 20
Ⅳ
Conclusions

## Slide 21
Conclusions
By using some ewll=designed model and climate scenario, we conducted the susceptibility assessment of landslides for a case study of mountain Umyeonsan, estimating the impacts and the expected costs of infrasturctures due to landslides and debris flow under climate change.
From the results of this study, we can conclude that the climate change-induced geo-disasters like landslides or debris flow will be increased, and the damage of infrastructures due to the geo-disasters will be increased.
The result of these study can be useful information for early warning system of landslides and debris flows.