## Slide 1: Sequestration of Atmospheric Carbon Dioxide as Inorganic Carbon under Semi-Arid Forests
Murray Moinester, Joel Kronfeld, Israel Carmi
Tel Aviv University
World Conference on Climate Change, October 24-26, 2016, Valencia, Spain

## Slide 2: Introductions
Murray Moinester | Prof. (Emeritus) of Physics,
Tel Aviv University
Joel Kronfeld | Prof. (Emeritus) Geosciences,
Tel Aviv University
Israel Carmi | Geosciences Researcher,
Tel Aviv University

## Slide 3: Greenhouse Gases
Atmosphere contains ~320 billion tons CO2
Annual increase is ~20 billion tons CO2
Excessive CO2 greenhouse gas may cause global warming,
climate change, rising sea levels, ocean acidification,
melting icefields, more forest fires, reduced food supply, etc.

## Slide 4: What can be done?
Burn Less Fossil Fuels. (difficult to achieve)
Nuclear power, develop safer reactors, deal more effectively with nuclear wastes.
(“Greens” opposition)
Climate engineering projects proposed for carbon dioxide removal (CDR) and solar radiation management (SRM). (large, expensive, controversial)
Carbon reduction & storage via forestation. (low cost & low tech)

## Slide 5
Leaves inhale CO2. Roots in semi-arid regions are deep. Exhale CO2 into USZ at high partial pressure
CO2 + H2O → dissolved
HCO3- bicarbonate,
combines with soil Ca+2,
precipitates CaCO3 calcite.
Trees in semi-arid regions sequester atmospheric CO2 long term underground as stable calcite, low rainfall
These trees also sequester atmospheric CO2 short term, as organic biomass.
But burning, decomposition of biomass reinject CO2 into the atmosphere.
CO2
Organic
Biomass
Inorganic
Calcite
CO2
CO2
Above Ground ~Organic
Underground Inorganic

## Slide 6: Yatir Forest in Israel → Global Extrapolation
Yatir forest, semi-arid, ~world’s driest. Beginning in 1966, Keren Kayemeth LeIsrael – Jewish National Fund foresters planted four million trees at Yatir. It is now the largest forest in Israel, covering 28 km2 (6920 acres or 2,800 hectares). Extrapolation: Global semi-arid forestation may remove ~2.6 billion tons of atmospheric CO2 per year.

## Slide 7: Global distribution of semi-arid (Steppe, 17.7%) regions

## Slide 8: Chemical Equations for Carbonate Precipitation
Soil gas dissolves into the soil moisture, forms carbonic acid.
CO2 + H2O ↔ H2CO3 ↔ H+ + HCO3-
Carbonic acid dissolves pre-existing soil calcite and releases calcium ions.
(2) CaCO3 + H+ ↔ Ca+2 +HCO3-
Released Ca+2 combines with the DIC, and precipitates calcite.
(3) Ca+2 + 2HCO3- → CaCO3↓ + CO2↑+ H2O
Eq. 3 (idealized) implies no net sequestration. Our isotopic data show net sequestration because: (a) most CO2 from Eq. 3 does not return to atmosphere, (b) many other cation sources contribute to Eq. 3, from silicate weathering, desorption of Ca+2 from clay, gypsum, sea spray, etc.

## Slide 9: Dissolved Inorganic Carbon (DIC) vs. Depth
CO2 from roots combines with soil water of Nizzanim Plants
unsaturated zone (USZ) to form DIC,
comprised mainly of HCO3- bicarbonate.
DIC concentration decreases with depth,
as water flows down, due to CaCO3
precipitation into USZ. Seen easily for
plants with shallow roots, not tree roots.
Depth (cm) | DIC (mmol C L-1)
30-60 | 4.5
60-90 | 3.4
Yatir Plants
Nizzanim Plants

## Slide 10: Yatir forest soil cores to 4.5 meters
Measure CO2 precipitation rate (into CaCO3) per cm per Liter of sediment (Ls) from decrease per cm of DIC (~1.6 mg cm-1Ls-1 at Yatir).
Measure flow rate of water (11 cm yr-1 at Yatir) using tritium in water (HTO) as tracer.
CO2 precipitation rate (within calcite CaCO3) at Yatir is ~18 mg yr-1 Ls-1 of CO2 (11 cm yr-1 x 1.6 mg cm-1Ls-1 ).

## Slide 11: Isotope exchange in Yatir (and Nizzanim) forests
13C and 14C are tracers for precipitation reaction
Soil contains up to 20% relict marine calcite.
DIC concentration decreases with depth.
Relict calcite: Δ14C = -1000 (zero 14C ).
Relict calcite: δ13C=0 (same 13C as standard)
Continuous exchange between DIC and marine
calcite in USZ as rainwater flows down.
δ13C and Δ14C values in solid (nodules) vary
due to exchange between DIC and relict calcite;
& precipitation onto nodule surface.
solid
DIC
solid
DIC
δ13C
Δ14C
Marine
calcite

## Slide 12: Isotopic evidence for CO2 incorporation and sequestration into pedogenic carbonate
δ13C and Δ14C trace the incorporation of atmospheric CO2 from DIC into pedogenic carbonate, as DIC descends down profile interacting with relict marine limestone
Depleted δ13C values in DIC from atmospheric CO2 - exchanges (continuous dissolution and precipitation) with δ13C- enriched relict marine limestone to form pedogenic calcite (solid) of intermediate δ13C values
Atmosphere is the sole source of 14C , introduced into the USZ as 14CO2 via roots and decay
Pedogenic solid in the USZ incorporates 14C, as DIC exchanges with relict limestone
Therefore: atmospheric CO2 tagged by radiocarbon is incorporated into pedogenic carbonate

## Slide 13: Yatir forest research implications
Until now, atmospheric CO2 sequestration by forestation was considered only for short-term organic carbon storage (tree biomass, tree liter, soil organics).
We prove that semi-arid forestation abstracts more atmospheric CO2 in a manner not previously considered. More importantly, forestation provides for long-term inorganic carbon storage into the USZ.
Our research quantifies inorganic carbon sequestration by forestation in semi-arid regions.

## Slide 14: Global Extrapolation of Inorganic Carbon Precipitation in Forest Soil Sediment
Consider sediment volume 1 km2 & 6 m depth (6x109 L), trees above, roots below. Precipitation ~105 tons of CO2 per year (18. x10-3 x 6x109 gm).
More accurate estimates require global data on calcite precipitation rates in semi-arid forests.
A particular global land management policy is tentatively suggested - widespread tree planting in semi-arid regions.
Extrapolating semi-arid sequestration rate globally yields rate of ~2.6 billion tons CO2/yr (~105 tons km-2 x 25 x 106 km2 ~ 2.6 Pg), ~13% of the rate by which atmospheric CO2 is currently increasing.

## Slide 15: Summary
Atmospheric derived CO2 is sequestered long term as calcite in USZ.
Yatir forest receives only ~28 cm/yr rainfall. Low rainfall precludes re-solution of calcite. Calcite sequestration much longer term than biomass carbon. Helped by deep roots compared to temperate regions.
Semi-arid forestation does not decrease productive temperate-region agricultural land. Provide steady employment instead of marginal herding & agriculture, & useful products (lumber, charcoal, off-sets, etc.).
Global extrapolation yields CO2 annual semi-arid forest sequestration rate of ~2.6 billion tons CO2/yr, ~13% of rate of atmospheric CO2 increase.

## Slide 16: THANK YOU!

## Slide 17: Sequestration of Atmospheric Carbon Dioxide as Inorganic Carbon under Semi-Arid Forests

## Slide 18: Paris Climate Agreement, April & Oct. 2016
The Paris Agreement deals with GHG emissions mitigation, adaptation and finance starting in the year 2020, to help stop the gradual warming of the Earth.
Main aim is to limit the increase in the global average temperature to well below 2°C above pre-industrial levels, by reducing GHG emissions.
Many researchers now claim that such targets require "negative emissions", i.e., extraction of CO2 from the atmosphere.
Paris Agreement opened for signature on 22 April 2016. On 5 Oct. 2016, it reached the required 55 countries representing 55 percent of global emissions for the accord to enter into effect. But these agreements need to be followed by actions.

## Slide 19: carbon dioxide removal (CDR)
Large & expensive climate engineering projects have been proposed for carbon dioxide removal (CDR) and solar radiation management (SRM). CDR captures CO2 produced by large industrial plants, compresses it for transportation, and then injects it deep into a rock formation for permanent storage. SRM projects seek to reduce global warming by reflecting sunlight, for example using stratospheric sulfate aerosols.
Carbon reduction & storage via forestation (our low cost & low tech project).

## Slide 20: The Carbon Cycle
Burning fossil fuels and decomposition of dead plants and animals inject CO2 into the atmosphere.
Organic carbon production via forestation provides useful short term organic carbon sequestration.
Semi-arid forests remove atmospheric carbon dioxide, fixing it underground long term as inorganic carbonate salts.
Inorganic
Carbon

## Slide 21: Isotope exchange in Yatir (and Nizzanim) forests
13C and 14C are tracers for precipitation reaction.
Continuous exchange between DIC and solid
sediment in USZ as rainwater flows down.
DIC concentration decreases with depth.
δ13C in solid marine calcite is a result of exchange
between DIC and relict marine calcite (δ13C=0), and
precipitation onto marine calcite surface, while DIC
enriched from -20 (C3 plants).
13C data show continuous exchange and
precipitation along path from DIC into solid sediment.
Δ14C in DIC depleted with depth, while solid
enriched from -1000 (no 14C).
14C exchanges demonstrate that CO2
precipitates out of DIC as calcite. Atmospheric
14CO2 via roots is only radiocarbon source.
solid
DIC
solid
DIC
δ13C
Δ14C
Marine
calcite

## Slide 22: Yatir forest soil cores to 4.5 meters
Measure DIC (as CO2) from CO2 mass & liters of water (Lw) extracted from USZ wet sediment by vacuum distillation (~250 mg CO2 Lw-1 at Yatir).
Porosity (~53%), Humidity (~12%), Dry sediment density (1.24 g cm-3) → A Liter of sediment has 0.47 L solid + 0.12 L water + 0.41 L gas.

## Slide 23: Forestation Cooling
Green Walls are being built/proposed over extensive geographical areas (Sahel, China, India, etc.) that have thicker USZ’s than Yatir.
But forests have reduced albedo; and therefore a warming effect. Forests can cool by evapotranspiration (ET), but do dry semi-arid forests have sufficient soil moisture?
Further study needed to evaluate possible net climate benefits of semi-arid forestation due to carbon sequestration.