## Slide 1: Preparation of Nanocrystal Formulation to Improve Oral Absorption of Mebendazole
Naofumi Hashimoto, Ph.D.
Faculty of Pharmaceutical Sciences
Setsunan Univenersity

## Slide 2
Nanosizing of compounds by wet beads milling is one of the methods to improve the dissolution rate and solubility of poorly water soluble compounds. Mebendazole (MBZ) is used as the anthelmintic drug widely. Furthermore, there were some reports that MBZ had the anticancer effect in preclinical study. However, the bioavailability of MBZ is low (≦ 10%) due to the poor solubility in water (ca. 0.5 µg/mL). The present studies aimed to develop the nanocrystal formulation of MBZ to improve the dissolution behaviour and enhance the oral absorption.
Preparation of Nanocrystal Formulation to
Improve Oral Absorption of Mebendazole
Naofumi Hashimoto, Ph.D.,
Professor, Faculty of Pharmaceutical Sciences of Setsunan University, Osaka, Japan.
E-mail : hashimoto@pharm.setsunan.ac.jp

## Slide 3
Material and Methods
Mebendazole (MBZ)
- M.W. : 295.29
- Melting Point : 287-289 ℃
- Solubility : 0.459 µg/mL (water), 9.04 μg/mL (pH 1.2)
- Bioavailability : 2 - 10%
- pKa : 6.6
Polymer solution (Dispersing agent)
Hydroxypropyl
cellulose–SSL
(HPC)
PVA copolymer
(POVA)
Polyvinyl
alcohol
(PVA)
R = H or CH3
Methylcellulose
SM-4 grade
(MC)
Pova : Polyvinyl alcohol - Acrylic acid –
Methyl methacrylate copolymer
Notes: Mebendazole is very insoluble drug in water. So, the bioavailability is very low and that is 2% in man. We tried to make nanoparticles of mebendazole to improve the oral absorption with good dispersibility by the rotation/revolution pulverizer. These polymer were used to get good dispersibility of nanoparticles.

## Slide 4
Polymer aqueous solution
(0.5 mL)
Zirconia beads
(Φ 0.1 mm, 2.5 g)
MBZ (50 mg)
Pulverization
2000 rpm, 3 min
Polymer aqueous solution
or water
(9.5 mL)
Dispersion
500 rpm, 1 min
Freeze-dried
Formulation
(Nanocrystal Formulation)
Freeze drying
Suspension
(5 mg/mL)
Preparation of MBZ Nanocrystal Formulation
The movement of vessel
NP-100
Notes: Procedure of pulverization by NP-100, NP-100 is one of the rotation/revolution pulverizer, this is a labs scale machine which can pulverize maximam amount of bulk 30 g of compound.
Zirconia beads and Mebendazole were added in the vessel and small amount of polymer aqueous solution was added to appropriate concentration of suspension. Start Np-100 at 2000 rpm for 3 min. Compound was pulverized to about 200 nm particles.
Polymer aqueous solution is added to get an aimed concentration of nano-suspension. The powder of nanoparticles can be obtained by freeze drying when the powder is needed.

## Slide 5
R and r are the radius of revolution and rotation, respectively. h is the horizontal distance of the beads from the center of the vessel. So, r + h corresponds to the distance by which the beads are accelerated. As the collision energy beads have is related to r + h , the largest r + h generates the highest collision energy. Thus, h = r produces the highest collision energy. h was expressed as Eq. 3 in a previous report. ω and Ω are the rotation speed and the revolution speed, respectively.
The Mechanism of the Rotation/Revolution Pulverizer
ω
Ω
ω
Ω
Center of Revolution
Notes: In the case of ordinary centrifuge, vessel revolve. When beads are added in the vessel, beads are pressed against the wall, position A, farthest place from the center. When the vessel rotates itself on the opposite direction against revolution, beads at A move to B, C, D. Beads can get the highest collision energy by the centrifugal force of revolution when they are released from D. longer distance makes higher accelelated velocity at A. Beads collide against drug bulk at A and the crystal particles of drug are pulverized. The most effective ratio of rotation/revolution was caluculated to be 1.

## Slide 6
Effect of Polymer on Dispersion Stability of MBZ Nanoparticles
PVA
HPC
MC
POVA
Effect of Polymer on Dispersion Stability of MBZ Nano-suspension
(MBZ : Polymer = 1:1, w : w)
Effect of Polymer on Re-dispersion Stability of MBZ Nanocrystal Formulation
Particle size (µm)
Volume (%)
Particle size (D90, µm)
Mass ratio of MBZ to polymer
(MBZ : Polymer)
The pulverized MBZ with PVA (MBZ : PVA = 1 : 3) was defined as the MBZ nanocrystal formulation.
Notes: This is the particle distribution when mebendazole suspension in each polymer aqueous solution was pulverized. Nanoparticles of mebendazole could dispersed very well in PVA and HPC aqueous solution. MC and Pova could not. These peaks of large particle sizes were aggregation of nanoparticles. To see the effect of polymer on redispersibility of mebendazole particles. 1 mL of water was added to the freeze-dried sample as to the amount of mebendazole 5 mg, and the particle size was measured by the laser diffractometer. The 1 to 3 ratio of mebendazole versus PVA showed good redispersibility at the small amount of polymer.

## Slide 7
 | D10 (µm) | D50 (µm) | D90 (µm)
Original MBZ | 2.097 ± 0.078 | 5.203 ± 0.124 | 13.76 ± 0.70
Microsized MBZ | 1.11±0.003 | 2.170 ± 0.015 | 4.379 ± 0.088
Nanosized MBZ | 0.076 ± 0.004 | 0.120 ± 0.004 | 0.203 ± 0.004
● Nanosized
● Microsized
× Original
Nanosized
Microsized
Original
Physical Properties of the Pulverized MBZ
Notes: In the condition of the 1 to 3 ratio of mebendazole versus PVA, nanoparticles of mebendazole was pulverized and showed sharp particle distribution. Microsized mebendazole was obtained by the pulverization using 1 mm zirconia balls and 1000 rpm of the rotation/revolution speed for 5 min. Both sized particles showed good crystallinity by PXRD. Table shows each particle sizes.

## Slide 8
 | D10 (µm) | D50 (µm) | D90 (µm)
Original MBZ | 2.097 ± 0.078 | 5.203 ± 0.124 | 13.76 ± 0.70
Nanosized MBZ | 0.076 ± 0.004 | 0.120 ± 0.004 | 0.203 ± 0.004
● Nanosized
× Original
Nanosized
Original
Physical Properties of the Pulverized MBZ
Notes: In the condition of the 1 to 3 ratio of mebendazole versus PVA, nanoparticles of mebendazole was pulverized and showed sharp particle distribution. Both sized particles showed good crystallinity by PXRD. Table shows each particle sizes.

## Slide 9
Physical Properties of
MBZ Nanocrystal Formulation
 | D10 (µm) | D50 (µm) | D90 (µm)
Original | 2.097 ± 0.078 | 5.203 ± 0.124 | 13.76 ± 0.70
Nanocrystal | 0.076 ± 0.004 | 0.120 ± 0.004 | 0.203 ± 0.004
● Nanocrystal formulation
(MBZ : PVA = 1 : 3)
× Original MBZ
Freeze dried Physical mixture
(MBZ : PVA = 1 : 3)
Freeze dried Nanocrystal
Suspension
Freeze dried Pulverized MBZ
Precipitate
Original MBZ
2θ
Notes: The pulverized MBZ without PVA was prepared by freeze drying the precipitation which obtained by the centrifugation of MBZ nano-suspension.

## Slide 10
▲: MBZ (Original) ■: Physical mixture (MBZ : PVA=1:3)
◆: Nanocrystal formulation (MBZ : PVA = 1 : 3)
10 mg MBZ was added into 900 mL vessel. Sample was filtrated with 0.1 µm membrane filter
(B) pH 6.8
(A) pH 1.2
Dissolution Profile
Notes: This is the dissolution test at pH 1.2 and 6.8. Nanoparticles showed the most rapid dissolution rate and the highest solubility 2.2 ug/mL compared to the solubility 0.44 ug/mL of original bulk at both pHs.

## Slide 11
Dissolution Profile
×: MBZ (Original)
●: Nanocrystal formulation (MBZ : PVA = 1 : 3)
10 mg MBZ was added into 900 mL vessel. Sample was filtrated with 0.1 µm membrane filter
(B) pH 6.8
(A) pH 1.2
Notes: This is the dissolution test at pH 1.2 and 6.8. Nanoparticles showed the rapid dissolution rate at both pHs and the highest solubility 2.2 ug/mL compared to the solubility 0.44 ug/mL of original bulk at pH 6.8.

## Slide 12
 | Original | Nanocrystal formulation
AUC0-8 (µg・h/mL) | 0.88±0.10 | 4.08±0.16**
Cmax (µg/mL) | 0.16±0.01 | 0.85±0.10**
Tmax (h) | 2.25±1.09 | 1.75±0.43
Oral Absorption
** : P<0.01, (n=3)
After oral administration of the MBZ nanocrystal formulation (10 mg MBZ/kg, MBZ : PVA = 1 : 3) in rats, the enhanced oral absorption of MBZ was observed with increases of Cmax and AUC0-8 by 5.3 and 4.8-fold, respectively, compared with those of the original MBZ
● Nanocrystal formulation (D90: 0.203 µm)
× Original (D90: 13.8 µm)
Notes: Nanosized mebendazole showed the faster and higher oral absorption than original bulk and the AUC was 5-fold improved.
Originalの溶解度：MBZ原末をTransport medium (TM) に分散させた。
Mirosizedの溶解度：Mirosized MBZ (MBZ : PVA = 1:3) を TMに分散させた。
Nanosizedの溶解度：半透膜透過実験とMircosizedの溶解度から算出した。

## Slide 13
Effects of Particle Sizes on The Oral Absorption of Mebendazole
● Nanosized (D90: 203 nm)
● Microsized (D90: 4.38 µm)
× Original (D90: 13.8 µm)
MBZの場合、ナノ粒子化による溶解度の向上は認められなかった。
 | AUC0-8h (µg・h/mL) | Solubility (µg/mL)
Nanosized | 4.08 ± 0.16 | 4.59
Microsized | 3.83 ± 0.30 | 4.37
Original | 0.88 ± 0.10 | 0.48
Notes: Nanosized mebendazole showed the best oral absorption among three particle sizes. The AUC of Microsized mebendazole close to nanosized one very much. The effect of particle size was not reflected on the absorption between nanosized and microsized. The reason is the both dissolution rates were not so different at pH 1.2 and mebendazole dissolve well in the acidic medium. Therefore, the both were thought to show the similar oral absorption.
Originalの溶解度：MBZ原末をTransport medium (TM) に分散させた。
Mirosizedの溶解度：Mirosized MBZ (MBZ : PVA = 1:3) を TMに分散させた。
Nanosizedの溶解度：半透膜透過実験とMircosizedの溶解度から算出した。

## Slide 14
Effects of Particle Sizes on The Oral Absorption of Mebendazole
● Nanosized (D90: 203 nm)
● Microsized (D90: 4.38 µm)
× Original (D90: 13.8 µm)
MBZの場合、ナノ粒子化による溶解度の向上は認められなかった。
 | AUC0-8h (µg・h/mL) | Solubility (µg/mL)
Nanosized | 4.08 ± 0.16 | 4.59
Microsized | 3.83 ± 0.30 | 4.37
Original | 0.88 ± 0.10 | 0.48
Notes: Originalの溶解度：MBZ原末をTransport medium (TM) に分散させた。
Mirosizedの溶解度：Mirosized MBZ (MBZ : PVA = 1:3) を TMに分散させた。
Nanosizedの溶解度：半透膜透過実験とMircosizedの溶解度から算出した。

## Slide 15
● Nanosized MBZ suspended in water
(D90: 203 nm)
● Microsized MBZ suspended in water
(D90: 4.38 µm)
● Original MBZ suspended in PEG400
× Original MBZ suspended in water
(D90: 13.8 µm)
 | AUC0-8h (µg・h/mL) | Solubility (µg/mL)
Nanosized | 3.91 ± 0.20 | 4.59
Microsized | 3.83 ± 0.31 | 4.37
Original in PEG400 | 1.07 ± 0.19 | 再実験中 !! (前回：約500)
Original in water | 0.80 ± 0.10 | 0.48
Dose : 10 mg MBZ /kg
Volume : 2 mL/kg
Mebendazoleの経口吸収性に及ぼす
粒子径の影響

## Slide 16
(B)
(A)
Sustaining of Nano-particles in the Intestine

## Slide 17
The MBZ nanocrystal formulation with PVA (MBZ : PVA =1:3) had the good redispersibility (D90 = 0.205 µm) of the freeze dried powder and crystallinity.
The dissolution behavior of MBZ was improved by pulverizing to nanoparticles.
The rapid and high systemic exposure of MBZ after oral administration of the nanocrystal formulation was significantly enhanced compared to the API.
The preclinical studies of cancer of MBZ may success by using MBZ nanocrystal formulation with PVA.
Conclusions

## Slide 18
 | D10 (µm) | D50 (µm) | D90 (µm)
Original MBZ | 2.097 ± 0.078 | 5.203 ± 0.124 | 13.76 ± 0.70
Microsized MBZ | 1.11±0.003 | 2.170 ± 0.015 | 4.379 ± 0.088
Nanosized MBZ | 0.076 ± 0.004 | 0.120 ± 0.004 | 0.203 ± 0.004
× Original
● Microsized
● Nanosized
Nanosized
Microsized
Original
MBZ粉砕粉末の物性評価