## Slide 1: Applications of UPLC-MS QTOF in Structural Elucidation of Small Molecules
Peng Chen, Ph.D.
Chemic Laboratories, Inc.
Canton, MA 02021, USA

## Slide 2
provides expertise via 4 business units: CMC Data production; QC monograph testing, Extractables/Leachables assessment, Organic synthesis and drug product production.
Chemic Laboratories..
Chemic’s clients..
are fortune 100 to virtual companies in the Pharmaceutical, Biotech, Veterinary medicine, and Medical device industries.
through continuous recruitment of scientific professionals and acquisition of state of the art equipment allowing us to meet the rigorous needs of our client sponsors.
Chemic continues to offer quality services..
Chemic measures success..
by successfully completing and reporting contracted programs leading to numerous approved IND, NDA, ANDA, BLA, PMA & 510(k) submissions.

## Slide 3: Credo
Quality
We believe quality comes first …All projects can be completed in strict compliance to cGMP or GLP. Every Chemic employee is dedicated to continuous professional development. This policy ensures that Chemic generates only the highest quality data.
Service
We believe service is the definition of technical expertise and quality…Chemic identifies a program leader for each contracted program. Specialized employee positions have been developed allowing program sponsors direct access to data, timelines and program information throughout the life of the program.
Commitment
We believe in value added partnerships… Chemic looks to develop long term strategic alliances with our clients to assist those clients in achieving their goals faster and more efficiently.

## Slide 4
FAQ
Established 1998
480 Neponset street, Bldg. 7, Canton MA (15 mi. sw of Boston)
Privately owned, MA, Sub-S corporation
22,500 ft2
45 employees
9 FDA inspections, most recent Dec 2017
> 15 US DEA inspections
On average 20+ client audits annually
GC (FID,TCD,NPD,MS, MS-MS, NCD, Headspace): 10
HPLC (DAD, RI, FL, MS (APCI & ESI), MS-MS, High res MS, RAM): 16
Mass Spectrometers: 17

## Slide 5
Agilent 6550 iFunnel Q-TOF LC/MS
Quadrupole Time of Flight LC/MS
Agilent 1290 Infinity II UPLC System

## Slide 6
Agilent 6550 iFunnel Q-TOF LC/MS
Femtogram-level sensitivity.
Sub-ppm mass accuracy and ~45K resolution.
Wide dynamic range with excellent detection limits and reproducibility.
Powerful MassHunter software for profiling, characterizing, identifying and
quantifying compounds in mixtures via high-definition MS and MS/MS.
All Ions MS/MS technique.
Other assisting software such as Molecular Structure Correlator (MSC).

## Slide 7
Instrument Features Utilized for Structural Elucidation
Sufficient chromatographic separation for compounds of interest
Mass accuracy and resolving power to derive a formula list based
on the exact mass, isotopic abundance and isotopic spacing.
MS/MS capability to allow insight into structural details of a molecule.
Pseudo MS3 to probe fragment ions for further structural information.
MSC software to aid in analysis of fragmentation pathways.

## Slide 8
Application 1
Analysis of Synthetic Compounds by UPLC-MS QTOF
Assist synthetic chemists in their chemical synthesis.
Determine synthetic routes, product identities, and purities.

## Slide 9
Bromination Reaction

## Slide 10
Route A
Product A

## Slide 11
Route B
Product B

## Slide 12
MS/MS Spectra of Route A Product

## Slide 13
MS/MS Spectra of Route B Product

## Slide 14
Proposed structure for Route A product and its major MSMS fragments
C12H12BrNO4
Exact Mass: 312.99497
(M+H)+: 314.00225
(M+Na)+: 335.98419
(M+K)+: 351.95813

## Slide 15
Proposed structure for Route B product and its major MSMS fragments

## Slide 16
Application 2
Analysis of Impurities, Additives and Degradation Compounds
Associated with Pharmaceuticals and Medical devices
Impurities in pharmaceuticals.
Additives and degradation compounds.

## Slide 17
RRT 0.31
MS TIC of sample
DAD @260 nm of sample
RRT 0.31
API

## Slide 18
RRT 0.31
MS TIC of Active sample
DAD @260 nm of Active sample

## Slide 19
RRT 0.31
UV spectrum (190-400 nm) of peak apex of RRT 0.31
UV chromatogram @260 nm of sample

## Slide 20
RRT 0.31
(M+Na)+
(2M+Na)+
MS spectrum of RRT 0.31

## Slide 21
Database search
Candidate 1: Phlorin

## Slide 22
Database search
Candidate 2: Glucosylisomaltol

## Slide 23
Auto MS/MS spectra of (M+Na)+ Ion 311

## Slide 24
Targeted MS/MS to obtain higher fragment signals for (M+Na)+ Ion 311
CID@10V
CID@40V
CID@20V

## Slide 25
Proposed MS/MS Fragmentation Pathway

## Slide 26
CID @10V
CID @20V
CID @40V
MS/MS of (2M+Na)+ Ion 599 to yield (M+Na)+ during fragmentation

## Slide 27
Confirmation with Glucosylisomaltol reference standard
Glucosylisomaltol
Mfr: HPC Standards GmbH, Germany
Lot No: 779373
CAS#: 85559-61-1

## Slide 28
TIC of 7.6-ppm Glucosylisomaltol standard
TIC of 5% ACN Blank
Glucosylisomaltol

## Slide 29
TIC of Sample
TIC of Glucosylisomaltol Standard
MS Spectrum of Sample
MS Spectrum of Glucosylisomaltol Standard
(M+Na)+
(2M+Na)+
Overlapped
interference
(M+Na)+
(2M+Na)+

## Slide 30
EIC of other overlapped peak
Overlapped
interference

## Slide 31
Targeted MS/MS Spectra of (M+Na)+ Ion 311 of Glucosylisomaltol Standard
CID@10V
CID@40V
CID@20V

## Slide 32
Targeted MS/MS Spectra of (M+Na)+ Ion 311 of Sample
CID@10V
CID@40V
CID@20V

## Slide 33
API
API
Glucosylisomaltol
3.107 min / 10.887 min = RRT 0.285
3.137 min / 10.946 min = RRT 0.287
Glucosylisomaltol
TIC of Sample
DAD of Sample

## Slide 34
API
Glucosylisomaltol
3.113 min / 10.887 min = RRT 0.286
3.107 min / 10.887 min = RRT 0.285
Glucosylisomaltol
Sample
Sample
DAD of Sample
DAD of Glucosylisomaltol Standard

## Slide 35
UV spectrum (190-400 nm) of peak apex @RT 3.11min of sample
UV spectrum (190-400 nm) of peak apex of Glucosylisomaltol

## Slide 36
Application 3
Identification of an unknown due to reaction
of internal standard in sample environment
via HPLC-MS QToF

## Slide 37
(M+Na)+
(M+H)+
(M+NH4)+
IS
Unknown

## Slide 38
(M+Na)+0
(M+H)+
(M+NH4)+
IS
Unknown

## Slide 41
MS/MS spectra of (M+H)+ ion 211 of the unknown

## Slide 42
MS/MS spectra of (M+NH4)+ ion 228 of the unknown

## Slide 43
ESI(-)

## Slide 44
(M-H)-
EIC of (M-H)-
IS
Unknown

## Slide 45
Assignment of major MSMS fragments
Proposed structure

## Slide 46
Note: no MS/MS spectra in the library on Benzil

## Slide 47
Observation
The unknown peak eluted out before the internal standard (2,2-Dimethoxy-1,2-diphenyl ethanone).
The unknown peak is not present in the samples without IS added, but is present in the samples
with IS added, suggesting that it came from the internal standard addition.
The unknown peak is not present in method control with or without IS addition, suggesting that
chemical conversion from IS to the unknown is only catalyzed in the sample environment.

## Slide 49
Hydrolysis mechanism of a ketal (DMPA) to a ketone (Benzil)

## Slide 50
Acknowledgement
Joseph St. Laurent
Scott Goodrich
Gerald Jones
Scott Walsh
David Bisordi
Chris McGee
Kin Chiu
Chemic Laboratories, Inc.