## Slide 1: Invertebrate community composition enables to predict compliance to microbial pathogen related standards of rivers
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be
Rubén Jerves-Cobo, I. Nopens, P. Goethals
Ruben.JervesCobo@UGent.Be
Laboratory of Environmental Toxicology and Aquatic Ecology

## Slide 2
Materials and methods
Results
Conclusion
Background and objective
OUTLINE
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 3
1-BACKGROUND AND OBJECTIVE (I)
total coliforms and fecal coliforms and/or Escherichia coli
The indicators used to verify microbial contamination of water are:
drinking water, recreational purpose, Irrigation
The quality of the water must accomplish standards.
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 4
1-BACKGROUND AND OBJECTIVE (II)
Checking the fulfillment requires expensive and highly trained personnel in laboratories
Biota works as a permanent monitor of water
biological samples can :
predict average values of chemical parameters
reflect an increase in pollution.
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 5
Objective
Introduce a quick way of checking the fulfillment of fecal coliforms standards using macro-benthos.
Analyzes the requirement to include biology and hydro-morphology aspects in Ecuadorian regulations to assess river ecosystem health.
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 6
LOCATION
2- MATERIALS AND METHODS

## Slide 7
LAND USE

## Slide 8
DATA COLLECTION:
Completed information on 33 locations
Physicochemical, hydraulic, microbiological
Laboratory
  BOD5, COD, Nitrate + Nitrite, Ammonia, Organic Nitrogen, Phosphates, Total Phosphorus, Fecal and Total Coliforms, Real Color, Turbidity, Total Solids
Field: Flow Velocity, Ph, Conductivity, Temperature, Dissolved Oxygen
Macro-benthos
39 families (taxa) found

## Slide 9
Variables Variation

## Slide 10
Ecuadorian Water Quality Regulation for Fecal Coliforms
Regulations | Water used to | Fecal Coliforms Limited Value MPN/100 ml
First | Recreational with primary contact | ≤200
Second | Agriculture and Livestock | ≤1,000
Third | raw water previous to non-conventional treatment* | ≤2,000
* Conventional treatment refers to chemical addition, rapid mixing, flocculation and sedimentation |  | 
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 11
ECOLOGICAL WATER QUALITY
Biological Monitoring Working Party Index - Col
BMWP-Col = f(Sensitivity of Macrobenthos)
Sensitivity -> 1-10 (Low – High Sensitivity)
Class | Quality | BMWP | Color
I | Very Good | > 100 | 
II | Good | 61 - 100 | 
III | Moderate | 36 - 60 | 
IV | Deficient | 16 - 35 | 
V | Bad | ≤ 15 | 
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 12
Measurement set
Training dataset
Ecosystem
1
2
Validation dataset
Model development

## Slide 13
Classification trees: searching for if-then rules (threshold values): 100% reliable and ‘safe’ models
Absence
Presence
a
c
b
B<a
B>=a
O<=b
O>b
O<c
O<=c
O
Methodology
Pruned Multi-target Clustering Trees (PMCT)

## Slide 14
Model Performance
Models must be evaluated based on statistical and ecological criteria.
Models must be as clear and simple as possible.
Settings
Machine learning software: Waikato Environment for Knowledge Analysis (WEKA)
Three, five, ten-fold cross validation (k fcv)
Pruning process
  Pruning confidence factors (PCF): 0.25, 0.10
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 15
Model Performance
Confusion matrix from Decision Tree Models:
Correctly Classified Instances (CCI):> 0.70
Cohen´s Kappa Statistic: > 0.40
Lowest value for the false negative (FN) will increase sensitivity
 |  | Predicted Class | 
 |  | Yes | No
Observed Class | Yes | TP | FN
 | No | FP | TN
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 16
Model Optimization:
Cost sensitive classifier (CSC): gives new weights in training instances FN, FP
Overall confusion entropy of a confusion matrix (CEN): evaluates the confusion level of the class distribution of misclassified samples:
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 17
Model Optimization:
  : confusion probability of class
  confusion entropy of class .
  and are the misclassification probability of classifying the samples of class to class subject to class
  Higher accuracy correspond to lower confusion entropy
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 18
BMWP-Col:
- 9 good
- 15 moderate
- 6 poor
- 3 bad
ECOLOGICAL WATER
QUALITY
3- RESULTS

## Slide 19
Analysis of Ecuadorian Water Quality Regulation for Fecal Coliforms in relationship BMWP-Col
BMWP-Col | First Preservation Regulation | Second Preservation Regulation | Third Preservation Regulation
Bad | 2 | 2 | 2
Deficient | 2 | 2 | 2
Moderate | 8 | 5 | 5
God or very god | 2 | - | -
TOTAL non Fulfillment | 14 | 9 | 9
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 20
Fulfillment of Fecal Coliforms limits in relationship to water use
(a) Recreational with primary contact | (b) Agricultural - Livestock use and (c) raw water

## Slide 21
Model Performance (1)
First Model: Primary Contact – Fecal Coliforms Regulation.
CCI = 73%
Kappa = 0.46
FN = 2
CEN = 0.762
Chironomidae families include species with large differences in tolerance to pollutants

## Slide 22
Model Performance (2)
Second model: Agriculture - Livestock Irrigation and raw water previous to non-conventional treatment
CCI = 94%
Kappa = 0.85
FN = 1
CEN = 0.348

## Slide 23
Model Optimization (2)
First Model: Primary Contact – Fecal Coliforms Regulation.
CCI = 91%
Kappa = 0.81
FN = 0
CEN = 0.285

## Slide 24
Model Optimization (3)
Second model: Agriculture - Livestock Irrigation and raw water previous to non-conventional treatment
CCI = 100%
Kappa = 1.0
FN = 0
CEN = 0

## Slide 25
Four models were selected.
  Two Models: fecal coliforms threshold in recreational with primary contact water use.
  Two Models: fecal coliforms limits in agricultural - livestock water use, or raw water for drinking water treated with non-conventional processes.
The cost-sensitive classifier (CSC) in the Weka can reduce false negatives (FN) in the confusion matrix, improved the reliability of the resulting models.
Confusion entropy of a confusion matrix (CEN) was lower when the confusion matrix had lower FN values.
4- CONCLUSION

## Slide 26
Acknowledgement
VLIR-UOS IUC Programme - University of Cuenca
VLIR Ecuador Biodiversity Network Project
Council of the Machangara River Basin
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 27
Thank you
?
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be

## Slide 28
Bibliography:
D'Heygere, T., P. L. M. Goethals, and N. De Pauw. 2003. Use of Genetic Algorithms to Select Input Variables in Decision Tree Models for the Prediction of Benthic Macroinvertebrates. Ecological Modelling 160:291-300
Maimon, O., and L. Rokach. 2005. Data Mining and Knowledge Discovery Handbook. Springer.
Roldán Pérez, G. 1999. Los Macroinvertebrados y Su Valor Como Indicadores de la Calidad del Agua. Academia Colombiana de Ciencia 23:375-387.
Ting, K. M. 2002. An instance-weighting method to induce cost-sensitive trees. Ieee Transactions on Knowledge and Data Engineering 14:659-665.
Wei, J.-M., X.-J. Yuan, Q.-H. Hu, and S.-Q. Wang. 2010. A novel measure for evaluating classifiers. Expert Systems with Applications 37:3799-3809
BIG DATA AND DATA MINING 2016, London, England, Date (26/09/2016)
Laboratory of Environmental Toxicology and Aquatic Ecology, Research Group Aquatic Ecology (AECO) Ruben.JervesCobo@UGent.be