## Slide 1: Synthetic jet fuel from renewable energy sources for sustainable aviation
Friedemann Albrecht, Stefan Estelmann, Ralph-Uwe Dietrich
German Aerospace Center (DLR e.V.)
Petroleum Engineering 2017
29.06.2017, Madrid, Spain

## Slide 2: Agenda
Current developments within the Aviation sector
  Growth rates
  CO2-reduction targets (IATA)
  Expected future demand on alternative fuels
  “Green” jet fuel options
  Certified fuels by ASTM
  Potential fuel yields for Germany/Europe
  Introduction to Fischer-Tropsch fuels
  Case study on green Fischer-Tropsch fuels
  Techno-economic evaluation
  CO2-Abatement costs
  Summary and outlook

## Slide 3: Growth sector aviation
Source: Thess et al., DGLR-Mitgliedermagazin „Luft- und Raumfahrt“ edition 2/2016, p.20 et seq.
Time axis
Europe
North America
China
Fuel for sustainable aviation
+ 73 %
+ 20 %
+ 560 %
(in billion passenger kilometers /a)
Aviation mileage within three world regions

## Slide 4: Political paradigm shift rises the pressure
COP21 Main agreements
Hold global temperature increase below 2 ᵒC
De-carbonization of global economy in this century
Main targets: EU Roadmap 2050 – White paper
40% use of sustainable low carbon fuels in aviation
COP21: 12.12.2015, Paris
What does this mean for the aviation sector?

## Slide 5: IATA Technology Roadmap 4. Edition, June 2013
1
2
3
[1] FuelsEurope “Statistical Report“ 2010
Forecasted CO2 emissions without reduction measures
Improvement of technologies, operations and airport
CO2-certificates and other economic measures
Radical technology transitions and alternative fuels
CO2 emissions
Planned Measures:
No action
Main aims:
Improvement of fuel efficiency about 1,5 % p.a. until 2020
Carbon-neutral growth from 2020
Potential CO2 emissions reductions by 2050
2010 2020 2030 2040 2050
3
Technology
Quelle: iata.org
1
2
Operations
Infrastructure
European Aviation energy demand in 2010: ca. 56.5 Mt[1]
-50 % CO2 by 2050
Expected demand for Europe 2050:
≈ 56 - 60 Mt green kerosene equivalent

## Slide 6: Certified sustainable jet fuels: ASTM D7566 – 14c [1]
AtJ in Europe (EU28)? – For example wheat
  Wheat area2014[2]: 26.7 Mio.ha  Ethanol yield: 2.2 t/ha[3] (range -30 % European yield average[]) Conversion to fuel[4]: 0.56 tkerosene/tethanol Kerosene wheat based: 23.0 to 32.9 Mt/a (≈ 40.1 – 58.2 % of the aviation demand)
[1] ASTM International, „ASTM D7566 - 14C: Standard Specification for Aviation Turbine Fuel Containing Synthesized Hydrocarbons“, 2015
[2] Eurostat „Crop statistics“ 2014
[3] Specialist agency renewable raw materials e. V., „Introduction of fuel ethanol”, 2016
[4] NREL, „Review of Biojet Fuel Conversion Technologies”, Golden, 2016
Feedstock | Synthesis technology | Fuel
Coal, natural gas, biomass, CO2 & H2 | Fischer-Tropsch (FT) synthesis | Synthetic paraffinic kerosene
Lipids from Biomass (e.g. algae, soya, jatropha) | Hydroprocessed esters and fatty acids (HEFA) | Synthetic paraffinic kerosene
Sugar from Biomass | Direct Sugars to Hydrocarbons (DSHC) | Synthetic iso-paraffins / Farnesane
Bioethanol (-propanol, -butanol) | dehydration+oligomerization+hydration (Alcohol-to-Jet, AtJ) | AD-SPK

## Slide 7: Certified sustainable jet fuels: ASTM D7566 – 14c [1]
DSHC in Europe (EU28)? – For example sugar beets
  Sugar beet area2014[2]: 1.6 Mio.ha  sugar beet yield: 131 Mt[2]  sugar contentaverage ≈ 18 %[3] Conversion to fuel[4]: 0.168 tkerosene/tsugar Kerosene sugar based: 3.96 Mt/a (≈ 7.0 % of the Aviation demand)
[1] ASTM International, „ASTM D7566 - 14C: Standard Specification for Aviation Turbine Fuel Containing Synthesized Hydrocarbons“, 2015
[2] Eurostat „Crop statistics“ 2014
[3] Specialist agency renewable raw materials e. V., „Introduction of fuel ethanol”, 2016
[4] NREL, „Review of Biojet Fuel Conversion Technologies”, Golden, 2016
Feedstock | Synthesis technology | Fuel
Coal, natural gas, biomass, CO2 & H2 | Fischer-Tropsch (FT) synthesis | Synthetic paraffinic kerosene
Lipids from Biomass (e.g. algae, soya, jatropha) | Hydroprocessed esters and fatty acids (HEFA) | Synthetic paraffinic kerosene
Sugar from Biomass | Direct Sugars to Hydrocarbons (DSHC) | Synthetic iso-paraffins / Farnesane
Bioethanol (-propanol, -butanol) | dehydration+oligomerization+hydration (Alcohol-to-Jet, AtJ) | AD-SPK

## Slide 8: Fuels for a sustanable aviation sector
Synthetic jet fuels (ASTM D7566 – 14c)[1]
HEFA in Europe (EU28)? – For example rape oil
  Rapeseed area2014[2]: 12.9 Mio.ha  rape yield: 24.1 Mio.t  oil contentaverage ≈ 42 %[3]
  Conversion to fuel[4]: 0.49 tkerosene/trape oil Kerosene sugar based: 7.3 Mio.t/a (≈ 12.9 % of the Aviation demand)
Feedstock | Synthesis technology | Fuel
Coal, natural gas, biomass, CO2 & H2 | Fischer-Tropsch (FT) synthesis | Synthetic paraffinic kerosene
Lipids from Biomass (e.g. algae, soya, jatropha) | Hydroprocessed esters and fatty acids (HEFA) | Synthetic paraffinic kerosene
Sugar from Biomass | Direct Sugars to Hydrocarbons (DSHC) | Synthetic iso-paraffins / Farnesane
Bioethanol (-propanol, -butanol) | dehydration+oligomerization+hydration (Alcohol-to-Jet, AtJ) | AD-SPK
[1] ASTM International, „ASTM D7566 - 14C: Standard Specification for Aviation Turbine Fuel Containing Synthesized Hydrocarbons“, 2015
[2] Eurostat „Crop statistics“ 2014
[3] UFOP “Rapeseed the Power Plant“ 2017
[4] DBFZ, „Abschlussbericht Projekt BurnFAIR”, 2014

## Slide 9: Biomass potential from agricultural products in Europe
Direct competition to food markets
Ineffective conversion of sun light to biomass
Kerosene from | Production [Mt/a] | [%] | Cultivation area [Mha] | EU28 [%]
Wheat | 23.0 – 32.9 | 40.1 – 58.2 | 26.7[1] | 30.2
Sugar | 3.9 | 7.0 | 1.6[1] | 1.8
Rapeseed | 7.3 | 12.9 | 12.9[1] | 13.3
Σ | 34.3 – 44.2 | 60.7 – 78.2 | 39.9 | 45.2
[1] Eurostat „Crop statistics“ 2014

## Slide 10: Fuels for a sustanable aviation sector
Synthetic jet fuels (ASTM D7566 – 14c)[1]
Feedstock | Synthesis technology | Fuel
Coal, natural gas, biomass, CO2 & H2 | Fischer-Tropsch (FT) synthesis | Synthetic paraffinic kerosene
Lipids from Biomass (e.g. algae, soya, jatropha) | Hydroprocessed esters and fatty acids (HEFA) | Synthetic paraffinic kerosene
Sugar from Biomass | Direct Sugars to Hydrocarbons (DSHC) | Synthetic iso-paraffins / Farnesane
Bioethanol (-propanol, -butanol) | dehydration+oligomerization+hydration (Alcohol-to-Jet, AtJ) | AD-SPK
Fischer-Tropsch synthesis
  Large scale, commercial technology
  Based on synthesis gas, which can be produced from almost any carbon and hydrogen source
  Fully synthetic kerosene achievable[2]
[1] ASTM International, „ASTM D7566 - 14C: Standard Specification for Aviation Turbine Fuel Containing Synthesized Hydrocarbons“, 2015
[2] UK Ministry of Defense, „DEF STAN 91-91: Turbine Fuel, Kerosene Type, Jet A-1,“ UK Defense Standardization, 2011.

## Slide 11: Production routs of alternative Kerosene
Biofuel 1. Gen.
Biomass-to-Liquid (BtL)
Waste-to-Liquid (WtL)
Power-to-Liquid (PtL)
Power and Biomass-to-Liquid (PBtL)
Coal/Gas-to-Liquid (CtL/GtL)
Power and Coal/Gas/Waste-to-Liquid
Cultivated plants (wheat, rape, beets etc.)
Fuel synthesis (2nd generation):
Fischer-Tropsch / Methanol-to-Gasoline / Mixed Alcohol / etc.
CO2
Waste
Biomass
(straw, organic waste, residues forest wood etc.)
Green electricity (wind, sun, water)
Conventional electricity generation
CO2-source (air, industrial flue gas)
Coal, natural gas
Biodiesel, HEFA, Methanol, Ethanol, etc.
Optional production route
- Low usable raw material potential
- Too large CO2 footprint
The supply of large quantities of alternative kerosene within low GHG emissions is possible by coupling the sectors electricity generation and fuel markets (without biomass imports).

## Slide 12: 2. Applied methodology for fuel evaluation
CO2-abatment costs
CO2-footprint
production costs
Results calculated with TEPET:
DLR-Sfotwaretool:

## Slide 13: Investigated Fischer-Tropsch concepts
-From biomass (Biomass-to-Liquid, BtL)

## Slide 14: Investigated Fischer-Tropsch concepts
-From power and CO2 (Power-to-Liquid, BtL)

## Slide 15: Investigated Fischer-Tropsch concepts
-From power and biomass (Power&Biomass-to-Liquid, BtL)

## Slide 16: Investigated Fischer-Tropsch concepts
Overview of concepts
More information available in recent publication:
F. G. Albrecht, D. H. König, N. Baucks und R. U. Dietrich, „A standardized methodology for the techno-economic evaluation of 1 alternative fuels,“ Fuel, Bd. 194, pp. 511-526, 2017.

## Slide 17: Exergy flows - Biomass-to-Liquid
Exergy input:
100 MW (Biomass)
Largest exergy destruction during gasification

## Slide 18: Exergy flows - PBtL
Exergy input:
37 MW (Biomass)
63 MW (Power)
Largest exergy destruction during electrolysis!

## Slide 19: Technical process assessment
Process parameter | BTL | PBTL | PTL
Energy efficiency XTL | 36.3 % | 51.4 % | 50.6 %
Power consumption | - 4.2 kWh/kgfuel | 15.8 kWh/kgfuel | 24.4 kWh/kgfuel
Biomass/CO2 demand | 7.5 kgBM/kgfuel | 2.0 kgBM/kgfuel | 3.1 kgCO2/kgfuel
Carbon efficiency C | 24.9 % | 97.7 % | 98.0 %
[1] T. Smolinka, M. Günther and J. Garche, „Stand und Entwicklungspotenzial der Wasserelektrolyse zur Herstellung von Wasserstoff aus regenerativen Energien,“ NOW GmbH, 2011, in German
[2] K. Qin, „Entrianed Flow Gasification of Biomass, Ph. D. thesis,“ Technical University of Denmark (DTU), Kgs. Lyngby, 2012.
[3] P. Kaiser, F. Pöhlmann and A. Jess, "Intrinsic and effective kinetics of cobalt-catalyzed Fischer-Tropsch synthesis in view of a Power-to-Liquid process based on renewable energy," Chemical Engineering Technology, vol. 37, pp. 964-972, 2014.
Case study equipment selection and assumptions:
Proton exchange membrane electrolyzer (PEM), h = 4.3 kWh/Nm³ [1]
Entrained flow gasifier, , p = 30 bar, pure O2 [2]
Fischer-Tropsch synthesis, , p = 25 bar, a = 0.85, XCO = 40 % [3]
BTL fuel yield can be increased by the factor 3 – 4 by the PBTL concept
Approximately full carbon conversion for PBTL and PTL applying oxy-fuel combustion and recycle concept
PBTL XTL-efficiency comparable high as for PTL with reduced power consumption

## Slide 20
Biomass-to-Liquid – Carbon flow diagram
75 % of biomass carbon lost as CO2
Fuel
25 %
CO2
29 %
CO2
41 %
CO2
5 %
C-Biomass
100 %
Molar ratio of H2/CO > 2 required for FT
100 kWth
36 kWth

## Slide 21
Power&Biomass-to-Liquid – Carbon flow diagram
98 % of biomass carbon used in fuel
C-Biomass
100 %
100 kWth
Electrolysis
167 kWel
H2
Fuel
98 %
CO2
2 %
137 kWth
Molar ratio of H2/CO > 2 required for FT

## Slide 22: 2. Applied methodology for fuel evaluation
CO2-abatment costs
CO2-footprint
production costs
Results calculated with TEPET:
DLR-Sfotwaretool:

## Slide 23
Literature survey
Step 1
Identification elementary process steps
Rough material and energy balance
Step 2
Process simulation
Detailed process model
First optimization (process layout and heat integration)
Techno-economic assessment
TEPET-ASPEN Link
Step 3
Transfer of process parameters
Control and economic optimization
Determination of specific product costs (CAPEX, OPEX, etc.)
Sensitivity analyses
Iteration
Step 4
Identification of critical process steps
Experiments at DLR
Step 5
Definition of optimal operating conditions
Step 6
Aspen Plus®
Exchange with project partners
Techno-economic assessment (TEA)

## Slide 24
Plant and unit sizes
material and energy balance
Production costs
€/l , €/kg , €/MJ
Raw materials
Operating materials
Maintenance
Wages …
Equipment costs
Piping & installation
Factory buildings
Engineering services …
Process simulation results
Aspen Plus®
Capital costs
Operational costs
TEPET-ASPEN Link
Methodology applied for TEA
Meets AACE class 3-4 Accuracy: +/- 30 %

## Slide 25: Assumptions dictate results of TEA
Investitionskosten:
PEM-Elektrolyszer: 640 €/kW [1] (installed capacity)
Entrained flow gasification: 103.650 €/(kgSlurry/h) [2] (scale-factor 0.7)
Raw material prices:
Power: 105 €/MWh [3] (industrial consumer)
Biomass (35% moisture): 97.4 €/t [4]
General economic assumptions:
Reference year: 2014 System operation: 30 a Operating hours: 8,260 h/year Capital interest: 7 %
Plant size: 100 MWth (Biomass input LHV)
[1] G. Saur, Wind-To-Hydrogen Project: Electrolyzer Capital Cost Study, Technical Report NREL, 2008
[2] P. Kerdoncuff, Modellierung und Bewertung von Prozessketten zur Herstellung von Biokraftstoffen der zweiten Generation, Dissertation, KIT, Karlsruhe, 2008
[3] Eurostat, Êlectricity prices for industrial consumer, 2014
[4] C.A.R.M.E.N. – Preisentwicklung bei Waldhackschnitzel (Energieholz-Index)

## Slide 26: Comparison of Costs BTL / PBTL / PTL Plant size: “100 MWth”
Biomass-to-Liquid (BTL)
Investment: ca. 395.2 mio. € Fuel production: 24.17 Mt
Fuel costs: ca. 2.34 €/l
Power&Biomass-to-Liquid (PBTL)
Investment: ca. 751 mio. € Fuel production: 91.27 Mt
Fuel costs : ca. 2.24 €/l
Power-to-Liquid (PTL)
Investment: ca. 672.5 mio. € Fuel production: 91.27 Mt
Fuel costs : ca. 2.74 €/l
Electrolyzer
Entrained flow gasification
Pyrolyse
Fischer-Tropsch
Selexol
Remaining (CAPEX)
Power[3]
Biomass[4]
Remaining (Utilities)
Maintenance
Labor costs
Remaining (OPEX)
Chart: 
| Electrolyzer | EF-gasifier | Pyrolyse | Selexol | Fischer-Tropsch | Remaining (CAPEX) | Power | Biomass | Remaining (Utility) | Maintenance | Labor costs | Remaining (OPEX)
 | 0 | 0.46641 | 0.10481 | 0.074895 | 0.057736 | 0.24402 | 0 | 0.44932 | 0 | 0.42907 | 0.039372 | 0.47618
Chart: 
| Electrolyzer | EF-gasifier | Pyrolyse | Selexol | Fischer-Tropsch | Remaining (CAPEX) | Power | Biomass | Remaining (Utility) | Maintenance | Labor costs | Remaining (OPEX)
 | 0.143 | 0.12355 | 0.027766 | 0 | 0.057737 | 0.12515 | 1.1357 | 0.14138 | 0.013369 | 0.21602 | 0.016787 | 0.23693
Chart: 
| Electrolyzer | EF-gasifier | Pyrolyse | Selexol | Fischer-Tropsch | Remaining (CAPEX) | Power | Biomass | Remaining (Utility) | Maintenance | Labor costs | Remaining (OPEX)
 | 0.143 | 0.12355 | 0.027766 | 0 | 0.057737 | 0.12515 | 1.1357 | 0.14138 | 0.013369 | 0.21602 | 0.016787 | 0.23693
CAPEX:
40.4 %
CAPEX:
21.3 %
CAPEX:
15.6 %
6 %
20 %
19 %
51 %
67 %

## Slide 27: Sensitivity analysis for PBTL
OPEX are the main cost driver for PBTL
Power price mostly defines the net production costs
Minor influence of CAPEX
Chart: Deviation from reference value
| -0.8 | 0 | 0.8
Electricity (From grid) | 1.3376 | 2.2522 | 3.1668
Costs electrolyzer | 2.0315 | 2.2522 | 2.4729
Costs EF-gasifier | 2.0615 | 2.2522 | 2.4429
Wet biomass | 2.1384 | 2.2522 | 2.3661
Fischer-Tropsch reactor | 2.1631 | 2.2522 | 2.3413

## Slide 28: Techno-economic assessment
Cost-efficient fuel production depends mainly on the boundary conditions e.g. plant size and power price
“optimal” production concept depends on boundary conditions!
PTL (Example)
BTL (Example)
PBTL (Example)

## Slide 29: 2. Applied methodology for fuel evaluation
CO2-abatment costs
CO2-footprint
production costs
Results calculated with TEPET:
DLR-Sfotwaretool:

## Slide 30: CO2-Footprint - Methodology
Fuel Production plant
Black box
O2
Biomass
Power
Carbon dioxide
Oxygen
Fuel
Carbon footprint of used raw materials and energy sources defines carbon footprint of produced fuel!

## Slide 31: CO2 Footprint – Basics
Biomass
O2
Power
Carbon dioxide
Oxygen
Functional unit | [kgCO2eq/t]a | [kgCO2eq/MWh]b | [kgCO2eq/t]c | [kgCO2eq/t]d
Low boundary | 13.6 | 10 | 5 | 10
Average | 134.3 | 272.5 | 77.5 | 75
High boundary | 255 | 535 | 150 | 140
a Taking into account biomass type (forest residues, straw etc.) and transport distances. CO2-emissions during cultivation and harvesting are accounted for.
b Low boundary value for pure wind electricity taken from [1]. High value corresponds to the actual CO2-footprint of the German electricity sector [2].
c Representing emissions arising from sequestration of CO2 from flue gas (cement industry and coal fired power plants). The probably fossil nature of the flue gas was not taken into account. Low/high value: energy demand of CO2-sequestration is covered with wind energy/German electricity mix.
d ProBas databank [1]. Low/high value due to different electricity sources.
[1] Umweltbundesamt, “Prozessorientierte Basisdaten für Umweltmanagementsysteme,” http://www.probas.umweltbundesamt.de/php/index.php.
[2] Umweltbundesamt, “Entwicklung der spezifischen Kohlendioxid-Emissionen des deutschen Strommix in den Jahren 1990 – 2016,“ Dessau-Roßlau,2017.

## Slide 32: CO2 Footprint – Calculation
Chart: CO2-Footprint / gCO2/MJ
| Low | Av. | High | Low | Av. | High | Low | Av. | High | BtL | PBTL | PTL
Oxygen | 0.74916 | 5.6187 | 10.4882 | -0.2618 | -1.9635 | -3.6652 | -0.82517 | -6.1888 | -11.5523
Biomass | 2.4338 | 24.034 | 45.6342 | 0.64469 | 6.3663 | 12.0879 | 0 | 0 | 0
Power | 0 | 0 | 0 | 3.5318 | 96.2411 | 188.9503 | 5.755 | 156.8228 | 307.8907
CO2 | 0 | 0 | 0 | 0 | 0 | 0 | 0.36853 | 5.7121 | 11.0558
Fossil fuel reference:
Ca. 83.8 gCO2/MJ
CO2-Abatement
PtL-concepts only viable when using renewable power!
CO2-Abatement costs:
Case1:
Price of fossil kerosene: ca. 0.5 €/l
Power price: 105 €/MWh
Biomass price: 100 €/t
CO2-Abatement costs € / |  |  |  |  | 
Case | BtL-Low | BtL-Av. | BtL-High | PBtL-Low | PtL-Low
1 | 662 | 985 | 2756 | 631 | 827
2 | 406 | 605 | 1183 | 134 | 155
Case | BtL-Low | BtL-Av. | BtL-High | PBtL-Low | PtL-Low
1 | 662 | 985 | 2756 | 631 | 827
2 | 406 | 605 | 1183 | 134 | 155
Case2:
Price of fossil kerosene: ca. 1 €/l
Power price: 30 €/MWh
Biomass price: 60 €/t
Current Price of CO2 - European Emission Allowances:
ca.5 €/tCO2

## Slide 33: Required: Feedstock shift for sustainable aviation
Raw materials and energy requirements for 60 Mt of green jet fuel:
Demand | Unit | BtL | PBtL | PtL
Powera | TWh | - | 890 | 1450
Biomassb | Mt | 451 | 119 | -
CO2c | Mt | - | - | 186
To be compared with:
a Total produced renewable electricity in EU (2015): 930 TWh1
Expected development potential wind: ≈ 40,000 TWh2
b Total bioenergy consumption in EU (2014): 105.5 Mt3
Expected wood potential (2030 EU): 146 Mt4
c Total CO2,eq. emissions (2015 EU): 4,451.1 Mt5
[1] Eurostat database, “online data codes: nrg_105a and tsdcc330,” 2017
[2] EEA Technical report, “Europe's onshore and offshore wind energy potential”, No 6/2009
[3] AEBIOM „Statistical Report 2016 - Key findings“
[4] European Commission, Agriculture and rural development, „Biomass potential“
[5] Eurostat „Total greenhouse gas emissions by countries”
European jet fuel consumption (2010) ca. 56.5 Mt/a
EU target (2050): 40 % sustainable low carbon fuels
Expected “green” jet fuel demand in 2050: 55-60 Mt/a
Six fully “green” refineries!
Just for aviation!!

## Slide 34: Summary
EU aviation emission targets  large demand for green jet fuel
Mass production of green jet fuel  renewable power-based fuel production concepts (Fischer-Tropsch)
Syncrude from Fischer-Tropsch synthesis has to be upgraded  Update existing refinery infrastructure
Alternative fuel costs are currently not competitive compared to fossil jet fuel  political demand  Identify the most viable fuel options in terms of fuel costs / CO2-abatement costs
Use the standardized DLR methodology for the evaluation of alterative jet fuels with respect to technical, economic and ecological key performance parameters (CAPEX, OPEX, net production costs, CO2-Abatement costs)
Think of a Time beyond Oil – Start Now!

## Slide 36: Otherwise? – How about biking?
The Gossamer Albatross crossed the English Channel between Folkestone and Cap Gris-Nez
Bryan Allen on June 12, 1979
Distance: 35,8 km
Travel time: 2:49 hours
Quelle: https://de.wikipedia.org/wiki/Gossamer_Albatross
This corresponds to:
Flight from Frankfurt am Main (FRA)  Madrid (MAD): 1.450 km
Calculated flight time: 114 hours

## Slide 37: THANK YOU FOR YOUR ATTENTION!
German Aerospace Center (DLR) Institute of Engineering Thermodynamics, Stuttgart
Research Area Alternative Fuels
ralph-uwe.dietrich@dlr.de http://www.dlr.de/tt/en