## Slide 1: About Omics Group
OMICS Group International through its Open Access Initiative is committed to make genuine and reliable contributions to the scientific community. OMICS Group hosts over 400 leading-edge peer reviewed Open Access Journals and organize over 300 International Conferences annually all over the world. OMICS Publishing Group journals have over 3 million readers and the fame and success of the same can be attributed to the strong editorial board which contains over 30000 eminent personalities that ensure a rapid, quality and quick review process.

## Slide 2: About Omics Group conferences
OMICS Group signed an agreement with more than 1000 International Societies to make healthcare information Open Access. OMICS Group Conferences make the perfect platform for global networking as it brings together renowned speakers and scientists across the globe to a most exciting and memorable scientific event filled with much enlightening interactive sessions, world class exhibitions and poster presentations
Omics group has organised 500 conferences, workshops and national symposium across the major cities including SanFrancisco,Omaha,Orlado,Rayleigh,SantaClara,Chicago,Philadelphia,Unitedkingdom,Baltimore,SanAntanio,Dubai,Hyderabad,Bangaluru and Mumbai.

## Slide 3: Development of a high power coherent quantum cascade laser array mounted in extended-cavity system
R. Vallon1, B.Parvitte1,G.M. de Naurois2, G. Maison2, M. Carras2, V. Zéninari1
1 Groupe de Spectrométrie Moléculaire et Atmosphérique, UMR 7331 CNRS, Université de Reims
2 III-V lab, GIE Alcatel – Thales – CEA LETI

## Slide 4: Outline
Motivations
Technical challenges
Array QCL emitters performances
Preliminary results in extended cavity
Conclusion & perspectives

## Slide 5: Introduction
Single-mode
Tunable
Wide-spectral range
Room temperature
High power technology
EC-QCL
High power extended-cavity QCL for spectroscopic applications
  photo-acoustic,
  saturated molecular absorption
  …

## Slide 6: Context Power vs current
QCL Optical performances limited by thermal resistance
Pulse operation
Rth =3,5 K/W
Rth =4 K/W
Rth = 5 K/W
Rth = 8 K/W
Current (A)
Power (W)
Slope
Threshold current
No warming

## Slide 7: Context Increase heat extraction
Double trench process
Buried process
Rth= 10 °K/W
Rth= 4 °K/W
Active
region

## Slide 8: Context
Optical performances : not limited by thermal resistance but by injection current
Pulse operation
Rth =3,5 K/W
Rth =4 K/W
Rth = 5 K/W
Rth = 8 K/W
Current (A)
Power (W)
No warming

## Slide 9: Context Increase current
Current (A) size of gain medium
Power (W)
Beam quality
35µm
30µm
25µm
20µm
15µm
10µm
warming
performances limited by active region size
Pulse operation

## Slide 10: One solution : buried + micro-structured QCL
Thermal dissipation enhancement
µ-structure increase thermal surface exchange
InP:Si
InP:Fe
Active
region

## Slide 11: One solution : buried + micro-structured QCL
µ-structure pitch: Λ=w+D
Active
region
w
D
Λ < 3*λ/2 for dual-lobe operation (anti-symetric supermode)
w ~ 2µm
2 µm<D <8µm @ 8.2µm
Evanescent coupling

## Slide 12: µ-stipes QCL Near field
Below threshold
Above threshold
G.M. de Naurois et al, Optics Letters, Vol. 37, No.3 (2012)
Spontaneous emission
Stimulated emission

## Slide 13: µ-stripes QCL Far field : dual lobes emission
2µm width, 6µm pitch
Simulation
Measurement

## Slide 14: µ-stripes QCL Far field
2µm width, 6µm pitch
Simulation
Measurement
4 emitters in extended cavity

## Slide 15: µ-stripes EC-QCL Experimental setup
FTIR
interferometer
HR coated – uncoated (R=30%)
90°

## Slide 16: µ-stripes EC-QCL Experimental setup
Output beam

## Slide 17: µ-stripes EC-QCL P(I)
Pulse operation 100ns-100kHz

## Slide 18: µ-stripes EC-QCL Threshold
Threshold : 730mA
700mA

## Slide 19: µ-stripes EC-QCL P(I)

## Slide 20: µ-stripes EC-QCL P(I)

## Slide 21: µ-stripes EC-QCL P(I)

## Slide 22: µ-stripes EC-QCL Spectral range
Mono-mode operation : 19.5 cm-1
multimode : 30 cm-1
D : 1.45 cm-1

## Slide 23: µ-stripes EC-QCL Gas analysis : setup

## Slide 24: µ-stripes EC-QCL Gas analysis : Acetone
10 Torr, 20 cm

## Slide 25: Conclusion / Perspectives
Preliminary results of EC-µstripe QCL array
Perspectives :
Increase optical feedback to increase tunable spectral range
32 emitter array EC-QCL
CW operation
…
Application : photoacoustic spectrometer
…
Acknowledgement : French Research Agency

## Slide 26: Electric Field & µ-stripe

## Slide 28: Let Us Meet Again
We welcome all to our future group conferences of Omics group international
Please visit:
www.omicsgroup.com
www.Conferenceseries.com
http://optics.conferenceseries.com/