## Slide 1: Effect of Gravity on Heat Feedback of Small-scale Pool Fires
Ryo Takahashi*, Akihiko Ito, Hiroyuki Torikai
Graduate School of Science and Technology,
Hirosaki University
5th World Congress on
Petrochemistry and Chemical Engineering
December 05-07, 2016 Phoenix, Arizona, USA
Notes: Thank you, chairman.
Good morning everyone.
I’m Ryo Takahashi from Hirosaki University, JAPAN..
I’ll talk about Effect of Gravity on Heat Feedback of Small-scale Pool Fires.
それでは「液面燃焼の熱フィードバック量に及ぼす重力の影響」と題しまして、弘前大学大学院 高橋諒が発表します。

## Slide 2: Oil tank fire
In order to prevent and suppress pool fires, it is necessary to clarify and understand
1) combustion character,
2) flame structure,
3) combustion mechanism.
Therefore, there are a lot of fundamental studies on pool fires.
Japan is an earthquake country.
After occurrence of a huge earthquake,
an oil tank fire (large-scale pool fire) sometimes occurs due to the impact.
Notes: Japan is an earthquake country.
After occurrence of a huge earthquake,
an oil tank fire (large-scale pool fire) sometimes occurs due to the impact.
In order to prevent and suppress pool fires, it is necessary to clarify and understand 1) combustion character,
2) flame structure,
3) combustion mechanism.
Therefore, there are a lot of fundamental studies on pool fires.

## Slide 3: Combustion mechanism of pool fire
In order to sustain a stable pool fire, heat transfers from the combustion zone to the liquid fuel (heat feedback) is important .
Fuel
Heat
Feedback
Fuel Vapor
The liquid fuel is evaporated due to the heat transferred from the flame to the liquid fuel and supplied to the flame.
Flame
Notes: In order to sustain a stable pool fire, heat transfers from the combustion zone to the liquid fuel (heat feedback) is important .
The liquid fuel is evaporated due to the heat transferred from the flame to the liquid fuel and supplied to the flame.

## Slide 4: Heat feedback mechanism
Heat
Feedback
Heat feedback is carried out by convective and radiative heat transfers.
Convection
Radiation
Fuel
Flame
The dominant heat transfer process in a pool fire depends on a scale.
Notes: Heat feedback is carried out by ●convective and ●radiative heat transfers.
The dominant heat transfer process in a pool fire depends on a scale.

## Slide 5: Scale effect on heat transfer mechanism
Turbulent flame
Radiative
heat transfer
Laminar flame
Convective
heat transfer
We have a lot of knowledge on a pool fire in a normal gravity environment.
Combustion condition:
Heat transfer
Mechanism:
1G
Scale:
Small
Large
Notes: We have a lot of knowledge on a pool fire in a normal gravity environment.
For example, Combustion condition and heat transfer mechanism,

## Slide 6: Space exploitation
Quoted from JAXA HP. (http://www.jaxa.jp/)
Earth
Normal Gravity
Environment
Space
Microgravity
Environment
0.17G
0.38G
Moon
Mars
Partial Gravity Environment
μG
1G
As space research and technology progress, activity range of human spreads to various gravity environments.
A fire in a spacecraft and station is also a greatly feared hazard.
Notes: On the other hand,
As space research and technology progress, activity range of human spreads to various gravity environments.
A fire in a spacecraft and station is also a greatly feared hazard.

## Slide 7: Gravity effect on heat transfer mechanism
Gravity level
1G
μG
Buoyancy-induced flows in combustion phenomena occur in a normal gravity.
As a result, conduction and convective heat transfer is a key factors to determine the flame characteristic.
There is no buoyancy = no natural convection.
As a result, radiative heat transfer is dominant factors to sustain a combustion in a microgravity environment.
Small scale
Notes: In a microgravity environment,
There is no buoyancy = no natural convection.
As a result, radiative heat transfers is dominant factors to sustain a combustion
On the other hand,
Buoyancy-induced flows in combustion phenomena occur in a normal gravity.
As a result, convective heat transfer is a key factors to determine the flame characteristic.

## Slide 8: Gravity-scale diagram
The dominant heat transfer mechanism changes depending on a gravity level and a scale of a fire.
Gravity level
Convection
Radiation
Radiation
1G
μG
Small
Large
Scale
Partial gravity
A partial gravity environment is important for planetary exploration.
Notes: The dominant heat transfer mechanism changes depending on a gravity level and a scale of a fire.
●A partial gravity environment is important for planetary exploration.

## Slide 9: Gravity-scale diagram
There has been little combustion research in a partial gravity.
Gravity level
1G
μG
Small
Large
Scale
Partial gravity
We have to clarify combustion characters, flame structure and combustion mechanism in partial gravity environment.
Convection
Radiation
Radiation
Notes: There has been little combustion research in a partial gravity.
We have to clarify combustion characters, flame structure and combustion mechanism in partial gravity environment.

## Slide 10: Our previous study
10mm
Ethanol
Pan diameter 15mm
In order to understand the combustion characters in a partial gravity, we focused on a small-scale pool fire.
A small scale pool fire is the one of the basic models of liquid fuel combustion.
The flame shape, structure and so on, depends strongly on a natural convective flow field.
→Natural convection is caused by a buoyant force, which is determined by a gravity level.
Which kind of heat transfer process is important in small scale pool fire in a partial gravity environment?
Notes: In order to understand the combustion characters in a partial gravity, we focused on a small-scale pool fire
A small scale pool fire is the one of the basic models of liquid fuel combustion.
The flame shape, structure and so on, depends strongly on a natural convective flow field.
Which kind of heat transfer process is important in small scale pool fire in a partial gravity environment?

## Slide 11
We have built a drop tower in a campus of Hirosaki university.
The test package including an experimental setup falls 8m.
We can establish a partial gravity environment for about one second.
Drop tower to establish a partial gravity condition
Notes: This is a schematic drawing of Experimental facility Partial Gravity Drop Tower
It is constructed at Hirosaki University

## Slide 12
We have built a drop tower in a campus of Hirosaki university.
The test package including an experimental setup falls 8m.
We can establish a partial gravity environment for about one second.
Drop tower to establish a partial gravity condition
Notes: The test package falls 8 meters
It’s kept the partial gravity environment for about one second

## Slide 13
The gravitational acceleration
in a partial gravity
G:Gravity level
We can control the gravity level by changing the weight of the test package.
The gravitational acceleration
In a normal gravity
Drop tower to establish a partial gravity condition
Notes: The gravity level G [-], is defined as ga/g
We can change the gravity level by controlling the weight of the package

## Slide 14
Fuel: Ethanol, Pan diameter: 15 mm
Playback speed：0.5x
G = 0.55
0.9 s
The flame shape changes right after the gravity level goes down.
Flame in Partial gravity
This video shows the small scale pool fire in a partial gravity environment.
Notes: This video shows the small scale pool fire in a partial gravity environment.
And this figure shows the time variation of the gravity level
Please show the video
●When turn off the LED light , at the same time, test packcage start to fall.
Decreased gravity level
The flame shape changes right after the gravity level goes down.

## Slide 15
When a gravity is reduced from 1 g to 0.55 g, all flow velocities induced by the combustion decreases .
Acetone
Pan diameter 15mm
Flow visualization
In order to grasp the flow field in the partial gravity combustion, we have used PTLS method to visualize the stream lines.
The flame height also decreases.
Notes: In order to grasp the flow field in the partial gravity combustion, we have used PTLS method to visualize the stream lines.
When a gravity is reduced from 1 g to 0.55 g, all flow velocities induced by the combustion decreases.
The flame height also decreases.

## Slide 16
Question
Findings in our previous study
Small-scale pool fire under a partial gravity condition
・The flame height decreased
・The buoyancy induced flow velocity decreased
The decrease in the flame height may be caused by the reduction of amount of heat feedback from the flame to the liquid fuel.
We focus on clarification of the heat transfer mechanism.
Which kind of heat transfer process is dominant in the heat feedback mechanism in small scale pool fire under a partial gravity condition?
Notes: Findings in our previous study is that.
The decrease in the flame height may be caused by the reduction of amount of heat feedback from the flame to the liquid fuel.
Which kind of heat transfer process is dominant in the heat feedback mechanism in small scale pool fire under a partial gravity condition?
We focus on clarification of the heat transfer mechanism.

## Slide 17: Heat Transfer Mechanism of Pool Fire
Flame
Heat
Feedback
Evaporated
Fuel
In order to grasp qualitatively the amount of the heat feedback and the heat transfer mechanism, we have to measure the temperature field in the pool fire.
Fuel
Rim
Notes: In order to grasp qualitatively the amount of the heat feedback and the heat transfer mechanism, we have to measure the temperature field in the pool fire.

## Slide 18
Our objective
A temperature measurement with a fine-wire thermocouple has been carried out.
The flame shape has been recorded with a high-speed camera.
The amounts of heat feedbacks on both the convective and radiative heat transfers have been calculated from the temperature field and the flame shape.
〇Experiments
The partial gravity experiment on a small-scale pool fire has been performed.
〇Measurements
〇Analyses
Notes: Experiments
The partial gravity experiment on a small-scale pool fire has been performed.
Measurements
A temperature measurement with a fine-wire thermocouple has been carried out.
The flame shape has been recorded with a high-speed camera.
Analyses
The amounts of heat feedbacks on both the conductive and radiative heat transfers have been calculated from the temperature field and the flame shape.

## Slide 19
Our objective
From the experimental results, we clarify the dominant heat feedback mechanism in a small-scale pool fire under a partial gravity condition.
Notes: From the experimental results, we clarify the dominant heat feedback mechanism in a small-scale pool fire under a partial gravity condition.

## Slide 20: Experimental Apparatus & Method
Notes: Now, describe the experimental apparatus and method
それでは、実験装置と方法について説明します。

## Slide 21
Experimental Apparatus
＜Thermocouple probe＞
R-type (Pt-PtRh13%)
＜Overview＞
Notes: This figure shows a schematic of the experimental apparatus inside the test package, including the measuring system.
The fuel pan diameter is 15 mm.
The fuel level was kept at the upper rim of the pan using a level controller.
A digital camera (CASIO, EX-F1, 300fps) recorded the flame behavior of the pool fires.

## Slide 22
Experimental Apparatus
＜Overview＞
＜Thermocouple probe＞
R-type (Pt-PtRh13%)
Notes: This is an R-type thermocouple (TANAKA, Pt-PtRh13%) probe. it was used for temperature measurement.

## Slide 23
Fuel Type
5mm
Ethanol
Acetone
Brightness:
Low
High
To investigate effect of gravity on radiation, we used ethanol and acetone which have different amount of soot.
The two fuel types have different brightness.
Notes: To investigate effect of gravity on radiation, we used ethanol and acetone which have different amount of soot.
The two fuel types have different brightness.

## Slide 24
Experimental Condition
Thermocouple
Fuel | Ethanol, Acetone
Pool diameter [mm] | 15
Gravity level G [-] | 1, 0.55
Thermocouple height z [mm] | 1-2
Sampling rate [s] | 0.1
Frame rate [fps] | 30
Exposure time [s] | 1/30
Pre-combustion time [s] | 60
Number of trials | 3
Correction of thermocouple indication temperature had not done in this experiment
Notes: The thermocouple position was defined by r [mm] and z [mm] as shown in this figure,
The origins of r and z are both the center of the fuel surface.

## Slide 25: Experimental results
Notes: Experimental results

## Slide 26
Decrease in Flame Height
Decreasing rate of flame height varies
depending on fuel species.
The flame height is decreased because of
decreasing of fuel evaporation.
Notes: The acetone flame height was decreased 7.2%
To decrease rate of flame height depend on fuel species
So, it has possibility that the flame height may decrease by decreasing of fuel evaporation

## Slide 27
Experimental Results
<Ethanol，z=2.3mm>
The average temperature is used as a representative temperature.
● G=1
○ G=0.55
Rim
Flame Sheet
Flame
Pan
0
Notes: This figure is the temperature distribution of ethanol fire
In this research, we assumed that the temperature distributions were axially symmetrical.
The average temperature, ethanol and acetone, are used as a representative temperature

## Slide 28: Representative Temperature
Flame height and representative temperature is different in
a partial gravity environment.
 | Ethanol | Acetone
G=1 | 1190 [K] | 1222 [K]
G=0.55 | 1128 [K] | 1188 [K]
Decreasing Rate | 5.2% | 2.8%
Decreasing Rate of Flame Temperature
The average temperature
Calculate the amount of heat feedback from the flame temperature.
Notes: This is an average value of the flame temperature
Decreasing Rate of Flame Temperature is defined as this
In ethanol, the ratio of the decrease in temperature at G = 0.55 compared with G = 1 is 5.2 %.
Acetone is 2.8%
We calculated the heat feedback amount from the flame temperature

## Slide 29: Amount of Heat Feedback
Notes: So we considered about the heat feedback amount
そこで燃料蒸発量を決定する要因である
熱フィードバック量について考えました

## Slide 30
Convection
Radiation
Equations of Heat Transfer
： Heat flux [W/cm2]
：absorption ratio [-]
：emissivity [-]
：representative temperature [K]
：The temperature of
the fuel liquid surface [K]
： Stefan-Boltzmann coefficient [W/]
<Stefan-Boltzmann law>
：Heat flux [W/cm2]
：Temperature [K]
：Thermal conductivity [-]
<Fourier's law>
Notes: There are basic equations of heat transfer，Convection and Radiation
From Fourier's law, ●Convection depends on temperature gradient
From Stefan-Boltzmann law, ●radiation depends on temperature to the power of 4
Both we need to investigate flame temperature to understand heat feed back
これらの伝熱機構の基礎式を示します。
対流項はフーリエの法則・ニュートンの冷却則により、●温度勾配へ依存します。
一方、放射項はステファン・ボルツマンの法則より、●温度の4乗に依存します。
いずれにしても、これらの伝熱機構を検討するには、火炎周囲の温度測定が必要となります。

## Slide 31
○: G=1
△: G=0.55
T [○C]
z [mm]
Temperature gradient in the z direction
Temperature at z=0 is assumed boiling point at fuel surface.
In 0.55G, flame temperature decreased.
<Ethanol, r = 6.0 mm>
Calculation of Convective Heat Flux
Notes: First, I will explain Calculation method of Convective Heat Flux
This graph is temperature gradient in the z direction.
●Temperature at z=0 is assumed boiling point at fuel surface.
●In 0.55G, flame temperature decreased.

## Slide 32: Calculation of Convective Heat Flux
<Ethanol, r = 6.0 mm>
G=0.55
819.56
[K/mm]
○: G=1
△: G=0.55
T [○C]
z [mm]
G=1
881.19
[K/mm]
Calculate temperature gradients at z = 0.
Temperature gradients decrease in 0.55G.
Temperature gradient in the z direction
Notes: We calculated temperature gradients at z = 0.
Temperature gradients decrease in 0.55G.

## Slide 33: Distribution of Convective Heat Flux
Heat flux to the fuel surface decreases in 0.55G
Flame
Pan
0
Especially, qc at r = 6 mm decreases significantly.
Notes: This graph is distribution of Convective Heat Flux
Heat flux to the fuel surface decreases in 0.55G.
●Especially, qc at r = 6 mm decreases significantly.

## Slide 34: Calculation of Radiative Heat Flux
Acetone
The was assumed as the straight distance from the heat receiving surface to the flame sheet.
[m] ：Optical thickness as viewed from the heat
receiving surface
[]：Absorption coefficient
<Stefan-Boltzmann law>
To estimate emissivity , we used the “flame radiation absorption model”. Following this model, emissivity depends on 𝑙.
Notes: Next, I will explain Calculation method of radiative Heat Flux
To estimate emissivity, we used the “flame radiation absorption model”. Following this model, emissivity depends on 𝑙.
The 𝑙 was assumed as the straight distance from the heat receiving surface to the flame sheet.

## Slide 35: Calculation of Radiative Heat Flux
Acetone
[m] ：Optical thickness as viewed from the heat
receiving surface
[]：Absorption coefficient
<Stefan-Boltzmann law>
φ
Heat flux has a distribution in the φ direction. Because φ changes the value of 𝑙.
Therefore, we calculated the heat flux by each φ.
Notes: We defined the angle φas shown in this figure.
Heat flux 𝑞_𝑟 has a distribution in the φ direction. Because φ changes the value of 𝑙.
Therefore, we calculated the heat flux by each φ.

## Slide 36: Distribution of Radiative Heat Flux
Flame
Pan
0
φ=0
φ=0.5
As gravity level increases, the heat flux decreases.
Notes: This graph is distribution of radiative heat flux.
As gravity level increases, the heat flux decreases.
これよりφ方向の熱流束の分布を図に示しました
全体的な傾向としてφが大きくなるにつれて𝑞_𝑟は小さくなる
φ=0でG=1，0.55Ｇの𝑞_𝑟の差が最も大きい

## Slide 37: Distribution of Radiative Heat Flux
Flame
Pan
0
1G
0.55G
In φ =0, the heat flux decreased most in 0.55G.
Because the change of 𝑙 is the largest.
As φ increases, the heat flux came to little change.
Because the width of the flame does not change.
Notes: In φ =0, the heat flux decreased most in 0.55G.
Because the change of 𝑙 is the largest.
●As φ increases, the heat flux came to little change.
Because the width of the flame does not change.

## Slide 38
Calculation of Heat Feedback
The amount of heat feedback was derived
by integrating the calculated heat flux.
Amount of
heat feedback
Heat flux
Notes: The amount of heat feedback was derived by integrating the calculated heat flux.

## Slide 39
[W]
Compare the amount of heat feedback of
the radiation with that of the conduction
→ Decrease
→ Slight decrease
has little effect of gravity decreasing
on the amount of radiative heat feedback.
Fuel | Ethanol |  | Acetone | 
G=1 | 0.35 | 6.78 | 0.72 | 7.75
G=0.55 | 0.29 | 6.18 | 0.67 | 7.17
diff. | -0.06 | -0.6 | -0.05 | -0.58
Fuel | Ethanol |  | Acetone | 
G=1 | 0.35 | 6.78 | 0.72 | 7.75
G=0.55 | 0.29 | 6.18 | 0.67 | 7.17
diff. | -0.06 | -0.6 | -0.05 | -0.58
Calculation Result
Notes: Compare the amount of heat feedback of the radiation with that of the conduction
𝑄𝑐 decreased
𝑄𝑟 Slight decreased
So, 𝑄𝑟 has little effect of gravity decreasing on the amount of radiative heat feedback.

## Slide 40
Fuel | Ethanol | Acetone
G=１ | 4.91 % | 8.50 %
G=0.55 | 4.48 % | 8.55 %
The ratio of amount of radiative heat feedback
Acetone has larger proportion of the radiative heat feedback.
Ethanol | Acetone
8.9% | 7.2%
Decreasing rate of flame height
Acetone has small decreasing rate of flame height.
The Ratio of Radiative Heat Feedback
（=))
Notes: This table is the ratio of amount of radiative heat feedback
Acetone has larger proportion of the radiative heat feedback.
On the other hands,
This is decreasing rate of flame height
Acetone has small decreasing rate of flame height.

## Slide 41: Discussion
Notes: So we considered about the heat feedback amount
そこで燃料蒸発量を決定する要因である
熱フィードバック量について考えました

## Slide 42
Fuel
Heat Feedback
Fuel evaporation
Natural convective
flow
Gravity
Rim
Flame
Structure of The Pool Fire
Fuel evaporation due to heat feedback from the flame.
Occurrence of natural convection due to gravity.
Normal gravity environment
Notes: In normal gravity environment,
●Major characteristics in the pool fire is occurrence of natural convection by gravity
●Natural convection transport fuel vapor, oxygen and combustion gas
Fuel vapor is burned and fuel receive heat feedback from the flame

## Slide 43
Fuel
Rim
Flame
Natural convective
flow
Gravity
Structure of The Pool Fire
Decrease natural convection due to gravity
Heat Feedback
Fuel evaporation
Partial gravity environment
Notes: In partial gravity environment,
Natural convection is decreased ●

## Slide 44
Fuel
Heat Feedback
Fuel evaporation
Rim
Flame
Natural convective
flow
Gravity
Structure of The Pool Fire
Amount of fuel vapor is decreased by decrease heat feedback
Decrease natural convection due to gravity
Partial gravity environment
Notes: And amount of Fuel vapor is decreased by decreasing heat feedback

## Slide 45
Fuel
Heat Feedback
Fuel evaporation
Rim
Flame
Natural convective
flow
Gravity
Structure of The Pool Fire
Partial gravity environment
The radiative heat feed back is hardly affected by the gravity.
So, Flame height of acetone doesn’t relatively decreased.
Notes: The radiative heat feedback is hardly affected by the gravity.
So, Flame height of acetone doesn’t relatively decreased.

## Slide 46
Conclusion
The amount of heat feed back decreases in partial gravity environment
2. Flame height is decreased due to that amount of
fuel vapor is decreased
3. The flame which has large proportion of the radiation
has little influence by gravity.
We have performed the partial gravity experiment
to estimate the heat feedback of a small-scale pool fire
Notes: We have performed the partial gravity experiment to estimate the heat feedback of a small-scale pool fire
The amount of heat feed back decreases in partial gravity environment
Flame height is decreased due to that amount of fuel vapor is decreased
The flame which has large proportion of the radiation has little influence by gravity.

## Slide 47
Thank you for your kind attention

## Slide 48: Heat feedback mechanism(仮)
As pool fire scale more lager, convective heat feedback decrease. And radiation become to be dominant.

## Slide 49
燃料槽上端から z = 5 mm
・ 火炎面への空気流入
・ z の増加に伴い速度増加
G = 1
0.5 m/s
2
4
6
8
10
0
2
4
6
8
1
3
5
7
Rim
r [mm]
2
4
6
8
10
0
2
4
6
8
1
3
5
7
Rim
r [mm]
Flame
sheet
Flame
sheet
G = 0.5
z [mm]
z [mm]
火炎基部流れ場ベクトル図

## Slide 50: Pool Fire
Small-scale
Middle-scale
Large-scale
Feedback of knowledge
It is difficult to treat a large-scale pool fire experimentally.
In this study, we will discuss on small-scale pool flame.
By finding and using a scaling law, it is possible to grasp the burning characteristics of an actual scale fire from the experimental results of laboratory scale fire.
Notes: In the fire research, it is desirable that we do the experiments with real scale.
But, handling of large-scale pool fire is dangerous and difficult.
Therefore, small-scale pool flame is targeted in this study.
We aim to apply the resulting knowledge to the real scale of the flame.
火災研究においては、実規模による研究を行うのが最も望ましいですが、大型プール火炎の取り扱いは危険かつ困難です。
そこで、●本研究では実験室で取り扱い可能な小型プール火炎を対象とし、●得られた知見を実規模の火炎に応用することを目標としています。

## Slide 51: Pool Fire
Flame
Fuel
Heat
Feedback
Evaporated
Fuel
Radiation
Convection
The heat feedback amount
Convection
Radiation
The radiation is dominant in real scale fire
The structure of the pool flame
Notes: There are two the heat feedback, Convection and Radiation.
Radiation is dominant in the real scale fire.
ここで熱フィードバック量には対流項と放射項の２種類があり、実規模火災では放射項が支配的となります

## Slide 52: 熱流束の算出 –Calculation of Heat Flux-
is the thermal conductivity of air for the average temperature between z=0 and 1.
＜Fourier’s Law＞
：Heat flux
：Thermal Conductivity
Notes: 続いて、フーリエの法則を用いて液面方向への熱流束を算出します。
本研究ではガスの流動による熱伝達を考慮せず、火炎内のガスの熱伝導のみで考えます。
●熱伝導率λには、z=0 と 1 との平均温度に対する空気の熱伝導率を使用します。
●そして、熱伝導率λと先程算出した温度勾配を乗じて、熱流束qを算出しました。

## Slide 53: 温度勾配 -Temperature Gradient-
<Ethanol, r = 6.0 mm>
z = 0 における温度勾配を算出
Calculate temperature gradients at z = 0
低重力環境 → 温度勾配は低下
Temperature gradients decrease under partial gravity environment
G=1
881.19
[K/mm]
G=0.55
819.56
[K/mm]
○: G=1
△: G=0.55
T [○C]
z [mm]
Notes: このz方向の温度分布から、●今度は液面 (z=0) における、液面方向への温度勾配を算出します。
低重力環境ではこちらに数値で示したように、●z=0における温度勾配dT/dzは低下していることがわかります。