## Slide 1: Wind Stress over Water Surfaces: Comparisons of Various Estimation Methods
Professor S. A. Hsu
Coastal Studies Institute,
Louisiana State University
Email: sahsu@lsu.edu

## Slide 2
Wind stress τ = ϱ U*2 = ϱ Cd U102
Where ϱ is the density of air,
U* is the friction velocity,
Cd is the drag coefficient, and
U10 is the wind speed at 10m above the water surface.

## Slide 3
www.gfdl.noaa.gov/

## Slide 4
1. Wind-wave Interaction Method
When U10 is less than 7.5 m/s, surface tension and thermal effects dominate the air-water interaction;
When U10 > 7.5 m/s, mechanical turbulence takes over, so that the logarithmic wind profile prevails,
U10 = (U*/k) Ln (10/Zo) (1)
Where k (=0.4) is the von Karman constant,
Zo is the aerodynamic roughness length.

## Slide 5
According to Taylor and Yelland (2001, JPO),
Zo / Hs = 1200 (Hs/Lp) 4.5 (2)
Lp = g Tp 2 / (2π) = 1.56 Tp2 (3)
Where Hs is significant wave height,
Lp is peak wave length, g is gravitational
acceleration, and Tp is dominant wave period.

## Slide 6
2. Wave Method
According to Csanady (2001) and JONSWAP
Wave Spectra (Carter, 1982), for U10 > 20m/s after wave breaker saturation (Amorocho and DeVries,1980; and Geernaert et al.,1987),
g Hs/U*2 = 0.053 (g Tp /U*) 3/2 (4)
Therefore,
U* = 36 Hs2/ Tp 3 (5)

## Slide 7
3. Turbulence Intensity or Gust Factor Method
According to Hsu (1988, Coastal Meteorology)
And Hsu (2003, Journal of waterway, Port,
Coastal, and Ocean Engineering),
U* = k p U10 (6)
G = 1 + 2P (7)
U2 / U1 = (Z2 / Z1) p (8)
P = σu / U10 (9)
G = Ugust / Usustained (10)