## Slide 1: PHTHALATES RELEASED FROM PLASTIC BOTTLES TO INNER DRINKING WATER WHICH THREATEN FOOD SAFETY
Prof. Dr. Magdy M. Saad
Food Safety Dept., NRC, Egypt

## Slide 2: INTRODUCTION & SCIENTIFIC BACKGROUND
Recently, since 2007 the EU and FSIS focused on the problem of phthalate-congeners which used as plasticizers' to enhance the properties of packaging materials (HARDNESS, TRANSPARENCEY, FLEXIBILITY & TIGHT).
During 2008 – 2012 the EU & FSIS recommended some analytical methods to determine phthalate residues in certain kinds of food through distinct program of food safety. No recommended official method is available, so far.

## Slide 3: NATURE & EXPOSURE
Phthalate congeners are phthalic acid esters which could easily released to the surrounding area of food because of the weak covalent bond between phthalates and organic substances mixed with food or containers and packaging materials.
Phthalate(s) could reach up to 50% (w/w) of the packaging materials used in food industry. So far, more than 15.000 kind of packaging materials are available in food industry

## Slide 4: NATURE & EXPOSURE
Both temperature and storage period have a positive effect on the released concentrations of phthalate(s) to food.
Exposure to phthalates could be occurred through; SKIN CONTACT & INHALATION, but it’s confirmed that food still the main route and source to such hazard(s).

## Slide 5: OCCUREENCE ANDTYPE OF FOOD
Many studies exhibited that bottled water contain high concentrations of phthalate congeners.
Also, fatty foods or the high fat content foods are the most probable sources of phthalate(s) contamination (OILS AND ITS MIXTURES, DAIRY PRODUCTS esp. CHEESE AND BUTTER).

## Slide 6: EXPOSURE TO PHTHALTES
Phthalates rank order: DINP > DIDP = DEHP
Life stages: Toddlers > infants > children > women of
reproductive age
Sources: food most important
routes not clear
Example: PVC packaging for meat: DEHP

## Slide 7: PHTHALATES MANAGING RISKS
Phthalates in PVC are not bound
they will
leach out
Exposure difficult to manage
Importance of phthalate
free plastics (PP, PE)

## Slide 8: SUCEPTIBLE POPULATION
Infants and children more susceptible
  Eat, drink water, and breathe more per unit of body weight than adults
  Put their fingers in their mouths
  Less well-developed immune systems and body detoxification processes
Fetal exposure may increase risk of autism, asthma, learning disorders

## Slide 9: OBJECTIVES
Focusing on chemical methodology using GC-MS to evaluate and recommend accurate, selective, sensitive and suitable method(s) to determine phthalate residues in different brands of BOTTLED WATER .
Statistical analyses to determine (uncertainty of measurement, limit of detection (LOD), accuracy, repeatability, reproducibility.

## Slide 10: OBJECTIVES
Determination of the RISK ASSESSMENT OF EXPOSURE TO PHTHALATE CONGENEERS.
Estimating the National Daily Intake (ENDI) as recommended by the criteria of Codex Alim., 2011.

## Slide 11: RESULTS AND DISCUSSION

## Slide 12
Phthalate esters | Retention time(Rt) | Regression Curve | Accuracy (R) | Less Detect. concent.
DMP | 29.10 | Y = 1.9 x + 0.3 | 0.993 | 25 ng/ ml.
DEP | 33.22 | Y = 3.1 x + 0.4 | 0.991 | 25 ng./ ml
DBP | 40.56 | Y = 8.2 x + 1.4 | 0.989 | 25 ng./ ml
BBP | 45.69 | Y = 6.3 x + 1.2 | 0.998 | 25 ng./ ml
DEHP | 55.35 | Y = 3.6 x + 0.7 | 0.990 | 25 ng./ml
DOP | 58,92 | Y = 2.7 x + 0.6 | 0.988 | 25 ng./ ml
Mean |  |  | 0.991± 0.016 | 
Retention Time, Regression curve, accuracy and less detectable concentrations of 6 phthalate esters

## Slide 13
The retention time (Rt) versus the relative abundance of 6
Phthalates using GC-MS. Injected volume 1 ul containing
25 ng each of DMP, DEP, DBP, BBP, DEHP & DOP

## Slide 14
Phthalates | Concentrations (ng./ ul) |  |  | Av. Ac.% | Av.Pr. %
 | 25 | 50 | 100 |  | 
DMP | 0.222 | 0.470 | 0.910 | 1.18 % | 3.12 %
DEP | 0.314 | 0.612 | 1.150 | 2.71 % | 3.22 %
DBP | 0,266 | 0.488 | 0,870 | 3.10 % | 3.74 %
BBP | 0.315 | 0.590 | 1.100 | 3.07 % | 3.56 %
DEHP | 0.360 | 0.710 | 1.310 | 2.96 % | 3.02 %
DOP | 0.284 | 0.530 | 1.101 | 3.11 % | 3.11%
Overall mean ± SD |  |  |  | 2.69 ± 0.96 | 3.29 ± 0.36
The percentages of average of accuracy and average
Of precision

## Slide 15
Phthalates | Concentrations (ng./ ul) |  |  | Average Recovery % | Coeffic. Of Var. %
 | 25 | 50 | 100 |  | 
DMP | 84.6 | 86.5 | 88.1 | 86.4 % | 4.8 %
DEP | 83.7 | 81.4 | 84.6 | 83.2 % | 5.3 %
DBP | 95.7 | 96.7 | 97.1 | 96.5 % | 4.3 %
BBP | 96.8 | 97.4 | 96.8 | 97.0 % | 3.9 %
DEHP | 91.4 | 95.3 | 98.4 | 95.0 % | 4.2 %
DOP | 83.6 | 87.1 | 86.3 | 85.7 % | 4.7 %
Overall mean ± SD |  |  |  | 90.6 ± 6.9 | 4.5 ± 0.7
. percentages of recovery of spiked blank water samples. show the
Notes: Table 2 show the average of recovery

## Slide 16
Phthalate esters | Brands A B C 1 3 6 1 3 6 1 3 6 |  |  |  |  |  |  |  | 
S | --- | --- | --- | --- | --- | --- | --- | --- | ---
DMP M | --- | --- | --- | --- | --- | --- | --- | --- | ---
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
S | --- | --- | --- | --- | --- | --- | --- | --- | ---
DEP M | --- | --- | --- | --- | --- | --- | --- | --- | ---
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
S | --- | --- | --- | --- | --- | --- | --- | --- | ---
DBP M | --- | --- | --- | --- | --- | --- | --- | --- | ---
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
S | --- | --- | --- | --- | --- | --- | --- | --- | ---
BBP M | --- | --- | --- | --- | --- | --- | --- | --- | ---
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
S | --- | --- | --- | --- | --- | -++ | --- | --- | --+
DEHP M | --- | --- | --- | --- | --- | --+ | --- | --- | --+
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
S | --- | --- | --- | --- | --- | --+ | --- | --- | --+
DOP M | --- | --- | --- | --- | --- | --+ | --- | --- | ---
L | --- | --- | --- | --- | --- | --- | --- | --- | ---
Phthalate residues in 3 bottled water brand with 3 sizes
At 3 different intervals.

## Slide 17: CONCLUSION
Although, the presented data showed negligible levels of phthalates-contamination with no significant occurrence in bottled drinking water, there is an urgent need to; firstly, develop more reliable and validated methods of analysis suites the different matrices of foods

## Slide 18: CONCLUSION
Secondly, to determine and establish the relation between the concentration of the released phthalates, temperature and storage time of packaged foods during their shelf life..

## Slide 19: CONCLUSION
Thirdly, to initiate extensive studies of risk assessment dealing with phthalate(s) hazards and considering the unavoidable multi-sources of exposure to such hazards

## Slide 20
Thank you
Prof.Dr. Magdy M. Saad