## Slide 1
Automating Farms Irrigation in
Saudi Arabia
Challenges of a Large-Scale System
Sami A. Alhasan

## Slide 2
Welcome from Saudi Arabia

## Slide 3
Who Am I?
Sami Alhasan from Saudi Arabia
Got MS and PhD from Georgia Tech 1999
Intelligent Control Systems (Fuzzy, NN, Genetic)
Worked on Intelligent Autonomous Areal Vehicles
Dean of Ahsa Tech College for four years
GM for Saudi Control Solutions Company
Academic Consultant for KFU University
GM for MISC Global Company

## Slide 4
Saudi Arabia
Area = 2,150,000 km2
Population = 31 M
Main resource = Oil/Gas
Al Ahsa Region
Area = 534,000 km2
Population < 1,000,000

## Slide 5
Al Ahsa Farms
~ 20% of 25 M palm trees in Al Ahsa (Sea of Palm Trees)

## Slide 6
Al Ahsa Palm Trees

## Slide 7
The 1972 Project
King Faisal launched the Irrigation Project in Al Ahsa

## Slide 8
The 1972 Project

## Slide 9
Open-Channel Irrigation
Open concrete channels of a total length = 1,500 km

## Slide 10
Main Irrigation Channels

## Slide 11
Branch Irrigation Channels

## Slide 12
The Problem
Water wells were depleted
Water evaporates in open channels ( 40% )
Lots of water is wasted by
- Unmaintained channels
- Abuse of water resources

## Slide 13
The Solution
A 293 M USD Project
Replace open channels with a pipeline network
Use recycled water for farm irrigation
Automate farm irrigation
Apply sprinkler irrigation in the farms

## Slide 14
Al Ahsa Top View
Agricultural area in Al Ahsa = 80 km2 ( ~ 20% of Ahsa area)

## Slide 15
The 10 Farm Zones
Agricultural area with 24,570 farms divided to 10 zones

## Slide 16
Design and Implementation
Each Zone  Water Reservoir/Tanks
Main Pumping Station
Valve-controlled pipeline network
Multi-level Zone Irrigation Control System
Zone controllers supervised by a Master Controller

## Slide 17
Removing the Open Channels

## Slide 18
The Pipeline Network

## Slide 19
The Pipeline Network
Total length of the closed pipeline network is > 1,000 km

## Slide 20
The Automated Irrigation System
A Multi-Level SCADA System
Irrigation Optimization Problem
Xi = f (Ci, Ai, Si, Ti)
Xi = irrigation water volume supplied to farm I m3
Ci = Crop Water Consumption m3/m2 . month
Ai = Farm Area m2
Si = Month (i.e. Jan, Feb … Dec)
Ti = Ambient Temperature C

## Slide 21
The Control System Hierarchy

## Slide 22
What is the Project Status?
70% of the pipeline network finished
(still zones 1, 2 & 3 not finished)
Zone 6 finished and functional
- Area = 12 km2, with 3,508 Farms
- Project value = 43.7 M USD
- 100% Tertiary-recycled irrigation water
- 3-Level SCADA Control System

## Slide 23
Zone 6 Reservoir

## Slide 24
Zone 6 Tanks
15,000 m3 Irrigation Tanks

## Slide 25
Zone 6 Pumping Station
6 MV pumps (4 Operating, 2 Standby) each = 500 L/sec

## Slide 26
Zone 6 Main Pipeline

## Slide 27
Zone 6 MCC Room

## Slide 28
Zone 6 Control (levels 2 & 3)

## Slide 29
Zone 6 SCADA Software
SCADAPack from Schneider Electric

## Slide 30
Zone 6 Control Room

## Slide 31
Zone 6 Control (levels 3 & 4)

## Slide 32
Farm Brach Control (Level 4)
RTU Twido PLC with Modbus Cable Communication

## Slide 33
Farm Brach Servo Valve Box

## Slide 34
Challenges
Operation:
* Automatic vs. Manual
Maintainability:
  * Maintain 25,000 farm RTUs
  * Unstructured agricultural environment
  * Spare Parts

## Slide 35
Challenges
3. Expandability:
* New farms, farms expand, change crops
4. Technology:
  * Technology changes & becomes obsolete
  * Interface different technologies

## Slide 36
Thank You
Sami A. Alhasan
+966 50 492 5915
salhasan@tvtc.gov.sa