## Slide 1: Bioenergy Supply Chain Optimization: Models and Applications
World Bioenergy Congress and Expo, Rome, Italy
06/14/2016
Sandra D. Eksioglu, PhD
Department of Industrial Engineering

## Slide 2
1
2
3
4
Data Analysis and Numerical Study
5
Conclusions
6
Research Motivation and Literature Review
Supply Chain Model and Case Study
Presentation Outline

## Slide 3: Introduction and Motivation
Increased interest in many areas of research related to bioenergy for the following reasons
  Bioenergy it is expected to contribute in meeting global future energy needs.
  Bioenergy is a clean source of energy; reduces the risk of oil embargos, price strikes, geopolitical dependence; supports farmers and local economy.
  In US, the Renewable Fuels Standard (RFS) established a target of 36BGY by 2022.
  Etc.
Current research has been focused (among other areas) on the optimization of the bioenergy supply chain.
“Bioenergy supply chain” includes the necessary operations to harvest biomass, preprocess, store and transport from the farm to a processing facility and distribution of bioenergy to consumers.
Notes: Cellulosic biomass, such as corn stover, has 20 percent to 30 percent supply variations, compared to 12 percent to 15 percent variations for corn grain (http://www.renewableenergyworld.com/articles/2015/11/cellulosic-biofuel-reducing-cost-through-cellulosic-biomass-supply-strategy.html )
http://www.bioenergyconnection.org/article/billion-ton-update-where-biomass

## Slide 4: Introduction and Motivation
  Bioenergy supply chain costs are high:
  Physical characteristics of biomass and biofuels.
  Biomass supply and costs are uncertain.
  The “Billion-Ton Study” of US DOE & ORNL estimates that the US could produce about 85BGY, 30% of current petroleum consumption.
  A 2012 study by the Idaho National Laboratory demonstrate a delivered biomass logistics cost of $35/dt.
  The main goal of research in bioenergy supply chains is to design sustainable and robust supply chains which lower bioenergy delivery cost, lessen environmental impacts, and improve social outcomes.
The long-term goal of the supply chain-related research is to contribute to a smooth switchover from a fossil fuel-based energy to bioenergy-based economy.
Notes: Cellulosic biomass, such as corn stover, has 20 percent to 30 percent supply variations, compared to 12 percent to 15 percent variations for corn grain (http://www.renewableenergyworld.com/articles/2015/11/cellulosic-biofuel-reducing-cost-through-cellulosic-biomass-supply-strategy.html )
http://www.bioenergyconnection.org/article/billion-ton-update-where-biomass
Physical characteristics impact: transportation and collection costs. Uncertainties: impact inventory holding costs.

## Slide 5: Supply Chains Decisions
Supply chain decisions are:
    Long-term: facility location, technology selection, etc.
    Mid-term: supplier selection, transportation mode selection, etc.
    Short-term: collection, storage, production and transportation schedule, etc.
Biomass supply chains decisions are impacted by:
  Biomass availability and seasonality
  Biomass quality, supply and price uncertainties
  Large number of farmers

## Slide 6: Supply Chain Literature
Reviewed Models
Scope
Strategic
Tactical
Operational
Product Characteristics
Perishable
Non-Perishable
Objective
Economic
Environmental
Social
MIP
SP
Simulation
Modeling
Deterministic
Stochastic
Game theoretic
LP
NLP
Non-coop.
Sequen.
Liquid

## Slide 7
Supply Chain Planning and Design for Biodiesel Production via Wastewater Sludge*
*Marufuzzaman, M, S.D. Ekşioğlu, R. Hernandez, “Environmentally Friendly Supply Chain Planning and Design for Biodiesel Production via Wastewater Sludge,” Transportation Science, 48(4), 555-574, 2014. http://dx.doi.org/10.1287/trsc.2013.0505
**Marufuzzaman, M, S.D. Ekşioğlu, Y. Huang, “Two-Stage Stochastic Programming Model for Biocrude Supply Chain,” Computers and OR, Vol. 49, 2014, 1-17. http://dx.doi.org/10.1016/j.cor.2014.03.010

## Slide 8: BIODIESEL Supply Chain Structure
Municipal WWT Plants
Pulp & Paper
Meat Packing
Poultry Slaughtering & Processing
Animal & Marine
Fresh/Frozen Fish
Sludge Supply
Biocrude
Plants
Diesel
Plants
Customers

## Slide 9: BIODIESEL Supply Chain
  Research Questions
    Estimate supply-chain related costs for production of biodiesel.
  Biomass transportation (sludge):
    What factors have a great impact to the transportation cost of sludge?
    Under what conditions pipeline becomes a viable transportation mode?
  Supply chain design and management:
    Should a biocrude plant be co-located at a WWT facility?
    What factors have a great impact on the supply chain costs?
  Provide insights about biodiesel supply chain related costs to potential investors.

## Slide 10: Solution Approach
        Sludge Transportation
        Techno-Economic Analysis
        Sludge Supply Analysis
        Regression Analysis
        GIS Tools
        Supply Chain Design & Mgmt.:
      Optimization Model
        Model Validation & Verification
        GIS Tools
        Sensitivity Analysis
Input Analysis
Output Analysis

## Slide 11: Transportation Cost Analysis
Facility-owned Single Trailer Truck, 30m3 capacity.
Similar analyses is conducted for rented Single Trailer Truck, facility-owned and rented Tandem Trucks of 30m3 and 40m3 capacity.
(a) Fixed costs ($/m3)
Fuel cost
Labor cost
Maintenance and repair cost
Tire cost
Cost of ownership
Annual sale taxes
License fees and taxes
Management and overhead cost
Insurance cost
(b) Variable costs ($/m3/mile)

## Slide 12: Transportation Cost Analysis
II. Pipeline Transportation of Sludge
Smaller the capacity, higher transp. costs.

## Slide 13: Transportation Cost Analysis
Data: Mississippi Department of Environmental Quality.
Pipeline vs. truck for volume of sludge shipped: 843.5 m3/day
Variable cost ($/mile/m3) is smallest for facility-owned tandem trailer truck.
As transportation distance increases, pipeline costs decrease.

## Slide 14: Sludge Transportation Costs in MS
A 20% increase in the cost of labor
and fuel:
VC of pipelines is smallest for
distances over 220 miles.
A 10% increase in the cost of labor
and fuel:
VC of pipelines is smallest for
distances over 700 miles.

## Slide 15: Summary: Sludge Transportation Costs

## Slide 16: Distribution of Sludge supplier, Biodiesel Plants and Population in MS
Sludge Supply | No. Suppliers
WWT plants | 64
Pulp & paper mills | 8
Poultry slaughtering & processing | 11
Fresh & frozen fish processing plants | 9
Fat & oil from animal and marine | 1
Meat packing plants | 1
Total | 94
Sludge supplier
Biodiesel Plants
Population by county

## Slide 17: Trends Analysis
Sludge Yields in Mississippi
Population in MS
* Hurricane Katrina, Aug. 2005
* Oil Spill in the Gulf, April 2010

## Slide 18
A Two-Stage Stochastic Programming Model
First-stage decisions x
Uncertainty
()
Second-stage
decisions y(, x)
Biomass supply uncertainty
Strategic decisions:
Plant locations/sizes
Pipeline location/size
Nr. of trucks purchased
Planning decisions:
Production
Transportation
Shortage
.

## Slide 19: Supply Chain Optimization Model
  Objective: Minimize the expected supply chain costs.
  Decision Variables
    Location and capacity of biocrude production plants
    Transportation mode selection
      Pipeline, facility-owned trucks, rented trucks
    Sludge processing and delivery
    Biocrude processing and delivery
    Biodiesel delivery

## Slide 20: Model Formulation: Constraints
Supply Point k
Supply
Point k+1
Plant j
Plant j+1
Sludge Supply
Trans. Mode m
Refinery i
Refinery i+1
Plant j
Plant j+1
Production Capacity
Pipeline & Truck Capacity
Flow Balance

## Slide 21: Model Formulation: Constraints
Demand is Satisfied
Customer g
Customer g+1
Market
Refinery i
Refinery i+1
Binary Const.
Non-Negativity Const.

## Slide 22: Solving the Two-Stage SP Model
NO
Solve sub-problems
(yn(), n) , Calc. UB
n = n +1
Add nth optimality cut to MP.
Solve the Master Prob.
(xn, zn, vn) & LB
L-shaped algorithm
Initialize; n = 1
UB – LB < 
n > Nmax
Stop; Report solution
YES
1. Using CPLEX
2. Lagrangean Relax.
Solve Master Prob.
1. One aggregate cut
2. Multiple cuts
Optimality Cut

## Slide 23: Scenario Definitions & Probabilities: Supply Uncertainty
Scenario | Explanation | Probability
1-5 | Historical data collected from previous five years | 0.15*5 = 0.75
6 | Sludge supply of every facility is increased by 20% | 0.05
7 | Sludge supply of every facility is decreased by 20% | 0.05
8 | Supply from WWT plants changes by as much average change of population in MS in the last 10 year | 0.05
9 | Sludge supply from pulp & paper industry decreases by 20% | 0.05
10 | Sludge supply from poultry increased by 20% | 0.05

## Slide 24: Supply Chain Decisions: Min Costs
Val. of Stochastic Solution
$3. 36M
Stochastic Solution
Costs: $311.60 M
Capacity: 80MGY
Production: 75.59MGY
Expected Val. Solution:
Costs: $314.96 M
Capacity: 75MGY
Production: 72.55MGY
Distribution of Unit Cost ($2.72/gal)
1. Large capacity plants centrally located.
2. Co-locate with large WWT facilities.
3. Truck transportation

## Slide 25: Bioenergy and Environment
  US is committed to reduce GHG emissions by 17% below 2005 levels by 2020
  Environmental policy on physical processes
    Energy efficient facility/vehicles: USDA Alternative Fuel & Fleet Efficiency programs
    Alternative fuels: Biodiesel Income Tax Credit, Excise Tax Credit, Alternative Fuel Excise Tax
    Focus on physical processes overlooks the impact of business processes and operational practices on emissions
      Inventory replenishment decisions impact emissions
    Inventory Inventory
      Outsourcing, centralized warehousing, rapid-response logistics, just-in-time production, etc. impact emissions.
Notes: Regional Greenhouse Gas Initiative (RGGI), the Western Climate
Initiative (WCI), and the Midwest Greenhouse Gas Reduction Accord (MGGRA)

## Slide 26: Adding an Environmental Objective
  The following function represents total emissions:
  Where, is the amount of carbon emitted by transportation mode m when shipping sludge from supply location k to biocrude plant j.
  the amount of carbon emitted for shipping biocrude
  the amount of carbon emitted for shipping biodiesel

## Slide 27: Solution Approaches
  Weighted sum method:
  -constraint method:

## Slide 28: Modeling Environmental Policies
Environmental Policies
Carbon Cap
Carbon Tax
Carbon Cap-and-Trade
Carbon Offset
Evaluate the impact of environmental policies on supply chain operations.

## Slide 29: Modeling Carbon Cap
  The following constraints is added to the mathematical model:
  for each 

## Slide 30: Modeling Carbon Tax
  The following term is added to the objective function:
  Where, is the carbon tax (in $/kg).

## Slide 31: Pipeline Emissions Calculations
Input:
Pipeline capacity, Cpipe (tons/year)
Pump power, Pp (hp)
Pump Efficiency, ηp
Operating hour per year, Oh (hr/year)
CO2 emissions to generate electricity ECO2 (kg/kWh)a
Calculations:
Electricity required (kWh/year): Epump = (Pp * 0.746 * Oh) / (ηp)
Emissions per unit (kg/ton): Empump = (Epump * ECO2) / (Cpipe)
Inlet Station
Outlet Station
Booster Stations
a Greenhouse gas protocol: www.ghgprotocol.org
a Energy Information Administration: http://www.eia.gov/cneaf/electricity/page/co2_report/co2emiss.pdf

## Slide 32: Truck Emissions Calculations
Loading
Unloading
Transporting
Fixed Emission
* Pump Power
* Pump Efficiency
* Volume Flow Rate
* Fluid properties
Fixed Emission
* Pump Power
* Pump Efficiency
* Volume Flow Rate
* Fluid properties
Variable Emission
* Fuel Efficiency for
Loaded & Unloaded
Truck
* Diesel CO2 emission /gal

## Slide 33: Carbon Cap and Tax Mechanism
Stochastic solution have smaller total systems costs & higher production
The system reacts faster to an emission cap than an emission tax.

## Slide 34: Supply Chain Decisions: Min CO2 Emissions
(a) Carbon Cap 2800 tons/year
(c) Carbon Cap 2000 tons/year
(b) Carbon Cap 2400 tons/year
Jackson POTW, Hinds County
Weyerhaeuser Co.
Pulp & Paper Complex, Lowndes County
Hattiesburg South Lagoon, Jones County
Forest POTW, Scott County
Peco Foods, Madison County
Oxford POTW, Lafayette County

## Slide 35: Summary & Conclusions
Transportation activities in the supply chain will add on average $0.16/gal to the cost of sludge-based biodiesel.
Investments in improving biocrude technology will have a great impact on biodiesel production level and costs.
Carbon regulatory policies will have an impact on supply chain operations.
  Shifting transportation modes from truck to pipeline.
Stochastic programing model provides better solutions to our problem.

## Slide 36: Research Team
  Department of Industrial Engineering, Clemson University
  Sandra D. Eksioglu, PhD
  E-mail: seksiog@clemson.edu
  Mohammad Marufuzzaman
  E-mail: maruf237@gmail.com
  Department of Chemical Eng. Mississippi State Univ.
  Rafael Hernandez, PhD
  Todd French, PhD
  Andro Mondala, PhD
  Department of Civil & Env. Eng. Mississippi State Univ.
  Dennis D. Traux, PhD

## Slide 37: Thank you! Questions ?
Sandra D. Eksioglu
E-mail: seksiog@clemson.edu