## Slide 1
“SFC-MS as a Tool for Flower absolutes composition analysis”
Cyrille SANTERRE –Analytical chemistry engineer / Cosmetologist
Valencia –September 28th

## Slide 2
THEORY
CHAPTER I

## Slide 3
SEPARATIVE METHODS
GC : analytical et …
Supercritical chromatography : analytical and preparative
* Non-volatil, polar, no derivatization
* thermolabile compound
* Heavy molecular weight compounds
HPLC : analytical and preparative
* Faster analysis
* Less pressure
* Same columns
* Numerous detectors easy hyphenation
* High resolution power~5X/HPLC
Versus
Versus

## Slide 4
CO2 STATE DIAGRAM
http://chemwiki.ucdavis.edu/Core/Physical_Chemistry/Physical_Properties_of_Matter/States_of_Matter/Phase_Transitions/Phase_Diagrams
73,8 bar
31,1 °C

## Slide 5
OTHER POSSIBLE FLUIDS
http://www.portail-fluides-supercritiques.com/Fluides-supercritiques.55.0.html
CO2 easy to produce
Water : corrosive and possible thermal damages for products
Propane uses in other countries
T Critique (°C) : 374
P Critique (Bar) : 220
T Critique (°C) : 32,2
P Critique (Bar) : 48,8
T Critique (°C) : 9,5
P Critique (Bar) : 50,8
T Critique (°C) : 31,1
P Critique (Bar) : 73,8
T Critique (°C) : 241
P Critique (Bar) : 61,4

## Slide 6
BENEFITS OF CO2
Not expensive : 1 kg = 1 euro
Non-toxic fluid: analytical and extraction methods are « green »
Bit agressive for compounds and colums (vs HPLC)
Physical properties:
  Low viscosity = less pressure drop (quicker analysis),
  diffusivity = increased efficiency.
What is a Supercritical Fluid ? Author: Michel PERRUT - SEPAREX
 | LIQUID | SUPERCRITICAL (T~Tc P~1 à 4 Pc) | GAS (T & P room)
Density(kg/m3) | 600-1600 | 100 - 900 | 0,6 - 2
Viscosity (Pa.s) | 10-3 | 10-5 - 10-4 | 10-5
Diffusivity D (m2/s) | 10-9 | 10-8 | 10-5

## Slide 7
OUR APPARELS
Co-solvent pump
CO2 pump
UV detector
SFC-UV
SFC-QTOF

## Slide 8
COSMETIC ALLERGENS
CHAPTER II

## Slide 9
COSMETIC ALLERGENS
Column RXSIL 150mm*4,6mm*5µm
Chromatographic conditions:
BPR : 150 bar
Column temperature: 30 °C
Flow : 2,5 mL/min
Mobile phase : CO2 / ACN
Analysis run time 16 minutes and 3 minutes post-run
Time (Min) | %A | %B | Flow (ml/min)
0,00 | 98,0 | 2,0 | 2,500
6,00 | 98,0 | 2,0 | 2,500
10,00 | 80,0 | 20,0 | 2,500
11,00 | 80,0 | 20,0 | 2,500
14,00 | 98,0 | 2,0 | 2,500
UV detection :
Wavelength : 210 nm Width : 4 nm
Wavelength : 254 nm Width : 4 nm
Wavelength : 280 nm Width : 4 nm
Reference : 360 nm Width : 50 nm

## Slide 10
COSMETIC PRODUCT FROM MARKET
Formula :
Aqua / water, sodium laureth sulfate, dimethicone, coco-betaine, cetyl alcohol, hydroxystearyl cetyl ether, sodium chloride, ci 47005 / acid yellow 3, guar hydroxypropyltrimonium chloride, cocamide mipa, sodium benzoate, sodium cocoate, sodium hydroxide, ppg-5-ceteth-20, jojoba wax peg-120 esters, salicylic acid, limonene, linalool, propylene glycol, carbomer, methyl cocoate, citric acid, hexyl cinnamal, parfum / fragrance.
Limonène
Benzyl salicylate
Hexyl cinnamal
Alpha isomethyl ionone
Linalol
Citronellol
Géraniol
Benzyl alcohol
Lilial
Lyral
limonène
linalol
hexyl cinnamal
STANDARD
SHAMPOO AFTER EXTRACTION

## Slide 11
ESSENTIAL OILS
CHAPTER III

## Slide 12
CLOVE ESSENTIAL OIL
Column HYPERCARB 150mm*4,6mm*5µm
UV detection:
Wavelength: 200 nm Width: 4 nm
Wavelength : 254 nm Width : 4 nm
Wavelength : 280 nm Width : 4 nm
Reference : 360 nm Width : 50 nm
Chromatographic condition:
BPR : 150 bar
Column temperature: 30 °C
Flow: 2,5 mL/min
Mobile phase : CO2 / ACN
Time (Min) | %A | %B | Flow (ml/min)
0,00 | 95,0 | 5,0 | 2,500
3,00 | 95,0 | 5,0 | 2,500
15,00 | 80,0 | 20,0 | 2,500
17,00 | 95,0 | 5,0 | 2,500
Material & Method

## Slide 13
Chart: Concentration en % m/m
| 0.3669194132904357 | 6.146132658488955E-2 | 1.5703781439412413E-2 | 3.7521612383571768E-3 | 9.2756677298180996E-4
 | 15656.8 | 2850.1731 | 732.4935 | 168.9477 | 38.8945
Calibration curve
Repeatability & reproducibility
Repeatability and reproducibility parameters are « acceptable » to use for an assay method.
AVERAGE | 3014,61
STD DEV | 22,33
%REPETA | 0,74
AVERAGE | 7637,02
STD DEV | 50,36
%REPRO | 0,66
CLOVE ESSENTIAL OIL

## Slide 14
LOD : 3 ppm
LOQ : 11 ppm
Recovery rate: 99,1%
AVERAGE | 81,46
STD DEV | 0,68
RSD% | 0,83
Clove essential oil analysis
Other compound could be detected and analyzed.
Eugenol
CLOVE ESSENTIAL OIL

## Slide 15
CLOVE LEAF OIL
AVERAGE | 86,67
STD DEV | 0,23
RSD% | 0,27
Clove leaf oil analysis
LOD : 3 ppm
LOQ : 11 ppm
Recovery rate : 99,1%
Eugenol
Acétate Eugenyl
b-Caryophyllène
AFNOR?

## Slide 16
FLOWER ABSOLUTES
CHAPTER IV

## Slide 17
JASMINE ABSOLUTE
Jasminum grandiflorum
165.1277 jasmone
293,2482 methyl (Z)-linolenate
225,1563 (Z)-methyl epi-jasmonate

## Slide 18
Jasminum grandiflorum
163,0752 C10H10O2
163,1481 C12H18
163,1111 C11H14O
JASMINE ABSOLUTE

## Slide 19
Jasminum grandiflorum
500-700
700-900
950-1500
JASMINE ABSOLUTE

## Slide 20
TIC
SFC-QTOF Generic Method

## Slide 21
EXACT MASS ARE CREATED
1 Oxygène, 2 O …

## Slide 22
NARCISSUS

## Slide 23
JONQUIL

## Slide 24
NARCISSUS VS JONQUIL
Family : Amaryllidaceae,
Sub-family : Amaryllidoideae,

## Slide 25
LAVANDIN

## Slide 26
GRANDIFLORUM JASMINE
SFC PROFILE
GC PROFILE

## Slide 27
SAMBAC JASMINE
SFC PROFILE
GC PROFILE

## Slide 28
PROFILES

## Slide 29
POS MODE VS NEG MODE IN APPI

## Slide 30
POS MODE VS NEG MODE IN APPI

## Slide 31
GRANDIFLORUM VS SAMBAC IN POS MODE

## Slide 32
GRANDIFLORUM VS SAMBAC IN NEG MODE

## Slide 33
POS MODE POS VS NEG MODE IN APCI

## Slide 34
POS MODE POS VS NEG MODE IN APCI

## Slide 35
POS MODE VS NEG MODE IN ESI

## Slide 36
POS MODE VS NEG MODE IN ESI

## Slide 37
STATISTICAL ANALYSIS PCA (PRINCIPLE COMPONENT ANALYSIS)

## Slide 38
STATISTICAL ANALYSIS MFA (MULTI FACTORIAL ANALYSIS)

## Slide 39
Chart: Observations (axes F1 et F2 : 75,03 %)
| -9.4817022728913702 | -11.97964050648125 | 2.731678790517027 | 25.825841347973494 | -7.0961773591179025
 | -3.2458 | -4.1244 | 22.1075 | -7.4465 | -7.2908
STATISTICAL ANALYSIS PCA (PRINCIPLE COMPONENT ANALYSIS)

## Slide 40
CONCLUSIONS
Complementary with GC information and more molecules in one analysis (HPLC + GC)
Better information with HRMS
Interest to test different ionization sources and modes
We could correlate graphical view and PCA treatment
Species are well separated
Same family are closed but separated
Confirm results with more samples
Try method with other absolutes

## Slide 41
THANKS FOR YOUR ATTENTION
Alain Brunelle (DR1)
David Touboul (CR1)
Mass Spectrometry team
Nadine Vallet (PEPS team manager)