## Slide 1: Screening of a wide range of pre-treatments for improving the algal biomass solubilization and biogas potential Serge R. Guiot, Caroline Roy and Jean-Claude Frigon
Biofuels and Bioenergy,
August 25-27, 2015
Valencia, Spain

## Slide 2: Anaerobic digestion (AD) of algal biomass
AD: microbiological conversion of organic material in the absence of oxygen, that results in the production of biogas (renewable energy) and digestate (fertilizer)
Mitigated yield: 50% conversion;
Hydrolysis is the limiting-step;
Apply pretreatment to improve hydrolysis ⇒ higher CH4 yield; better stabilized digestate
Part of an algal biorefinery approach
    Tap CO2 from an emitter;
    Grow biomass in wastewater (free N and P);
    Generate added value with a bioproduct (or not);
    AD of whole or residual algae : renewable energy;
    Closed-loop. Effluent recirculation upstream.

## Slide 3: Scenedesmus sp.-AMDD
Why this strain ?
High biomass yield. Robust.
Experience with larger-scale growth in wastewater;
High methane potential: top 3 from a screening of > 20 strains.
J.-C. Frigon, F. Matteau-Lebrun, R. Ganda Bachir, P.J. McGinn, S. O'Leary &d S.R. Guiot. 2013. Screening microagae strains for their productivity in methane following anaerobic digestion. Applied Energy, 108:100-107.

## Slide 4: Culture of Scenedesmus
300 L Brite-BoxTM PBR;
Growth rate 0.3-0.4 d-1;
Continuous operation;
Algal cell density 7-10 X 106;
CO2 on demand; pH 7.0;
T°: 25°C.
Szumski R., A. Patrzykat. Value proposition alternatives for the industrial cultivation of microalgae in Canada. 3rd International Conference on Algal Biomass, Biofuels and Bioproducts, Toronto, CAN, June 2013.
Paste at ~ 280 gVS/kg

## Slide 5: Pretreatments
30 different assays: single and combined pretreatment;
Monitoring TS, TVS, SS, VSS, pH, sCOD, VFA, NH4.
Enzymatic | Chemical | Physical - thermal
Pectate-lyase (PL) | NaOH | Autoclave (121°C, 30 minutes)
Cellulase (C) | H2SO4 | Microwave
Commercial mix | H2O2 | Pressure vessel (PV) (2000 psi)
2 PL loading (1400, 4600 U/gVS) | 2 NaOH concentration (0.2N, 0.6N) | 2 microwave temperature (175 – 300°C)
2 reaction time (3h, 24h) | 2 reaction time (2h, 24h) | 4 PV temperature (25-180°C)

## Slide 6: Justification of enzymatic pretreatment
Chemical or thermal: non specific attack;
Cell wall: pectic and cellulose layer;
Pectate-lyase / cellulases.
Cronodon. (2015). Algae - building bodies from balls, chains, sheets and tubes. Retrieved June 24th 2015, from http://cronodon.com/BioTech/Algal_Bodies.html

## Slide 7: Pretreatment tests : solubilisation results
Best practical conditions:
Enzymes (PL + cellulase) and thermal;
NaoH 0.2N and thermal.
75% solubilisation on a
sCOD/TVS basis
Combined > Single

## Slide 8: Pretreatment results: examples
 | VS (g/kg) | sCOD (g/kg)
Suspension | 49.3 | 11.8
Pretreatment |  | 
Pectate-lyase (PL) | 46.5 | 28.7
PL + Cellulase + T (150°C) | 30.5 | 107.8
NaOH 0.2N 2h | 48.8 | 16.8
NaOH 0.2N 24h + T (150°C) | 15.6 | 78.2
Microwave 175°C | 44.0 | 27.9
Microwave + NaOH | 11.3 | 72.5

## Slide 9: Solubilisation vs methane production
No substantial improvement of biodegradation and methane yield, following pretreatment, at best 19 %
Sometimes, negative at higher T°
Heating/solubilisation: releasing inhibitors ?
Solubilized yet non-degraded organic matter in the AD effluent: soluble proteins
(150°C)

## Slide 10
UASB digesting pretreated Scenedesmus biomass
Anaerobic granule = aggregate of bacteria, auto-immobilization
Short HRT compared to CSTR: 6 d
Higher OLR: up to 5 g TVS/Lrxr·d
Without pre-treatment: TVS degradation efficiency : approaching 50%
Upflow anaerobic sludge bed (UASB) reactor:
high density of bacteria
Working volume: 3.5 L;
effluent recirculation, liquid vUP: 2 m/h

## Slide 11
UASB digesting pretreated Scenedesmus biomass
(cont’d)
Enzymatic {24 h}
  pectate-lyase [1340 U/gTVS]
  + cellulase [970 U/gTVS]
Enzymatic {24 h} + thermal (121°C − 150°C) {30 min}
Pre-treatments selected
Raw algal suspension

## Slide 12
Parameters | Control UASB | UASB after pretreatment |  |  |  | 
 |  | Phase 1 | Phase 2 | Phase 3 | Phase 4 | Phase 5
Operational time |  | Weeks 1 - 5 | Weeks 6-10 | Weeks 11-24 | Weeks 25-30 | Weeks 31-35
Pre-treatment | No | Enzymatic | Enzymatic + thermal (121°C) |  | Enzymatic + thermal (150°C) | 
Solubilization % (sCOD/TVS) | n/a | 77 ± 23 | 79 ± 5 | 55 ± 14 | 86 ± 8 | 98 ± 9
HRT (d) | 4.1 | 6.2 | 6.4 | 6.1 | 6.3 | 6.2
OLR (gTVS/LRXR.d) | 2.95 | 1.28 ± 0.44 | 2.48 ± 0.69 | 4.73 ± 1.16 | 2.20 ± 0.09 | 4.2 ± 0.1
pH | 7.2 - 7.6 | 7.2 ± 0.3 | 7.1 ± 0.1 | 7.3 ± 0.1 | 7.3 ± 0.2 | 7.2
Degradation % (1-TVSeff/TVSin) | 52 | 49 ± 6 | 52 ± 14 | 49 ± 11 | 44 ± 11 | 59 ± 4
sCOD (g/L) | 0.1 - 0.2 | 0.42 ± 0.09 | 1.13 ± 0.31 | 2.43 ± 0.77 | 2.62 ± 0.89 | 4.85 ± 1.3
VFA (g/L) | <0.05 | < 0.05 | < 0.05 | 0.14 | 0.05 | 0.14
NH4 (mg/L) | 100 - 250 | 189 ± 35 | 514 ± 161 | 952 ± 138 | 813 ± 147 | 1090 ± 57
Q CH4 (L/LRXR.d) | 0.53 | 0.27 | 0.57 | 0.80 | 0.55 | 1.13
Y CH4 (L/TVSin) | 0.18 | 0.21 ± 0.08 | 0.23 ± 0.08 | 0.18 ± 0.06 | 0.27 ± 0.02 | 0.24
UASB digesting pretreated Scenedesmus biomass
(cont’d)
no substantial improvement of degradation efficiency
and methane production
high solubilisation
≅ HRT
↗︎ load

## Slide 13
Residual methane potential from the UASB effluent
methane produced after 12 weeks of incubation, which reached 23 mLSTP CH4/g TVSin
i.e. only 9% of the methane produced in 6 days in the UASB
UASB digester efficient at extracting most of the methane potential from the algal biomass (in less than half the time)

## Slide 14: Concluding remarks
Pretreatments increases hydrolysis, solubilisation of algal biomass :
    Combination including thermal: best impact;
    Up to 75% solubilisation.
Conversion efficiency and methane yield of the hydrolyzed algal biomass, usually only marginally higher, 35% at best
    Possible inhibitors at high temperature;
    Solubilized yet non-degraded organic matter: soluble proteins
    Revise pretreatment scheme to target protein, e.g. thermal followed by enzymes, incl. peptidases
Main benefit:
    Allows for operating a high-rate digester on pretreated algal biomass : much shorter time to produce the methane, e.g. 6 days vs 15-28 days.

## Slide 15
15
Bioengineering Group
Energy, Mining & Environment
6100 Royalmount Avenue,
Montreal, H4P 2R2 Canada
Email: serge.guiot@cnrc-nrc.gc.ca