## Slide 1: About OMICS Group
OMICS Group International is an amalgamation of Open Access publications and worldwide international science conferences and events. Established in the year 2007 with the sole aim of making the information on Sciences and technology ‘Open Access’, OMICS Group publishes 400 online open access scholarly journals in all aspects of Science, Engineering, Management and Technology journals. OMICS Group has been instrumental in taking the knowledge on Science & technology to the doorsteps of ordinary men and women. Research Scholars, Students, Libraries, Educational Institutions, Research centers and the industry are main stakeholders that benefitted greatly from this knowledge dissemination. OMICS Group also organizes 300 International conferences annually across the globe, where knowledge transfer takes place through debates, round table discussions, poster presentations, workshops, symposia and exhibitions.

## Slide 2: About OMICS Group Conferences
OMICS Group International is a pioneer and leading science event organizer, which publishes around 400 open access journals and conducts over 300 Medical, Clinical, Engineering, Life Sciences, Pharma scientific conferences all over the globe annually with the support of more than 1000 scientific associations and 30,000 editorial board members and 3.5 million followers to its credit.
OMICS Group has organized 500 conferences, workshops and national symposiums across the major cities including San Francisco, Las Vegas, San Antonio, Omaha, Orlando, Raleigh, Santa Clara, Chicago, Philadelphia, Baltimore, United Kingdom, Valencia, Dubai, Beijing, Hyderabad, Bengaluru and Mumbai.

## Slide 3: A Microbial Fuel Cell-Based Detection System for the Heating Value of Sludge
Shaoan Cheng
shaoancheng@zju.edu.cn
State Key Laboratory Clean Energy Utilization
Zhejiang University
Aug. 11-13, 2014, San Antonio, USA

## Slide 4
Background
Experiments and results
Conclusions
Contents

## Slide 5
Drying process
wastewater
River sidement
fertilizer
Building materials
fuel
Sludge and utilization
Water
Organics
Inorganics

## Slide 6
Landfill
burn
fertile land
Amount increased >10%
Utilization depends on
heating value
It is highly needed to first and quickly know the heating value of sludge before used it
Sludge and utilization

## Slide 7
special apparatus
complicated measurement steps
long detection time.
Proximate analysis based multiple regression models
oxygen bomb
element analysis
industrial analysis
Present method for measuring
the heating value of sludge methods

## Slide 8: New technology:microbial fuel cell
Heating value of sludge----TCOD of sludge
TCOD---SCOD
Heating value of sludge----Microbial fuel cell
Microbial fuel cell----SCOD
？

## Slide 9: What’s microbial fuel cell
A MFC is a device that use bacteria to oxidize organic matter and produce electricity. The bacteria (attached to the anode) produce electrons that travel to the cathode (current).
Proton Exchange membrane
load
Anode
Cathode
bacteria
Oxidation products (CO2)
Fuel (wastes)
e-
e-
O2
H2O
H+
Reference: Liu et al., Environ. Sci. Technol. 2004
This is how a MFC works
Mediater
Direct
Nanowire

## Slide 10
Waste water
Container
Clean water
Container
CO2
Bacteria
H+
O2-
O2
IN PUT
e-
OUT PUT
e-
Fan
CO2
H+
Organics
Anode
Cathode
O2-
Application : treat wastewater
and recovery energy
Notes: 10

## Slide 11
Waste water
Container
Clean water
Container
CO2
Bacteria
H+
O2-
O2
IN PUT
e-
OUT PUT
e-
Fan
CO2
H+
Organics
Anode
Cathode
O2-
Treating wastewater for recovery of energy
Microbial fuel cell
Notes: 11

## Slide 12: MFC:Power and COD removal
Hong et al, EST, 2005
Power generation related to the COD, specially in low COD region

## Slide 13: Voltage of MFC ---SCOD
Hong Liu, et al, Environ. Sci. Technol., 2004, 38 (14), pp 4040–4046

## Slide 14: Experiments
R
Reference
Nickel foam air cathode
Glass fiber separator
Ti wire
Carbon brush anode
Sludge
four kinds of sludge with different heating values :1674，1838， 1762，1892 J/Kg；and COD: 3960，6040，4498，6247 mg/L, respectively。
Single chamber MFC

## Slide 15: Experiments
Inoculation: activated sludge as inocula, batch mode, external resistance of 1000 Ω
Operation: when the voltage of the MFC was less than 10 mV, the reactor was refilled fresh sludge. The above process repeated until the voltage of MFC went to a constant value.
Optimization external reisitance: After start up, the reactors were conducted with ploarization and power density curves for obtaining optimization external resistance.
Performance: To explore the effect of concentration of sludge on the electricity generation and the relationship between the sludge concentration and the electricity generation, two kinds of sludges were diluted with phosphate buffer solution (PBS) as the ratios of sludge to PBS: 1:1、1:2、1:4、1:8。

## Slide 16: Results---power generation and polarization
Chart: Current (mA)
| 0.26200000000000001 | 0.41400000000000031 | 0.53332999999999997 | 0.62500000000000089 | 0.74544999999999995
a-1:1 | 2.4516 | 3.0606 | 3.0476 | 2.7902 | 2.1831
a-1:2 | 3.5438 | 4.5721 | 4.8576 | 4.3457 | 3.2468
a-1:4 | 1.2757 | 1.4 | 0.9219 | 0.60071 | 0.33247
1 | 262 | 207 | 160 | 125 | 82
2 | 315 | 253 | 202 | 156 | 100
4 | 189 | 140 | 88 | 58 | 32
Chart: Current (mA)
| 0.26200000000000001 | 0.41400000000000031 | 0.53332999999999997 | 0.62500000000000089 | 0.74544999999999995
a-1:1 | -270 | -224 | -187 | -161 | -127
a-1:2 | -307 | -273 | -230 | -193 | -148
a-1:4 | -179 | -133 | -83 | -56 | -30
1 | -6 | -19 | -28 | -39 | -48
2 | 4 | -21 | -30 | -41 | -48
4 | 10 | 7 | 5 | 2 | 2
Power density and polarization
Electrode polarization
The electricity generation at different concentration of sludge mainly depends on the anode polarization.

## Slide 17: Results---current generation at different concentrations for four sludges
Chart: Time (h)
Chart: Time (h)
Chart: Time (h)
Chart: Time (h)
A
D
B
C
1:1
1:2
1:4
1:8

## Slide 18: The relationship between the current and heating value
Chart: Current (mA)
| 0.7811399999999995 | 0.47097000000000039 | 0.36195000000000038 | 0.30360000000000031 | 0.29616000000000031 | 0.18344000000000033 | 0.16747999999999999 | 0.13664999999999999 | 0.47950000000000031 | 0.29160000000000008 | 0.1080000000000001 | 7.5999999999999998E-2 | 0.69499999999999995 | 0.41100000000000031 | 0.19700000000000001 | 8.3000000000000046E-2
热值J/kg | 837 | 558 | 419 | 455 | 335 | 364 | 186 | 202 | 562.3 | 374.8667 | 224.92 | 124.9556 | 780.9 | 520.6 | 312.36 | 173.5333
Chart: COD (mg/L)
| 2673.3333300000054 | 1346.6666700000001 | 1060 | 874 | 816.66666999999859 | 761.33333000000005 | 585.33333000000005 | 379.33332999999948 | 1572 | 867.2 | 515.20000000000005 | 279.2 | 2660 | 1672 | 824 | 438
热值J/kg | 837 | 558 | 419 | 455 | 335 | 364 | 186 | 202 | 562.3 | 374.8667 | 224.92 | 124.9556 | 780.9 | 520.6 | 312.36 | 173.5333
linear relationship between the heating value and the current generated.
linear relationship between the heating value and the COD values

## Slide 19: Conclusions
New detection system Based on the single chamber microbial fuel cell has sample structure, low cost and easy to be applied for fast measuring the Heating Value of sludge.
Heating value of sludge has good linear relationship with current production of MFC, therefore, measuring the current under the certain resistance can quickly estimate the heating value of sludge.

## Slide 21
National natural science foundation
(No.21073163, No.51278448)
National High Technology Research
and Development of China (863)
No.2011AA060907, No. 2012AA051502
Natural science foundation of Zhejiang
No.Z4110186, No.2010C31014
No.2011010110018

## Slide 22
Thank You !

## Slide 23: Let Us Meet Again
We welcome you all to our future conferences of OMICS Group International
Please Visit: www.omicsgroup.com
www.conferenceseries.com
www.pharmaceuticalconferences.com