## Slide 1: ‘Biochemical methane potential of Ulva spp. seaweed biorefinery residues.’
Dr Silvia Tedesco
Lecturer and Researcher
Dublin City University
Notes: Seaweeds (macroalgae) have been recently attracting more and more interest as a third generation feedstock for bioenergy and biofuels. However, several barriers impede the deployment of competitive seaweed-derived energy. The high cost associated to seaweed farming and harvesting as well as their seasonal availability and biochemical composition currently make macroalgae exploitation too expensive for energy production only. Recent studies have indicated a possible solution may lay in seaweed integrated biorefinery, in which a bioenergy and/or biofuel production step ends an extractions cascade of high-value chemicals. This results in the double benefit of producing renewable energy while adopting a zero waste approach, as fostered by recent EU societal challenges. This study investigates the biogas potential of residues from Ulva spp. seaweed after biorefinery extractions, which resulted close to raw un-extracted seaweed.

## Slide 2: Towards Third Generation Feedstock for biofuels
Introduction
Food crops
Lignocelluloses
Algae
Food vs fuel
Arable land
Lignin
Notes: Food vs fuel debate
Use of arable land + presence recalcitrant compounds
no land used, fast growing rates, no nutrients addition required in case of cultivation in sea, no or low lignin

## Slide 3
Why Algae
Notes: http://ecolocalizer.com/2010/08/13/lake-erie-mess-a-sign-of-environmental-backsliding/
http://www.powerplantccs.com/ccs/cap/fut/alg/algae__the_biofuel.html

## Slide 4
Eutrophication effects on Irish coastal waters
EPA, 2010
Notes: IMAGE: GREEN TIDES adapted from EPA, 2010 (SEA LATTUCE 10,000 TONNES)
http://www.sciencedirect.com/science/article/pii/S0956053X13002948
http://www.irishenvironment.com/iepedia/eutrophication/ :
When a lake or surface water body or groundwater gets too many nutrients added to it, then certain organisms in the water grow rapidly and cause damage to the water. Common nutrients include phosphates and nitrates, which occur naturally but also are added to the environment by human activities. When the phosphates and nitrates enter the water system in excessive amounts, they promote the growth of algae that absorbs the oxygen and deprives fish and other organisms of the oxygen they need to survive. This depletion of oxygen in the water is called hypoxia. A symptom of the condition is the presence of algae blooms, and it can reduce the biodiversity of the ecosystem where it occurs.
Eutrophication can occur naturally but it is more commonly the result of human activities. Activities that promote eutrophication include fertilisers from farming, lawns and gardens, sewage from treatment plants or faulty septic systems, stormwater runoff from developed land, and even washing with soap in or near the water course.
As fertilizers used in farming, often in excessive applications, and discharge of raw sewage are the most frequent causes, laws and regulations controlling these sources have been effective in reducing the impacts. The construction and improvement of wastewater treatment plants to reduce or eliminate raw sewage are expensive but necessary and effective. The European Union Nitrates Directive is intended to reduce the negative impacts from the use of fertilisers in farming but it has met with opposition from the farming community.

## Slide 5
Integrated biomass conversion processes.
Anaerobic co-digestion for biogas production.
Combined heat and power (CHP), Biomethane.
Current Research –
Background
Notes: Biorefineries with integrated biomass conversion processes produce fuels, power, heat, and valuable chemicals.
This project assesses the biogas potential of waste seaweed residues downstream of existing industrial extraction processes of high-value products (e.g., food supplements, cosmetics, pharmaceutical, etc.).
The primary focus is on finding out the commercial feasibility of implementing the biogas production step into existing Irish seaweed biorefineries.
The commercial feasibility scenarios under evaluation are: the production of biomethane and combined heat and power (CHP).
Benefits for the company: seaweed residues are currently a waste product of the company, and they have now become a resource.

## Slide 6
High-value by-products from ethanol production of seaweed
Notes: http://www.ask-force.org/web/Delft-Seaweeds/Kraan-Mass-Cultivation-Macroalgae-2010.pdf

## Slide 7
Biogas
Extraction
residues
Mannitol
Laminarin
Alginate/Ulvan
Proteins
Fucoidan
IBA Configuration under
investigation in DCU
Notes: Methodologies:
file:///C:/Users/Silvia/Downloads/Boonstra_MA.pdf :
The biomass is crushed in small particles. Ethanol is added, in order to bleach the biomass (to avoid the production of coloured sodium alginate). A high recycling rate is assumed for the ethanol.  During acidification, a small amount of acid is added to the solution. This makes alginic acid to be formed, which is insoluble to water.  Subsequently, sodium carbonate is added for the extraction step, which solubilizes the alginates with the sodium cations in the solution.  This process takes 3 hours. By making use of filtration (without (A) or with (B) cellulose), the sodium alginate is recovered from the aqueous solution.  Again, HCl is added to the solution to promote the formation of a gel of precipitated alginic acid.  Finally a smaller amount of sodium carbonate is added to the gel to form sodium alginate. The drying occurred by a convective dryer.

## Slide 8
Characterization Results
Spp. Ulva | Empiric Formula* | C/N ratio in reactors | TS [%] | VS [% TS] | COD [g/l] | VS fed reactor
October | C3.38H4.96N0.26S0.03O2.21 | 11.3 | 20.5 | 73.3 | 8.4±4 | 2±0.3
May/June | C3.18H4.46N0.19S0.03O2.21 | 14.7 | 15.0 | 64.7 | 15.6±1 | 2±0.1
*Molecular weight: C=12.0107, H=1.00794, N=14.0067, S=32.065, O=15.9994. |  |  |  |  |  | 
Species | SMP [mL gVS-1] | SMP* *Values from [Allen et al.,2013 and 2015]. | Actual CH4 [mL gVS-1] | ACTUAL STD | Biodegradability Index (BI)
UR (Oct) - sludge | 433 | 431 | 72 | 35 | 0.166859
UR (Jun) - sludge | 504 | - | 475 | 19 | 0.943441
UR (Jun)- rotting | 504 | - | 367 | 34 | 0.728319
*Values from Allen et al. (2015) |  |  |  |  | 

## Slide 9
SMP vs Actual Yield
Chart: Stoichiometric (SMP) and actual methane yields [mL gVS-1]
| UR (Oct) - sludge | UR (Jun) - sludge | UR (Jun)- rotting
SMP | 432.7 | 503.9 | 503.9
Actual CH4 | 72.2 | 475.4 | 367
Species | SMP [mL gVS-1] | SMP* *Values from [Allen et al.,2013 and 2015]. | Actual CH4 [mL gVS-1] | ACTUAL STD | Biodegradability Index (BI)
UR (Oct) - sludge | 433 | 431 | 72 | 35 | 0.166859
UR (Jun) - sludge | 504 | - | 475 | 19 | 0.943441
UR (Jun)- rotting | 504 | - | 367 | 34 | 0.728319
*Values from Allen et al. (2015) |  |  |  |  | 

## Slide 10
Final Remarks
Extraction subtracts about 5% of the total VS available to fermentation.
VS content still in range with raw seaweed (70%-80%).
tCOD increases significantly from cold to warm seasons: 8,4 – 15,6 g/L.
C/N ratio to be balanced in reactors.
SMP in range with values from starch and Miscanthus.
Biodegradation efficiency (17%-94%).
Methane 40% - 61% (peaks at 70%).
High gaseous NH3 (>300 ppm) and H2S (>100ppm) released.

## Slide 11
SEAWEED-BASED BIOGAS:
Enzymatic and biological treatments effect to be evaluated
Ideal inoculum and co-substrates among local resources/wastes to be identified
Low inhibition but excessive gaseous H2S and NH3
Collaboration Opportunities
GOAL:
To design and develop a customized biorefinery cascade with an integrated energy production step for each Irish seaweed species that is sustainable and economically viable.

## Slide 12
Dr Silvia Tedesco
(Ph.D., CEng., MEng., B.Eng.)
School of Mechanical and Manufacturing Engineering
Faculty of Engineering and Computing
Dublin City University
THANKS FOR YOUR ATTENTION
Email: silvia.tedesco@dcu.ie