## Slide 1
Electromagnetic-based Ethanol Chemical Sensor using Metamaterial Absorber
Sungjoon Lim (Ph.D.)
Microwave Wireless Communication Lab (MWCL)
School of Electrical and Electronics Engineering,
Chung-Ang University
sungjoon@cau.ac.kr
May 2017

## Slide 2: Agenda of Today’s Talk
Research Background
Design and Structure
Results and Discussion
Conclusion

## Slide 3
· Conventional process for bioassays and sensing chemical liquid
Tubes or valves are used. Most of liquids are wasted
· Microfluidic channel Minimize wasted liquid
Using A little amount Sensitivity
[ Most of liquid are wasted ]
[ Minimize wasted liquid]
[ Conventional Equipment]
[ Microfluidic channel ]
Research Background

## Slide 4
reference: Google
Making use of appropriate fabrication processes and ingredients, microstructure PDMS elastomers may exhibit favorable electrical performance, and withstand severe folding, twisting, and straining without any mechanical failures.
Research Background
Microfluidic Channels for Different Applications

## Slide 5
Research Background
Microfluidically Tunable RF Structures
[1] Pourghorban Saghati, J. Singh Batra, J. Kameoka and K. Entesari, "A Microfluidically Reconfigurable Dual-Band Slot Antenna With a Frequency Coverage Ratio of 3:1,“
in IEEE Antennas and Wireless Propagation Letters, vol. 15, no. , pp. 122-125, 2016.
Switchable dual band slot antenna [1]
Flexible liquid metal microstrip patch antenna [2]
[2] G. J. Hayes, J. H. So, A. Qusba, M. D. Dickey and G. Lazzi, "Flexible Liquid Metal Alloy (EGaIn) Microstrip Patch Antenna," in IEEE Transactions on Antennas and
Propagation, vol. 60, no. 5, pp. 2151-2156, May 2012.

## Slide 6
Research Background
Metamaterials
Split Ring Resonator (SRR)
It responds to EM waves with a magnetic response.
Resonant permeability (μ) is produced.
Electric Ring Resonator (ERR)
It responds to EM wave with electric response.
Resonant permittivity (ε) is produced.
ERR with Conducting Ground Plane
It generates both electric and magnetic responses.
Electric response can be controlled by the geometry of the ERR.
Magnetic response can be controlled by the spacing between the ERR and ground plane.
Watts, Claire M., Xianliang Liu, and Willie J. Padilla. "Metamaterial electromagnetic wave absorbers." Advanced materials 24.23 (2012): OP98-OP120.

## Slide 7
Research Background
Electric ring resonator (ERR) is placed on the top of the substrate.
Thin cut wire is placed on the bottom of the substrate.
Electric response can be controlled by the geometry of the ERR.
Magnetic response can be controlled by the spacing between the ERR and bottom wire.
Currents in the ERR and wire are anti-parallel.  Magnetic couples to them providing a resonant μ.
From these phenomena, metamaterial absorber can match the impedance to free space.
It use losses in the homogeneous layer to absorb the incident radiation.
N. I. Landy, S. Sajuyigbe, J. J. Mock, D. R. Smith, and W. J. Padilla, “Perfect metamaterial absorber,” Phys. Rev. Lett., vol. 100, no. 20, 2008.
Metamaterial absorber

## Slide 8
Tailor the effective permittivity and permeability of the metamaterial.
Metamaterial’s impedance and air’s impedance can be matched.
Minimize reflection and maximize losses, so we can realize a perfect absorber.
< Metamaterial absorber design >
MTM
Air
η2
η1
Research Background
Principle of the metamaterial absorber

## Slide 9: Agenda of Today’s Talk
Research Background
Design and Structure
Results and Discussion
Conclusion

## Slide 10
Design and Structure
Structure of the proposed metamaterial sensor
The split-ring cross resonator (SRCR) is adopted because of its symmetric and simple structure.
The bottom layer is fully covered with conductor to prevent transmission.
The LC resonance of the SRCR can be generated from the inductance of the crossed wire as well as the capacitance of the gap at the circular ring.
The capacitive components of the SRCR are dependent of the effective dielectric constant around the gap, as shown in the following equation :
< Layout of the proposed sensor >
W. Withayachumnankul, C. Fumeaux, and D. Abbott, “Compact electric-LC resonators for metamaterials,” Optics Express, vol. 18, no. 25, pp. 25912-25921, 2010.

## Slide 11
Design and Structure
Simulated E-field distribution and channel layout of the proposed sensor
For designing the microfluidic channels, the electric field distribution of the metamaterial absorber is simulated.
The E-field of the incident wave is strongly coupled around the SRCR, especially at the left and right side capacitive gaps.
Therefore, the microfluidic channel should be designed considering all capacitive gaps of the SRCR.
< Simulated E-field distribution >
< Layout with a meandering channel >

## Slide 12
Design and Structure
Final design of the proposed sensor
The proposed chemical sensor consists of three layer.
The microfluidic structure is engraved in the dielectric substrate. Extra devices for the microfluidic channels are not required.
Considering practical measurement environments, the final chemical sensor, including the liquid inlet and outlet, is shown in the figure above.
< Three-dimensional structure >
< Top view of the final chemical sensor >
Conductive Pattern
Layer (SRCR)
Fluidic Channel Layer
Bottom Layer

## Slide 13: Agenda of Today’s Talk
Research Background
Design and Structure
Results and Discussion
Conclusion

## Slide 14
The prototype sample was fabricated by combining three layers of FR4 substrate with a permittivity of 3.7 and dielectric loss of 0.02.
The first layer consists of a conductive SRCR pattern etched on 0.1-mm-thick FR4 substrate at the top of the entire structure.
The second layer, placed in the middle, is the microfluidic channel with a 0.1-mm thickness carved by using craft-cutting technology.
The bottom layer of 0.8-mm-thick FR4 substrate is fully covered with copper on only one side.
Each layer is attached by adhesive laminating film.
Results and Discussion
Fabricated prototype sample of the proposed sensor
< Photograph of the fabricated sample >
Empty state
Liquid-filled state

## Slide 15
Electric and magnetic responses of the proposed sensor
Results and Discussion
< Empty state >
< Filling with DI water >
The electric and magnetic responses of the proposed chemical sensor can be understood by investigating the electric and magnetic field distributions.
When the microfluidic channel is in the empty state, the electric and magnetic fields are strongly distributed around the SRCR at 12.12GHz.
The strong electric and magnetic responses are only generated at 10.64GHz for a 20% concentration, and only at 11.33GHz for an 80% concentration of the ethanol.
The proposed chemical sensor has its electric and magnetic resonance at different frequencies in accordance with the types and concentrations of the substances that fill the microfluidic channels.
Using this principle, the proposed sensor can detect the concentrations of the ethanol injected into the microfluidic channels.
< Ethanol 80% >
< Ethanol 20% >

## Slide 16
Relative permittivity and permeability of proposed metamaterial
Results and Discussion
Real and imaginary values of simulated relative permittivity and permeability for (a) empty state, (b) filled with DI-Water, and (c) 20% and (d) 80% concentrations of the ethanol (vertical lines indicate the resonant frequencies).

## Slide 17
Reaction of laminating film with different chemicals
Results and Discussion
The absorptivity of the proposed chemical sensor is measured for different liquids.
However, the type of liquid is limited because the adhesive laminating film is reacted with Acetone, Propanol, Benzene and Tetrahydrofuran as shown in the figure below.
When the laminating film with 0.06 mm thickness reacts to Acetone, Propanol, Benzene and Tetrahydrofuran, the film gets thicket to 0.296, 0.29, 0.31 and 0.42 mm, respectively.
Therefore the proposed sensor cannot be used for these mentioned chemicals because the microfluidic channel gets stuck.

## Slide 18
The absorptivity can be calculated by,
But, transmission is zero because of
the metallic bottom layer.
Two WR-90 waveguide adapters and Anritsu MS2038C network analyzer are used for measurement.
The waveguides are placed on the top and bottom of the prototype sample, and the reflection coefficients were measured.
We used the dominant TE10 mode of WR-90, the incident wave from WR-90 into the prototype sample is longitudinal.
Therefore, we placed the prototype sample horizontally.
Results and Discussion
Waveguide measurement setup

## Slide 19
The proposed sensor has 92.9% absorptivity at 12.12 GHz in the empty state of the channel.
When the liquids are injected into the channel, the resonant frequency shifts to 11.46 GHz (ethanol), 10.54 GHz (tap water), and 10.42 GHz (DI water).
When the polarization is changed, the proposed chemical sensor produces almost the same results.
Results and Discussion
Simulation and measurement results for different liquids
< Different liquids >
< Polarizations >

## Slide 20
The performance of the prototype sample is measured using Ethanol diluted with DI water, from 0% (DI water 100%) to 100%.
When the concentration of ethanol is changed from 5% to 80%, the resonant frequency of the proposed sensor is observed to shift linearly from 10.49 GHz to 11.33 GHz.
From the resonant frequency shift, sensitivity of the proposed sensor can be defined.
( a = 0.0105 [GHz/%], sensitivity )
Results and Discussion
Measurement results for different concentration of Ethanol
< Measured absorptivity >
< Resonant frequency shift >

## Slide 21
The performance of the prototype sample is measured using Methanol diluted with DI water, from 0% (DI water 100%) to 100%.
When the concentration of Methanol is changed from 0% to 100%, the resonant frequency of the proposed sensor is observed to shift from 10.25 GHz to 11.2 GHz.
Results and Discussion
Measurement results for different concentration of Methanol
< Measured absorptivity >
< Resonant frequency shift >

## Slide 22
The performance of the prototype sample is measured using Acetonitrile diluted with DI water, from 0% (DI water 100%) to 100%.
When the concentration of Acetonitrile is changed from 0% to 100%, the resonant frequency of the proposed sensor is observed to shift from 10.2 GHz to 11.6 GHz.
Results and Discussion
Measurement results for different concentration of Acetonitrile
< Measured absorptivity >
< Resonant frequency shift >

## Slide 23
The performance of the prototype sample is measured using Propanol diluted with DI water, from 20% (DI water 100%) to 100%.
When the concentration of Acetonitrile is changed from 0% to 80%, the resonant frequency of the proposed sensor is observed to shift from 10 GHz to 11.15 GHz.
Results and Discussion
Measurement results for different concentration of Propanol
< Measured absorptivity >
< Resonant frequency shift >

## Slide 24
The performance of the prototype sample is measured using Acetone diluted with DI water, from 20% (DI water 100%) to 100%.
When the concentration of Acetonitrile is changed from 0% to 80%, the resonant frequency of the proposed sensor is observed to shift from 10.1 GHz to 10.35 GHz.
Results and Discussion
Measurement results for different concentration of Acetone
< Measured absorptivity >
< Resonant frequency shift >

## Slide 25: Agenda of Today’s Talk
Research Background
Design and Structure
Results and Discussion
Conclusion

## Slide 26
A novel electromagnetic-based ethanol sensor using a microfluidic metamaterial absorber is proposed.
The proposed chemical sensor can detect ethanol concentrations by measuring the changes in a resonant frequency.
The resonant frequency of the proposed chemical sensor changes from 10.49 GHz to 11.46 GHz when the concentration of ethanol is varied from 5% to 100%.
It is experimentally demonstrated that the proposed sensor is insensitive to incident polarization.
It is experimentally verified that the proposed chemical sensor is working up to 100% ethanol, 100% methanol, 100% acetonitrile, 80% propanol, 80% acetone and 5% benzene.
When the proposed metamaterial resonator is extended to a large periodic array, the chemical sensor can be effectively used for wireless chemical sensors.
Conclusion

## Slide 28
Appendix
Figure shows the reflection peaks while the loss factor in the material is varied.
When the dielectric loss tangent is changed to zero (from 0.02), the reflections are increased from -19 dB to -4.5 dB at 9.7 GHz.
In addition, when copper is replaced by a PEC with infinite conductance, the reflection is increased to 0 dB.
Varying loss factors of metamaterial absorber