## Slide 1: Monitoring Water Quality of Inland Lakes by Remotely Sensed Observations
Wei Yang
Center for Environmental Remote Sensing
Chiba University, Japan
2017-June-1

## Slide 2: Outline
Sect. 4
Sect.2
Sect.3
Sect. 1
Enhanced Three-band Index for monitoring Chlorophyll-a
SAMO-LUT algorithm for monitoring water constituent concentrations
General introduction
General conclusions
2

## Slide 3
Advantage of Satellite Remote Sensing
Satellite remote sensing can provide
synoptic observations of water area
Waste Water
3

## Slide 4
Material
Target Water Area
SATELLITE
Bio-optical model
Physical Principle of Remote Sensing in Water Body
Scattered
a(λ)
Absorbed
Backward
bb(λ)
Pure Water
CDOM
Tripton
Phytoplankton
Reflectance: R(λ)
4
b(λ)
Inherent Optical Properties (IOP)
Specific Inherent Optical Properties (SIOP) = IOP/Concentration

## Slide 5
Case I waters : waters are those dominated by phytoplankton (e.g. open oceans).
Case II waters : waters are containing not only phytoplankton, but also non-phytoplankton suspended solids (i.e., tripton) and colored dissolved organic matters (CDOM) (e.g. coastal and inland waters).
Still challenging
Chl-a can be satisfactorily estimated with satellite images (Gordon & Morel, 1983)
Water Types: the Perspective of Remote Sensing
5

## Slide 6
Interactions between Different
Components
Difficulty for Monitoring Case II Waters
Case I waters
Case II waters
Phytoplankton
Tripton
6
CDOM

## Slide 7
Case I waters
Case II waters
Tripton = 90 g m-3
Reflectance spectra for case I and II waters
7

## Slide 8
A number of methods have been proposed, e.g., Matrix Inversion Method (Hoogenboom et al., 1998), Band-ratio index (Gons, 1999; Ammenberg et al., 2002), Three-band index (Gitelson et al., 2008), and so on.
The basic idea for all of the methods is to isolate the interactions between different components.
Among these methods, the 3-band index significantly outperformed other indices (Gitelson et al., 2008).
Review of Previous Studies for Remote Sensing
in Case II Waters
8

## Slide 9: Principle of the 3-band index: Absorption
λ2≈ 708nm
λ3≈740nm
λ1≈ 665nm
9

## Slide 10
λ2≈ 708nm
λ3≈740nm
λ1≈ 665nm
Principle of the 3-band index: Backscattering
10

## Slide 11
Principle of the 3-band index: Reflectance
3-band Index
Chl-a
0
=
Constants
11

## Slide 12: Problem of the 3-band index
is not reasonable anymore (Le et al., 2009).
For waters with high turbidity (e.g. some Asian Lakes), the assumption
In these cases, the 3-band index becomes:
The existing methods still cannot provide satisfactory estimations for turbid case II waters.
Denominator includes the absorption not only
phytoplankton, but also tripton and CDOM
12

## Slide 13: Main objectives of my research
1
To develop more effective methods to isolate the interactions between water components
2
To validate their performances using simulation, in situ and satellite datasets
13

## Slide 14: Section 2
Sect. 2
An Enhanced 3-band Index for estimating Chl-a in turbid Case II waters
14

## Slide 15: Absorption properties for turbid water case (e.g. TSS=20 g m-3)
Hints for new index
λ2≈ 708nm
λ1≈ 665nm
λ3≈740nm
15

## Slide 16
Development of the Enhanced 3-band Index
Chl-a = l × New Index + m
New Index
Chl-a
0
Constants
16

## Slide 17: Study Areas
Lake Kasumigaura,
Japan
Location: Ibaraki
Area: 171 ㎞2(western)
Average depth：4 m
Case II water:
・mixture of phytoplankton, tripton, and CDOM
・dominant species
diatom（winter）
cyanobacteria（summer）
Field survey: 3 times
(Feb. 18, 2006; Aug. 7, 2008; Sep. 1, 2009; routine field survey)
total 61 sites
20km
30km
Lake Dianchi,
China
Location: Yunnan Province, China
Area: 300 ㎞2
Average depth：6 m
Case II water:
・mixture of phytoplankton, tripton, and CDOM
・dominant species
cyanobacteria
Field survey: 4 times
(Oct. 23, 2007; Jul. 15, 2008; Mar. 12, 2009; Jul.-Aug., 2009)
Total 53 sites
17
Notes: 17

## Slide 18
Data Collections
Phytoplankton (Chl-a)
Samples taken to lab;
SCOR-UNESCO equations.
Remote sensing reflectance
Water-leaving radiance;
Downward irradiance;
Downward radiance of skylight.
18

## Slide 19: Results for Lake Kasumigaura, Japan
y = 282.18x + 29.12
R
2
= 0.82
0
20
40
60
80
100
120
-0.05
0.05
0.15
0.25
0.35
Original three-band index
Measured Chl-a (mg m
-3
)
(A)
y = 161.24x + 28.04
R
2
= 0.90
0
20
40
60
80
100
120
-0.1
0.1
0.3
0.5
0.7
Enhanced three-band index
Measured Chl-a (mg m
-3
)
(B)
y = 0.55x + 27.98
R
2
= 0.48
0
20
40
60
80
100
120
0
20
40
60
80
100
120
Measured Chl-a (mg m
-3
)
(C)
Estimated Chl-a (mg m
-3
)
from original three-band index
RMSE = 13.97 mg m
-3
MNB =
-
4.53%
NRMS = 19.01%
y = 0.85x + 15.76
R
2
= 0.83
20
40
60
80
100
120
140
20
40
60
80
100
120
140
Measured Chl-a (mg m
-3
)
(D)
Estimated Chl-a (mg m
-3
)
from enhanced three-band index
RMSE = 8.68 mg m
-3
MNB = 6.83%
NRMS = 12.30%
Original 3-band
Enhanced 3-band
Original 3-band
Enhanced 3-band
19

## Slide 20: Results for Lake Dianchi, China
y = 259.87x + 10.29
R
2
= 0.84
0
20
40
60
80
100
120
140
160
0
0.1
0.2
0.3
0.4
0.5
Original three-band index
Measured Chl-a (mg m
-3
)
(A)
y = 119.57x + 10.26
R
2
= 0.91
0
20
40
60
80
100
120
140
160
0
0.25
0.5
0.75
1
1.25
Enhanced three-band index
Measured Chl-a (mg m
-3
)
(B)
y = 0.58x + 35.72
R
2
= 0.74
0
50
100
150
200
250
300
350
0
50
100
150
200
250
300
350
Measured Chl-a (mg m
-3
)
(C)
Estimated Chl-a (mg m
-3
)
from original three-band index
RMSE = 41.29 mg m
-3
MNB = 0.75%
NRMS = 35.83%
y = 0.89x + 8.67
R
2
= 0.96
0
50
100
150
200
250
300
350
0
50
100
150
200
250
300
350
Measured Chl-a (mg m
-3
)
(D)
Estimated Chl-a (mg m
-3
)
from enhanced three-band index
RMSE = 15.82 mg m
-3
MNB =
-
3.26%
NRMS = 21.43%
Original 3-band
Enhanced 3-band
Original 3-band
Enhanced 3-band
20

## Slide 21: Section 3
Sect. 3
Estimation of water constituent concentrations in case II waters by semi-analytical model-optimizing and look-up-tables (SAMO-LUT)
21
Objective:
To provide information of not only Chl-a, but also tripton and CDOM.

## Slide 22
Tripton estimation model:
Chl-a estimation model (3-band index):
B5, B7, B9, and B10 denote MERIS bands 5 (555-565 nm), 7 (660-670 nm), 9 (703-713 nm), and 10 (750-757 nm), respectively
CDOM estimation model:
Selection of Three Previous
Semi-analytical Models
(Gitelson et al., 2008)
(Ammenberg et al., 2002)
(Ammenberg et al., 2002)
22

## Slide 23
Remote-sensing reflectance generated from:
[Chl-a] ranges： 1-300 mg m-3;
[Tr] ranges： 1-250 g m-3;
[CDOM] ranges： 0.1-10 m-1.
In total, 19,964 samples for regression analysis
Simulation test for re-analyzing previous models
23

## Slide 24: Problem for previous model (Chl-a vs. 3-band index)
Chl-a=300 mg m-3
24

## Slide 25: Problem for previous model (Tripton vs. Rrs(B10))
25

## Slide 26: Problem for previous model (CDOM Vs. Rrs(b7)/ Rrs(b5))
26

## Slide 27: Development of the new algorithm Semi-Analytical Model-Optimizing and Look-Up Table (SAMO-LUT)
Basic idea of this new method is an imaginary case II water, in which only one component changes while the other two are controlled as constants.
Constants
Rrs is changing only with Chl-a.
Possibility for improving three-band index
27
E.g. Tr and CDOM are constants; only Chl-a is changing :

## Slide 28: Example of tripton and CDOM controlled as constants (e.g. Chl-a vs. 3-band index)
(I)Tr=1, CDOM=0.1
(II)Tr=110, CDOM=2
(III)Tr=250, CDOM=10
28

## Slide 29: Construction of Look-up Tables (LUT) using simulation data
The coefficients of Chl-a model for each combination of Tripton and CDOM are stored in the LUT.
The practical problem is how to find the optimal models for a given pixel?
29

## Slide 30: Iteration strategy in the SAMO-LUT method (Step 1: getting initial values)
30

## Slide 31: Iteration strategy in the SAMO-LUT method (Step 2: optimizing estimation model)
Repeat !
Chla0 = Chla1
Tr0 = Tr1
31

## Slide 32: Ending the iteration by difference between the current and last iterations
10 times
32

## Slide 33
Validation results: By simulated data (noise-free)
RMSE
（0.43,0.42,0.06）
33

## Slide 34
Validation results: By in situ data ( low noise)
RMSE
（3.4,1.8,0.2）
34

## Slide 35
Validation results: by MERIS data ( high noise)
RMSE
(8.8, 6.9, 0.25)
35

## Slide 36
Kunming City
Weak Wind
Strong Wind
Spatial Distribution of Water Quality
36

## Slide 37: Long-term Monitoring in Lake Kasumigaura
(Matsushita, Jaelania, Yang et al., 2015, RSSJ)
Time-series of satellite estimation show high agreements with field measurements.

## Slide 38: Conclusions: my proposed algorithms
38

## Slide 39: Take-home Messages
Scientists in Chiba University, Japan are working on satellite monitoring of water quality.
Our proposed algorithm worked well in long-term monitoring of water quality parameters in Japan’s lakes.
We are challenging the continental/global monitoring of inland lakes, to aid the conventional investigations.
39

## Slide 40: Thank you!