## Slide 1: Fermentation technology to recover energy and high-value added products from seaweed
Yutaka Nakashimada
Hiroshima University
Supported by
Bioprocess and Biosystems Engineering 2016

## Slide 2: Marine biomass as energy and material feedstock
Chart: 
| Brawn algae | Red algae | Green algae
Yield amount (Mt/y) | 1.301 | 0.807 | 0.2
Production potential (Mt/y) | 13.299 | 1.803 | 0.5
Land biomass
・Agricultural crops (1st gen.)
（Sweet potato、Cane etc.）
・Non-edible biomass (2nd gen.)
Problems for use
・Competition among food demand
・Costly pretreatment of lignocellulosic materials
Marine Biomass (3rd gen.)
Advantage of use of marine algae
・Less competition among food demand
・Huge abundance all over the world
・Easy pretreatment due to low lignin contents
Crop straws
Forest remaining mat.
Notes: We think marine biomass is third generation as the feedstock for biomass refinery.
Use of marine biomass has several advantages compared to that of Land Biomass such as lsee competition among food demand, huge abundance all over the world and easy pretreatment due to low lignin contents.

## Slide 3: The most popular seaweed in Japan Brown algae, Laminaria Japonica (Makonbu)
Tokyo
Hiroshima
Hakodate, Hokkaido
The most harvested and cultivated site of Makkonbu in Japan
Aquafarming site of seaweed
Cultured seaweed
Drying seaweed

## Slide 4: Biomass yield of marine algae
 | Yield (t-DW/ha/yr) | Ref.
Brawn algae |  | 
Laminaria japonica | 30 | 1
Macrocystis pyrifera | 40 | 1
2nd generation of land biomass |  | 
Napiergrass | 85 | 2
Parennial ryegrass | 27 | 2
Sorgam | 47 | 2
Switchgrass | 15 | 2
1st generation of land biomass |  | 
Sugarcane | 50 | 2
1) Yokoyama et al. 2007
2) Asia biomass handbook
Notes: Furthermore, marine biomass, especially brawn algae has the yield competitive to 1st and 2nd generation of biomass feedstocks.

## Slide 5: Element composition of marine biomass with high salt content
Chart: 
固形物 | 10
水分 | 90
Chart: 
マンニトール | 26.1
アルギン酸 | 20.7
繊維質（セルロース） | 9.7
その他糖質 | 5.2
タンパク質 | 5
脂質 | 1.5
灰分 | 29.3
Ex）Brawn algae (Laminaria Japonica, Makonbu)
High salt content
（ca.2〜3% in wet algae）
but contains valuable metals
Feedstock for methane fermentation
, and oil production?
Notes: 海藻は、ワカメ等の褐藻類、ノリに代表される紅藻類、アオサ等の緑藻類に大別されます。
紅藻類および、緑藻類については、すでにエネルギー開発が盛んに行われておりますが、褐藻類については、ほとんどされておりません。
その大きな理由として、海藻に特異的な多糖であるアルギン酸を分解するためには、特別な酵素であるアルギン酸リアーゼが必要であり、その酵素を持っている微生物は限られているからです。
そこで、本研究では褐藻類からの燃料生産を目的としました。
まず、褐藻類からのメタン生産技術には二段発酵法の検討を行いました。次に、エタノール生産技術開発におきましては、アルギン酸を資化し、エタノール生産可能な微生物の探索から行いました。時間の都合上、本発表ではアルギン酸資化エタノール生産菌叢の解析および単離について報告致します。

## Slide 6
Materials
Valuable organic matters
（EPA, DHA, carrotenoids）
Marine algae
Development of key technologies for complete utilization of macro algae as energy and material resources with unique metabolism of marine microorganisms
Valuable inorganic matters
Methane
Energy
Green effluent
Salt-tolerant methane fermentation
Valuable oil fermentation
Pretreatment of algal biomass
Recovery of useful materials
with
waste treatment
Marine microorganisms
methanogenic consortium
Oil producing microorganisms
photosynthetic bacteria
Characteristics of marine seaweeds
・High salinity（〜 3%）
・Particular polysaccharides
（Alginate、agalose etc.）
・Accumulation of valuable metals
Valuable organic matters

## Slide 7: Developing key fermentation technologies of seaweeds
Salt-tolerant methane fermentation by marine microorganisms
Valuable oil fermentation from specific carbohydrates of seaweed
Metal recovery and oil production from residue after fermentation of seaweed

## Slide 8: Presentation
Salt-tolerant methane fermentation by marine microorganisms
Valuable oil fermentation from specific carbohydrates of seaweed
Metal recovery and Oil production from residue after fermentation of seaweed

## Slide 9: Restriction of biogas production from marine seaweed
Inhibited methane formation under high salinity
☞ to overcome high salinity:
i. Dilution of feedstock with pure water.
x need large system for fermentation and wastewater treatment
ii. Acclimation of methanogenic microbial community to high salinity
x It takes long time for acclimation
ii. Use of salt tolerant microbial community in sea environments

## Slide 10: Tidal-flat as microbial resources under saline condition
2. Tidal-flat, Tokyo Bay, Bhiba
3. Tidal-flat, Hiroshima Bay, Hiroshima
1. Tidal-flat, Sea of Aliake, Saga

## Slide 11: High methanogenic activity from brawn algae under salinity condition of marine microorganisms from tidal-flat in Japan
Butyrate,
Propionate
Acetate
H2
Methane
Hydrolysis/acidogenesis
Acetogenesis
Methanogenesis
Seaweed
（Laminaria
Japonica）
T. Miura, et al.; Biores. Technol. 169, 362-366 (2014)
Microbial source | NaCl | Conversion activity (mg-COD/g-VS in sediment/d) |  |  |  | 
 |  | Hydrolysis/ acidogenesis | Acetogenesis |  | Methanogenesis | 
 |  |  | Propionate | Butyrate | H2-CO2 | Acetate
Conventional mesophilic granule |  | 1,735 | 17 | 184 | 3,250 | 54
 | + | 608 (35.0)a | NDb (0) | 27 (14.7) | 2,940 (90.5) | ND (0)
MSc -1 | + | 405 | 79 | 121 | 1,170 | 48
MS-2 | + | 617 | ND | 719 | 1,130 | 45
MS-3 | + | 697 | 35 | 315 | 1,040 | 30

## Slide 12
Undiluted
brown
algae
Stable methane production from undiluted seaweed using the sludge acclimated from marine sediments
Semi-continuous
operation
Fed-batch
acclimated culture
Semi-continuous culture
+
Undiluted
brown algae-
derived salts
Chart: Time (days)
Acetate | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.70228 | 1.2567 | 3.4039 | 4.9004 | 9.4632 | 7.6307 | 8.344 | 11.617 | 14.0895 | 18.7289 | 22.5975 | 10.6057 | 6.5257 | 3.5928 | 5.2156 | 2.5548 | 3.291 | 3.6077 | 3.6474 | 3.574 | 0 | 1.6004 | 0 | 2.4522 | 2.0739 | 1.8531 | 2.2585 | 0 | 0 | 0 | 0 | 2.1823
Propionate | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.2165 | 1.7235 | 3.7682 | 5.6409 | 5.3341 | 7.4587 | 7.7536 | 8.9032 | 10.6953 | 8.0688 | 5.0554 | 2.8181 | 0.9382 | 0.9674 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Methane
Acetate
Propionate
Condition 1
2.0
39
Condition 2
2.9
28
Condition 3
1.7
46
OLR (gVS/kg/day):
HRT (days):
Optimum organic loading rate
= 1.7 kg-VS/m3/d
（HRT=45d, salinity =ca. 2.0% NaCl eq.）
T. Miura et al., Bioresour. Technol. (2016).
Notes: Marine macroalgae contain salts in addition to water, and salts are inhibitory to microbes involving in biomethane production.
Furthermore, for efficient methane production, organic matter content in water-containing macroalgae should be high.
So, macroalgae should be used under undiluted conditions.
So, by using fed-batch acclimated miarine sediment-derived culture, which had high activity under high salinity, we examined whether methane was produced continuously from undiluted brown algae as macroalgae.
We were able to produce methane semi-continuously from undiluted brown algae under three conditions although methane production became slightly unstable during a high organic loading rate in condition 2.
Methane was produced continuously and stably during a decreased OLR in condition 3.

## Slide 13: Comparison of methane production from various species of brown algae
Substrate | OLR (g VS/L/day)a | Methane yield (mL/g VS) | HRT (days) | Methane production rate (mL/L/day)b | Ref.
Diluted conditions |  |  |  |  | 
Laminaria hyperborea | 1.65 | 280 | 24 | 462 | Hanssen, 1987
Laminaria saccharina | 1.65 | 230 | 24 | 380 | Hanssen, 1987
Ascophyllum nodosum | 1.75 | 110 | 24 | 193 | Hanssen, 1987
Laminaria hyperborea | 1.00 | 230 | 20 | 230 | Hinks, 2013
Undiluted conditions |  |  |  |  | 
Saccharina latissima | 1.73 | 238 | 38 | 412 | Jard, 2012
 | 2.17 | 137 | 33 | 297 | Jard, 2012
Saccharina japonica | 2.00 | 358 | 39 | 695 | This study
 | 2.87 | 335 | 28 | 961 | This study
 | 1.74 | 346 | 46 | 602 | This study
Methane was produced under mesophilic conditions. |  |  |  |  | 
a,bThe unit of OLR and methane production rate in this study were g VS/kg/day and mL/kg/day, respectively. |  |  |  |  | 
bThe rate was calculated by multiplying the OLR by the methane yield. |  |  |  |  | 
T. Miura et al., Bioresour. Technol. (2016).
Notes: Achievable methane production rate in the stable methane production in this study, which was calculated by multiplying OLR by methane yield, was higher than any other cases containing diluted and undiluted conditions.
So, semi-continuous culture in this study can highly produce methane from undiluted brown algae.

## Slide 14: Characteristics of microbial consortia developed during anaerobic digestion under high salinity (3-5% NaCl) of dried algal biomass with marine sediments
Miura et al., Biores. Technol. 187, 275 (2015)
Bacteria
Archaea
After acclimation
Original sediment
Unique
Fusobacteriaceae
family
67.09%
Unassigned (4.24%)
Unassigned (4.61%)
14.94% (Piscirickettsiaceae family)
Halotolerant Methanosaeta spp. (41.54%)
After
acclimation
Original sediment
Methanosarcinaspp. (11.07%)
Methanogeniumspp. (20.25%)
Methanosaeta
spp. (0.25%)
Methanosarcinaspp. (0.16%)
Unassigned
(33.51%)
Methanogeniumspp. (0.2%)
18.42% (Methanomicrobia class)
Unassigned (0.02%)
5.93% (Methanomicrobiaceae family)

## Slide 15: Halotolerant methanogens in marine sediments
Figure 6, Kita et al.
Chart: NaCl (M)
| 0.0 | 0.171232876712329 | 0.342465753424658 | 0.513698630136987 | 0.684931506849315 | 0.856164383561644
 | 0.016 | 0.016 | 0.015 | 0.0055 | 0 | 0
 | 0.0366 | 0.0358 | 0.0339 | 0.0272 | 0.0041 | 0
Halotolerant Methanosaeta HA
Methanothermus fervidus (J03375)
Methanohalobium evestigatum (CP002069)
Methanohalophilus mahii (CP001994)
Methanosarcina barkeri (CP000099)
Methanosaeta concilii NBRC 103675T (AB679170)
Methanosaeta thermophila PT (CP000477)
Methanosaeta harundinacea 6Ac (CP003117)
Methanosaeta pelagica 03d30qT(AB679169)
Methanosaeta strain HA (LC033612)
88
100
100
96
99
99
0.1
Phylogenetic tree of based on McrA sequences
Conventional
M. Concilii
Strain HA
Kita et al., J. Biosci. Bioeng., 121(2), 196 (2016)

## Slide 16: High-rate methane production from acetate by acetoclastic methanogens from marine sediments
Na.Acetate 5 g/L
NaCl 30 g/L
Fixed bed-reactor
Pump
CH4
Eff.
Water
bath
Resovoir
Marine sediment
Fixed bed by marine sediment
Chart: Dilution rate (d-1)
| 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 2.0 | 3.74 | 3.74 | 3.74 | 3.74 | 3.74 | 3.74 | 3.74 | 4.4 | 4.89 | 3.79 | 3.79 | 3.79 | 4.8 | 4.8 | 7.45 | 7.45 | 7.45 | 9.2 | 9.2 | 9.2 | 9.2 | 9.2 | 9.2 | 10.7 | 10.7 | 15.6 | 15.6 | 16.2 | 16.2 | 16.2 | 16.2 | 19.8 | 19.5 | 19.8 | 20.1 | 19.5
 | 130.06 | 112.6 | 110.78 | 132.92 | 124.24 | 161.82 | 112.71 | 201.4 | 201.4 | 215.42 | 194.14 | 204.49 | 285.67 | 285.67 | 307.71 | 284.8 | 201.3036 | 205.2629 | 264.853 | 283.6575 | 329.7314 | 358.6008 | 365.4466 | 391.2475 | 412.732 | 459.366 | 401.3215 | 414.8721 | 438.2097 | 509.5834 | 504.9743 | 689.2393 | 703.3315 | 752.2728 | 761.977 | 736.3089 | 628.8962 | 658.0071 | 628.0364 | 710.9846 | 713.0811 | 716.9732
Max. methane production rate：
760mol/m3/d = 12.2 kg/m3/d = 619MJ/m3/d
=18L-oil eq./m3/d = 0.64 kg--oil eq./m3/h
Kita et al., J. Jpn. Petrol. Inst., 59 (1), 9-15 (2016)

## Slide 17: Two-stage methane fermentation process of seaweed
Methanogenesis
(fixed bed)
47 kg-CODCH4/m3/d
with marine sludge acclimated
Acids
Seaweed
Methane
〜20 Nm3/m3/d
750 MJ/m3/d
ca. 57 kg-dry mass/m3/d
(available VS: 80%)
ca. 44 kg-VS/m3/d
Hydrolysis/
acidogenesis
47 kg-CODCH4/m3/d
Organic
subst.

## Slide 18: Developing key technologies
Salt-tolerant methane fermentation by marine microorganisms
Valuable oil fermentation from specific carbohydrates of seaweed
Metal recovery and oil production from residue after fermentation of seaweed

## Slide 19: Valuable oil fermentation by from specific carbohydrates of seaweed
Valuable oil producing
Labyrinthulea
（Aurantiochytrium spp.）
Acetyl-CoA
palmitic acid
Eicosapentaenoic acid (EPA)
Docosahexaenoic acid (DHA)
Mevalonate
Astaxanthin
Squalene
fatty acid synthesis
Polyketide synthesis
Molecular breeding for enhancement of lipid production
No fermentation ability for specific carbohydrates of seaweed
Brawn algae: Mannitol, Alginate
Red algae: Agar

## Slide 20: Valuable oils and carotenoids production from mannitol by two-stage fermentation of Gluconobacter and Aurantiochytrium spp.
Chart: Culture period (hr)
| 0.0 | 2.0 | 6.0 | 10.0 | 12.0 | 12.0 | 33.0 | 60.0 | 84.0 | 108.0 | 120.5 | 156.0 | 180.0
EPA | 1.377 | 4.6236 | 4.9545 | 6.5483 | 6.051 | 4.426 | 3.2731 | 22.1678 | 19.8352 | 12.423 | 6.3915 | 3.535 | 1.8325
DPA | 0 | 0 | 0 | 0 | 0 | 1.977 | 3.3771 | 14.8957 | 11.8298 | 10.1472 | 10.2039 | 4.8635 | 4.7946
DHA | 0 | 0 | 0 | 0 | 0 | 5.7337 | 14.5642 | 53.6811 | 39.3143 | 27.582 | 26.1454 | 10.4351 | 8.8185
Chart: Culture period (hr)
| 0.0 | 4.0 | 8.0 | 12.0 | 12.0 | 33.0 | 60.0 | 84.0 | 108.0 | 132.0 | 156.0 | 180.0
Total carotenoid | 10.1944 | 7.2449 | 9.6153 | 9.6677 | 13.7273 | 11.7448 | 32.4785 | 44.1553 | 43.2331 | 88.2588 | 95.4054 | 78.2999
β-carotene | 0 | 0 | 0 | 0 | 0.54241 | 1.8181 | 6.0508 | 6.8112 | 6.6616 | 10.9955 | 12.5956 | 10.4949
Canthaxanthin | 2.5341 | 2.6732 | 10.3844 | 16.0218 | 16.718 | 29.6717 | 34.7823 | 29.4438
Astaxanthin | 2.9354 | 0 | 0 | 0 | 7.6483 | 6.0169 | 5.7761 | 5.9117 | 5.2511 | 18.0065 | 13.4287 | 10.4168
K.H.V. Arafiles, et al., Appl. Microbiol. Biotechnol. 98, 9207 (2014)
Dried algae
Mannitol
Fructose
EPA, DHA
Astaxanthin
Squarene
Extraction by water
Gluconobacter sp.
Mannitol converter
Salt addition
Growth
Inhibition
Marine Aurantiochytrium
Salt
addition
Single reactor

## Slide 21: “Sugar converters” for production of value-added lipids from marine algae by Aurantiochytrium
Brown algae Laminaria japonica
Carbohydrates 52%
Proteins
15%
Lipids
2%
Ash 31%
Mannitol
30%
Alginate
25%
Cellulose
17%
Fucoidan
etc.
Production of value-added lipids from marine algae by Aurantiochytrium
Gluconobacter
Dysgonomonas
Cellulophaga
Lindra
Laminaran
Gluconobacter
Arafiles, Unpublished
Notes: Chemical methods for the analysis of sulphated galactans from red algae
A new procedure for the separation of water-soluble polysaccharides from brown seaweeds
Zvyagintseva, Tatiana N., et al., Carbohydrate Research, 322.1, 32-39, (1999)
特定
Monthly Determination of Alginate, M/G Ratio, Mannitol, and Minerals in Cultivated Laminaria japonica
Direct fermentation of Laminaria japonica for biohydrogen production by anaerobic mixed cultures
Zvyagintseva, Tatiana N., et al., Carbohydrate Research, (1999)
Honya, Masura, et al., Bulletin-Japanese Society of Scientific Fisheries, 59, 295-295, (1993)
Shi, Xueqing, et al., international journal of hydrogen energy, 36.10, 5857-5864, (2011)

## Slide 22: Valuable oil fermentation by from specific carbohydrates of seaweed
Valuable oil producing
Labyrinthulea
（Aurantiochytrium spp.）
Acetyl-CoA
palmitic acid
Eicosapentaenoic acid (EPA)
Docosahexaenoic acid (DHA)
Mevalonate
Astaxanthin
Squalene
fatty acid synthesis
Polyketide synthesis
Molecular breeding for enhancement of lipid production
fermentation of seaweed via converter microorganisms without genetic engineering for application to food industry

## Slide 23: Developing key technologies
Salt-tolerant methane fermentation by marine microorganisms
Valuable oil fermentation from specific carbohydrates of seaweed
Metal recovery and oil production from residue after fermentation of seaweed

## Slide 24
Metal amount absorbed on Kelp
 | (ppm)* | Ocean (ppm) | Condense (time) |  | (ppm)* | Ocean (ppm) | Condense (time)
K | 18720 | 3.90E+02 | 48 | Ni | 2.00 | 5.00E-04 | 4.00E+03
Na | 1710 | 1.08E+04 | 0.16 | B | 1.5 | 4.50E+00 | 4.00E+03
Mg | 1624 | 1.30E+03 | 1.25 | Mn | 1.1 | 3.00E-05 | 3.67E+04
Ca | 2544 | 4.10E+02 | 6.20 | Ti | 0.98 | 1.00E-05 | 9.80E+04
P | 912 | 6.50E-02 | 1.40 | Zn | 0.96 | 3.20E-04 | 3.00E+03
Fe | 21.6 | 6.00E-05 | 3.60E+05 | Cu | 0.25 | 2.00E-04 | 1.25E+03
Al | 13.0 | 3.00E-04 | 4.33E+04 | Co | 0.21 | 1.20E-06 | 1.75E+05
Y | 12.7 | 1.50E-05 | 8.47E+05 | Cd | 0.00049 | 7.00E-05 | 7
Cr | 5.6 | 2.50E-04 | 2.24E+04 |  |  |  | 
Minor metal
Rare earth
Heavy metal
*0.5 g of dried kelp was dissolved in nitric acid and heated.
Metal concentration was calculated based on moisture content of fresh alga (90%) and specific gravity (1.0).
Okamura et al., unpublished

## Slide 25: Schematic diagram of metal removals from fermentation residues by photosynthetic bacteria
clean water
Metals and organics in fermentation residues
Screening of Marine bacteria
High-functional photosynthetic bacteria
with metal resistance and recovery
Metal concentrating
Heavy, minor metals,
rare earths
Liquid fuel producer
from residual organic carbon
Liquid fuels

## Slide 26: Screening of photosynthetic bacteria (PSB) capable to recover various metal ions
Accumulation of PSB
in sea water
Subculture in
PSB medium
Subculture of PSB medium
with１mM metals（10）
Subculture
Accumulation in PSB medium
with１mM metals（10 sp.）
（Mn,Cd,Co,Se,Te,Ni,Pb,Mo,Cu,Zn）

## Slide 27
Metal removal by Photosynthetic Bacteria
 | Initial conc. (ppm) | Spent medium (ppm) | Harvested cells (ppm) | Recovery* (%) | In kelp** (ppm)
Co | 0.4 | 0.217 | 0.127 | 32.1 | 0.21
Cd | 1.1 | 3.22x10-2 | 1.00 | 91.5 | 0.00049
Cu | 0.77 | 0.111 | 0.615 | 80.1 | 0.25
Y | 128 | 4.38 | 123.55 | 96.5 | 12.7
Metal ion was added into medium individually.
*Recovery (%) = The amount of ion in harvested cells / Sum of ion amounts X 100.
** actual measured value
Minor metal
Rare earth
Heavy metal
Okamura et al., unpublished
Notes: Using this cocktail, cobalt, cupper and cadmium were recovered at high efficiency and rare earth element are also recovered using other cocktail.
These recovery rates promise to remove the metals from kelp wastewater completely.

## Slide 28: Oil-producing bacteria from acetic and propionic acids
Oil content 70%
Mainly (50%) 2-butenoic acid 1-methylethyl ester
10mM NH4Cl
(B) 1mM NH4Cl
(C) 0.1mM NH4Cl
(D) N starvation
Wastewater treatment
Effluent
Seaweed
Anaerobic
digestion
Oil production by newly isolated marine microorganism
Pre-treatment
In wastewater
acetate
propionate
Hydrocarbons (Oil)
Chart: 
 | 7.75 | 246.8 | 209.96 | 705.79
10
1.0
0.1
0
NH4Cl [ mM ]
Total lipid / DCW [mg/g]
Okamura et al. (2016) Bioresour. Technol., 201, 215-221.

## Slide 29: Research achievement
Valuable lipid production
Hydrothermal
treatment
Waste water treat.
Valuable metal recovery
Seaweed
Undiluted salt tolerant
methane fermentation
・ Salt tolerant methanogenic communities were discovered in marine sediments.
・ Microbial community with stable methane formation at 4.5%NaCl was developed.
・ Continuous methane fermentation with undiluted seaweed at HRT 45 day was possible
・ 80% of solid fraction in L. Japonica is solubilized by hydrothermal treatment with and without salt between 150 and 190 oC
・ It was developed novel two-stage fermentation process to produce valuable oil and from algae carbohydrates with Aurantiochytrium and specific converter.
・Whole genome of Aurantiochytrium was sequenced.
・ Over expression of CrtBY accelerated carotenoid production by Aurantiochytrium
・ Several photosynthetic bacteria communities possessing the ability to recover heavy and rare metals was screened.
・Oil-producing bacteria from acetic and propionic acids (main VFAs in the fermentation residue) was discovered.
Green water

## Slide 30: Acknowledgements
Prof. T. Aki (Hiroshima University)
Prof. Matsumura (Hiroshima University)
Assoc. Prof. Y. Okamura (Hiroshima University)
This study is financially supported by CREST, JST, Japan.