## Slide 1: An ARQ Retransmission Scheme for Real-Time Video Multicasting over Mobile Communication Networks
Tsang-Ling Sheu
Department of Electrical Engineering
National Sun Yat-Sen University
Kaohsiung, Taiwan

## Slide 2: Outline
Introduction
Related Work
ARQ Retransmission
Simulation and Discussion
Conclusion

## Slide 3: Introduction
Motivation
  Video Streaming on a Mobile Communication Network
    High bit error rate due to noise and interference
    No retransmission scheme for multicasting a video stream
Proposed Solution
  Integrate retransmission requests from MS in a multicast group to reduce extra bandwidth requirements
  To meet delay constraint of a retransmitted packet
    Buffer and retransmit erroneous packets in the last hop
    Consider different decoding rates of MS

## Slide 4: Related Work
Authors | Pros | Cons
Jinhe Zhou | Unequal Error Protection (UEP) for I/B/P frames to improve retransmission efficiency Use cross-layer solution | 1. Use end-to-end retransmission, no good for real-time 2. Retransmission is determined by application layer. It requires extra overhead to read frame type in RTP headers
James She | Consider retransmitting I/B/P frames for different levels of video quality Consider waiting time and scheduling time at BS buffer | The authors did not consider the time constraints in playout buffer at MS
Jiang Yu | Retransmission does consider delay constraint of each MS | It did not consider network condition, such as PLR It did not consider extra bandwidth required for packet retransmission
A. Nafaa and A. b. Jantan | It considers error burst pattern caused by interferences and noise among neighboring MS Retransmit packets using one-hop Proxy to save delay time | Proxy may require large buffer It did not consider delay constraints for Retransmission timeout

## Slide 5: An OFDMA frame

## Slide 6: System Architecture

## Slide 7: Retransmission
Send feedback
Packet error
BS
Feedback
Retransmission Buffer
Retransmit Packet
Transmission Buffer
IP camera
Video Stream Packet
Packet error
Send feedback
Interference
Interference

## Slide 8: Three conditions for the proposed ABR
ABR (ARQ Block Retransmission)
  Real-time constraints
  SACK threshold
  Extra bandwidth

## Slide 9: The Proposed ABR
An IP Fragment is segmented to a number of ARQ blocks (AB)
Every AB has a block sequence number (BSN)
MS uses ARQ feedback (AF) message to report to BS
Video Slice
GOP
I/B/P frames
IP Fragments
ARQ Blocks
MPDU

## Slide 10: Modified ARQ Header
  Fragmentation sub-header (FSH)
  Use 3-bit reserved field
  Repeated: to number the repeated BSN
ARQ feedback header
  Repeated, Map Size, HOL time
ACK bit map
  Use bit map to record all AB
    1: Successful )。
    0: failed ()。

## Slide 11: The Proposed ABR (1/2)
37
36
35
34
34
34
34
34
34
IP camera
BS
Packet error
Interference
Check if connection is enable ARQ
Divide into ARQ blocks

## Slide 12: The Proposed ABR (2/2)
IP camera
BS
36
Feedback
SACK34 = 0
Feedback
SACK34 = 1
Feedback
SACK34 = 1
Feedback
SACK34 = 0
Feedback
SACK34 = 0
Send ARQ feedback
Check BSN and Repeated number

## Slide 13: Retransmission Delay
Retransmission Delay : | 
Round-Trip Time : | 
Retransmission Delay : | 
Round-Trip Time : | 

## Slide 14: Threshold

## Slide 16: Simulation
Use NS-3
Traffic generator
  Generate I/B/P frames
  Convert I/B/P frames to ARQ blocks
ARQ block retransmission (ABR) modules

## Slide 17: Simulation Topology
MS ID | I frame | B frame | P frame | Decoding rate
1 | 30,488 bytes | 1,524 bytes | 7,622 bytes | 2.5 Mbps
2 | 36,585 bytes | 1,829 bytes | 9,146 bytes | 3.0 Mbps
3 | 42,683 bytes | 2,134 bytes | 10,671 bytes | 3.5 Mbps
4 | 48,780 bytes | 2,439 bytes | 12,195 bytes | 4.0 Mbps
Parameters | Settings
Frame Duration | 10 ms
Duplexing mode | TDD
DL/UL | 1:1
Modulation | 16-QAM
Max packet length | 1,500 bytes
ARQ block size | 1,024 bytes
video stream FPS | 50 FPS
video stream GOP | 10

## Slide 18: Traffic generator
Chart: OFDMA frames
Chart: OFDMA frames
Chart: Seconds
| 0~1 | 1~2 | 2~3 | 3~4 | 4~5 | 5~6 | 6~7 | 7~8 | 8~9 | 9~10 | 10~11 | 11~12
Background | 0 | 0 | 3.0025 | 2.7177 | 1.7259 | 1.6059 | 1.5787 | 2.7721 | 2.8012 | 2.7245 | 0.45897 | 0.43293
Multicast | 3.7348 | 3.6198 | 2.7147 | 2.8624 | 2.7946 | 2.3806 | 3.4865 | 2.9643 | 1.8816 | 1.8135 | 1.6858 | 1.7704

## Slide 19: HOL time
Chart: HOL time in MS (in OFDMA)
Chart: HOL time in BS (in OFDMA)

## Slide 20: Round-trip time
Chart: OFDMA frames
Chart: OFDMA frams

## Slide 21: Percentage of Retransmitted BW vs Multicast BW for different error rates (for I/B/P frames)
Chart: Error Rate (%)
| 5 | 10 | 15 | 20
∆ ≥ 1/4 | 7.6575 | 8.7834 | 8.9228 | 9.0862
∆ ≥ 2/4 | 1.8052 | 4.5005 | 6.5649 | 7.4922
∆ ≥ 3/4 | 0.13522 | 0.30911 | 1.5832 | 2.8444

## Slide 22: Percentage of Retransmitted BW vs Multicast BW for different error rates (for I frames only)
Chart: Error Rate (%)
| 5 | 10 | 15 | 20
∆ ≥ 1/4 | 3.6757 | 5.6496 | 6.7277 | 7.083
∆ ≥ 2/4 | 0.40535 | 1.4779 | 2.219 | 3.5492
∆ ≥ 3/4 | 0.038821 | 0.077641 | 0.26371 | 0.65866

## Slide 23: Improved Video Quality Indicator (1/2)
Chart: Error Rate = 5%
| 2.5 | 3 | 3.5 | 4
∆≥1/4, Original | 88.8333 | 91.4815 | 93.6905 | 94.6528
∆≥1/4, ARQ | 98.2778 | 98.3333 | 98.2937 | 97.4653
∆≥2/4, Original | 91.3889 | 92.3148 | 93.6508 | 93.8542
∆≥2/4, ARQ | 92.1111 | 93.3796 | 94.3254 | 94.6181
∆≥3/4, Original | 89.7222 | 90.6481 | 91.9841 | 94.375
∆≥3/4, ARQ | 89.8333 | 90.7407 | 91.9048 | 94.375
Chart: Error Rate = 10%
| 2.5 | 3 | 3.5 | 4
∆ ≥ 1/4, Original | 81.0556 | 85.6481 | 87.1825 | 87.6389
∆ ≥ 1/4, ARQ | 95.6667 | 96.4815 | 95.0794 | 93.3681
∆ ≥ 2/4, Original | 81.8333 | 83.5648 | 87.5397 | 89.0625
∆ ≥ 2/4, ARQ | 85.2778 | 86.6204 | 89.2063 | 90.3125
∆ ≥ 3/4, Original | 81.7778 | 85.0926 | 86.3889 | 87.7431
∆ ≥ 3/4, ARQ | 82 | 85.2778 | 86.5873 | 87.9514

## Slide 24: Improved Video Quality Indicator (2/2)
Chart: Error Rate = 15%
| 2.5 | 3 | 3.5 | 4
∆ ≥ 1/4, Original | 66.7222 | 76.8981 | 79.3651 | 82.6042
∆ ≥ 1/4, ARQ | 89.2778 | 93.5648 | 88.254 | 89.8264
∆ ≥ 2/4, Original | 72.5 | 77.037 | 81.9444 | 82.1875
∆ ≥ 2/4, ARQ | 78.8889 | 82.037 | 85.7937 | 85.8333
∆ ≥ 3/4, Original | 70.5556 | 75.4167 | 78.9286 | 83.2986
∆ ≥ 3/4, ARQ | 71.6667 | 76.3426 | 79.6429 | 84.0278
Chart: Error Rate = 20%
| 2.5 | 3 | 3.5 | 4
∆≥1/4, Original | 62.5556 | 68.6111 | 71.4286 | 76.875
∆≥1/4, ARQ | 87.8889 | 85.9259 | 83.6905 | 85.2778
∆≥2/4, Original | 62.7222 | 67.6389 | 73.2937 | 76.1111
∆≥2/4, ARQ | 74.2778 | 79.3056 | 81.8254 | 82.4653
∆≥3/4, Original | 60.3889 | 67.4537 | 75.119 | 76.7361
∆≥3/4, ARQ | 62.6667 | 69.4444 | 76.3095 | 77.8472

## Slide 25: Conclusion
(for a fixed bit error rate)
  For a large
  the same erroneous blocks among MS appears
Bit error rate and decoding bit rate (for a fixed )
  When bit error rate is low and decoding bit rate is high, video quality can be improved more significantly by using the proposed ABR

## Slide 26
Thank you
Q & A